## Slide 1
David R. Maidment
Center for Research in Water Resources
University of Texas at Austin
Presentation for TWDB Water for Texas Conference, Austin,Texas, 22 January 2017
Acknowledgments: Ed Clark, National Weather Service; Yan Liu, University of Illinois;
David Tarboton, Utah State University; David Arctur, Harry Evans, Xing Zheng, University of Texas
at Austin; City of Austin, National Weather Service, NCAR, CSEC, Texas Division of Emergency
Management, ESRI, Kisters, National Science Foundation, colleagues and students at UT Austin.
Applying the National Water Model in Texas

## Slide 2: The Opportunity
New National Water Center established on the Tuscaloosa campus of University of Alabama by the National Weather Service and federal agency partners
Has a mission to assess hydrology in a new way at the continental scale for the United States

## Slide 3: NWS River Forecast Centers (RFCs)
  Prepare river and flood forecasts using models based on average basin characteristics
  Provide forecast guidance to Weather Forecast Offices (WFOs)
  Issue daily stage and streamflow forecasts, rainfall and drought data and information, and flash flood guidance
  Work with water managers and other Federal Agencies
3
6600 sub-basins in continental US
Notes: RFC Summary

## Slide 4: Centralized Water Forecasting
National Water Center
Notes: TRANSITION INTO METHODS
FY15 PROJECT HAS FOUR CORE COMPONENTS
RFC archive
Model evaluation service
Modeling testbed
Centralized modeling demonstration

## Slide 5
Inaugural Meeting – May, 2014
This meeting led to an engagement between the academic community of the United States and the National Weather Service to help build the National Water Model

## Slide 6: National Water Prediction Model Configurations
Short-Range
‘Flood Prediction’
Long Range
‘Water Resources’
Analysis & Assimilation
Hourly
3-Hourly
~Daily (x16)
- 3 hrs
Cycling Frequency
Four Forecasting Horizons for National Water Model
0-2 days
0-30 days
Forecast Duration
1km/250m/NHDPlus Reach
1km/250m/NHDPlus Reach
1 km/catchment /NHDPlus Reach
Spatial Discretization & Routing
MRMS blend/ HRRR-NAM bkgnd.
Downscaled HRRR /RAP/NAM blend
Downscaled & bias-corrected CFS
Meteorological Forcing
Medium Range
‘Flow Prediction’
Daily
0-10 days
1km/250m/NHDPlus Reach
Short-range + Downscaled GFS
Operational on 16 August 2016

## Slide 7: Forecasts from National Water Model
Now
Analysis
Best estimate of current conditions
Short Range
Hourly for 15 hours ahead
Medium Range
3 Hourly for 10 days ahead
Long Range
Daily for 30 days ahead
Ensemble of 4 forecasts each 6 hours (16 forecasts total)
2.7 million
stream reaches
(5 TB of forecast information per day)
10AM 19 Jan 2017
San Bernard River near Boling, Texas

## Slide 8: NOAA National Water Model in Texas
Continuous real-time water forecasting
on 190,000 miles of streams and rivers
divided into 98,000 reaches. Data are
publicly accessible now
A transformative improvement for flood resilience in our state!
10AM 19 Jan 2017
San Bernard River near Boling, Texas

## Slide 9: Texas Division of Emergency Management
State Operations Center
Regional Coordinators
Disaster Districts
Counties
Chief Nim Kidd Director, TDEM

## Slide 10: Flood Emergency Response in Texas
Local governments (counties, cities, or towns) respond to emergencies daily using their own resources
They rely on mutual aid and assistance agreements with neighboring jurisdictions
When local jurisdictions cannot meet incident response resource needs, they may ask the state for assistance

## Slide 11: Information Flow During a Flood Emergency
Weather and
Flood Forecasting
Flood Impacts
Assessment of
Conditions
Emergency
Response
Communications
cycle

## Slide 12: Storm in San Bernard Basin, 18 Jan 2017
http://gisdev.srh.noaa.gov/rfcdss2.html
San Bernard River near Boling

## Slide 13: Area of Concern: San Bernard Basin in Brazoria, Fort Bend, Wharton and Matagorda Counties in Texas
Wharton
Matagorda
Brazoria
Fort Bend
San Bernard Basin
San Bernard River
San Bernard River near Boling
NWS Forecast Point BOLT2

## Slide 14: NWS Forecast Points and Basins in San Bernard Basin

## Slide 15: West Gulf River Forecast Center Largest Impact: Forecast of Moderate Flooding (at BOLT2) (made at 7:19PM 18 Jan 2017)
http://water.weather.gov/ahps2/hydrograph.php?wfo=hgx&gage=bolt2

## Slide 16: National Water Model Forecast Map
Wharton
Matagorda
Brazoria
Fort
Bend
http://water.noaa.gov/map
San
Bernard
River

## Slide 17: Forecast of National Water Model for San Bernard River at Boling (peak of 4727 cfs at 10AM) (made at 3 AM Central Time, accessed at 5:30AM 18 Jan 2017)

## Slide 18: National Water Model in San Bernard Basin (800 catchments and stream reaches)
Forecasts are available
for each individual stream

## Slide 19: TDEM Flood Inundation Mapping System
San Bernard River near Boling, TX
Water Depth = 20.3 ft
(from synthetic rating curve)
Discharge = 4767 cfs (from National Water Model)
Forecast of discharge from National Water Model
Converted to depth using a synthetic rating curve
(these data are from the 2AM NWM forecast because
of the time lag to do the conversion to depth)

## Slide 20: Comparison of WGRFC and NWM/TDEM forecast of Water Depth on San Bernard River near Boling, TX
Stage Height of Forecast = 22.9 ft
Minus Stage Height at Zero Discharge ~ 2.8 ft
Equals Water Depth in Stream of 20.1 ft from WGRFC Forecast
Water Depth in Stream from
synthetic rating Curve applied to
National Water Model forecast = 20.3 ft
There is less than 1 foot difference between these two forecast depths!
Water Depth = 20.3 ft
(from synthetic rating curve)

## Slide 21: Lesson Learned: Need Local Intelligence
Need for information
from impacted areas
during floods
Crowd sourcing
Twitter
Send a photo or video
Georeference this info
Use it to update
predictions
800
stream
reaches

## Slide 22: Flood Response Mapping
Level 1 – approximate inundation mapping
Level 2 – approximate impact mapping
Level 3 – detailed inundation mapping
Level 4 – detailed impact mapping
Uses National Elevation Dataset
and rating curves
Impact at County scale
Uses LIDAR and
detailed hydraulic modeling
Impact at Stream Reach scale

## Slide 23: Texas Address Points
8.6 million points
Used for dispatching emergency
response vehicles in 911 systems
Can TNRIS help to
maintain these data?

## Slide 24: What is a Floodplain?

## Slide 25: Method for Determining Flood Risk: Height Above Nearest Drainage (HAND)
HAND
Flood
Normal
Flooding occurs when Water Depth is greater than HAND
Address Point at a home

## Slide 26: Real-Time Flood Inundation Mapping Onion Creek at Highway 183
http://water.weather.gov/ahps2/inundation/inundation_google.php?gage=atit2

## Slide 27: Continental-Scale Flood Inundation Mapping
Catchments and Flowlines
Digital Elevation Model
Height Above Nearest
Drainage (HAND) (relative elevation of land
surface cell above cell in
stream to which it flows)

## Slide 28: Height Above Nearest Drainage for Texas

## Slide 29: Height Above Nearest Drainage for Address Points in Williamson Creek

## Slide 30: This Information Can be Used for Detailed Flood Response Planning by First Responders

## Slide 31: USGS Rating Curve at a Stream Gage
Measure
Water Level
Determine Discharge
Onion Creek at Highway 183

## Slide 32: Reach Hydraulic Parameters
Comid | y | A | R | P | T | V | Ab | As
5781175 | 3 |  |  |  |  |  |  | 
5781175 | 4 |  |  |  |  |  |  | 
Wetted Bed Area
L
As
Ab
V
T
P
A
y
Surface Area
Volume
Depth
T
P
Cross Section Area
Wetted Perimeter
Top Width
R
Hydraulic Radius

## Slide 33: Rating Curve – Connects Discharge with Depth
Chart: Rating Curve for Eanes Creek, ComID = 5781289
| 0 | 607.56406134719555 | 2490.8796015163871 | 5785.1592347077603 | 10565.65567829302 | 16808.943658196451 | 24277.138771673799
Stage Height, h (ft) | 0 | 2.0669 | 3.937 | 5.807 | 7.6443 | 9.4159 | 10.9907
Chart: Rating Curve for Eanes Creek, ComID = 5781289
| 0 | 607.56406134719555 | 2490.8796015163871 | 5785.1592347077603 | 10565.65567829302 | 16808.943658196451 | 24277.138771673799
Stage Height, h (ft) | 0 | 2.0669 | 3.937 | 5.807 | 7.6443 | 9.4159 | 10.9907
Forecast Discharge, Q,
from National Water Model
Flood Depth, y (ft)

## Slide 34: Continental-Scale Flood Inundation Mapping
2
1
1. Forecast discharge with National Water Model
2. Convert discharge to depth using rating curve
3. Convert depth to inundation using HAND
4. Add Address Points to assess impact
3
4

## Slide 35: The challenge of increasing Digital Elevation Model (DEM) resolution
1980’s DMA 90 m
102 cells/km2
1990’s USGS DEM 30 m
103 cells/km2
2000’s NED 10-30 m
104 cells/km2
2010’s LIDAR ~1 m
106 cells/km2
National Elevation Dataset
LIDAR

## Slide 36: Flood Response Mapping
Level 1 – approximate inundation mapping
Level 2 – approximate impact mapping
Level 3 – detailed inundation mapping
Level 4 – detailed impact mapping
Uses National Elevation Dataset
and rating curves
Impact at County scale
Uses LIDAR and
detailed hydraulic modeling
Impact at Stream Reach scale