## Slide 1: TxDOT’s Role in Flood Management
Jack Kayser, P.E., Ph.D., CFM
TxDOT – Austin District – Hydraulics Team
Flash Flood Awareness Meeting
October 8, 2010
Texas Department of Transportation

## Slide 2: Outline of Presentation
TxDOT’s Organizational Structure
Jurisdiction and Responsibilities
Emergency Flood Response Procedures
Contributions to Floodplain Management
Process of Hydrology and Hydraulic Design
Example of Cross Drainage Culvert Design
Summary and Conclusions
References
Texas Department of Transportation

## Slide 3: TxDOT’s Organizational Structure
Texas Department of Transportation
As of August 2009 there are 13,015 TxDOT employees, 11.7% of which are P.E.s or E.I.T.s [1].

## Slide 4: Jurisdiction and Responsibilities
Texas Department of Transportation
For Travis and Williamson Counties there are 1,170 On-System miles and 7,205 Stratmap miles,
statewide there are 80,067 On-System miles and 306,403 Stratmap miles (centerline miles) [2].

## Slide 5
Texas Department of Transportation
Jurisdiction and Responsibilities
On-System:
Plan, Design, Build, Operate, and Maintain
Emergency Response per internal and external request
Off-System:
Inspect All Public Bridges and Bridge Class Culverts
Oversight of Federal Transportation Funds
Emergency Response per Governor’s Office of Emergency Management

## Slide 6: Emergency Flood Response Procedures [3]
Maintenance personnel are encouraged to use their own judgment, eliminating chain of
command delays. Such personnel often personally know local DPS, Fire and EMS personnel.
73% of TxDOT staff are over 40 years of age and 53% have 11 or more years with the agency [4].
Texas Department of Transportation

## Slide 7: Highway Condition Reporting System
Texas Department of Transportation

## Slide 8: Contributions to Floodplain Management
Texas Department of Transportation
Sponsored USGS and
university hydrology and
hydraulic research and
publications, used in
engineering practice.
Standard hydraulic structure
designs and specifications,
used throughout the industry.
Hosting and supporting the
TFMA – NFIP training
program from 2004 to 2008.

## Slide 9: Process of Hydrology and Hydraulic Design [5]
Texas Department of Transportation

## Slide 10: Example of Cross Drainage Culvert Design
Texas Department of Transportation

## Slide 11
Texas Department of Transportation
Where is Structure - What is Scope of Work

## Slide 12
Texas Department of Transportation
Delineation of Watershed

## Slide 13
Texas Department of Transportation
Delineation of Channel

## Slide 14: Revision of Conveyance Due to Ditch Carryover
Texas Department of Transportation

## Slide 15: Hydraulic Analysis of Culvert and Ditch
Texas Department of Transportation

## Slide 16: Summary and Conclusion
Texas Department of Transportation
Two central aspects of dealing with floods:
a. Responding
b. Mitigation
Nature of TxDOT’s response depends on the situation:
a. On-System versus Off-System
b. How the request reaches Maintenance
c. Decisions Made On-Site
Mitigation is made up of two parts:
a. Identifying the Risks
b. Avoiding Adverse Impacts

## Slide 17
Texas Department of Transportation
References
Highway Engineer Staffing Analysis, Texas Comptroller of Public Accounts, January 2010, page 7.
Annual Report – Highway Status Open to Traffic Only, Texas Department of Transportation, Transportation Planning and Programming Division, August 17, 2009.
Information Sharing Plan – Austin District, June 8, 2010
Survey of Organizational Excellence Data Report, Texas Department of Transportation, 2008, pages 2 and 3.
Hydraulic Design Manual, Texas Department of Transportation, March 2009.

## Slide 18: Questions?
Texas Department of Transportation