## Slide 1: Inundation Mapping from BLE Models at River Basin Scale
Prepared by Andy Carter and David Maidment
How to extend flood inundation mapping from gage locations to the whole basin?
Flood Decision Support Toolbox prepared by Interagency Flood Risk Management (InFRM)
https://webapps.usgs.gov/infrm/
Base Flood Engineering Models on River Basins
Inundation Maps at USGS Gages
Presentation for NOAA National Weather Service, 15 September 2020

## Slide 2
Inundation Mapping from BLE Models at River Basin Scale
National Weather Service Flood Inundation Mapping (FIM) Services for Texas
Process for Base Level Engineering (BLE) to FIM for 1-D HEC-RAS Models
Example of 2-D HEC-RAS Model to FIM
Next Steps
Rating
Curve
Average
Stream Depth
Inundation
Map
Flood Discharge Forecast
from the National Water Model
or WGRFC Model
Flow Rate

## Slide 3
Inundation Mapping from BLE Models at River Basin Scale
National Weather Service Flood Inundation Mapping (FIM) Services for Texas
Process for Base Level Engineering (BLE) to FIM for 1-D HEC-RAS Models
Example of 2-D HEC-RAS Model to FIM
Next Steps
Rating
Curve
Average
Stream Depth
Inundation
Map
Flood Discharge Forecast
from the National Water Model
or WGRFC Model
Flow Rate

## Slide 4: National Water Model
Version 2.0
Deployed: June 2019
Domains: CONUS and Hawaii
CONUS Configurations:
3-Hour and 28-Hour Analysis and Assimilation (Hourly and Daily)
18-Hour Short Range Forecast (Hourly)
10-Day Medium Range Forecast (6-Hourly)
30-Day Long Range Forecast (Daily)
Hawaii Configurations:
3-Hour Analysis and Assimilation (Hourly)
60-Hour Short Range Forecast (6-Hourly)

## Slide 5: NHDPlus: One reach = one catchment for US
Geospatial Foundation for the National Water Model
NHDPlus
2.7 million reach catchments in US
average area 3 km2
reach length 2 km
Uniquely labelled
National Elevation Dataset
National Hydrography Dataset
Watershed Boundary Dataset
National Land Cover Dataset

## Slide 6: Flood Information for one NHDPlus Catchment
Deputy Jessica Hollis
19 September 2014
National Hydrography Dataset Plus
catchment for Bear Creek
(area = 5.71 km2)
Low water crossing at
3400 Fritz Hughes Park Rd

## Slide 7: Complementary Hydrologic Prediction Systems
Advanced Hydrologic
Prediction Service
National Water Model
1 forecast point for every 1,000 river miles
Replace
Route
and

## Slide 8: NWC FIM Services
Replace and Route FIM Services
National Water Model FIM Services
FIM v2.X MS
FIM v1.0 FR
None
FIM v2.Xc
FIM v1.0c
FIM v2.X MS
None
Note: Replace and Route FIM only available downstream of RFC forecast points.
Note: National Water Model FIM available along all modeled river segments..
All this mapping is based
on the Height Above
Nearest Drainage
(HAND) method

## Slide 9
Elevation of Land Surface
Williamson Creek
Williamson Creek
Elevation above Creek Bed
HAND: Relative Elevation above Creek Bed
1 foot HAND contours

## Slide 10
10m National Elevation Dataset
National Hydrography Dataset
HAND
Supercomputer
HAND at Continental Scale

## Slide 11: Example: Llano Flood, 16 October 2018
USGS Observation
National Water Model forecast
and HAND-based rating curve
Water Level (ft)
0
10
20
30
40
Llano River at Llano
HAND method assumes
Uniform flow
Velocity, depth, area
constant along reach
Largest flood on Llano River since 1939
Real-time snapshot
from TxDOT Flood
Portal

## Slide 12: Indirect Measurement of Flow at Llano Gage (Scott Grzyb, USGS)
V = 9.9 ft/s
A = 28,500 ft2
V = 11.1 ft/s
A = 25,500 ft2
V = 12.0 ft/s
A = 23,500 ft2
V = 12.3 ft/s
A = 22,900 ft2
Flow
Q = 282,000 cfs, Gage Height = 40.18 ft
BLE models assume
Nonuniform flow
Velocity, depth, area
vary along reach
Reach Length = 2900 ft (0.55 miles); Bed Slope = 0.18%

## Slide 13
Inundation Mapping from BLE Models at River Basin Scale
National Weather Service Flood Inundation Mapping (FIM) Services for Texas
Process for Base Level Engineering (BLE) to FIM for 1-D HEC-RAS Models
Example of 2-D HEC-RAS Model to FIM
Next Steps
Rating
Curve
Average
Stream Depth
Inundation
Map
Flood Discharge Forecast
from the National Water Model
or WGRFC Model
Flow Rate

## Slide 14: Question: Can Equivalent Mapping be developed from BLE Models?
InFRM – Interagency Flood Risk Management (FEMA Region 6)
InFRM flood map specifications
Base Level Engineering Models
https://webapps.usgs.gov/infrm/
Base Level
Engineering Models
InFRM Flood
Inundation Maps

## Slide 15: BLE Input Data Req’d
https://webapps.usgs.gov/infrm/estBFE/
12100201_UpperGuadalupe.gdb
Needed Feature Classes
XS = “Cross Sections”
WTR_LN = “HEC-RAS stream centerlines”
XS Attributes Needed:
WTR_NM = “HEC-RAS Model Name –matched to .PRJ”
XS_LN_ID = “Station of Cross section in model”
E_Q_0_2PCT = “500 year peak flow”
WTR_LN Attributes Needed:
WTR_NM = “HEC-RAS Model Name –matched to .PRJ”

## Slide 16: BLE Surface Data Utilized
BLE report provides documentation of LiDAR utilized for HEC-RAS models
Create a GeoTIFF DEM (1m resolution) for each HUC-12 using the same terrain datasets.
Convert each HUC-12 DEM to the BLE coordinate reference zone
Adjust the vertical units if necessary
Convert the GeoTIFF into a HEC-RAS Terrain file (HDF5) using RAS_Mapper

## Slide 17: HEC-RAS Cross-Sections from BLE Modeling

## Slide 18: Upper Guadalupe Basin, HUC8 = 12100201
36 HUC12 Subwatersheds
775 NHPlus Reaches
Upper Johnson Creek, HUC12 = 121002010109
21 NHDPlus Reaches
5 USGS Gages

## Slide 19: Upper Johnson Creek, 21 NHDPlus Catchments and Reaches indexed by COMID
COMID = 3585420

## Slide 20: HEC-RAS Model from Base Level Engineering
Produces a flood inundation map

## Slide 21: Verify BLE HEC-RAS model to HEC-RAS Terrain File
HEC-RAS HDF5 Terrain
Vs
BLE HEC-RAS Model
Note that HEC-RAS surfaces are created via script using DEM grids served by TNRIS using the Amazon Web service
https://s3.amazonaws.com/data.tnris.org/

## Slide 22: HEC-RAS Model from Base Level Engineering
Average Depth Rating Curve

## Slide 23: Flood Inundation Map Library
Avg Stream
Depth 4 ft
Avg Stream
Depth 13 ft

## Slide 24: Flood Inundation Map Library
Stream
Depth 4 ft

## Slide 25: Flood Inundation Map Library
Stream
Depth 6 ft

## Slide 26: Flood Inundation Map Library
Stream
Depth 8 ft
Stream
Depth 8 ft

## Slide 27: Flood Inundation Map Library
Stream
Depth 10 ft

## Slide 28: Flood Inundation Map Library
Stream
Depth 12 ft

## Slide 29: Flood Inundation Map Library
Stream
Depth 13 ft

## Slide 30: Flood Inundation Map Library from BLE Procedure
Download and composite a ground elevation data (1m resolution derived from LiDAR). Convert for use with HEC-RAS (Terrain HDF). Convert to same coordinate reference system (CRS) as the BLE models. Convert vertical units to feet if necessary.
Base Level Engineering:
HEC-RAS Models
Vector Spatial Data
National Hydrography Dataset
(Medium Resolution)
Vector Spatial Data [streams]
Step 1: Acquire Input Data
Create a ‘cross-walk’ that identifies which BLE model corresponds to particular NHD-MR stream reach
For each COMID, determine the upstream and downstream cross section for the BLE within the limits of the COMID. Get maximum flow in these sections (500 yr) from BLE
Step 3: Determine modeling limits & peak flows for each stream in NHD-MR
Step 2: Conflate BLE Streams to NHD-MR Streams
Step 4: Get the terrain data (1m resolution) for the subject watershed

## Slide 31: Flood Inundation Map Library from BLE Procedure
Step 5: Create HEC-RAS Model for each COMID
Interpolate the flow that generates depth at a specified interval (0.5 ft). Save the rating curve data. Revise the HEC-RAS input flow data and re-simulate the model.
Step 7: Interpolate rating curve to even depth intervals
Step 6: Compute HEC-RAS Average Depths on reach
Step 8: Compute and export grids for the specified intervals
Clip BLE HEC-RAS model to limits of cross sections from step 3. Create corresponding steady flow and plan file for truncated model
Up to the 500yr flow, iterate multiple flows down the 1D reach and determine the average reach stream depth for each flow.
Extract the flood depth grid (GeoTIFF) of each of the computed depth interval. Automatically generated using HEC-RAS Mapper.

## Slide 32: Flood Inundation Map Library from BLE Procedure
Step 9: Convert grids and supporting data to InFRM FDST compliant data
Step 10: Upload flood libraries to REST service
Convert data (shapefiles, grids and metadata to Interagency Flood Risk Management (InFRM) Flood Decision Support Toolbox (FDST) compliant format and projections
The flood libraries can be paired with the predictive reach flow to determine mapped limits of estimated flooding.
Graphic derived from InFRM Flood Decision Support Toolbox
Executive Summary and Submittal Guidance (August 13, 2019)
Rating
Curve
Average
Stream Depth
Inundation
Map
Flood Discharge Forecast
from the National Water Model
or WGRFC Model
Flow Rate

## Slide 33: InFRM Deliverables

## Slide 34: InFRM Deliverables

## Slide 35: InFRM Inundation Map Documentation

## Slide 36: Flood Inundation Mapping, Guadalupe River at Spring Branch
https://webapps.usgs.gov/infrm/fdst/

## Slide 37: NHD-MR vs. Base Level Engineering(Stream Cardinality)
Turtle Creek –
One HEC-RAS model in BLE =
16 COMID’s in NHD-MR
Turtle Creek BLE HEC-RAS Model
27 Stream Miles
Turtle Creek:
NHD-MR to BLE
16:1

## Slide 38: NHD-MR vs. Base Level Engineering
#1 BLE HEC-RAS model
Is shorter than the NHD-MR
stream
#3 NHD-MR
has no corresponding
BLE model
#2 Stream studied in
BLE but not in the
NHD-MR dataset

## Slide 39: Limited Domain of Inundation Limits
Inundation limits for COMID
#3587586 stops at limits of
BLE ‘Stream1332’ HEC-RAS
COMID #3587672 has no
BLE model to which it
conflates

## Slide 40: Five Gage Flood Map Datasets in Flood Decision Support Toolbox
Transformed to 2020 Km or 1250 miles of river mapping in
600+ reach flood map datasets in BLE to FIM library

## Slide 41
Inundation Mapping from BLE Models at River Basin Scale
National Weather Service Flood Inundation Mapping (FIM) Services for Texas
Process for Base Level Engineering (BLE) to FIM for 1-D HEC-RAS Models
Example of 2-D HEC-RAS Model to FIM
Next Steps
Rating
Curve
Average
Stream Depth
Inundation
Map
Flood Discharge Forecast
from the National Water Model
or WGRFC Model
Flow Rate

## Slide 42: 2D Analysis: West Navidad River at I-10

## Slide 43: HEC-RAS 2D Model for the NWM Catchment at Bridge
Credit: Cam Ackerman, USACE Hydrologic Engineering Center; Andy Carter, UT Austin

## Slide 44: Mean Water Depths for Water Surface Profile along Stream
Chart: Distance along Profile (ft)
Average Depth for 71,868 cfs | 24.6327 | 24.6327
Average Depth for 48,151 cfs | 21.3846 | 21.3846
Average Depth for 20,425 cfs | 16.646 | 16.646
Average Depth for 8520 cfs | 14.1873 | 14.1873
Average Depth for 1705 cfs | 11.4885 | 11.4885
I-10 bridge
71,868 cfs
48,151 cfs
20,425 cfs
1,705 cfs
8,520 cfs

## Slide 45: Rating Curves for Stream Reach and Bridge
Chart: Average Stream Depth and Bridge Depth Rating Curves West Navidad River NHD Catchment #7845263
| 1705.122476 | 5016.4773370000003 | 8520.2400839999991 | 12967.95089 | 14613.255370000001 | 18435.126810000002 | 20424.553690000001 | 27353.165489999999 | 35472.011930000001 | 48151.203780000003 | 59301.353739999999 | 71868.145610000007 | 106847.0624
 | 11.5 | 13.3 | 14.2 | 15.2 | 15.5 | 16.3 | 16.6 | 17.9 | 19.3 | 21.4 | 23 | 24.6 | 28.5
 | 12.22 | 14.38 | 15.56 | 16.66 | 17.02 | 17.78 | 18.18 | 19.4 | 20.75 | 22.69 | 24.3 | 25.64 | 29.08

## Slide 46
Inundation Mapping from BLE Models at River Basin Scale
National Weather Service Flood Inundation Mapping (FIM) Services for Texas
Process for Base Level Engineering (BLE) to FIM for 1-D HEC-RAS Models
Example of 2-D HEC-RAS Model to FIM
Next Steps
Rating
Curve
Average
Stream Depth
Inundation
Map
Flood Discharge Forecast
from the National Water Model
or WGRFC Model
Flow Rate

## Slide 47: Next Steps
Solid foundation for state-wide flood forecasting
  WGRFC Model for main stems and National Water Model for tributaries
Operational state-wide flood inundation mapping services
  Built using HAND on 10m National Elevation Dataset
Build flood inundation map services on LIDAR
  Use BLE models where available
  Use HAND for the rest
What we have now:
What is needed:
Build BLE to FIM into a production system
Base Level Engineering to Flood Inundation Mapping
Elevation data on 1m grid

## Slide 48: Implement BLE to FIM for Main Stem Rivers? Support Replace and Route with HEC-RAS inundation mapping
Many HEC-RAS models
available for these rivers