## Slide 1: Streamflow Measurement at TxDOT Bridges
Texas Department of Transportation, 21 October 2019
Acknowledgements: Chris Glancy, Project Manager, Saul Nuccitelli, TxDOT Chief Hydraulics Engineer, Kenneth Mora, Director, Design Divn;
TxDOT Project Team: Abderrahmane Maamar-Tayeb, Sean Yoon, Adam Jack, Brian Dodge, Jennifer Lyons, Kathleen Newton.
Xing Zheng, Christine Thies, Center for Water and Environment; Peter Ward, Hydrological Services America; Dirk Schwanenberg, Kisters;
Jim Navarro, Air-Sea Systems; Scott Gallagher, EarthViews; Tim Osting, Aqua Strategies; Andy Carter, LandDev;
Cam Ackerman, Hydrologic Engineering Center; Andy Rooke, AR Consults; Gert Van Maren ESRI; Meghan Roussel, Milton Sunvison, USGS.
Barney Austin
Annabeth McCall
Aqua Strategies,
Dripping Springs, TX
Matt Ables
Brandon Azvedo
Kisters North America, Sacramento, CA
Courtney Gallagher
Brian Footen
EarthViews,
Wimberley, TX
Closeout Presentation
TxDOT Project #5-9054-01
David Maidment
Paola Passalacqua
Harry Evans
Center for Water and the Environment,
University of Texas at Austin
David Arctur
Leah Huling
Notes: How do we answer the question of how many people are going to be impacted, especially if large areas of the state are not covered by LIDAR or National Flood Hazard Layer? The researchers developed a process called Height Above Nearest Drainage or HAND.

## Slide 2: Streamflow Measurement at TxDOT Bridges
Transect
LIDAR
Gage
Results
Modeling
Correlation

## Slide 3: Transect of Gages on I-10 Flood security of a highway
Notes: In order to see where we are going we have to understand the past.
Lets look at a brief history of flood mapping during an emergency response.

## Slide 4
National Water Model
Spatially Continuous Water Prediction Forecasts
Operational hydrologic forecast model running 24/7 on Weather and Climate Operational Supercomputing System (WCOSS)
Streamflow forecasts for 2.7M river reaches depicted in National Hydrography Dataset-Plus (NHDPlus)
National Water Center started operations on 1 October 2019.
Slide: adapted from Fernando Salas, NWS
Tuscaloosa, Alabama
Notes: NWM V2.0 Configurations
  CONUS
  Analysis and Short-Range (each hour)
    Extended Analysis (daily)
  Ensemble Medium-Range (synoptic)
  Ensemble Long-Range (daily, time-lagged)
  Hawaii
  Analysis and Short-Range (synoptic)

## Slide 5: Water Measurement Sites
550 USGS Streamflow Gages
(data presently used in NWM)
27,000 TxDOT Bridges on 15,700 NWM reaches
(potential additional measurement sites)

## Slide 6
Transect of 20 Measurement Sites on I-10
Site | Location
101 | Sabine River at I-10
102 | Adams Bayou at I-10
103 | Bairds Bayou at I-10
104 | Neches River at I-10
105 | Hillebrandt Bayou at TX-124
106 | Willow Marsh Bayou at I-10
107 | North Fork Taylor Bayou at I-10
108 | Turtle Bayou at I-10
109 | Cedar Bayou at I-10
110 | Bessies Creek at I-10
111 | East Bernard Creek at I-10
112 | San Bernard at I-10 (moved to Church Creek at I-10)
113 | East Bernard River at US-90
114 | West Navidad River at I-10
115 | Peach Creek at I-10
116 | Plum Creek at I-10
117 | Geronimo Creek at I-10
118 | Santa Clara Creek at I-10
119 | Leon Creek at I-10
120 | Guadalupe River at US-87
Credit: Harry Evans, CWE; Matt Ables and Brandon Azvedo, Kisters; Jim Navarro, Air-Sea Systems;

## Slide 7: Findings and Recommendation: Radar Bridge Sensors
Idea of an autonomous bridge streamflow sensor worked
Self contained, solar power, cell phone communication
Measuring both water level and velocity is valuable
Cost $15,000
Installation time ~ 3 hours
Reliable and low maintenance
If bridge overflows, gage overflows
Recommendation:
Need to consider elevating gages
Site 106: Willow Marsh Bayou,
Beaumont, after TS Imelda

## Slide 8: Findings and Recommendation: Transect of Gages on I-10
Concept of a transect of gages along a highway is innovative
Largest set of radar streamflow measurement sites in the US
Many gages already installed in Harris County so no need to gage there
9 gages in Beaumont District
Recommendation:
Consider additional transects
above and below I-10 especially
in South-East Texas
(4 Presidentially Declared flood
disasters in the last 5 years)

## Slide 9: LIDAR for Site Characterization Measuring stream cross-section
Notes: In order to see where we are going we have to understand the past.
Lets look at a brief history of flood mapping during an emergency response.

## Slide 10
Measurement of Water Elevation and Velocity using Radar
Peter
Ward
Wolfram &
Christoph
Sommer

## Slide 11
Procedure for Computing Discharge
Specified at installation
Measured by gage
Computed in Kisters cloud
Credit: Matt Ables, Kisters

## Slide 12
Specification of River Cross-Section

## Slide 13: LIDAR DEM, and LIDAR Point Cloud on Bridge Used to characterize cross-section profiles at site
Very close agreement between LIDAR and GPS surveying

## Slide 14: Acoustic Doppler Profiler Measurement For Rivers with Permanent Water: All Sites on I-10 East of Houston
Measures Depth
and Velocity
Credit: Barney Austin, Annabeth McCall, Tim Osting, Aqua Strategies

## Slide 15: Stream Cross-Section and Road Profile Developed from LIDAR and sonar measurement
Chart: Normal Conditions at Site 105: Hillebrandt Bayou at TX-124
| 141.33000000000001
Sensor | 16.794
Road | 16.7531 | 16.7531
Low Chord | 15.2331 | 15.2331
Sea Level | 0 | 0
Standing water at sea level
LIDAR
Sonar (ADCP)

## Slide 16
https://arcg.is/0WqTS0
ArcGIS StoryMap for Site Characterization
Credit: David Arctur, CWE

## Slide 17: Findings and Recommendation: LIDAR for Site Characterization
Texas new 1m LIDAR data are very accurate
Can be used for 3D characterization of road and stream profiles
GPS Survey of gage location in (x,y,z) is critical
All gages east of Houston on I-10 have stream bed below sea level
Supplement LIDAR with ADCP
Recommendation:
Consider measurement of
stream bathymetry all along rivers

## Slide 18: Data Processing and Results Kisters Big Data System in the cloud
Notes: In order to see where we are going we have to understand the past.
Lets look at a brief history of flood mapping during an emergency response.

## Slide 19
Kisters Big Data System
(located in Aachen, Germany)
Kisters is the largest water data management company in the world

## Slide 20
TxDOT National Water Model Bridge Portal
Neches River
during TS Imelda
Present
NWM
Forecast
TxDOT
Measurement
Water Level (ft)
Provides state-wide coverage of National Water Model forecasts for Texas
(102,000 river reaches covering 190,000 miles of streams and rivers)
Credit: Matt Ables, Brandon Azvedo, Kisters North America

## Slide 21
TxDOT Water Data Viewer (details of individual sites)
Enables retrospective view of observed water data at individual sites for chosen time periods

## Slide 22: Radar Streamflow Measurement during TS Imelda Gage simultaneously measures water level and surface velocity, then computes discharge
Chart: Water Level (ft), Velocity (ft/s)

## Slide 23: EarthViews 360°Imagery at Hillebrandt Bayou
Virtual Staff Gage
Radar Sensor
https://arcgis.earthviews.com/public/105-hillerbrandt-bayou#22
Credit: Courtney Gallagher and Brian Footen, EarthViews

## Slide 24: Water Level on Virtual Staff Gage
Chart: Tropical Storm Imelda at Hillebrandt Bayou
Peak water level 19.7 feet
above stream bed

## Slide 25: Local Observation Network in Beaumont Area
Jefferson County
Drainage District No. 6

## Slide 26: Summary and Findings: Data Processing and Results
Kisters Big Data System is a reliable repository for large scale data
Various viewers and services for data output
Handles large scale data from National Water Model effortlessly
Processes data from radar sites
Can provide alerts
Recommendation:
Add more local networks
LCRA, Houston, Jefferson County DD6

## Slide 27: Statistical Analysis Correlation along streams and along I-10
Notes: In order to see where we are going we have to understand the past.
Lets look at a brief history of flood mapping during an emergency response.

## Slide 28
Data Assimilation Application in West Navidad Basin
(Correlation along the streams)

## Slide 29
Proof of Concept: Upstream Alteration

## Slide 30
Proof of Concept: Downstream Propagation

## Slide 31
Next Steps - Single Channel v. Branched Network
Study Area Boundary
Contributing stream segment
Missed stream segment
Single Channel Network
Branched Network
Credit: Leah Huling and Paola Passalacqua, UT Austin, Dirk Schwanenberg, Kisters

## Slide 32
Extent of Longitudinal Correlation along Streams
15 miles
upstream
30 miles
downstream

## Slide 33
Correlation of Flows in Streams Crossing I-10 during TS Imelda
Variogram meets sill at about 50 miles – Extent of lateral correlation along I-10
(Correlation along I-10)

## Slide 34: Summary: Correlation along Streams and Along I-10
Current gage spacing ~ 1 gage per 20 miles on I-10 West of Houston,1 gage per 10 miles on I-10 in Beaumont
Streams
I-10

## Slide 35: Possible Future Transects
Transects are about 70 miles apart
Probably need to be about half
this distance

## Slide 36: Findings and Recommendation: Statistical Analysis
Flows are correlated laterally along I-10 and longitudinally along streams
Correlation on the order of 40-50 miles
Current gage spacing is 10-20 miles
This is dense enough to avoid gaps
Results are preliminary
Recommendation:
More detailed study of TxDOT and USGS
data coupled with National Water Model

## Slide 37: Flow Modeling at Bridges Details of depth and velocity
Notes: In order to see where we are going we have to understand the past.
Lets look at a brief history of flood mapping during an emergency response.

## Slide 38: Watershed of Gage on West Navidad River at I-10

## Slide 39: Representation in the National Water Model as 23 Reach Catchments

## Slide 40: Terrain Data Near I-10
10m x 10m cells
1m x 1m cells

## Slide 41: Elevation Profiles along I-10
Chart: Distance Along Profile (m)
LIDAR measures road profile accurately

## Slide 42: HEC-RAS 2D Model for Catchment of this Gage
Credit: Cam Ackerman, USACE Hydrologic Engineering Center; Andy Carter, LandDev

## Slide 43: Flood Frequency from National Water Model Reanalysis (1993-2018)
Credit: Xing Zheng, CWE

## Slide 44: Maps of Water Depth and Velocity (produce flood inundation map library by varying discharge)

## Slide 45: Flow through the Bridges (30% on left, 70% on right)
Gage at Site 116

## Slide 46: Rating Curve at Bridge: West Navidad River at I-10
Discharge (cfs)
Water Level (ft)

## Slide 47: Findings and Recommendations: Flow Modeling at Bridges (this component was not part of the original project scope)
2D flow modeling on 1m LIDAR gives good engineering scale results
Enables flood risk at bridge to be reliably estimated
Can be used with National Water Model reanalysis
Produces rating curve at bridge
Recommendations:
Do this modeling at all
bridge streamflow sites
Define a methodology for
flood security of I-10

## Slide 48: Project Assessment What was achieved, where to now?
Notes: In order to see where we are going we have to understand the past.
Lets look at a brief history of flood mapping during an emergency response.

## Slide 49
What was achieved?
Installation of 20 Gages along I-10
Beaumont, Houston, Yoakum, and San Antonio Districts
Gages record water level, velocity, and discharge
A unique new system of radar streamflow measurement along a highway transect
Creation of forecast portal
Provides access to TxDOT observed data and National Water Model forecasts
Topographic-bathymetric survey
GPS survey at 11 sites west of Houston, GPS and sonar bathymetry survey at 9 sites East of Houston
Statistical Analysis
Correlation of data along streams and along I-10
Flow Modeling at a Bridge
Detailed maps of flow velocity and depth

## Slide 50: This was a large project …
4 TxDOT Districts
11 members of project team
11 additional contributors
5 commercial firms as subcontractors
(Kisters, EarthViews, Aqua Strategies, Sea-Air Systems, AR Consults)
4 additional commercial firms supplied or rented equipment
Hydrological fieldwork for gage installation
GPS Surveying
Sonar Bathymetry measurement
360º photography
Terrain analysis using GIS
Big Data System in the cloud
Statistical analysis of large data volumes
Engineering scale modeling at bridges
… that required a wide variety of technical skills

## Slide 51: How to Sustain this Long Term?
Continue to use Kisters data system
  for data maintenance and processing
Engage US Geological Survey
  for gage maintenance and installation of additional transects
Imbed Data in District Flood Operations
  Case Study in Beaumont District
  Focus on Chambers, Jefferson
  and Orange Counties
  Collaborate with Lamar University
Develop methodology for highway
flood risk assessment on I-10
  In real-time as floods occur
  As a planning tool for flood security
  Extend to other highways later