## Slide 1: Subcommittee on Sedimentation’s Proposed National Stream Morphology Database
Faith Fitzpatrick1, Matt Collins2, and John R. Gray1
1U.S. Geological Survey
2National Oceanic and Atmospheric Administration
Synopsis – December 1, 2010
Stream Morphology in Arc Hydro River Meeting, Austin, TX

## Slide 2: SOS Proposed National Stream Morphology Database
Subcommittee on Sedimentation
Under the Department of the Interior’s Advisory Committee on Water Information
Four workgroups:
  Federal Interagency Sedimentation Conferences
  Dam Removal/Sediment Management Guidelines
  Reservoir Sedimentation Database, RESSED
  Stream Morphology Database

## Slide 3: SOS Proposed National Stream Morphology Database
Why do we need a morphology database?
Centrally accessible data available to partners, cooperators, public
Tracking trends over time (upgrade of Vigil Network)
Multidisciplinary studies – linking stream morphology data with streamflow, ecology, habitat, reservoir sedimentation, sediment transport, and water chemistry data sets
Characterization of channels and sediment
  Stream restoration design
  Dam removal
  Channel stability
  Transportation/hydraulic studies
  Habitat assessment
  GIS/stream networks
  Flow routing/modeling

## Slide 4: SOS Proposed National Stream Morphology Database
Why now?
  Widespread collection of stream morphology data
    Main driver is bankfull regional curves, many done by USGS Water Science Centers
    Channel monitoring related to restoration and other channel change/sediment source studies
  Profusion of instrument types and methods
  No national database/data-element standard available
  National efforts for modeling & stream network development
  Powerful links to Streamstats--timing is right.

## Slide 5: SOS Proposed National Stream Morphology Database
OBJECTIVES
Evaluate/identify data-storage protocols for stream morphology data,
Compile and/or organize certifiably credible stream morphology data as appropriate,
and
Render these data publically available.

## Slide 6: SOS Proposed National Stream Morphology Database
Stream Morphology Database Attributes
1. Store many types of geomorphic data (spatial, raw and calculated) with supporting documentation (photographs, scanned field notes, maps).
2. Be displayed in spatial, graphical and tabular forms.
3. Accommodate repeat measurements to enable temporal and spatial river morphology comparisons.
4. Provide an online means to efficiently view, analyze, and export data.
5. Link to National Water-Quality Monitoring Council ACWI “metadata” to facilitate comparison/sharing of data

## Slide 7: SOS Proposed National Stream Morphology Database
Spatial data needs include:
Innovative methods for linking 3-D and multiple spatial scales and resolutions of data
  Not trivial! It’s why we currently don’t have a database
Diverse data types
Identifier that can link to other data types, inc. drainage basin characteristics, streamflow, sediment transport, ecological data

## Slide 8: SOS Proposed National Stream Morphology Database
Raw data include:
Survey information from a variety of instruments, including GPS and conventional equipment
Pebble count information which could include map, soft sediment information and vegetation info
Bank characteristics, quantitative and qualitative
Bank erosion location/size /estimated bank retreat
Erosion pin data
Lab reports from sediment analysis

## Slide 9: SOS Proposed National Stream Morphology Database
Calculated data include:
Analyzed survey data into x-sections & longitudinal profiles
Summary statistics about channel shape (width, depth, area, etc.) for each cross section and reach averages for both the active channel and bankfull channel
Pebble count bins, summary stats, graphs (% type, D50, etc.)
Multiple slope measurements (riffle, water surface, bankfull, thalweg, etc.)
Channel and valley shape metrics (flood prone width, bankfull width to depth ratio, entrenchment ratio, etc.)
Planform characteristics (sinuosity, meander radius, etc.)
Basin land-use characteristics

## Slide 10: SOS Proposed National Stream Morphology Database
Additional data include:
Scans of raw field notes and lab sheets
Photographs, inc. location info, photographer
Additional supporting files from the gage information (Station Analysis, Station Description, rating curve, Log-Pearson Type III analysis, etc.)
Discharge measurements and short-term stage information (or direct link to miscellaneous measurements portion of ADAPS)
Protocol used for collection, agency & personnel

## Slide 11: SOS Proposed National Stream Morphology Database
2011 Workshop
Participants to include experts that have collected stream morphology data, database designers, those interested in applications of the data (GIS, modeling), and those involved in the development of NWQMC’s and FGDC meta data
Some draft questions:
  Are there appropriate example databases already developed?
  What types of data should be stored?
  What are possible funding mechanisms to develop the database?
  Who should be the host of the database?
  Should we start out with an example/test case and where?
Publish workshop outcomes in AGU EOS or Forest Service Stream notes and provide recommendations to SOS.
Notes: Discuss existing databases

## Slide 12: SOS Proposed National Stream Morphology Database
2011 National Stream Morphology Database Workshop – Sponsored by the SOS
Approved this week by the SOS
Planning phase start
Probably late Spring 2011
Location TBD – Madison, WI?
Notes: Discuss existing databases