## Slide 1: Desalination and Long-Haul Transfer as a Drinking Water Supply
Ashlynn Stillwell December 4, 2008 CE394K: GIS for Water Resources
http://www.webberenergygroup.com

## Slide 2: Outline
Background on Desalination
Purpose of Project
Assumptions
Case Study Map
Results and Discussion
Implications
Questions

## Slide 3: Background on Desalination
Treats brackish water or seawater to potable quality
Types of desalination
  Multi-effect distillation
  Multi-stage flash
  Reverse osmosis
Source: Lawler & Benjamin

## Slide 4: Purpose of Project
Dallas-Fort Worth Metroplex is growing
  Metro statistical area: 5.6 million people (2003)
  Dallas water use: 238 gal/person/day
  Fort Worth water use: 177 gal/person/day
Population increases 2% annually, on average
Depleted water supplies
Looking toward alternative supplies

## Slide 5: Assumptions
20 MGD desalination facility
  Sufficient for 100,000 people at current DFW water use
  Real estate available
No financial consideration – energy only
Pipe friction factors based on laminar flow

## Slide 6: Desalination and Long-Haul Transfer Map
Straight Pipeline from Houston to Dallas-Fort Worth

## Slide 7: DEM and Cumulative Elevation Changes
Cumulative elevation change: 700 m (2,300 ft)
Pipeline length: 413 km (257 mi)
Straight Pipeline from Houston to Dallas-Fort Worth

## Slide 8: Desalination and Long-Haul Transfer Map
Right-of-Way Pipeline from Houston to Dallas-Fort Worth

## Slide 9: DEM and Cumulative Elevation Changes
Cumulative elevation change: 745 m (2,400 ft)
Pipeline length: 486 km (302 mi)
Right-of-Way Pipeline from Houston to Dallas-Fort Worth

## Slide 10: Energy Requirements for Desalination and Long-Haul Transfer
Total: 407,000 kWh/day
Total: 28,500 kWh/day

## Slide 11: Air Emissions from Energy Production
Electricity generated by coal:
933,000 lbs CO2
2,700 lbs SO2
2,000 lbs NOx
Electricity generated by natural gas:
466,000 lbs CO2
407 lbs SO2
12 lbs NOx
407,000 kWh/day

## Slide 12: Implications for Energy and Water Policy
Desalination scenario requires 14 times more energy than standard water treatment
Additional environmental concerns over disposal of concentrate
“Alternative” water supply – Conservation
  Water Conservation Implementation Task Force recommends 140 gal/person/day
  Saving water saves energy

## Slide 13: Questions?

## Slide 14: END
Ashlynn Stillwell Graduate Research Assistant Cockrell School of Engineering Department of Environmental & Water Resources Engineering Lyndon B. Johnson School of Public Affairs
University of Texas at Austin
ashlynn.holman@mail.utexas.edu
http://www.webberenergygroup.com