## Slide 1: Texas Coastal Wetlands Linking Water & Land
By: James McDonald

## Slide 2: Background
5 Million people reside on or near the Texas Gulf Coast
Project Objectives:
  Are wetlands disappearing?
  At what rate?
  How will this affect us?

## Slide 3: Wetland Functions & Importance
Habitats
Hydrologic & Hydraulic
Water Quality

## Slide 4: Project Analysis
Galveston Bay and surrounding area
Data sets (1956, 1989) – USGS
Habitat classification – wetland type

## Slide 5: Data Source
Data was obtained from the USGS
  Includes 31 quadrangle maps at 1:24,000 scale, developed by the National Wetlands Inventory (NWI)

## Slide 7: Organization by Field Calculator

## Slide 8: Merged Data

## Slide 9: 1956
Palustrine Wetlands
Estuarine/Marine Wetlands

## Slide 10: 1989
Palustrine Wetlands
Estuarine/Marine Wetlands

## Slide 11: 1956
Palustrine Wetlands
Estuarine/Marine Wetlands

## Slide 12: 1989
Palustrine Wetlands
Estuarine/Marine Wetlands

## Slide 13: 1956
1989

## Slide 14: Wetland Loss
 | Area (km2) |  | 
 | 1956 | 1989 | Difference
Marine Wetland | 10 | 9 | -1
Freshwater Emergent Wetland | 193 | 90 | -103
Freshwater Forested Wetland | 11 | 23 | 12
Freshwater Shrub Wetland | 14 | 8 | -6
Estuarine Wetland | 542 | 513 | -29
Rivers | 13 | 12 | 
Lakes | 48 | 87 | 
Freshwater Pond | 6 | 16 | 
Deep Water | 1498 | 1539 | 
Upland | 1990 | 2021 | 
Total Wetlands | 770 km2 | 643 km2
Loss of 16%

## Slide 15: Conclusions
Wetlands are diminishing
Galveston Bay reduction rate = 3.8 km2/year
Palustrine (freshwater) wetlands have seen more severe adverse affect
  Particularly at river deltas

## Slide 16: Consequences
Loss of habitat, ecologic integrity
Vulnerability:
  Storm surge: 1 km of wetlands reduces surge by 7 cm
  Flooding: 1 km2 of wetlands can store 250-350 gallons of water

## Slide 17: Future Work
Flood inundation area with reduced storm surge
1977 data set – trend for future loss
Determining wetland loss using remote sensing
  Center of Space Research (UT)

## Slide 18: I hope this flood of information has saturated your thirst for wetlands. Questions?