## Slide 1: Herbicide Use in the Buffalo River Watershed
Cody Hudson

## Slide 2: Background
America’s First National River
Over 95,000 acres of protected land
Over 1 million visitors every year

## Slide 3: Motivation
Herbicide is being used in an effort to control vegetation along power lines
Escort©
  Partition Coefficient
    Measure of Hydrophobicity
    Kow<10 , Hydophilic 
    Kow(Escort)=.018
  Half-Life= 6 weeks
  Density=1.74 g/mL @ 25° C
Notes: -power line locations assumed to be in same locations as roadways

## Slide 4: Time of Concentration
Time in cell function of slope, T(S)
Kirpich Equation
  L=Length of Cell (ft)
  N=0.8
    Forrest/Dense Grass areas
Notes: -Kirpich equation describes overland flow
-used raster calculator to determine time of concentration based on slope

## Slide 5: Chemical Decay
K=0.000011 min-1
Notes: -K calculated from half life data
-tc used to calculate decay multiplier by using raster calculator

## Slide 6: Mass Grid
Manufacturer’s Suggested Application Rate
  4 oz-weight/acre
  0.54 oz-weight/30m2 grid
Notes: -Oz per grid calculated based on 60 ft of right of way times 30 meters in length

## Slide 7: Dinf Decaying Accumulation
Inputs
  Dinf Flow Direction
  Decay Grid
  Mass Grid
Maximum Value
  33,370 oz-weight
  143 gal
  4.6 barrels

## Slide 8: Concentration
Boxley Gage
  16 mg/L
St. Joe Gage
  30 mg/L

## Slide 9: Conclusions
Concentration level greater than MCL of many other chemicals in EPA drinking water standards
    2,4-D Herbicide MCL=0.07 mg/L
Numbers reflect “perfect storm” situation
  No accumulation in soils or vegetation
  Herbicide transport modeled as overland flow
  Concentration based on application of herbicide to entire area at one instant
Notes: -Kow very low so most will not adsorb
-If spray is applied prior to rain event, with antecedent wet conditions, herbicide will be majority overland flow
-in reality area may be sprayed over a period of months
-http://www.epa.gov/safewater/contaminants/index.html , EPA Standards
-MCL (maximum contaminant level)

## Slide 10
Questions?