## Slide 1: Hydrologic Balance in the Mexico Valley
Fernando Almada Calvo

## Slide 2: What and where is the Mexico Valley? (Also called Anahuac: Nahuatl for Close to water )
Closed hydrologic system, situated in Central Mexico.
Mexico City and Pachuca
Area: 9,611km2 (1.5 times the area of Delaware)
Mexico City
City of Pachuca
Popocatepetl
(5384 m/17664 ft)

## Slide 3: Why is this important?
Less that 1% of territory.
19 million people live in the Valley (20%)
1/3 of Mexico’s GNP is concentrated there
Density: Averaged in valley:~2,000 hab/km2
NYC :~9,000 hab/km2
Mexico City:~5,000 hab/km2

## Slide 4: Objectives
Perform a hydrologic mass balance on the Mexico Valley
Estimate the power needed to pump water from the Cutzamala System to the Mexico Valley.
Mexico Valley
Inflows
Outflows

## Slide 5
Filled
Raw
-
=

## Slide 6: Balance diagram
Surface water or in engineered systems
Groundwater

## Slide 7: Data acquisition
National Institute of Geography and Statistics (INEGI)
  River shapefiles
  Water bodies
National Water Commission (CNA)
  Water use and consumption
  Water flow in drainage system
Water technology Institute (IMTA)
  Daily precipitation data (1978-1998)
  Evapotranspiration
Shuttle Radar Topography Mission
  DEM

## Slide 8
Precipitation
(mm/year)
Precipitation:
6,347 Mm3/year

## Slide 9
Pan Evaporation and
Evapotranspiration (mm/year)
Name of waterbody | Area km2
Tecocomulco Lagoon | 26.19048
Zumpango Lagoon | 18.15263
Texcoco Lake | 9.104374
Guadalupe Reservoir | 4.532924
Marin reservoir | 0.881915
Evapotranspiration: 5,001 Mm3/year
(Contreras et al)

## Slide 10: Balance diagram
Imports
600 Mm3/year
(CNA)
Precipitation
6,347 Mm3/year
Evapotranspiration
5,002 Mm3/year
Outflow from the valley
1,861 Mm3/year
(CNA)
Use
2,449 Mm3/year
(IMTA)
Groundwater
DV=-992 Mm3/year
Superficial Water bodies
Evaporation from water bodies
~100Mm3/year
1639
(IMTA)
210
(IMTA)
698
Runoff ratio 0.11
647
1692
Unknown Losses
~67Mm3/year
(Unknown or illegal use?)
Losses during use
917 Mm3/year
(IMTA)
1532
(IMTA)
329
539

## Slide 13: Work to do
Locate in map reservoirs and canals of Cutzamala system.
Calculate the energy required for pumping 19m3/sec of water to the Mexico Valley.
Write Report

## Slide 14: Questions?