## Slide 1: CE 394K: GIS in Water Resources Small Dam in Village of Tlamacazapa, Mexico Robin Lynch

## Slide 2: Tlamacazapa, Guerrero
Remote mountain village
Wells contaminated with: Arsenic, Lead, and Fecal Runoff
Severe 6 month dry season
Limited piped water (~2 hours/week)

## Slide 3: Wet Season
“Agua de Shrek”

## Slide 4: Dry Season (Same well)

## Slide 5: Goal of Project
Create a dam to meet water needs
Delineate stream network
Determine best location for dam
Delineate watershed
Size the dam using Sequent Peak Method

## Slide 6: Stream Delineation
Drains from village runoff, too polluted
Too far from road, difficult to maintain
Perfect!

## Slide 7: Watershed delineation
Drainage Area = 7689600 m2
Dam

## Slide 8: Average Rainfall (2003-2007)
Chart: Average Rainfall (mm/month)
| January | February | March | April | May | June | July | August | September | October | November | December
Average | 0.52 | 8.2 | 8.532 | 7.984 | 83.776 | 222.388 | 183.496 | 211.808 | 188.656 | 87.876 | 19.52 | 0

## Slide 9: Flow Calculation
Runoff ratio, w = 0.2
Drainage Area, DA = 7689600 m2
Q = P*DA*w
Calculated per month

## Slide 10: Water Demand
Calculate volume for 3 scenarios
Assume population of 6000 people
Water Use Per Day: |  | 
Current | 15 | L/c/day
Minimum | 40 | L/c/day
Optimum | 100 | L/c/day
Monthly Volume |  | 
Current | 2700 | m3/month
Minimum | 7200 | m3/month
Optimum | 18000 | m3/month
~2.5 flushes
~7 flushes
~17 flushes

## Slide 11: Dam Location

## Slide 12: Dam Sizing

## Slide 13: Sequent Peak Method
 |  |  | (m3/month) |  |  | 
t | Rt | e | Lt | Qt | Kt-1 | Kt
 |  | mm/mo |  |  |  | 
May | 18000 | 60 | 71.63157 | 128840.8 | 0 | 0
June | 18000 | 60 | 71.63157 | 342015 | 0 | 0
July | 18000 | 60 | 71.63157 | 282202.2 | 0 | 0
August | 18000 | 60 | 71.63157 | 325743.8 | 0 | 0
September | 18000 | 60 | 71.63157 | 290137.8 | 0 | 0
October | 18000 | 60 | 71.63157 | 135146.3 | 0 | 0
November | 18000 | 93 | 111.0289 | 30020.2 | 0 | 0
December | 18000 | 93 | 111.0289 | 0 | 0 | 18111.03
January | 18000 | 93 | 556.4386 | 799.7184 | 18111.03 | 35867.75
February | 18000 | 93 | 879.081 | 12610.94 | 35867.75 | 42135.89
March | 18000 | 93 | 966.0064 | 13121.53 | 42135.89 | 47980.36
April | 18000 | 93 | 1034.379 | 12278.75 | 47980.36 | 54735.99
Water Demand
Evaporation Losses
Inflow
Minimum Capacity (m3)

## Slide 14: Dam Sizing
 | m3/month | Kt (m3) | Height (m)
Current | 2700 | 4899 | 3.5
Minimum | 7200 | 14016 | 5.5
Optimum | 18000 | 54736 | 10.5
Chart: Volume (m3)
| 623.79124999999999 | 6012.4917500000001 | 17106.098875 | 36121.421124999993 | 63444.12862499999
 | 1 | 3.5 | 6 | 8.5 | 11

## Slide 15: Next Steps/Pitfalls
Geological survey
Community Participation
Clear organizational structure
Affordable pricing

## Slide 16: Questions?