## Slide 1: Key Spatial Analysis Concepts from Exercise 3
Contours and Hillshade to visualize topography

## Slide 2: Zonal Average of Raster over Subwatershed

## Slide 3: Subwatershed Precipitation by Thiessen Polygons
Thiessen Polygons
Feature to Raster (Precip field)
Zonal Statistics (Mean)
Join
Export to DBF (Excel)

## Slide 4: Subwatershed Precipitation by Interpolation
Kriging (on Precip field)
Zonal Statistics (Mean)
Join
Export

## Slide 5: Runoff Coefficients
Interpolated precip for each subwatershed
Convert to volume, P
Sum over upstream subwatersheds
Runoff volume, Q
Ratio of Q/P
Watershed | HydroID's
Plum Ck at Lockhart, TX | 330
Blanco Rv nr Kyle, TX | 331, 332
San Marcos Rv at Luling, TX | 331,332,333,336

## Slide 6: Digital Elevation Model Based Watershed and Stream Network Delineation
Conceptual Basis
Eight direction pour point model (D8)
Flow accumulation
Pit removal and DEM reconditioning
Stream delineation
Catchment and watershed delineation
Geomorphology, topographic texture and drainage density
Generalized and objective stream network delineation

## Slide 7: Readings
Arc Hydro Chapter 4
At http://help.arcgis.com, start from “An overview of the Hydrology tools” http://help.arcgis.com/en/arcgisdesktop/10.0/help/009z/009z0000004w000000.htm to end of Hydrologic analysis sample applications

## Slide 8: Conceptual Basis
Based on an information model for the topographic representation of downslope flow derived from a DEM
Enriches the information content of digital elevation data.
  Sink removal
  Flow field derivation
  Calculating of flow based derivative surfaces
  Delineation of channels and subwatersheds

## Slide 9: Duality between Terrain and Drainage Network
Flowing water erodes landscape and carries away sediment sculpting the topography
Topography defines drainage direction on the landscape and resultant runoff and streamflow accumulation processes

## Slide 10: The terrain flow information model for deriving channels, watersheds, and flow related terrain information. Watersheds are the most basic hydrologic landscape elements
Raw DEM
Pit Removal (Filling)
Flow Field
Channels, Watersheds, Flow Related Terrain Information
Notes: This slide shows the general model for deriving flow field related derivative surfaces from digital elevation data. The input is a raw digital elevation model, generally elevation values on a grid. This is basic information used to derive further hydrology related spatial fields that enrich the information content of this basic data. The first step is to remove sinks, either by filling, or carving. Then a flow field is defined. This enables the calculation of flow related terrain information. My focus has been on flow related information working within this framework. I try to leave other GIS functionality, like radiation exposure, line of sight analyses and visualization to others. I have distributed my software in ways that it easily plugs in to mainstream systems, such as ArcGIS to enhance ease of use.

## Slide 11: DEM Elevations
Contours
720
700
680
740
680
700
720
740
720
720

## Slide 12
80
74
63
69
67
56
60
52
48
80
74
63
69
67
56
60
52
48
30
Slope:
Hydrologic Slope
- Direction of Steepest Descent
30
ArcHydro Page 70

## Slide 13
32
16
8
64
4
128
1
2
Eight Direction Pour Point Model
ESRI Direction encoding
ArcHydro Page 69

## Slide 14
2
2
4
4
8
1
4
16
1
2
4
8
4
4
1
2
4
8
2
4
4
4
4
2
1
Flow Direction Grid
32
16
8
64
4
128
1
2
ArcHydro Page 71

## Slide 15: Flow Direction Grid
32
16
8
64
4
128
1
2

## Slide 16
Grid Network
ArcHydro Page 71

## Slide 17
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
10
1
0
14
4
1
19
1
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
10
1
0
1
4
14
19
1
Flow Accumulation Grid.
Area draining in to a grid cell
Link to Grid calculator
ArcHydro Page 72

## Slide 18
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
10
1
0
1
4
14
19
1
Flow Accumulation > 10 Cell Threshold
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
1
0
4
1
1
10
14
19
Stream Network for 10 cell Threshold Drainage Area

## Slide 19
1
1
1
1
1
1
1
2
1
1
1
1
1
1
3
3
3
11
2
1
2
5
15
20
2
The area draining each grid cell includes the grid cell itself.
1
1
1
1
1
1
1
2
1
1
1
1
1
1
3
3
3
11
2
1
5
2
2
25
15
TauDEM contributing area convention.

## Slide 20: Streams with 200 cell Threshold (>18 hectares or 13.5 acres drainage area)

## Slide 21
Watershed Draining to Outlet

## Slide 22: Watershed and Drainage Paths Delineated from 30m DEM
Automated method is more consistent than hand delineation

## Slide 23: The Pit Removal Problem
DEM creation results in artificial pits in the landscape
A pit is a set of one or more cells which has no downstream cells around it
Unless these pits are removed they become sinks and isolate portions of the watershed
Pit removal is first thing done with a DEM

## Slide 24: Pit Filling
Increase elevation to the pour point elevation until the pit drains to a neighbor

## Slide 26: Parallel Approach
Improved runtime efficiency
Capability to run larger problems
Row oriented slices
Each process includes one buffer row on either side
Each process does not change buffer row

## Slide 27: Pit Removal: Planchon Fill Algorithm
Initialization
1st Pass
2nd Pass
Planchon, O., and F. Darboux (2001), A fast, simple and versatile algorithm to fill the depressions of digital elevation models, Catena(46), 159-176.

## Slide 28: Parallel Scheme
Communicate
Initialize( D,P) Do for all i in P if D(i) > n P(i) ← D(i) Else P(i) ← n endfor Send( topRow, rank-1 ) Send( bottomRow, rank+1 ) Recv( rowBelow, rank+1 ) Recv( rowAbove, rank-1 ) Until P is not modified
D denotes the original elevation.
P denotes the pit filled elevation.
n denotes lowest neighboring elevation
i denotes the cell being evaluated

## Slide 29: Improved runtime efficiency
Parallel Pit Remove timing for NEDB test dataset (14849 x 27174 cells  1.6 GB).
128 processor cluster
16 diskless Dell SC1435 compute nodes, each with 2.0GHz dual quad-core AMD Opteron 2350 processors with 8GB RAM
8 processor PC
Dual quad-core Xeon E5405 2.0GHz PC with 16GB RAM

## Slide 30: The challenge of increasing Digital Elevation Model (DEM) resolution
1980’s DMA 90 m
102 cells/km2
1990’s USGS DEM 30 m
103 cells/km2
2000’s NED 10-30 m
104 cells/km2
2010’s LIDAR ~1 m
106 cells/km2

## Slide 31: Capabilities Summary
Capability to run larger problems |  |  |  | 
 |  | Processors used | Grid size | 
 |  |  | Theoretcal limit | Largest run
2008 | TauDEM 4 | 1 | 0.22 GB | 0.22 GB
Sept 2009 | Partial implement-ation | 8 | 4 GB | 1.6 GB
June 2010 | TauDEM 5 | 8 | 4 GB | 4 GB
Sept 2010 | Multifile on 48 GB RAM PC | 4 | Hardware limits | 6 GB
Sept 2010 | Multifile on cluster with 128 GB RAM | 128 | Hardware limits | 11 GB
1.6 GB
0.22 GB
4 GB
6 GB
11 GB
At 10 m grid cell size
Single GeoTIFF file size limit 4GB

## Slide 32: Carving
Lower elevation of neighbor along a predefined drainage path until the pit drains to the outlet point

## Slide 33
Filling
Carving
Minimizing Alterations

## Slide 34
+
=
 Take a mapped stream network and a DEM
 Make a grid of the streams
 Raise the off-stream DEM cells by an arbitrary elevation
increment
 Produces "burned in" DEM streams = mapped streams
“Burning In” the Streams

## Slide 35
AGREE Elevation Grid Modification Methodology – DEM Reconditioning

## Slide 36
ArcHydro Page 74
172
201
204
202
206
203
209
Each link has a unique identifying number
Stream Segments

## Slide 37
Vectorized Streams Linked Using Grid Code to Cell Equivalents
Vector
Streams
Grid
Streams
ArcHydro Page 75

## Slide 38
DrainageLines are drawn through the centers of cells on the stream links. DrainagePoints are located at the centers of the outlet cells of the catchments
ArcHydro Page 75

## Slide 39: Catchments
For every stream segment, there is a corresponding catchment
Catchments are a tessellation of the landscape through a set of physical rules

## Slide 40: Raster Zones and Vector Polygons
Catchment GridID
Vector Polygons
DEM GridCode
Raster Zones
3
4
5
One to one connection

## Slide 41
Catchments, DrainageLines and DrainagePoints of the San Marcos basin
ArcHydro Page 75

## Slide 42
Catchment, Watershed, Subwatershed.
ArcHydro Page 76
Watershed outlet points may lie within the interior of a catchment, e.g. at a USGS stream-gaging site.
Catchments
Subwatersheds
Watershed

## Slide 43: Summary of Key Processing Steps
[DEM Reconditioning]
Pit Removal (Fill Sinks)
Flow Direction
Flow Accumulation
Stream Definition
Stream Segmentation
Catchment Grid Delineation
Raster to Vector Conversion (Catchment Polygon, Drainage Line, Catchment Outlet Points)

## Slide 44: Delineation of Channel Networks and Catchments
500 cell theshold
1000 cell theshold

## Slide 45: How to decide on stream delineation threshold ?
AREA 1
AREA 2
3
12
Why is it important?

## Slide 46
Hydrologic processes are different on hillslopes and in channels. It is important to recognize this and account for this in models.
Drainage area can be concentrated or dispersed (specific catchment area) representing concentrated or dispersed flow.

## Slide 47: Examples of differently textured topography
Badlands in Death Valley. from Easterbrook, 1993, p 140.
Coos Bay, Oregon Coast Range.
from W. E. Dietrich

## Slide 48: Gently Sloping Convex Landscape
From W. E. Dietrich

## Slide 49: Topographic Texture and Drainage Density
Same scale, 20 m contour interval
Sunland, CA
Driftwood, PA

## Slide 50
Lets look at some geomorphology.
    Drainage Density
    Horton’s Laws
    Slope – Area scaling
    Stream Drops
“landscape dissection into distinct valleys is limited by a threshold of channelization that sets a finite scale to the landscape.” (Montgomery and Dietrich, 1992, Science, vol. 255 p. 826.)
Suggestion: One contributing area threshold does not fit all watersheds.

## Slide 51: Drainage Density
Dd = L/A
Hillslope length  1/2Dd
L
B
B
Hillslope length = B
A = 2B L
Dd = L/A = 1/2B
 B= 1/2Dd

## Slide 52: Drainage Density for Different Support Area Thresholds
EPA Reach Files
100 grid cell threshold
1000 grid cell threshold

## Slide 53: Drainage Density Versus Contributing Area Threshold

## Slide 54: Hortons Laws: Strahler system for stream ordering
1
1
1
1
1
1
1
1
1
1
1
1
1
1
2
2
2
2
3

## Slide 55: Length Ratio

## Slide 56: Slope Ratio

## Slide 57: Constant Stream Drops Law
Broscoe, A. J., (1959), "Quantitative analysis of longitudinal stream profiles of small watersheds," Office of Naval Research, Project NR 389-042, Technical Report No. 18, Department of Geology, Columbia University, New York.

## Slide 58: Stream Drop Elevation difference between ends of stream
Note that a “Strahler stream” comprises a sequence of links (reaches or segments) of the same order
Nodes
Links
Single Stream

## Slide 59: Suggestion: Map channel networks from the DEM at the finest resolution consistent with observed channel network geomorphology ‘laws’.
Look for statistically significant break in constant stream drop property as stream delineation threshold is reduced
Break in slope versus contributing area relationship
Physical basis in the form instability theory of Smith and Bretherton (1972), see Tarboton et al. 1992

## Slide 60: Statistical Analysis of Stream Drops

## Slide 61: T-Test for Difference in Mean Values
72
130
0
T-test checks whether difference in means is large (> 2)
when compared to the spread of the data around the mean values

## Slide 62: Constant Support Area Threshold

## Slide 63
100 grid cell constant support area threshold stream delineation

## Slide 64
200 grid cell constant support area based stream delineation

## Slide 65: Local Curvature Computation (Peuker and Douglas, 1975, Comput. Graphics Image Proc. 4:375)
43
41
48
47
48
47
54
51
54
51
56
58

## Slide 66: Contributing area of upwards curved grid cells only

## Slide 67: Upward Curved Contributing Area Threshold

## Slide 68
Curvature based stream delineation

## Slide 69: Channel network delineation, other options
1
1
1
1
1
1
1
1
1
1
1
1
1
1
4
3
3
12
2
2
2
3
16
25
6
Contributing Area
1
1
1
1
1
1
1
1
1
1
1
1
1
1
2
2
2
3
1
1
1
2
3
3
2
Grid Order
4
5
6
3
7
2
1
8

## Slide 70
Grid network pruned to order 4 stream delineation

## Slide 71: Summary Concepts
The eight direction pour point model approximates the surface flow using eight discrete grid directions
The elevation surface represented by a grid digital elevation model is used to derive surfaces representing other hydrologic variables of interest such as
  Slope
  Flow direction
  Drainage area
  Catchments, watersheds and channel networks

## Slide 72: Summary Concepts (2)
Hydrologic processes are different between hillslopes and channels
Drainage density defines the average spacing between streams and the representative length of hillslopes
The constant drop property provides a basis for selecting channel delineation criteria to preserve the natural drainage density of the topography
Generalized channel delineation criteria can represent spatial variability in the topographic texture and drainage density

## Slide 73: Are there any questions ?
AREA 1
AREA 2
3
12