## Slide 1: Arc Hydro Groundwater & Time
Tim Whiteaker (UT Austin)
Gil Strassberg (Aquaveo)
David Maidment (UT Austin)

## Slide 2: Linking GIS and Water Resources
GIS
Water
Resources

## Slide 3: Arc Hydro Groundwater: GIS For Hydrogeology
Describes the data model – public domain
Chapter for each data model component
Will be released later this year
Notes: Notes:
Industrial partners: ESRI, Danish Hydraulic Institute, Camp,Dresser and McKee, Dodson and Associates
Government partners:
Federal: EPA, USGS, Corps of Engineers (Hydrologic Engineering Center)
State: Texas Natural Resource Conservation Commission, Texas Water Development Board
Local: Lower Colorado River Authority, City of Austin, Dept of Watershed Protection
Academic Partners: University of Texas, Brigham Young University, Utah State University

## Slide 4: Space-time datasets

## Slide 5: Space-time datasets
Single variable time series – A variable recorded at a location, such as stream discharge or groundwater levels
Multi variable time series – Multiple variables recorded simultaneously at the same location, such as chemical analysis of a water sample
Time varying surfaces (raster series) – Raster datasets indexed by time. Each rater is a “snapshot” of the environment at a certain time.
Time varying features (feature series) – A collection of features indexed by time. Each feature in a feature series represents a variable at a single time period.

## Slide 6: Variable Definition table
Catalog of time varying parameters (e.g. streamflow, water levels, concentrations, etc.)
Each variable is indexed with a HydroID

## Slide 7: TimeSeries table
Each measurement is indexed by space, time, and type
Space = FeatureID
Time = TsTime
Type = VarID
VarID provides information on the variable

## Slide 8: Time series views
We can “slice” through the data cube to get specific views of the data
Query by location
(FeatureID = 2791)
Where?
2791
TsTime
FeatureID
VarID
Query by type
(VarID = 6875)
What?
FeatureID
VarID
TsTime
6875
Query by location and type
(FeatureID = 2791 VarID = 6875)
Where and What?
2791
FeatureID
VarID
TsTime
6875

## Slide 9: Time series views
Well HydroID = 2791
Create a plot of time series related to a feature
Get all the data of VarID 6875 measured at Feature 2791

## Slide 10: Time series views
A type-time view: Get water levels (TSTypeID =2) for 1/1999
Water level in the Edwards Aquifer in 1/1999
Set of layers for different times creates an animation
1/1991
FeatureID
VarID
6875
TsTime

## Slide 11: Multi-variable time series
Variables (VarKey)
Multiple variables recorded simultaneously at the same location
Example – water quality parameters
Indexed by location (FeatureID), and time (TsTime)
Relationship to the VariableDefinition table is through the VarKey

## Slide 12: Multi-variable time series
Can query for multiple variables together
Well HydroID = 2833
New Braunfels Springs

## Slide 13: Raster Series
January 1991
January 1992
January 1993
Raster datasets indexed by time
Each raster represents a continuous surface describing a variable for a given time

## Slide 14: Feature Series
A collection of features indexed by time
Example of particle tracks
Features are indexed by VarID, TsTime, and GroupID
Each group of features creates a track over time

## Slide 15: Time series statistics
Summarize values over a given time
Custom tool - part of Groundwater Analyst

## Slide 16: Workflow
Import time series data into AHGW table format
Create time series views – Time Series Statistics tool
Interpolate to create rasters
Load and index rasters in the RasterSeries raster catalog
Animate data
Workflow
Automate workflows with custom models/scripts