## Slide 1: Space and Time
By David R. Maidment
with contributions from Gil Strassberg and Tim Whiteaker

## Slide 2: Linking GIS and Water Resources
GIS
Water
Resources
Water Environment
(Watersheds, gages, streams)
Water Conditions
(Flow, head, concentration)

## Slide 3: Data Cube
Space, FeatureID
Time, TsTime
Variables, VarID
D
“What”
“Where”
“When”
A simple data model

## Slide 4
2791
TsTime
FeatureID
VarID
FeatureID
VarID
2791
FeatureID
VarID
(a)
(b)
(c)
TsTime
TsTime
6875
6875
Time Series in the Data Cube
{FeatureID = 2791} gives all data for a feature
{VarID = 6875} gives all data for a variable
{Feature ID = 2791 and VarID = 6875} gives a time series

## Slide 5: Space, Time, Variables and Observations
Variables (VariableID)
Space (FeatureID)
Time
Observations Data Model
Data from sensors (regular time series)
Data from field sampling (irregular time points)
An observations data model archives values of variables at
particular spatial locations and points in time

## Slide 6: Space, Time, Variables and Visualization
Variables (VariableID)
Space (FeatureID)
Time
Vizualization
Map – Spatial distribution for a time point or interval
Graph – Temporal distribution for a space point or region
Animation – Time-sequenced maps
A visualization is a set of maps, graphs and animations that display the variation of a phenomenon in space and time

## Slide 7: Space, Time, Variables and Simulation
Variables (VariableID)
Space (FeatureID)
Time
Process Simulation Model
A space-time point is unique
At each point there is a set of variables
A process simulaton model computes values of sets of variables at
particular spatial locations at regular intervals of time

## Slide 8: Space, Time, Variables and Geoprocessing
Variables (VariableID)
Space (FeatureID)
Time
Geoprocessing
Interpolation – Create a surface from point values
Overlay – Values of a surface laid over discrete features
Temporal – Geoprocessing with time steps
Geoprocessing is the application of GIS tools to transform spatial data and create new data products

## Slide 9: Space, Time, Variables and Statistics
Variables (VariableID)
Space (FeatureID)
Time
Statistical distribution
Represented as {probability, value}
Summarized by statistics (mean, variance, standard deviation)
A statistical distribution is defined for a particular variable defined over a particular space and time domain

## Slide 10: Space, Time, Variables and Statistical Analysis
Variables (VariableID)
Space (FeatureID)
Time
Statistical analysis
Multivariate analysis – correlation of a set of variables
Geostatistics – correlation space
Time Series Analysis – correlation in time
A statistical analysis summarizes the variation of a set of variables over a particular domain of space and time

## Slide 11
CUAHSI Observations Data Model
Space-Time Datasets
Sensor and laboratory databases
From Robert Vertessy, CSIRO, Australia

## Slide 12: Geospatial time series
Time series = {value, time}
Attribute series = {featureID, value, time}
  Fixed geometry, only attributes change with time
Raster series = {raster, time}
Feature series = {shape, value, time}
  Both shape and attributes vary in time
Notes: Layers give you the view on the data that you need to perform your analyses.

## Slide 13
TimeSeries
AttributeSeries
RasterSeries
FeatureSeries
Geospatial time series

## Slide 14: Arc Hydro II: Dataset Overview
[TimeSeries]
[RasterSeries]
DatasetCatalog
SeriesCatalog
Variables
[FeatureSeries]
[AttributeSeries]
workflows
workflows
indexes
indexes
associations
associations
Framework
Extended
Notes: The brackets indicate that the name of this table can be whatever a user wants. So, the user can have a feature series called “Hurricanes”, and another one called “InundationPolygons”. I’m allowing the TimeSeries table to have multiple names for flexibility. The Variables, FeatureVariableIndex, and DatasetVariableIndex tables have predefined names that must be used.

## Slide 15: Framework Schema
Variables
TimeSeries
SeriesCatalog
[TimeSeries]
SeriesCatalog
Variables
indexes
associations

## Slide 16: Variables
A variable has a name, plus other properties
A variable can be represented by many time series datasets
Indexed by VariableID, or VarKey when a String is required
Variables
VariableID
VarName VarDesc
VarUnits
SmplMedium
VarCode
Vocabulary
VarKey
IsRegular
TimeUnits
TimeStep
DataType
NoDataVal

## Slide 17: TimeSeries
FeatureID
VariableID
[TimeSeries]
VariableID
FeatureID
TsTime
UTCOffset
TsValue
Variables
VariableID
VarName VarUnits
VarDesc
Etc…
[FeatureClass]
HydroID
Shape
Time
Space
Variables
TsTime
Data value
TsValue
Data values indexed by Location, Variable, Time
Notes: Time series for Arc Hydro II is an atomic representation of the data cube. In other words, each data value has a row in a TimeSeries table. This design is very flexible. Time is subordinate to Space and Variables here. In the TimeSeries table, time is just another piece of metadata for the data value.

## Slide 18: SeriesCatalog
3
4
Indexes time series for a given feature and variable
Supports fast queries to identify data series
SeriesCatalog
SeriesID
FeatureID
FeatClass
VariableID
TsTable
StartTime
EndTime
ValueCount
Time
Space
Variables
SeriesID
1
2
Where
When
What
Notes: This table summarizes time series. It enables faster searches for data series to figure out what you have in the database (but to retrieve the data values themselves, you still have to query the TimeSeries table).

## Slide 19: Extended Schema Adds Items
Typically derived from models or observations
Contains
  TsTime
  UTCOffset
  Location Index or Shape
DatasetCatalog indexes entire datasets for a variable
[RasterSeries]
DatasetCatalog
[FeatureSeries]
[AttributeSeries]
workflows
indexes

## Slide 20: DatasetCatalog
DatasetCatalog
VariableID
DsType
DsSource
TsTable
StartTime
EndTime
StepCount
Raster Series
Feature Series
Attribute Series, e.g., NEXRAD
Notes: The NEXRAD example might be confused with a feature series. Actually, no time stamps are associated with the HRAP features. Each feature has a unique ID, which relates to rainfall data in an attribute series table. This dataset should be indexed in the DatasetVariableIndex table, and not the FeatureVariableIndex table, because we don’t care about rainfall in an individual HRAP cell. We tend to view the dataset as a whole, and do spatial/temporal interpolation to extract that the data that we need for other purposes. An example of this is interpolating rainfall onto catchments.
The NEXRAD images was obtained from http://www.idswater.com/Common/Paper/Paper_176/z7.jpg.

## Slide 21
A Feature Series – Particle Tracking