## Slide 1: Arc Hydro Groundwater Data Model
GIS in Water Resources
Fall 2011

## Slide 2: Arc Hydro: GIS for Water Resources
Arc Hydro
  An ArcGIS data model for water resources
  Arc Hydro toolset for implementation
  Framework for linking hydrologic simulation models
The Arc Hydro data model and
application tools are in the public
domain
Published in 2002, now in revision for Arc Hydro II
Notes: Notes:
Industrial partners: ESRI, Danish Hydraulic Institute, Camp,Dresser and McKee, Dodson and Associates
Government partners:
Federal: EPA, USGS, Corps of Engineers (Hydrologic Engineering Center)
State: Texas Natural Resource Conservation Commission, Texas Water Development Board
Local: Lower Colorado River Authority, City of Austin, Dept of Watershed Protection
Academic Partners: University of Texas, Brigham Young University, Utah State University

## Slide 3: Arc Hydro Groundwater: GIS For Hydrogeology
Describes the data model – public domain
Chapter for each data model component
Published in 2011
Notes: Notes:
Industrial partners: ESRI, Danish Hydraulic Institute, Camp,Dresser and McKee, Dodson and Associates
Government partners:
Federal: EPA, USGS, Corps of Engineers (Hydrologic Engineering Center)
State: Texas Natural Resource Conservation Commission, Texas Water Development Board
Local: Lower Colorado River Authority, City of Austin, Dept of Watershed Protection
Academic Partners: University of Texas, Brigham Young University, Utah State University

## Slide 4: Arc Hydro Groundwater Data Model
Notes: This is an overview diagram of the AHGW data model.
You can review the different components, talk about what each component is for:
Framework – includes hydrography, monitoring points, wells, aquifers, tables for managing time series (the framework includes a simplified temporal component). – with the framework you can get started on most water resources projects.
Borehole data – description of vertical information recorded along boreholes (hydrostratigraphy, well construction).
Geology – representation of data from geologic maps.
Hydrostratigraphy – building 2D and 3D hydrogeologic models including surfaces, cross sections, volumes.
Temporal – dealing with time varying data – plots, tracks, animations.
Simulation – integration with groundwater simulation models, especially MODFLOW.

## Slide 5: Arc Hydro Framework
Basic representation of surface water and groundwater
Components can be added to the framework to represent specific themes in more detail

## Slide 6: Hydrography
WaterLine, WaterBody represent hydrography
Watershed represents drainage areas
Notes: Representation of hydrography – including lines (streams, rivers) polygons (water bodies, lakes, ponds, etc), and points for representing features such as diversions, springs, structures, etc.
Watershed represents the drainage areas. In Arc Hydro surface water there are different definitions for the drainage areas (catchment, watershed, basin). In the framework we only include a general feature class.

## Slide 7: WaterPoint
WaterPoint represents points of interest such as structures, dams, springs, diversions, etc.
Notes: General point features that represent different features: For example we can use WaterPoints to represent springs, or sinks that recharge an aquifer.
We can also use WaterPoint to represent features along a river network (in the surface water components there is a special component for representing river networks) and the features can be linked to the river network at junctions. Examples are structures, dams, diversion points.

## Slide 8: Monitoring Point
MonitoringPoint features represent locations where water is measures
Notes: Monitoring points are locations where water is measured. Some examples – stream gages, collection points for water quality, rain gages. Basically any location where data is collected.
Monitoring points are related with time series.

## Slide 9: Aquifer features
Polygon features for representing aquifer boundaries

## Slide 10: Aquifer features
An aquifer is defined by one or a set of polygon features
Aquifer features can be grouped by HGUID

## Slide 11: Well
Location where the subsurface has been drilled
Attributes of wells describe the location, depth, water use, owner, etc.

## Slide 12: Well
Wells are defined as 2D point features
Only some basic attributes are predefined to describe the well use, and geometry and relationship with aquifers
Wells in the Edwards Aquifer

## Slide 13: Aquifer and well
Well features are related to Aquifers
An aquifer can be associated with one or more wells (1:M relationship)
Can take a different approach to support M:N relationship
*
HydroID
HydroCode
Name
HGUID
FType
Aquifer
HydroID
HydroCode
LandElev
WellDepth
AquiferID
AqCode
HGUID
FType
Well
1

## Slide 14: Aquifer and well
Well HydroID = 53

## Slide 15: Wells and TimeSeries
Well features are related with time series (water levels, water quality)
San Marcos springs
Springs
Sink Creek
San Marcos
Monitoring Well
(
295443097554201
)

## Slide 16: MonitoringPoint has time series
Monitoring points are related with time series (streamflow, water quality, precipitation)

## Slide 17: Integration of surface water and groundwater data
Streamflow Gage at Comal Springs, New Braunfels Texas
Well in the Edwards Aquifer)
The common framework supports analysis of surface water and groundwater data together

## Slide 18: Surface water - groundwater linkage
Relationships between surface water and aquifer enable analysis based on spatial and hydrologic relationships
Streams over the outcrop = recharge features

## Slide 19: Components
Geology - Representation of data from geologic maps
Boreholes – Description of well attributes and borehole data
Hydrostratigraphy – 2D and 3D description of hydrostratigraphy
Temporal – Representation of time varying data
Simulation – Representation of groundwater simulation models (focus on MODFLOW)

## Slide 20: Geologic maps
A geologic map is a cartographic product that portrays information about the geologic character of a specific geographic area
Groundwater features are closely tied to geology
Geologic maps vary in scale (continental, regional, local)
Provide a simple data structure to support mapping
Geology
Aquifers
Maps from the United States National Atlas (http://nationalatlas.gov/).

## Slide 21: Geology component
Map modified from: Geologic map of the Edwards Aquifer recharge zone, south-central Texas. U.S. Geological Survey SIM 2873
GeologyPoint: Point feature (e.g. springs, caves, sinks, and observation points)
GeologyLine: Line features (e.g. faults, contacts)
GeologyArea: Areal features (e.g. rock units and alteration zones)

## Slide 22: Components
Geology - Representation of data from geologic maps
Boreholes – Description of well attributes and borehole data
Hydrostratigraphy – 2D and 3D description of hydrostratigraphy
Temporal – Representation of time varying data
Simulation – Representation of groundwater simulation models (focus on MODFLOW)

## Slide 23: Borehole data
3D data (screens, completion intervals, stratigraphy) are referenced along the well
From depth (top) – To depth (bottom)

## Slide 24: BoreholeLog table
Stores 3D borehole data related with well features
Each row represents a point/interval along a borehole
Data are related to Wells using the WellID attribute
3D geometry is defined by the TopElev and BottomElev attributes

## Slide 25: 3D features (BorePoints and BoreLines)
Can create 3D features representing data in the BoreholeLog table
BorePoint is a 3D point feature class for representing point locations along a borehole (e.g. geologic contacts, samples)
BoreLine is a 3D line feature class for representing intervals along a borehole

## Slide 26: Components
Geology - Representation of data from geologic maps
Boreholes – Description of well attributes and borehole data
Hydrostratigraphy – 2D and 3D description of hydrostratigraphy
Temporal – Representation of time varying data
Simulation – Representation of groundwater simulation models (focus on MODFLOW)

## Slide 27: Hydrogeologic units
“Hydrogeologic unit is any soil or rock unit or zone which by virtue of its hydraulic properties has a distinct influence on the storage or movement of ground water” (USGS glossary of hydrologic terms)
Hydrogeology can be derived by classifying stratigraphic units
Georgetown Fm. (GTOWN)
Cyclic + Marine member (CYMRN)
Upper confining unit
Leached + collapsed member (LCCLP)
Regional dense member (RGDNS)
Grainstone member (GRNSTN)
Kirschberg evaporite member (KSCH)
Dolomitic member (DOLO)
Upper Glen Rose (UGLRS)
Stratigraphic units
Hydrogeologic units
Pearson Fm.
Basal Nodular member (BSNOD)
Kainer Fm.
Georgetown Fm.
Edwards Aquifer

## Slide 28: Hydrogeologic unit table
HydroGeologicUnit table provides a conceptual description of hydrogeologic units
Hydrogeologic units can be attributed with an AquiferID such that they can be grouped to represent an aquifer
Spatial features are indexed with a HGUID to relate to the conceptual representation of the units

## Slide 29: Hydrogeologic unit table
Hydrogeologic units are described with different spatial instances (outcrops, borehole intervals, surfaces, cross sections, and volumes)
HGUID is the key attribute
HGUID
HGUID
Conceptual description
Spatial description
GeoArea
Polygon
feature class
HydrogeologicUnit
Table
SectionLine
PointZ
feature class
GeoRasters
Raster dataset
GeoSection
Multipatch
feature class
GeoVolume
Multipatch
feature class
1
*

## Slide 30: GeoArea
GeoArea feature representing the Kainer hydrogeologic unit
GeologyArea features represent data from geologic maps
GeologyArea
2D polygons defining boundaries of hydrogeologic units
GeoArea (conceptual/interpolated boundary) ≠ GeologyArea (mapped outcrop)
Data points representing top elevations of the Kainer formation

## Slide 31: Representation of Cross Sections
SectionLine defines the 2D cross section
GeoSection represent 3D sections as 3D features
SectionID of the polygon relates back to the section line
A
A’
B
B’

## Slide 32: GeoSections

## Slide 33: XS2D Component

## Slide 34: 2D Cross Section Editing
Outcrop
Salt water interface
Borehole data
Panel
Panel divider
Edit cross sections in ArcMap

## Slide 35: Transform to 3D GeoSection

## Slide 36: GeoRasters
Raster catalog for storing and indexing raster datasets
Can store top and bottom of formations
Each raster is related with a HGU in the hydrogeologic unit table
Georgetown
Glen Rose
Kainer
Person

## Slide 37: GeoRasters
GeoRasters also store hydraulic properties such as transmissivity, conductivity, and specific yield
K (feet/day)
Raster of hydraulic conductivity in the Edwards Aquifer

## Slide 38: GeoVolume
Objects for representing 3D volume objects
Geometry is multipatch - Can create the volumes as a set of 3D triangles
Not real volume – can’t do any 3D operations

## Slide 39: Components
Geology - Representation of data from geologic maps
Boreholes – Description of well attributes and borehole data
Hydrostratigraphy – 2D and 3D description of hydrostratigraphy
Temporal – Representation of time varying data
Simulation – Representation of groundwater simulation models (focus on MODFLOW)

## Slide 40: Space-time datasets

## Slide 41: Types of time varying datasets

## Slide 42: Variable Definition table
Catalog of time varying parameters (e.g. streamflow, water levels, concentrations, etc.)
Each variable is indexed with a HydroID

## Slide 43: TimeSeries table
Each measurement is indexed by space, time, and type
Space = FeatureID
Time = TsTime
Type = VarID
VarID provides information on the variable

## Slide 44: Time series views
We can “slice” through the data cube to get specific views of the data
Query by location
(FeatureID = 2791)
Where?
2791
TsTime
FeatureID
VarID
Query by type
(VarID = 6875)
What?
FeatureID
VarID
TsTime
6875
Query by location and type
(FeatureID = 2791 VarID = 6875)
Where and What?
2791
FeatureID
VarID
TsTime
6875

## Slide 45: Time series views
Well HydroID = 2791
Create a plot of time series related to a feature
Get all the data of VarID 6875 measured at Feature 2791

## Slide 46: Time series views
A type-time view: Get water levels (TSTypeID =2) for 1/1999
Water level in the Edwards Aquifer in 1/1999
Set of layers for different times creates an animation
1/1991
FeatureID
VarID
6875
TsTime

## Slide 47: Multi-variable time series (attribute series)
Variables (VarKey)
Multiple variables recorded simultaneously at the same location
Example – water quality parameters
Indexed by location (FeatureID), and time (TsTime)
Relationship to the VariableDefinition table is through the VarKey

## Slide 48: Raster Series
January 1991
January 1992
January 1993
Raster datasets indexed by time
Each raster represents a continuous surface describing a variable for a given time

## Slide 49: Feature Series
A collection of features indexed by time
Example of particle tracks
Features are indexed by VarID, TsTime, and GroupID
Each group of features creates a track over time

## Slide 50: Components
Geology - Representation of data from geologic maps
Boreholes – Description of well attributes and borehole data
Hydrostratigraphy – 2D and 3D description of hydrostratigraphy
Temporal – Representation of time varying data
Simulation – Representation of groundwater simulation models (focus on MODFLOW)

## Slide 51: Representing simulation models
Georeference model inputs and outputs (in space and time)
Focus on MODFLOW, block centered finite difference grid (nodes are in the center of the cells)
Represent 2D and 3D models
Block-centered finite difference grid

## Slide 52: Simulation component
Features for representing data from simulation models

## Slide 53: Boundary
Polygon feature class for representing the extent and orientation of a simulation model

## Slide 54: Cell2D and Node
Cell2D: polygon feature class that represents cells or elements associated with a two-dimensional simulation model or a single layer of a three-dimensional model
Node: point feature class used in combination with Cell2D to represent the model’s mesh/grid.
Finite element mesh
Mesh centered finite difference grid
Cell centered finite difference grid

## Slide 55: Cell2D and Node
Used to create maps of model data

## Slide 56: Node3D and Cell3D
Node3D – a Z enabled point feature class
Cell3D - Multipatch feature class
Represent three-dimensional cells and Nodes
Used mostly for visualization of 3D models

## Slide 57: Summary Concepts
Arc Hydro Groundwater…
  extends Arc Hydro to represent groundwater datasets in GIS
  includes components for aquifers, wells, hydrogeologic features, time series, and simulation model output
  links features to hydrogeologic layers via HGUID, and to aquifers via AquiferID

## Slide 58: Resources
Hydro Resource Center http://resources.arcgis.com/content/hydro
Groundwater Tools and Data Model http://www.aquaveo.com/archydro-groundwater
Tutorials http://www.aquaveo.com/ahgw-learning
Contact for tool support support@aquaveo.com