## Slide 1: Fine Particulate Matter Concentrations in the Dallas-Fort Worth Area
Adam Pacsi

## Slide 2: Background
Liquid/Solid Condensed Phase in Air
Fine = less than 2.5 microns in diameter
Found to trend like ozone in most US Cities
Regulation: < 15 µg/m³ for a daily average
Courtesy: TCEQ

## Slide 3: Motivation
Health Effects: asthma and overall morbidity
Overall visibility and appearance
Funding for monitoring of PM2.5 has been reduced since 2000
Courtesy: texasdailyphoto.com

## Slide 4: Research Problem
Determine new PM monitoring sites from current ozone sites in DFW
Criteria:
  Predicted PM Concentration (from ozone levels)
  The Distance from a current PM site
  Local Population Density

## Slide 5: Current Monitoring Sites
Legend
PM
Ozone
Current Number of Sites
PM: 8
Ozone: 20

## Slide 6: Sources of Data
TCEQ
  Monitor Locations
  2008-2010 Average Ozone Concentrations
ESRI 2000 TIGER/Line Data
  Census tract shapefiles
  Tract population data
Courtesy: ESRI
Note: All datasets were in NAD83 and needed to be converted to Albers Projection from Exercise 1.

## Slide 7: Methods: Population Density
Census Tracts
Population by Tract
Population Density
Census Tract Database File
Table Join
Field Calculator

## Slide 8: Methods: Distance
Census Tract Data
Tract Data as Center Point
Distance to Current PM Site
PM Monitor Locations
Near
Mean Center

## Slide 9: Methods: Ozone Concentration
Ozone Values at Monitoring Sites
Interpolated Ozone Raster (float)
Interpolated Ozone Raster (int)
Ozone Raster Values as Points
Ozone Values by Tract Center
IDW
Kriging
Natural Neighbor
Int
Raster to Point
Near
Table Join
IDW
Ozone Value
by Tract
Census Tract Center Points

## Slide 10: Methods: Categorizing
Problem: Differing scales for parameters even when normalized
Solution: Categorizing Data each parameter
  x < Mean - 2σ
  Mean-2σ < x < Mean–σ
  Mean-σ < x < Mean+σ
  Mean+σ < x < Mean+2σ
  x > Mean+2σ
VB Script in Field Calculator

## Slide 11: Results: Spatial Distribution
IDW
Added the categorized values to get a score out of 15.

## Slide 12: Results: Which Sites?
Chart: Total Points Per Site (Max =15)
| Parker County | Frisco | Rockwall Heath | Greenville | Rockwall Heath | Parker County | Granbury | Parker County | Rockwall Heath | Frisco
Density | 1 | 2 | 2 | 2 | 2 | 1 | 2 | 1 | 2 | 2
Distance | 5 | 4 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 4
Concentration | 5 | 5 | 5 | 5 | 4 | 5 | 5 | 5 | 4 | 5