## Slide 1: Sharing Data Using the CUAHSI Hydrologic Information System
David Tarboton
Utah State University
Support
EAR 0622374
CUAHSI
HIS
Sharing hydrologic data
http://his.cuahsi.org/

## Slide 2: The CUAHSI Hydrologic Information System Team
University of Texas at Austin – David Maidment, Tim Whiteaker, James Seppi, Fernando Salas, Jingqi Dong, Harish Sangireddy
San Diego Supercomputer Center – Ilya Zaslavsky, David Valentine, Tom Whitenack, Matt Rodriguez
Utah State University – David Tarboton, Jeff Horsburgh, Kim Schreuders, Stephanie Reeder
University of South Carolina – Jon Goodall, Anthony Castronova
Idaho State University – Dan Ames, Ted Dunsford, Jiří Kadlec, Yang Cao, Dinesh Grover
Drexel University/CUNY – Michael Piasecki
CUAHSI Program Office – Rick Hooper, Yoori Choi, Jennifer Arrigo, Conrad Matiuk
ESRI – Dean Djokic, Zichuan Ye
Users Committee – Kathleen Mckee, Jim Nelson, Stephen Brown, Lucy Marshall, Chris Graham, Marian Muste
Support
EAR 0622374
CUAHSI
HIS
Sharing hydrologic data
http://his.cuahsi.org/

## Slide 3: What is CUAHSI?
Consortium of Universities for the Advancement of Hydrologic Science, Inc.
http://www.cuahsi.org/
111 US University members
7 affiliate members
17 International affiliate members
(as of October 2011)
Support
EAR 0753521
Infrastructure and services for the advancement of hydrologic science and education in the U.S.

## Slide 4: CUAHSI HIS
HydroServer – Data Publication
Lake Powell Inflow and Storage
HydroDesktop – Data Access and Analysis
HydroDesktop – Combining multiple data sources
HydroCatalog
Data Discovery
The CUAHSI Hydrologic Information System (HIS) is an internet based system to support the sharing of hydrologic data. It is comprised of hydrologic databases and servers connected through web services as well as software for data publication, discovery and access.

## Slide 5: Hydrologic Data Challenges
From dispersed federal agencies
From investigators collected for different purposes
Different formats
  Points
  Lines
  Polygons
  Fields
  Time Series
Rainfall and Meteorology
Water quantity
Soil water
Groundwater
Water quality
GIS
Data Heterogeneity

## Slide 6: The way that data is organized can enhance or inhibit the analysis that can be done
I have your information right here …
Picture from: http://initsspace.com/

## Slide 7: Hydrologic Science
Hydrologic conditions
(Fluxes, flows, concentrations)
Hydrologic Process Science
(Equations, simulation models, prediction)
Hydrologic Information Science
(Observations, data models, visualization
Hydrologic environment
(Physical earth)
Physical laws and principles
(Mass, momentum, energy, chemistry)
It is as important to represent hydrologic environments precisely with
data as it is to represent hydrologic processes with equations

## Slide 8: Data models capture the complexity of natural systems
NetCDF (Unidata) - A model for Continuous Space-Time data
Space, L
Time, T
Variables, V
D
Coordinate
dimensions
{X}
Variable dimensions
{Y}
ArcHydro – A model for Discrete Space-Time Data
Space, FeatureID
Time, TSDateTime
Variables, TSTypeID
TSValue
Terrain Flow Data Model used to enrich the information content of a digital elevation model
CUAHSI Observations Data Model: What are the basic attributes to be associated with each single data value and how can these best be organized?

## Slide 9
Data Searching – What we used to have to do
NWIS
NARR
NAWQA
NAM-12
request
request
request
request
request
request
request
request
return
return
return
return
return
return
return
return
Searching each data source separately
Michael Piasecki
Drexel University
Notes: 9

## Slide 10
What HIS enables
Searching all data sources collectively
NWIS
NAWQA
NARR
generic
request
GetValues
GetValues
GetValues
GetValues
GetValues
GetValues
GetValues
GetValues
ODM
Michael Piasecki
Drexel University
Notes: 10

## Slide 11: Web Paradigm
Catalog (Google)
Web Server
(CNN.com)
Browser
(Firefox)
Access
Catalog harvest
Search

## Slide 12: CUAHSI Hydrologic Information System Services-Oriented Architecture
Data Discovery and Integration
Data Publication
Data Analysis and Synthesis
HydroCatalog
HydroDesktop
HydroServer
ODM
Geo Data
Data Services
Metadata Services
Search Services
WaterML, Other OGC Standards
Information Model and Community Support Infrastructure

## Slide 13: Video Demo
http://his.cuahsi.org/movies/JacobsWellSpring/JacobsWellSpring.html

## Slide 14: What are the basic attributes to be associated with each single data value and how can these best be organized?
Value
DateTime
Variable
Location
Units
Interval (support)
Accuracy
Offset
OffsetType/ Reference Point
Source/Organization
Censoring
Data Qualifying Comments
Method
Quality Control Level
Sample Medium
Value Type
Data Type

## Slide 15: CUAHSI Observations Data Model
Streamflow
Flux tower
data
Precipitation
& Climate
Groundwater
levels
Water Quality
Soil
moisture
data
A relational database at the single observation level (atomic model)
Stores observation data made at points
Metadata for unambiguous interpretation
Traceable heritage from raw measurements to usable information
Standard format for data sharing
Cross dimension retrieval and analysis
Space, S
Time, T
Variables, V
s
t
Vi
vi (s,t)
“Where”
“What”
“When”
A data value

## Slide 16: Data Storage – Relational Database
Name | Latitude | Longitude
Cane Creek | 41.1 | -103.2
Cane Creek | 41.1 | -103.2
Town Lake | 40.3 | -103.3
Town Lake | 40.3 | -103.3
Values
Value
Date
Site
Variable
Sites
Site
Name
Latitude
Longitude
Value | Date | Site | Variable
4.5 | 3/3/2007 | 1 | Streamflow
4.2 | 3/4/2007 | 1 | Streamflow
33 | 3/3/2007 | 2 | Temperature
34 | 3/4/2007 | 2 | Temperature
Site | Name | Latitude | Longitude
1 | Cane Creek | 41.1 | -103.2
2 | Town Lake | 40.3 | -103.3
Simple Intro to “What Is a Relational Database”
Notes: HIS uses a relational database for data storage. If you’re unfamiliar with databases, here’s a quick intro. Suppose I have time series values for streamflow and temperature. I can store these in a table where I record the value, the date, the site where the measurement occurred, and the variable being measured. Now suppose I want to store more information about the site, such as its name and location. I could add some fields to the Values table, but if I have a million values, then I’m storing that same site information over and over again. A more efficient approach is to create a separate table with the site info, and relate one table to the other based on the Site number. A relational database is a set of tables with relationships like this.

## Slide 17
Horsburgh, J. S., D. G. Tarboton, D. R. Maidment and I. Zaslavsky, (2008), A Relational Model for Environmental and Water Resources Data, Water Resour. Res., 44: W05406, doi:10.1029/2007WR006392.
CUAHSI Observations Data Model http://his.cuahsi.org/odmdatabases.html
Notes: In designing ODM we asked: What are the basic attributes to be associated with each single data value and how can these best be organized? This involved community survey at a workshop and by email and based on the feedback received we came up with the ODM schema illustrated, published last year in WRR
This is quite a detailed slide, but it is the entire schema. Few database designs are simple enough to fit the entire schema on one slide. This shows at the center the data values table and off to the sides, the ancillary or metadata tables that record.

## Slide 18: Discharge, Stage, Concentration and Daily Average Example

## Slide 19: Site Attributes
SiteCode, e.g. NWIS:10109000
SiteName, e.g. Logan River Near Logan, UT
Latitude, Longitude Geographic coordinates of site
LatLongDatum Spatial reference system of latitude and longitude
Elevation_m Elevation of the site
VerticalDatum Datum of the site elevation
Local X, Local Y Local coordinates of site
LocalProjection Spatial reference system of local coordinates
PosAccuracy_m Positional Accuracy
State, e.g. Utah
County, e.g. Cache

## Slide 20
Feature
Waterbody
HydroID
HydroCode
FType
Name
AreaSqKm
JunctionID
HydroPoint
HydroID
HydroCode
FType
Name
JunctionID
Watershed
HydroID
HydroCode
DrainID
AreaSqKm
JunctionID
NextDownID
ComplexEdgeFeature
EdgeType
Flowline
Shoreline
HydroEdge
HydroID
HydroCode
ReachCode
Name
LengthKm
LengthDown
FlowDir
FType
EdgeType
Enabled
SimpleJunctionFeature
1
HydroJunction
HydroID
HydroCode
NextDownID
LengthDown
DrainArea
FType
Enabled
AncillaryRole
*
1
*
HydroNetwork
*
HydroJunction
HydroID
HydroCode
NextDownID
LengthDown
DrainArea
FType
Enabled
AncillaryRole
HydroJunction
HydroID
HydroCode
NextDownID
LengthDown
DrainArea
FType
Enabled
AncillaryRole
1
1
CouplingTable
SiteID
HydroID
Sites
SiteID
SiteCode
SiteName
Latitude
Longitude
…
Observations Data Model
1
1
OR
Independent of, but can be coupled to Geographic Representation
ODM
e.g. Arc Hydro

## Slide 21: Stage and Streamflow Example
Notes: Discharge Derived from Gage Height
Concepts:
Data derived from other data – single data point derived from a single observation (discharge from stage)
Data derived using a specific method (discharge from stage using rating curve)
Relationships:
Relationships between Values table and DerivedFrom table on DerivedFromID and ValueID
Relationship between Values table and Variables table on VariableID
Relationship between Values table and Methods table on MethodID
Relationship between Variables table and Units table on UnitID

## Slide 22
ValueAccuracy
A numeric value that quantifies measurement accuracy defined as the nearness of a measurement to the standard or true value. This may be quantified as an average or root mean square error relative to the true value. Since the true value is not known this may should be estimated based on knowledge of the method and measurement instrument. Accuracy is distinct from precision which quantifies reproducibility, but does not refer to the standard or true value.
Accurate
Low Accuracy, but precise
Low Accuracy
ValueAccuracy

## Slide 23: Water Chemistry from a profile in a lake
Notes: Water Chemistry From a Lake Profile
Concepts:
Grouped observations (all observations in one reservoir profile)
Observations made using an offset (observations made at multiple depths below the surface of a reservoir)
Observations made using a specific method (observations made using a particular field instrument)
Relationships:
Relationship between Values table and the Variables table on VariableID
Relationship between Values table and OffestTypes table on OffsetTypeID
Relationship between Values table and Methods table on MethodID
Relationship between Variables table and Units table on UnitID
Relationship between GroupDescriptions table and Groups table on GroupID
Relationship between OffsetTypes table and Units table on UnitID and OffsetUnitID

## Slide 24: Loading data into ODM
Interactive OD Data Loader (OD Loader)
  Loads data from spreadsheets and comma separated tables in simple format
Scheduled Data Loader (SDL)
  Loads data from datalogger files on a prescribed schedule.
  Interactive configuration
SQL Server Integration Services (SSIS)
  Microsoft application accompanying SQL Server useful for programming complex loading or data management functions
OD Data Loader
SDL
SSIS

## Slide 25
CUAHSI Observations Data Model
http://www.cuahsi.org/his/odm.html
1
2
3
Work from Out to In
4
5
6
7
At last …
And don’t forget …

## Slide 26: Importance of the Observations Data Model
Provides a common persistence model for observations data
Syntactic consistency (File types and formats)
Semantic consistency
  Language for observation attributes (structural)
  Language to encode observation attribute values (contextual)
Publishing and sharing research data
Metadata to facilitate unambiguous interpretation
Enhance analysis capability

## Slide 27
Set of query functions
Returns data in WaterML
WaterML and WaterOneFlow
WaterML is an XML language for communicating water data
WaterOneFlow is a set of web services based on WaterML
GetSites
WaterOneFlow
Web Service
GetValues
GetSiteInfo
GetVariableInfo
Notes: 27

## Slide 28: WaterML as a Web Language
Discharge of the San Marcos River at Luling, TX June 28 - July 18, 2002
USGS Streamflow data in WaterML language
This is the WaterML GetValues response from NWIS Daily Values

## Slide 29: Open Geospatial Consortium Web Service Standards
Map Services
Web Map Service (WMS)
Web Feature Service (WFS)
Web Coverage Service (WCS)
Catalog Services for the Web (CS/W)
Observation Services
Observations and Measurements Model
Sensor Web Enablement (SWE)
Sensor Observation Service (SOS)
These standards have been developed over the past 10 years ….
…. by 400 companies and agencies working within the OGC
OGC Hydrology Domain Working Group evolving WaterML into an International Standard
http://www.opengeospatial.org/projects/groups/waterml2.0swg

## Slide 30
Feature of Interest
Procedure (ID := “DAVIS_123“)
23 m/s 16.9.2010 13:45
Result
uom
Sampling Time
Observed Property := “Wind_Speed“
Observation
Sensor Observations Service: Get Observation
Notes: Basis for a standardized access to sensor data is the observation model defined in the Observations & Measurements standard. Let me briefly describe the main concepts / terms used in this model…

## Slide 31: HydroServer – Data Publication
Ongoing Data Collection
Data presentation, visualization, and analysis through Internet enabled applications
Internet Applications
Point Observations Data
Historical Data Files
GIS Data
ODM Database
GetSites
GetSiteInfo
GetVariableInfo
GetValues
WaterOneFlow
Web Service
WaterML
OGC Spatial Data Service from ArcGIS Server
Notes: A platform for publishing space-time hydrologic datasets that:
  Autonomous with local control of data
  Part of a distributed system that makes data universally available
Basis for Experimental Watershed or Observatory data management system
Standards based approach to data publication
  Accepted and emerging standards for data storage and transfer (OGC, WaterML)
Built on established software
  MS SQL Server, ArcGIS server
Open Source Community Code Repository
  Sustainability

## Slide 32
HydroCatalog
GetSites
GetSiteInfo
GetVariableInfo
GetValues
WaterOneFlow
Web Service
WaterML
Discovery and Access
Hydro
Desktop
Water Metadata Catalog
Harvester
Service Registry
Hydrotagger
Search Services
http://hiscentral.cuahsi.org
Search over data services from multiple sources
Supports concept based data discovery
CUAHSI Data Server
3rd Party Server
e.g. USGS

## Slide 33: Overcoming Semantic Heterogeneity
ODM Controlled Vocabulary System
  ODM CV central database
  Online submission and editing of CV terms
  Web services for broadcasting CVs
Variable Name
Investigator 1: | “Temperature, water”
Investigator 2: | “Water Temperature”
Investigator 3: | “Temperature”
Investigator 4: | “Temp.”
ODM VariableNameCV
Term
…
Sunshine duration
Temperature
Turbidity
…
From Jeff Horsburgh

## Slide 34
Dynamic controlled vocabulary moderation system
Local ODM
Database
Master ODM Controlled Vocabulary
ODM Website
ODM Controlled
Vocabulary Moderator
ODM Data Manager
ODM
Controlled Vocabulary
Web Services
ODM
Tools
Local
Server
XML
http://his.cuahsi.org/mastercvreg.html
From Jeff Horsburgh

## Slide 35: Thematic keyword search
Integration from multiple sources
Search on space and time domain
HydroDesktop – Data Access and Analysis

## Slide 36: HydroModeler
An integrated modeling environment based on the Open Modeling Interface (OpenMI) standard and embedded within HydroDesktop
Allows for the linking of data and models as “plug-and-play” components
In development at the University of South Carolina by Jon Goodall, Tony Castronova, Mehmet Ercan, Mostafa Elag, and Shirani Fuller

## Slide 37
Integration with “R” Statistics Package

## Slide 38: 37 Water Data Services on HIS Central from 12 Universities
Dry Creek Experimental Watershed (DCEW) (28 km2 semi-arid steep topography, Boise Front)
68 Sites
24 Variables
4,700,000+ values
Published by Jim McNamara, Boise State University
University of Maryland, Baltimore County
Montana State University
University of Texas at Austin
University of Iowa
Utah State University
University of Florida
University of New Mexico
University of Idaho
Boise State University
University of Texas at Arlington
University of California, San Diego
Idaho State University

## Slide 39: Water Agencies and Industry
USGS, NCDC , Corps of Engineers publishing data using HIS WaterML
OGC Hydrology Domain Working Group evaluating WaterML as OGC standard
ESRI using CUAHSI model in ArcGIS.com GIS data collaboration portal
Kisters WISKI support for WaterML data publication
Australian Water Resources Information System Water Accounting System has adopted aspects of HIS
NWS West Gulf River Forecast Center Multi-sensor Precipitation Estimate published from ODM using WaterML

## Slide 40: CUAHSI Water Data Services Catalog
69 public services
18,000 variables
1.9 million sites
23 million series
5.1 billion data values
(as of June 2011)
The largest water data catalog in the world
maintained at the San Diego Supercomputer Center

## Slide 41: Open Development Model
http://hydrodesktop.codeplex.com
http://hydroserver.codeplex.com
http://hydrocatalog.codeplex.com

## Slide 42: Summary
Data Storage in an Observations Data Model (ODM) and publication through HydroServer
Data Access through internet-based Water Data Services using a consistent data language, called WaterML from HydroDesktop
Data Discovery through a National Water Metadata Catalog and thematic keyword search system at Central HydroCatalog (SDSC)
Integrated Modeling and Analysis within HydroDesktop
This approach based on standards provides a general foundation and approach for integration and sharing of hydrologic data around the world.

## Slide 43: Are there any questions ?