## Slide 1: Data Sources for GIS in Water Resources by David R. Maidment, David G. Tarboton and Ayse Irmak GIS in Water Resources Fall 2011

## Slide 2
http://www.geodata.gov/
http://www.geodata.gov/

## Slide 3: USGS GIS data for Water
http://water.usgs.gov/maps.html

## Slide 4: Watersheds of the US
2-digit water resource regions
8-digit HUC watersheds

## Slide 5: Hydrologic Unit Code Watersheds
~ 2000 for US, about the size of counties

## Slide 6: Watershed Hierarchy
8 HUC
4
2
6
NHDPlus
10
12
Available
In Progress
Digit #

## Slide 7: Watershed Boundary Dataset
National Program by USGS and USDA (NRCS)
Boundaries for 10- and 12- digit watersheds
First cut is by automated delineation from NED
Hand checked and edited
10-digit watersheds

## Slide 8: Watershed Boundary DataSet
http://www.ncgc.nrcs.usda.gov/products/datasets/watershed/

## Slide 9: WBD for Nebraska
2990 HUC12 watersheds of average area 39.3 square miles
HUC12:HUC ~ 40:1 watersheds

## Slide 10: EPA River Reach File 1 (RF1)

## Slide 11
State and Local Data
Decisions
Watershed Management
.
TMDL
.
Source Water Protection
.
Stormwater
Data
Cartographic
Monitoring
Loadings
Models
HSPF - NPSM
QUAL2E
TOXIROUTE
Post-Processors
Tools
Target
Assessment
Data Mining
Reporting
BASINS - Integrating GIS and Water Quality Modeling
Target
Assess
DM

## Slide 12
River networks
for 8-digit HUC
watersheds
http://nhd.usgs.gov/

## Slide 14
Lower West Fork, Trinity River Basin
HUC = 12030102

## Slide 15: NHD River Reaches
412 River Reaches
In Upper West Fork of Trinity Basin

## Slide 16: River Reach Codes Used for river address locations
ReachCode =
12030102000151
ReachCode = 12030102000005
HUC#
Segment#
Location 0.392
on Reach
12030102000005

## Slide 17
http://www.horizon-systems.com/nhdplus/

## Slide 18: NHDPlus for a Portion of Oregon
http://www.horizon-systems.com/nhdplus/

## Slide 19: NHDPlus Reach Catchments ~ 3km2
About 1000 reach catchments in each 8-digit HUC
Average reach length = 2km
2.3 million reaches for continental US

## Slide 20: NHDPlus Reach Attributes
Slope
Elevation
Mean annual flow
  Corresponding velocity
Drainage area
% of upstream drainage area in different land uses
Stream order

## Slide 21: National Elevation Dataset
Digital Elevation Model with 1 arc-second (30m) cells
Seamless in 1° blocks for the United States
10 billion data
Derived from USGS 1:24,000 quadrangle sheets
http://seamless.usgs.gov/
Get the data:
http://ned.usgs.gov/

## Slide 22
From http://seamless.usgs.gov

## Slide 23
From http://seamless.usgs.gov

## Slide 24: Digital Elevation Model (DEM)
Contours
720
700
680
740
680
700
720
740
720
720

## Slide 25: Austin West 30 Meter DEM

## Slide 26
32
16
8
64
4
128
1
2
Eight Direction Pour Point Model
Water flows in the direction of steepest descent

## Slide 27: Flow Direction Grid
32
16
8
64
4
128
1
2

## Slide 28: Delineation of Streams and Watersheds on a DEM

## Slide 29
http://srtm.usgs.gov/

## Slide 30: HydroSheds derived from SRTM
http://hydrosheds.cr.usgs.gov/

## Slide 32: GTOPO30 - 1 km Digital Elevation Model of the Earth
http://eros.usgs.gov/#/Find_Data/Products_and_Data_Available/GTOPO30

## Slide 33: Drainage in North America
Hydro1K is
derived from
GTOPO30
using raster
GIS analysis
http://eros.usgs.gov/#/Find_Data/Products_and_Data_Available/gtopo30/hydro

## Slide 34
http://www.ngdc.noaa.gov/mgg/coast/

## Slide 35
http://www.soils.usda.gov/survey/geography/statsgo/
1:250,000 Scale Soil Information

## Slide 37
http://www.soils.usda.gov/survey/geography/ssurgo/
1:24,000 scale
soil information
SSURGO:
County Level
Digital Soil Maps

## Slide 38: Ssurgo for Travis County
103 soil map units described by 7530 polygons of average area 35.37 ha (87 acres)

## Slide 39
http://landcover.usgs.gov/

## Slide 40: National Land Cover Dataset
http://seamless.usgs.gov/
Get the data:

## Slide 42
http://www.nationalatlas.gov/atlasftp.html

## Slide 43
http://www.ncdc.noaa.gov/oa/ncdc.html

## Slide 44: PRISM Mean Annual Precipitation
http://www.wcc.nrcs.usda.gov/climate/prism.html

## Slide 45
http://www.daymet.org/

## Slide 46: National Water Information System
Web access to USGS water
resources data in real time
http://waterdata.usgs.gov/usa/nwis/

## Slide 47: USGS Water Watch
Web access to USGS water resources data in real time
http://waterdata.usgs.gov/nwis/rt

## Slide 48: USGS National Water Information System.
Real-time and Historic Data
  Streamflow and stage
  Groundwater levels
  Water Quality
  Site information
Tabular or Graphical Format

## Slide 49: NASA Satellite Data
https://lpdaac.usgs.gov/

## Slide 50: Global Energy and Water Experiment
http://www.gewex.org/

## Slide 51: http://water.weather.gov/ahps/

## Slide 52: http://water.weather.gov/ahps/

## Slide 53
http://www.wcc.nrcs.usda.gov/snotel/

## Slide 54: http://www.cbrfc.noaa.gov

## Slide 55: CBRFC SNOTEL Ensemble
http://www.cbrfc.noaa.gov/station/sweplot/sweplot.cgi?tglu1

## Slide 56: http://www.arcgis.com

## Slide 58: http://gis.utah.gov

## Slide 59: Utah Terrain Basemap
To use as a basemap in ArcGIS see instructions at
http://gis.utah.gov/map-services/new-utah-terrain-base-map-and-cached-tile-service-available

## Slide 60
Utah GIS Portal Download GIS Data
http://gis.utah.gov/download

## Slide 61
http://geology.utah.gov/maps/gis/index.htm

## Slide 62
http://www.wrcc.dri.edu/

## Slide 63
http://dnr.ne.gov/databank/geospatial.html

## Slide 64
http://dnr.ne.gov/databank/spat.html

## Slide 65: “National Map” in Nebraska
http://nmviewogc.cr.usgs.gov/viewer.htm?bbox=-104.5,39.5,-95,43.5

## Slide 66
http://nebraskaview.unl.edu/neview02.php

## Slide 67
http://drought.unl.edu/