## Slide 1: FEMA Flood Map Accuracy
David Maidment
University of Texas at Austin
http://www.nap.edu/catalog.php?record_id=12573

## Slide 2: FEMA Map Modernization
Five-year program 2003-2008 to modernize the nation’s flood maps and convert them to digital form
$1billion budget for FEMA and ~ $200 million from state and local partners
Produced Digital Flood Insurance Rate Maps
How accurate are they?

## Slide 5: NRC Committee on FEMA Flood Map Accuracy
Study commissioned from the National Academies of Science and Engineering by FEMA
Tasked to examine the technical factors that affect flood map accuracy and cost-effectiveness of Detailed versus Approximate studies
Inland and coastal flooding

## Slide 6: Committee Membership
David Maidment, Chair, University of Texas
David Brookshire, University of New Mexico
J. William Brown, City of Greenville, South Carolina
John Dorman, State of North Carolina
Gerald Galloway, University of Maryland
Bisher Imam, University of California, Irvine
Wendy Lathrop, Cadastral Consulting
David Maune, Dewberry
Burrell Montz, Binghamton University
Spencer Rogers, North Carolina Sea Grant
Karen Schuckman, Pennsylvania State University
Y. Peter Sheng, University of Florida
Juan Valdes, University of Arizona
Practitioners
Academics
Geodesy
Hydrology
Coastal
Economics
Risk

## Slide 7: Flood Maps
Riverine
Coastal
Two very different flood modeling and mapping problems

## Slide 8: Riverine Flood Mapping
Modeling and mapping technology is well established
Supported by a large observation database at stream gages
Floods flow along the line of the stream gages

## Slide 9: Coastal Flood Mapping
Modeling and mapping technology and guidance are evolving
Storm surges inland transverse to the line of tide gages
Large dependence on models, less on historical flood data

## Slide 10: Committee Charge: Task 3a
3. Investigate the impact that various study components (i.e., variables) have on the mapping of flood inundation boundaries:
a. Riverine flooding
      The accuracy of digital terrain information
      Hydrologic uncertainties in determining the flood discharge
      Hydraulic uncertainties in converting the discharge into a flood water surface elevation

## Slide 12: Previous NRC Studies: Flood Map Technologies (2007)
An examination of the accuracy of flood base map input data
  2D imagery and planimetrics
  3D elevation
Prompted by issues raised by Senate Appropriations Committee staff

## Slide 13
21% of population has maps meeting the floodplain boundary standard and engineering study standard
Adjusted goal: 92% of population and 65% of land area will have a modernized map
Midcourse Adjustment (2005)
Notes: 13

## Slide 14: Map Modernization in Texas
Source: FEMA Region VI RMC
Half of Texas Counties have updated digital flood maps (94% of population)

## Slide 15: Terrain Data for Case Studies
USGS DEMs (30m)
NCFPM Lidar (3m)

## Slide 16: Terrain data accuracy matters
USGS NED (30m)
NCFMP Lidar (3m)
Inundation for a 1ft storm surge or sea level rise in the Tar-Pamlico estuary (Source: USGS)

## Slide 17: North Carolina Case Studies http://www.ncfloodmaps.com/program_review.htm
H&H and Economics
H&H
Economics
(H&H = Hydrology and Hydraulics)
Mountains of Western NC
Rolling hills of Piedmont
Flat coastal plain
Studies done for the NRC Committee by the North Carolina Floodplain Mapping Program (NCFMP)

## Slide 18: One River Reach studied in detail in each region (each reach 5-7 miles long)

## Slide 19
NED - Lidar | Feet
Mean | -2.0
Standard deviation | 17.5
Maximum | 89.7
Minimum | -139.3
Lidar is higher
(purple)
NED is higher
(green)

## Slide 20
NED - Lidar | Feet
Mean | 14.7
Standard deviation | 15.6
Maximum | 81.5
Minimum | - 46.0
NED is higher
(green)
An elevation “bust”
Systematic and random errors

## Slide 21
NED - Lidar | Feet
Mean | 0.5
Standard deviation | 3.9
Maximum | 34.8
Minimum | -25.3

## Slide 22: Terrain Data
Our study demonstrates that there are large differences between LIDAR and NED
  Random differences everywhere
  Systematic differences in some places

## Slide 23: Defining Uncertainty in BFE Long term records of extreme stages recorded at USGS gages
At each gage the peak stage is recorded for each year along with the peak flow – do a frequency analysis of these.

## Slide 24: Frequency Analysis of Stage Heights at 31 gages
21 gages in NC
10 gages in FL
All gages have at least 20 years record
(average is 54 years)
6
8
7
Is pitted FL landscape different?

## Slide 25
Produced using the Corps HEC-SSP Program (Bulletin 17-B standard procedure)
Base flood discharge
Swannanoa River at Biltmore, NC (78 years of record)
T = 100 years
Discharge (cfs)
Annual Exceedence Probability

## Slide 26
Uncertainty in BFE = Uncertainty in 100-year stage height
Swannanoa River at Biltmore, NC (78 years of record)
T = 100 years
Stage (ft)
Annual Exceedence Probability
5% CL
95% CL
Sampling error =

## Slide 27: Sampling Error of 100-year Stage Heights
Average = 1.06 ft
Outlier (skewed frequency curve)
No systematic variation in sampling error by
drainage area or topographic region
Drainage Area (Sq miles)
Sampling Error (ft)

## Slide 28: Uncertainty in BFE
BFE and Base Stage Height differ by a constant amount (gage datum – geodetic datum)
This doesn’t affect uncertainty of statistical variation of sample data around the 100-year estimate
Average value of sample error at 30 of 31 gage sites is 1.06 ft
A Lower Bound on the uncertainty of the BFE is a standard error of estimate of approximately one foot
BFE, h
Geodetic datum
Gage datum
Base Stage Height
5% CL
95% CL

## Slide 29: Uncertainty in Floodplain Boundary Location
h
w
dw
dh
dw/dh = Run/Rise
County | Lateral slope (%) | Run/rise (ft)
Ahoskie Creek | 2.4 | 42
Long Creek | 9.8 | 10
Swannanoa River | 12.9 | 8
Lateral channel slope is calculated on HEC-RAS cross-sections at the point of intersection of water surface with land surface (left and right banks) and averaged for all cross-sections in the reach
A Lower Bound on the uncertainty of the floodplain boundary location ranges from approximately 8ft in the mountains to approximately 40 ft in the coastal plain

## Slide 30: USGS Peak-Flow Regression Equations for 100-year discharge

## Slide 31: Effect on BFE of Variation in Hydrologic Methods (Long Creek, Mecklenburg County)

## Slide 32: Effect of Hydrologic methods on BFE
Choice of hydrologic method affects the BFE by usually less than 1 foot
All methods in our study are calibrated to the gage frequency curve and all our reaches have a gage, so gage calibration dominates variation in hydrologic methods
Stream gage data are important

## Slide 33: Case Study: Hydraulic Model-Terrain Variants
Detailed
Limited Detailed
Approximate
(lidar)

## Slide 34: Effect on BFE of variation in hydraulic methods and terrain data (Swannanoa River)

## Slide 35: Effect on BFE of variation in hydraulic methods and terrain data (Ahoskie Creek)

## Slide 36: Effect on BFE of variation in hydraulic methods and terrain data (Long Creek)
Approximate Study using NED
21 ft

## Slide 37: Approximate Study BFE Profiles
Approximate - Lidar
Approximate - NED
Misalignment (100 – 200 ft) of mapped 2D planimetric streamline with NED 3D elevation data

## Slide 38
Alignment of planimetrics and
elevation data really matters

## Slide 39: Flood Hazard Zone Areas
At Ahoskie Creek and Swannanoa River the number of acres enclosed in the SFHA by Detailed and Approximate studies differs by < 1%
Difference at Long Creek = 20%
Detailed - lidar
Approximate-NED
Approximate studies give the same area of flood zone but a different shape
Detailed - NED
Swannanoa River

## Slide 40: Conclusions
Natural uncertainty in the Base Flood Elevation (BEF) is at least 1 foot, which translates to 8-40 ft horizontally depending on landscape
Terrain, terrain, terrain
  Largest impact on accuracy of the BFE is land surface elevation
  Requires Lidar or other detailed terrain data not NED
Report is available from National Academies Press: “Mapping the Zone….”