## Slide 1: Hydro Networks in GIS
Network model
Flow on Networks
Hydrologic networks
Linear referencing on networks
Some slides in this presentation were prepared by
Dr Francisco Olivera

## Slide 2: ArcGIS Resource Centers http://resources.arcgis/com
Desktop
Help
Getting to Readings in ArcGIS Resource Center Help for Desktop 10

## Slide 3: Reading (1)
ArcGIS Resource Center/Desktop 10/Help/Professional Library/Data Management/Geographic Data Types/Geometric Networks – What are geometric networks, A quick tour of geometric networks, Essential geometric networks
http://help.arcgis.com/en/arcgisdesktop/10.0/help/index.html#/What_are_geometric_networks/002r00000001000000/

## Slide 4: Reading (2)
ArcGIS Resource Center/ Desktop 10/Help/Professional Library/Guide books/Linear Referencing
- What is linear referencing; Essential linear referencing
http://help.arcgis.com/en/arcgisdesktop/10.0/help/index.html#/What_is_linear_referencing/003900000001000000/

## Slide 5: Key Concepts from Exercise 4
"smdem" - 10 * “flowLineReclas" - 0.02 * (500 - "distance") * ("distance" < 500)
Subtract 10 at all stream grid cells
Subtract an amount that tapers from 0.02*500=10 when distance is 0, to 0 when distance is 500 from stream
Only do taper when distance is less than 500, otherwise this is 0 and nothing is subtracted
500
500
10
10
DEM Reconditioning as an example of quantitative raster analysis
  Vector to Raster
  Distance
  Raster Calculation
  Volume removed analysis

## Slide 6: 3D Analyst Profiles
smdem
smrecon
diff

## Slide 7: Construct the Analysis Layer
Fill
Flow Direction
Flow Accumulation
Stream Definition
Stream Links
Catchments

## Slide 8: Convert to Vector
Vector streams
Vector catchments
Attribute feature with raster zonal statistics
Geometric Network
Tracing
Selection statistics

## Slide 9: Raster to Vector Transition
During the last week, you have been dealing with the flow of water through the landscape based on the raster data structures
Today we are making a transition in which we are going to use vector network data to describe water pathways.
We will connect the land and water flow systems by attaching the catchments and watersheds derived from raster data processing to our vector networks

## Slide 10: Four Key Concepts
Four key constructs
  Cell to cell water movement on DEMs
  Line to Line water movement on networks
  Area flows to line (connect land and water systems – Reach Catchments)
  Area flows to point on line (Watershed delineation from designated points)

## Slide 11: Cell Flows to a Cell
Core concept of flow on digital elevation models

## Slide 12: Line Flows to a Line
Geometric Network of NHDFlowlines

## Slide 13: Area Flows to a Line
Reach Catchments from NHDPlus
Flowline and Catchment have the same COMID

## Slide 14: Area Flows to a Point on a Line
Watersheds for USGS Gages

## Slide 15: Network Definition
A network is a set of edges and junctions that are topologically connected to each other.

## Slide 16: Network Model in GIS
Three components
  Geometric model: (x,y,z,m) coordinates of edges and junctions
  Logical model: which edges are connected to what junctions
  Addressing model: location on the network using measure

## Slide 17: Edges and Junctions
Simple feature classes: points and lines
Network feature classes: junctions and edges
Edges can be
  Simple: one attribute record for a single edge
  Complex: one attribute record for several edges in a linear sequence
A single edge cannot be branched
No!!

## Slide 18: Polylines and Edges

## Slide 19: Junctions
Junctions exist at all points where edges join
  If necessary they are added during network building (generic junctions)
Junctions can be placed on the interior of an edge e.g. stream gage
Any number of point feature classes can be built into junctions on a single network

## Slide 20: Connectivity Table
J124
J125
J123
J126
E1
E3
E2
J123 | J124, E1 |  | 
J124 | J123, E1 | J125, E2 | J126, E3
J125 | J124, E2 |  | 
J126 | J124, E3 |  | 
Junction
Adjacent Junction and Edge
This is the “Logical Network”

## Slide 21: Build Network Tables
Establishes connectivity of Edge and Junction features
Enables tracing
Generates Generic Junctions
Geometric Network Wizard in ArcCatalog

## Slide 22: Snapping Features

## Slide 24: Network Sources and Sinks
Each junction
feature class
in a network can
have junctions
which are sources
or sinks for flow
Use complex edge so that junction can be interior to edge

## Slide 25: Flow to a sink

## Slide 26: Flags

## Slide 27: Trace Solvers

## Slide 28: Upstream Trace Solvers

## Slide 29: Hydrologic Networks
Hydrologic data includes:
  Single-line streams
  Double-line streams
  Braided streams
  Manmade channel systems
  Waterbodies

## Slide 30: Flow Line
Traces movement of water in a one-dimensional flow system

## Slide 31: Location of the Flowline

## Slide 32: Introduction to the Hydro Network
Hydro Edge – think of Arc
Hydro Junction – think of Node
Waterbody – think of Polygon

## Slide 33: Flow Network
A connected set of flow edges
Edge
Junction

## Slide 34: Network Building
Define flow-paths within double-line streams and waterbodies.
Define network sinks and sources.

## Slide 35: Network Connectivity
Find connected
Find loops

## Slide 36: Network Flow Direction
Enable flow in flow-paths.
Disable flow in shorelines
Sink
Flow direction is unknown

## Slide 37: Network Flow Direction
Enable flow in flow-paths.
Disable flow in shorelines
Sink
Flow direction is known

## Slide 38: Uninitialized Flow Direction

## Slide 39: Assigned Flow Direction

## Slide 40: Network Tracing
Trace Upstream
Trace Downstream

## Slide 41: Trace Path
Find the shortest path
between two points on
the network

## Slide 42: Hydro Network for Holland

## Slide 43: Hydro Network for Colorado River Basin around Lake Travis

## Slide 44
Network Tracing on the Guadalupe Basin

## Slide 45: Some terminology
Hydrography – the mapping of water features
    Blue line features on topographic maps (streams, rivers, lakes,…)
    More generally, hydrography also includes the mapping of bathymetry and extent of estuaries and coastal waters
National Hydrography Dataset (NHD) – a data model for storing topographic map hydrography
  Medium resolution (1:100K) is complete for US
  High resolution (1:24K) is complete for most of the US
NHDPlus – a new data model integrating 1:100K resolution NHD with catchments and derived attributes from the National Elevation Dataset

## Slide 46: National Hydrography Dataset
Five feature classes with
NHDFLowline built into
A geometric network
NHDPoint, NHDLine,
NHDArea are point, line
and area water features
on map apart from flowlines
and waterbodies
Key feature classes

## Slide 47: National Hydrography Dataset

## Slide 48: NHD Waterbody

## Slide 49: NHD Geometric Network

## Slide 50: NHDPlus Reach Catchments ~ 3km2
About 1000 reach catchments in each 8-digit HUC
Average reach length = 2km
2.3 million reaches for continental US

## Slide 51: Reach Attributes
Slope
Elevation
Mean annual flow
  Corresponding velocity
Drainage area
% of upstream drainage area in different land uses
Stream order

## Slide 53: United States Experience with DEM Improvement
Error in delineated watershed area
5%
0.5%
3 arcsec: 90 m
1 arcsec: 30 m
DEM Cell Size
1990’s
2000’s

## Slide 54: National Elevation Dataset for Australia
9 Arc Second – 250 m
1 Arc Second – 30 m
1 cell
81 cells
Existing
New
Two orders of magnitude improvement! Wow!
Images: John Gallant, CSIRO

## Slide 55: National River Network for Australia
Line flows to Line
Geometric Network
Geometry model: Where am I? (x,y coordinates)
Logical model: Who am I connected to? (topology)
Addressing model: Where are things on me? (linear referencing)
Image: Elizabeth McDonald, BoM

## Slide 56: A challenge: those messy Aussie rivers have lots of loops and branches
Image: Michael Hutchinson, ANU

## Slide 57: A fundamental innovation: Connecting the Cell to Cell and Line to Line Models
Flow divergences have multiple flow directions on a single DEM cell
Image and Research: Janet Stein, ANU
Cell flows to Cell

## Slide 58: Reach Catchments Every stream reach has a local drainage area
Area flows to Line
Fundamental connection between the water and land systems
Image: Elizabeth McDonald, BoM

## Slide 59: Contracted Nodes and Catchments
Contracted Nodes
Contracted Catchments
Contracted nodes persist through successive versions of the geofabric
Area flows to a point on a line
A standardized tessellation of the landscape – one chosen among the infinite number of tessellations possible
Images: Elizabeth McDonald, BoM

## Slide 60: Linear Referencing
Where are we on a line?

## Slide 61: Addressing

## Slide 62: Coordinates of a 2-D Polyline

## Slide 63: Coordinates of a 2-D Polyline M

## Slide 64: Setting Line Measure

## Slide 65: Proportional Aliasing
Distance is measured
Relative to the length
of the line as a percentage
0% – 100%

## Slide 66: Setting Percent Measure
pMSeg.SetAndInterpolate
MsBetween 0, 100
pMSeg.SetAndInterpolate
MsBetween 100, 0
0 – 100 going upstream
0 – 100 going downstream

## Slide 67: Point and Line Events

## Slide 68: Summary Concepts
Four key constructs
  Cell to cell water movement on DEMs
  Line to Line water movement on networks
  Area flows to line (connect land and water systems – Reach Catchments)
  Area flows to point on line (Watershed delineation from designated points)

## Slide 69: Summary Concepts (2)
A network is a connected set of points (junctions) and lines (edges) that supports tracing functions
  Three data model components
    Geographic (x,y,z)
    Logical (point-line topology connections)
    Addressing (position m along the line)

## Slide 70: Summary Concepts (3)
Linear referencing can be used to locate point and line “events” on a network
This is like (x,y) event themes that you used earlier to map stream gage locations in geographic space