## Slide 1: HydroNetwork Applications
This lecture continues on from the slides we began on the last class
In this class, we talk about
  how to create HydroNetworks,
  Linear referencing on networks
  NHDPlus in the United States
  AWRIS project in Australia
There are no new additional readings

## Slide 2: Summary Concepts from Last Lecture
Four key constructs
  Cell to cell water movement on DEMs
  Line to Line water movement on networks
  Area flows to line (connect land and water systems – Reach Catchments)
  Area flows to point on line (Watershed delineation from designated points)

## Slide 3: Summary Concepts (2)
A network is a connected set of points (junctions) and lines (edges) that supports tracing functions
  Three data model components
    Geographic (x,y,z)
    Logical (point-line topology connections)
    Addressing (position m along the line)

## Slide 4: Hydrologic Networks
Hydrologic data includes:
  Single-line streams
  Double-line streams
  Braided streams
  Manmade channel systems
  Waterbodies

## Slide 5: Flow Line
Traces movement of water in a one-dimensional flow system

## Slide 6: Location of the Flowline

## Slide 7: Introduction to the Hydro Network
Hydro Edge – think of Arc
Hydro Junction – think of Node
Waterbody – think of Polygon

## Slide 8: Flow Network
A connected set of flow edges
Edge
Junction

## Slide 9: Network Building
Define flow-paths within double-line streams and waterbodies.
Define network sinks and sources.

## Slide 10: Network Connectivity
Find connected
Find loops

## Slide 11: Network Flow Direction
Enable flow in flow-paths.
Disable flow in shorelines
Sink
Flow direction is unknown

## Slide 12: Network Flow Direction
Enable flow in flow-paths.
Disable flow in shorelines
Sink
Flow direction is known

## Slide 13: Uninitialized Flow Direction

## Slide 14: Assigned Flow Direction

## Slide 15: Network Tracing
Trace Upstream
Trace Downstream

## Slide 16: Trace Path
Find the shortest path
between two points on
the network

## Slide 17: Hydro Network for Holland

## Slide 18: Hydro Network for Colorado River Basin around Lake Travis

## Slide 19
Network Tracing on the Guadalupe Basin

## Slide 20: Linear Referencing
Where are we on a line?

## Slide 21: Addressing

## Slide 22: Coordinates of a 2-D Polyline

## Slide 23: Coordinates of a 2-D Polyline M

## Slide 24: Setting Line Measure

## Slide 25: Proportional Aliasing
Distance is measured
Relative to the length
of the line as a percentage
0% – 100%

## Slide 26: Setting Percent Measure
pMSeg.SetAndInterpolate
MsBetween 0, 100
pMSeg.SetAndInterpolate
MsBetween 100, 0
0 – 100 going upstream
0 – 100 going downstream

## Slide 27: Point and Line Events

## Slide 28: Some terminology
Hydrography – the mapping of water features
    Blue line features on topographic maps (streams, rivers, lakes,…)
    More generally, hydrography also includes the mapping of bathymetry and extent of estuaries and coastal waters
National Hydrography Dataset (NHD) – a data model for storing topographic map hydrography
  Medium resolution (1:100K) is complete for US
  High resolution (1:24K) is complete for most of the US
NHDPlus – a new data model integrating 1:100K resolution NHD with catchments and derived attributes from the National Elevation Dataset

## Slide 29: National Hydrography Dataset
Five feature classes with
NHDFLowline built into
A geometric network
NHDPoint, NHDLine,
NHDArea are point, line
and area water features
on map apart from flowlines
and waterbodies
Key feature classes

## Slide 30: National Hydrography Dataset

## Slide 31: NHD Waterbody

## Slide 32: NHD Geometric Network

## Slide 33: NHDPlus Reach Catchments ~ 3km2
About 1000 reach catchments in each 8-digit HUC
Average reach length = 2km
2.3 million reaches for continental US

## Slide 34: Reach Attributes
Slope
Elevation
Mean annual flow
  Corresponding velocity
Drainage area
% of upstream drainage area in different land uses
Stream order

## Slide 35: Delivering on National Water Information Needs
David R. Maidment
Director, Center for Research in Water Resources
University of Texas at Austin
WIRADA Science Symposium
Melbourne, Australia
4 August 2011

## Slide 36: Our Journey Begins….. Melbourne Cup Day, November 2006
I was in Canberra doing a seminar jointly with Rob Vertessy about geospatial data for water
The Prime Minister met on this day in Canberra with the Premiers of all the States to confront the drought
The country was in crisis
The drought was already severe and its ultimate magnitude and duration were unknown
Action was needed!!!

## Slide 37: What was the state of water knowledge in Australia at that time?
Science – Rich – a real legacy of historical investment in CSIRO, ANU and elsewhere
Modeling – Rich – CRC’s for Catchment Hydrology and eWater, and elsewhere
Information – Limited
  250m DEM
  No consistent digital blue line stream hydrography (ouch!!)
  37 separate stream gaging networks
AWRIS and WIRADA were prompted by these and other deficiencies in information

## Slide 38: River Gage Networks
9079 gages in 37 networks
Average = 245 gages/network

## Slide 39: Some months pass…. then comes (Jan 2007)
http://www.nalwt.gov.au/files/national_plan_for_water_security.pdf

## Slide 40
Slide: Rob Vertessy
Australian Water Resources Information System (AWRIS)

## Slide 41
Slide: Rob Vertessy, BoM
Components of AWRIS
Notes: 41
41
AWRIS on a page.

## Slide 42: WIRADA (2008-2013) Water Information Research and Development Alliance
Slide: Rob Vertessy, BoM
CSIRO research program to support the AWRIS development being done by the Bureau of Meteorology

## Slide 43: Three years in ….. What is the state of Water Information now?
Progress has been made in each of these four components
They are very different to one another
The challenge now is how to link them

## Slide 44: Australian National Climate Database
This is a core competency of the BoM
Augment with evaporation derived from remote sensing
Std Dev of 8 methods of estimating evaporation
Image: Albert van Dijk, CSIRO

## Slide 45: Lake Argyll – Remote Sensing as Time Series!
Lake timeseries plus statistics and curve-fiting analysis.
Slide: Philippa Berry, DeMontfort University

## Slide 46: Australian Hydrological Geospatial Fabric
Four key constructs
  Cell to cell water movement on DEMs
  Line to Line water movement on networks
  Area flows to line (connect land and water systems – Reach Catchments)
  Area flows to point on line (Contracted Nodes and Catchments)

## Slide 48: United States Experience with DEM Improvement
Error in delineated watershed area
5%
0.5%
3 arcsec: 90 m
1 arcsec: 30 m
DEM Cell Size
1990’s
2000’s

## Slide 49: National Elevation Dataset for Australia
9 Arc Second – 250 m
1 Arc Second – 30 m
1 cell
81 cells
Existing
New
Two orders of magnitude improvement! Wow!
Images: John Gallant, CSIRO

## Slide 50: National River Network for Australia
Line flows to Line
Geometric Network
Geometry model: Where am I? (x,y coordinates)
Logical model: Who am I connected to? (topology)
Addressing model: Where are things on me? (linear referencing)
Image: Elizabeth McDonald, BoM

## Slide 51: A challenge: those messy Aussie rivers have lots of loops and branches
Image: Michael Hutchinson, ANU

## Slide 52: A fundamental innovation: Connecting the Cell to Cell and Line to Line Models
Flow divergences have multiple flow directions on a single DEM cell
Image and Research: Janet Stein, ANU
Cell flows to Cell

## Slide 53: Reach Catchments Every stream reach has a local drainage area
Area flows to Line
Fundamental connection between the water and land systems
Image: Elizabeth McDonald, BoM

## Slide 54: Contracted Nodes and Catchments
Contracted Nodes
Contracted Catchments
Contracted nodes persist through successive versions of the geofabric
Area flows to a point on a line
A standardized tessellation of the landscape – one chosen among the infinite number of tessellations possible
Images: Elizabeth McDonald, BoM

## Slide 55: Geofabric Summary
I’ve used test versions of these data – they work!
This enables water management to be built on a digital landscape rather than paper maps
Huge implications for all forms of water management in Australia
Large institutional and cultural change required to fully achieve benefits

## Slide 56: Hydrologic Models
Long historical experience with catchment hydrology modeling in Australia (CRC for Catchment Hydrology)
AWRIS requires a transition to landscape hydrology modeling
  AWRA-L; AWRA-R, AWRA-G
“I’m in hydrology heaven ……”

## Slide 57
Slide: Neil Viney, CSIRO

## Slide 58: What I was thinking about on the plane
I was asked to address “Delivering on National Water Information Needs”
In hydrology, we’ve always thought of national information as being built up from state and local information
Question: to what degree is national hydrologic modeling informed by global information?
Answer: Yes, for climate drivers

## Slide 59
http://gewex-srb.larc.nasa.gov/
W/m2

## Slide 60: Assembly of lots and lots of time series from more than 200 organizations
Rain gages
River gages
Evaporation gages
Reservoir levels
Groundwater levels
Water Pumpage
Diversions
A network of networks

## Slide 61
Slide: Brett Anderson, BoM

## Slide 62
Slide: Brett Anderson, BoM

## Slide 63
Slide: Brett Anderson, BoM