## Slide 1: Hydro Networks in GIS
Network model
Flow on Networks
Hydrologic networks
Linear referencing on networks
Some slides in this presentation were prepared by
Dr Francisco Olivera

## Slide 2: ArcGIS Resource Centers http://resources.arcgis/com
Desktop
Help
Getting to Readings in ArcGIS Resource Center Help for Desktop 10

## Slide 3: Reading (1)
ArcGIS Resource Center/Desktop 10/Help/Professional Library/Data Management/Geographic Data Types/Geometric Networks – What are geometric networks, A quick tour of geometric networks, Essential geometric networks
http://help.arcgis.com/en/arcgisdesktop/10.0/help/index.html#/What_are_geometric_networks/002r00000001000000/

## Slide 4: Reading (2)
ArcGIS Resource Center/ Desktop 10/Help/Professional Library/Guide books/Linear Referencing
- What is linear referencing; Essential linear referencing
http://help.arcgis.com/en/arcgisdesktop/10.0/help/index.html#/What_is_linear_referencing/003900000001000000/

## Slide 5: Key Concepts from Exercise 4
"smdem" - 10 * “flowLineReclas" - 0.02 * (500 - "distance") * ("distance" < 500)
Subtract 10 at all stream grid cells
Subtract an amount that tapers from 0.02*500=10 when distance is 0, to 0 when distance is 500 from stream
Only do taper when distance is less than 500, otherwise this is 0 and nothing is subtracted
500
500
10
10
DEM Reconditioning as an example of quantitative raster analysis
  Vector to Raster
  Distance
  Raster Calculation
  Volume removed analysis

## Slide 6: 3D Analyst Profiles
smdem
smrecon
diff

## Slide 7: Construct the Analysis Layer
Fill
Flow Direction
Flow Accumulation
Stream Definition
Stream Links
Catchments

## Slide 8: Convert to Vector
Vector streams
Vector catchments
Attribute feature with raster zonal statistics
Geometric Network
Tracing
Selection statistics

## Slide 9: Raster to Vector Transition
During the last week, you have been dealing with the flow of water through the landscape based on the raster data structures
Today we are making a transition in which we are going to use vector network data to describe water pathways.
We will connect the land and water flow systems by attaching the catchments and watersheds derived from raster data processing to our vector networks

## Slide 10: Four Key Concepts
Four key constructs
  Cell to cell water movement on DEMs
  Line to Line water movement on networks
  Area flows to line (connect land and water systems – Reach Catchments)
  Area flows to point on line (Watershed delineation from designated points)

## Slide 11: Cell Flows to a Cell
Core concept of flow on digital elevation models

## Slide 12: Line Flows to a Line
Geometric Network of NHDFlowlines

## Slide 13: Area Flows to a Line
Reach Catchments from NHDPlus
Flowline and Catchment have the same COMID

## Slide 14: Area Flows to a Point on a Line
Watersheds for USGS Gages

## Slide 15: Network Definition
A network is a set of edges and junctions that are topologically connected to each other.

## Slide 16: Network Model in GIS
Three components
  Geometric model: (x,y,z,m) coordinates of edges and junctions
  Logical model: which edges are connected to what junctions
  Addressing model: location on the network using measure

## Slide 17: Edges and Junctions
Simple feature classes: points and lines
Network feature classes: junctions and edges
Edges can be
  Simple: one attribute record for a single edge
  Complex: one attribute record for several edges in a linear sequence
A single edge cannot be branched
No!!

## Slide 18: Polylines and Edges

## Slide 19: Junctions
Junctions exist at all points where edges join
  If necessary they are added during network building (generic junctions)
Junctions can be placed on the interior of an edge e.g. stream gage
Any number of point feature classes can be built into junctions on a single network

## Slide 20: Connectivity Table
J124
J125
J123
J126
E1
E3
E2
J123 | J124, E1 |  | 
J124 | J123, E1 | J125, E2 | J126, E3
J125 | J124, E2 |  | 
J126 | J124, E3 |  | 
Junction
Adjacent Junction and Edge
This is the “Logical Network”

## Slide 21: Build Network Tables
Establishes connectivity of Edge and Junction features
Enables tracing
Generates Generic Junctions
Geometric Network Wizard in ArcCatalog

## Slide 22: Snapping Features

## Slide 24: Network Sources and Sinks
Each junction
feature class
in a network can
have junctions
which are sources
or sinks for flow
Use complex edge so that junction can be interior to edge

## Slide 25: Flow to a sink

## Slide 26: Flags

## Slide 27: Trace Solvers

## Slide 28: Upstream Trace Solvers

## Slide 29: Summary Concepts
Four key constructs
  Cell to cell water movement on DEMs
  Line to Line water movement on networks
  Area flows to line (connect land and water systems – Reach Catchments)
  Area flows to point on line (Watershed delineation from designated points)

## Slide 30: Summary Concepts (2)
A network is a connected set of points (junctions) and lines (edges) that supports tracing functions
  Three data model components
    Geographic (x,y,z)
    Logical (point-line topology connections)
    Addressing (position m along the line)