## Slide 1: The Schematic Processor
Presented by Dr. Tim Whiteaker
The University of Texas at Austin
18 October, 2011

## Slide 2: Outline
Background – Arc Hydro
Schematic Processor
Use Case – Bacterial loading

## Slide 3: Linking GIS and Water Resources
GIS
Water
Resources

## Slide 4: Arc Hydro: GIS for Water Resources
Arc Hydro
  An ArcGIS data model for water resources
  Arc Hydro toolset for implementation
  Framework for linking hydrologic simulation models
The Arc Hydro data model and
application tools are in the public
domain
Published in 2002, now in revision for Arc Hydro II
Notes: Notes:
Industrial partners: ESRI, Danish Hydraulic Institute, Camp,Dresser and McKee, Dodson and Associates
Government partners:
Federal: EPA, USGS, Corps of Engineers (Hydrologic Engineering Center)
State: Texas Natural Resource Conservation Commission, Texas Water Development Board
Local: Lower Colorado River Authority, City of Austin, Dept of Watershed Protection
Academic Partners: University of Texas, Brigham Young University, Utah State University

## Slide 5: What is a hydrologic data model
Booch et al. defined a model: “a simplification of reality created to better understand the system being created”
Objects
Aquifer
Stream
Well
Catchment
R.M. Hirsch, USGS

## Slide 6: Arc Hydro—Hydrography
The blue lines on maps

## Slide 7: Arc Hydro—Hydrology
The movement of water through the hydrologic system

## Slide 8
Flow
Time
Time Series
Hydrography
Network
Channel
Drainage
Hydro Features
What’s in Arc Hydro

## Slide 9: What makes Arc Hydro different?
Arc Hydro: All features have a unique HydroID
within a geodatabase.
HydroID to ID relationships
link features and help to trace water movement.
ArcGIS: All features have a unique ObjectID
within a feature class.

## Slide 10: HydroID Relationships
Watershed
HydroID - 23
JunctionID - 7
HydroJunction
HydroID - 7
NextDownID - 8
HydroJunction
HydroID - 8

## Slide 11: What makes Arc Hydro different?
Flow
Time
Time Series
HydroID
Hydro Features
Arc Hydro connects space and time:
hydro features are linked to time series.
TimeSeries
Value - 35 cfs
Time - May 7, 2011
FeatureID - 23

## Slide 12: Arc Hydro Tools
Dozens of tools for hydrologic
data development and analysis
…including schematic network creation

## Slide 13: Schematic networks represent connectivity
1) watersheds and streams
2) stream nodes
3) stream links
4) watershed centroids
5) watershed to stream
6) wetland

## Slide 14: We can move things through the network…
Decay
Bacterial Input
Direction of Flow
Bacterial Input
Node
Link
…simulating processes along the way

## Slide 15: We process values with receiving and passing behaviors
Link or Node
Incremental value, i
Received value(s), r
Passed value, p
Total value, t
Receiving behavior
t = f(r,i)
Passing behavior
p = g(t)

## Slide 16: This is implemented in GIS with the Schematic Processor

## Slide 17: You can create your own behaviors using Python
Build a
library of ops
First-order decay

## Slide 18: Total Maximum Daily Load Use Case
Bacterial loading in Copano Bay
(Slides courtesy of Dr. Stephanie Johnson)

## Slide 19: Motivating Factors
Statewide:
399 impaired
310 impaired for bacteria
Tidal Rivers:
20 impaired
12 impaired for bacteria
(Task Force, 2007) Tier 2 Part 3: “… develop simple load duration curve, GIS [geographic information systems], and/or mass balance models.”
Bays:
28 impaired
21 impaired for bacteria
As of August 2009:
Notes: A main motivator of this work was the LARGE number of bacterial impairments in the State. Also, the language in the Task Force report released in 2007 that said that the majority of the bacteria TMDL studies done in the state should use simple methods.
Classified waterbodies
399 violating for something
310 violating for bacteria
44 Classified Bays
28 violating for something 63.6%
21 violating for bacteria 47.7%
33 Classified Tidal Streams
20 violating for something 60.606%
12 violating for bacteria 36.364%

## Slide 20: What is a “Load”?
Load (#/year)
Amount (volume/year)
Concentration (#/volume)
Bacterial load:
CFU/year
Amount of water:
m3/day
Concentration of bacteria: CFU/100 m3
Notes: We are using loading models. First question is – what is a “load”?
Load is a function of two things - the amount of water and the concentration of bacteria in the water. So for all of our bacterial sources, we need to get info on those two things.
Watershed loading is calculated through a simple loading equation, where the mean annual load of bacteria = the mean annual volume of water * the expected bacterial concentration

## Slide 21: Non-Point Sources
Overland
Non-Tidal Rivers
decay
“Net” decay =
f (regrowth, resuspension, death)
First Order Decay:
QC = QCo*e-kτ L = Lo*e-k τ
C = concentration (CFU/100mL)
Q = flow (m3/yr)
L = load (CFU/yr)
Lo = initial load (CFU/yr)
k = net decay rate (yrs-1)
τ = residence time (yrs)
Notes: Overland Flow and Non-tidal streams

## Slide 22: Loading from Landscape
Load (CFU/yr)
Runoff (m3/yr)
Concentration (CFU/m3)
By land use category:
Data sources:
  Land use/Land cover: NLCD 1992, NHDPlus ‘catchmentattributesnlcd’ table
  Unit runoff by LULC: Quenzer, 1997
  Bacteria concentrations by LULC: Zoun, 2003
* Loading from other land uses accounted for with animal
specific loadings.

## Slide 23: Loading from Animals (Ag & Wildlife)
Load (CFU/yr)
# animals
Load/animal
(CFU/yr)
By land use category1:
1 Animals were distributed across the watershed by land use.
Data sources:
  Land use/Land cover: NLCD 1992, NHDPlus ‘catchmentattributesnlcd’ table
  # animals: Moench & Wagner, 2009
  Loading per animal: Moench & Wagner, 2009
Notes: A similar process was done for all of the agricultural animals and wildlife
Here we see the total number of animals in the watershed
Similar to cattle, these were all divided up amongst the catchments

## Slide 24: Septic Systems in Upper Watershed
Load (CFU/yr)
# septics
Load/septic
(CFU/yr)
% of systems that fail each yr
% of load from failed septic that reaches the stream
Data sources:
  Land use/Land cover: NLCD 1992, NHDPlus ‘catchmentattributesnlcd’ table
  # septics: 1990 Census, TCEQ OARS, county data
  Loading per septic: Protocol for Developing Bacteria TMDLs (EPA, 2005)
  % septics failing: estimated from literature values & local info (see App. C of dissertation)*
  % of load from failing system that reaches the bay: estimated from literature values (see App. C of dissertation)*
Notes: Also have septic systems in the upper watershed
Get data from TCEQ/local data source

## Slide 25: Total Nonpoint Source Load per Catchment
0*CFU/yr/failure
643*CFU/yr/deer
300*CFU/yr/hog
5*CFU/yr/hog
20*CFU/yr/horse
630*CFU/yr/cow
8*CFU/yr/sheep
30*CFU/yr/goat
+ LULC
Total nonpoint source load:
li = 2.6 x 1015 CFU/yr
Notes: 5 goats, 2 sheep, 1 dom hog, 0.2 poultry

## Slide 26: “Net” Decay
Q0, C0
Q, C
Reminder: L (CFU/yr) = Q (m3/yr) *C (CFU/m3)
Bacteria Load In
Bacteria Load Out
settle, death
Death, regrowth
resuspension
move right through …..
In-Segment Processes
Non-Tidal River
In-segment processes as a “black box” approach,
where “net” decay = f(settling, death, regrowth, resuspension, etc.) = k
QC = QCo*e-kτ

## Slide 27: Point Sources
Wastewater treatment plants
Failing septic systems around the bay
Bird colonies
decay
decay
Notes: Overland Flow and Non-tidal streams

## Slide 28: Build the Schematic Network
Notes: Go through how to build the network (in generality …….) Use appendix and rely on cached layers to flip through things.

## Slide 29: Apply Equations Using Schematic Processor
Nonpoint Sources
WWTP
Bird colony
Decay

## Slide 30: Calibrate Based on Monitoring Data
12952
12948
12943
12944
Station | Mean (CFU/100mL)
12943 | 107
12944 | 251
12948 | 394
12952 | 158
When:
Notes: OK, so we have our governing equations here.
Let’s concentrate on the loading from the watershed and how we calibrate to that value.
We have a number of locations throughout the watershed that we “know” what the mean annual bacterial load is.

## Slide 31: Evaluate Strategies To Reduce Load
Eliminate nearby septic systems
Implement best management practices to reduce non-point loads from watersheds
http://repositories.lib.utexas.edu/handle/2152/10654
Published in:

## Slide 32: Free Download
http://tools.crwr.utexas.edu/