## Slide 1: Performance of the Recovery System of an Oil Refinery
Prepared by
Ibrahim Kahraman

## Slide 2: Foreknowledge
Objective: Analyze the existing performance of recovery system in an oil refinery
  Groundwater Recovery
  Oil Recovery
  Site: Corpus Christi, Nueces County
  Projected coordinate system: NAD_1927_StatePlane_Texas_South_FIPS_4205
  Geographic Coordinate System: GCS_North_American_1927

## Slide 3: Geology of the Area
Source: Texas Water Development Board – Geologic Database of Texas
Notes: Qd – Deweyville Formation – Sand, silt, clay, and gravel, includes point bar, natural levee, and stream channel deposits, surface characterized by relict meanders of much larger radius of curvature than those of present streams; occurs along Nueces River at three levels: 5-20, 20-30, and 40-55 feet above level of Recent floodplain
Qb- Beaumont Formation – with barrier island and beach deposits.
Mostly clay, sild, and sand, and gravel: includes mainly stream channel, point bar, natural levee, backswamp deposits, and to a lesser entent coastal marsh, mud flat. Lagoonal.
Dominantly clay and mud of low permeability, high water holding capacity, high compressibility, high to very high shrink-swell potential, poor drainage, level of depressed relief, low shear strength

## Slide 4
All Petroleum Facilities’ Well in the Area

## Slide 5
Onsite Wells

## Slide 6: Why are those wells for?
CPT (Cone Penetrating Testing) – method used to provide soil properties and delineating soil stratigraphy(6 wells)
Recovery Wells – Used for Extraction LNAPL (Light Non-Aqueous Phase Liquid) and Groudwater (88 wells)
Observation Wells – Used for gauging only (85 wells
Monitoring Wells – Used for Gauging and Sampling (24 wells)

## Slide 7: Groundwater Quality Parameters
 | Well ID:
Parameters | Critical PCLs
Metals (SW846 6010 & 6020A) | 
Arsenic | 1
Barium | 200
Chromium (Total) | 10
Lead | 1.5
Nickel | 150
Volatile Organics (SW846 8260B) | 
1,2-Dichloroethane | 0.5
1,4-Dioxane | 19
2-Butanone (MEK) | 4400
Benzene | 0.5
Carbon disulfide | 730
Chloroform | 4.3
Ethylbenzene | 70
Methyl tert-butyl ether (MTBE) | 73
Toluene | 100
m & p-Xylenes | 1000
o-Xylene | 1000
Semivolatile Organics (SW846 8270C) | 
1-Methylnaphthalene | 510
2,4-Dimethylphenol | 150
2-Methylphenol (o-Cresol) | 370
4-Methylphenol/3-Methylphenol | 37
Benzenethiol (Thiophenol) | 0.073
Bis(2-ethylhexy)phthalate | 0.6
Diethylphthalate | 5800
Naphthalene | 57
Phenol | 2190

## Slide 8: ANT Effect on Confined/Unconfined LNAPL
Figures were provided from H2A Environmental Ltd.

## Slide 9
Source: H2A Environmental Ltd.

## Slide 10
LNAPL Isolepth Map

## Slide 11
Groundwater Surface Contour

## Slide 12: Total Recovery Rates of Wells in first half of 2011
Total Groundwater Recovery
Total Hydrocarbon Recovery

## Slide 13: Recovery Rates of Wells – 1998 thru 2011

## Slide 14: Questions?
ibrahimkahraman@utexas.edu
ibohero.3e@gmail.com
Thank you!