## Slide 1: Energy for public water supplies in Texas
Kelly T. Sanders
November 20, 2012

## Slide 2
Image courtesy of www.easyart.com
Recent analysis suggests that 12.6% of US energy use is consumed to pump, treat, distribute, and recondition water (Sanders and Webber 2012)
However, the energy embedded in water varies a great deal regionally
A lot of energy is embedded in the US water system

## Slide 3: We selected Texas as a case study to assess regional variability in energy-relate water use
Relatively good data availability at the state-level
Texas is projected to get drier and more populated
Large variations in climate and terrain make it an interesting case study
Small enough to model but big enough to serve as a proxy for the rest of the nation
[TWDB]
Hydrological Characteristics of Texas

## Slide 4: Based on my national analysis, I calculated the energy-intensity of water in six sectors…
US Water Withdrawals:
410 billion GPD
US Water-related Energy:
35 trillion BTU per Day
(Billion Gallons per Day)
(Trillion BTU per Day)
[Sanders and Webber 2012]
[USGS]
Energy Intensity in BTU per Gallon

## Slide 5: Water withdrawals and water-related energy consumption are not correlated within sectors
1 Billion
Gallons
Per Day
160 Billion
BTU Per Day
Mining
Power
Livestock
Industry
Public
Supply
Irrigation
Texas Water Withdrawals
Texas Water-related Energy
Consumption
[USGS]

## Slide 6: Water scarcity in Texas will affect future statewide water and water-related energy use
Expected Water Scarcity in TX in 2050
[data from NDRC & Tetratech]
Water scarcity metric considers:
  Future water demand
  Available precipitation
  Changes in available precipitation
  The ratio of groundwater withdrawals to total withdrawals
  Surface storage
  Changes in summer deficits in 2050
Notes: Metrics to evaluate 5 criteria in 2050:
  available renewable water
  groundwater use
  susceptibility to drought
  increased need for storage
  growth and water demand

## Slide 7: USGS data were converted from vector to raster format to enable raster calculations
GCS_North_American_1983

## Slide 8: The energy consumed for SW and GW treatment was calculated across the state
Raster Data Layer
(Volume)
Energy Intensity
(Energy per Volume)

## Slide 9: The energy consumed for SW and GW treatment was calculated across the state
Electricity consumption per county per day:
Mean = 27.6 MWh
Max = 866 MWh
Total for all counties: 7.0 GWh per day (<1% of ERCOT load)

## Slide 10: Thus, pumping and treating water are much less energy intensive than end-use preparation
*Average Heat Rate for TX power plants: ~7,200 BTU/ kWh [EPA]
160 Billion
BTU Per Day
Mining
Power
Livestock
Industry
Public
Supply
Irrigation
Texas Water-related Energy Consumption:
~15% of total primary energy consumption
Treatment = <<1% of total primary energy consumption (0.2%)*

## Slide 11: Water scarcity in Texas will affect future statewide water and water-related energy use
∆ in Water Withdrawals:
  Population ↑
  Climate Change ↑
  Future energy sources?
  Role of conservation?
  New technologies?
∆ in Water-related Energy:
  Desalination ↑
  Pumping↑
  Water Reuse↑
  Treatment standards?
Operating Desalination Plants
Total output:
~85 MGD (<1%
of TX water use)
[TWDB and GWI]

## Slide 12: Conclusions and Future Work
Water withdrawals and water-related energy use are not well-correlated
My preliminary analysis concludes:
  ~15% of Texas’ energy consumption is for water
  ~0.2% is for public water supply treatment and pumping
Future analyses will consider wastewater treatment and changes to treatment technologies
Texas’ Publicly owned
treatment works (wastewater)
[EPA]

## Slide 13
Kelly T. Sanders
The University of Texas at Austin
kellytwomeysanders@utexas.edu
www.webberenergygroup.com