## Slide 1: Data Sources for GIS in Water Resources by Ayse Irmak, David R. Maidment, and David G. Tarboton GIS in Water Resources Fall 2012

## Slide 2: Learning Objectives
The hierarchical system of watersheds and basins
Where to obtain data and maps
  National/State/Global Data repositories
  Hydrography
  USGS National Water Information System
  Land Cover
  Elevation
  Soil (Statsgo/Surgo)
  Weather
  Satellite Remote Sensing Data

## Slide 3
http://geo.data.gov/geoportal/catalog/main/home.page
Inland Water Resources
National Hydrography Dataset
Geo.Data.gov: One Stop shop for links to other data sites
Open Preview Add To Map Website Details Metadata

## Slide 4: USGS GIS data for Water
http://water.usgs.gov/maps.html

## Slide 5: The National Hydrography Dataset (NHD)
Surface-water component of the National map.
Surface water of the United States using common features such as lakes, ponds, streams, rivers, canals, stream gages, and dams.
Polygons are used to represent area features such as lakes, ponds, and rivers;
Lines are used to represent linear features such as streams and smaller rivers;
Points are used to represent point features such as stream gages and dams.
Lines also are used to show the water flow through area features such as the flow of water through a lake.
The combination of lines is used to create a network of water and transported material flow to allow users of the data to trace movement in downstream and upstream directions.
The Watershed Boundary Dataset (WBD) is a companion dataset to the NHD.
WBD defines the perimeter of drainage areas formed by the terrain and other landscape characteristics.

## Slide 6: Water Resources Regions of the US
Region 01 New England Region 02 Mid-Atlantic Region 03 South Atlantic-Gulf Region 04 Great Lakes Region 05 Ohio Region 06 Tennessee Region 07 Upper Mississippi Region 08 Lower Mississippi Region 09 Souris-Red-Rainy Region 10 Missouri Region 11 Arkansas-White-Red Region 12 Texas-Gulf Region 13 Rio Grande Region 14 Upper Colorado Region 15 Lower Colorado Region 16 Great Basin Region 17 Pacific Northwest Region 18 California Region 19 Alaska (Old numbering system) Region 20 Hawaii Region 21 Caribbean
There are 18 water resources regions in the Continental United States
2-digit water resource regions

## Slide 7: Watersheds of the US (Every watershed has a unique number!!!)
8-digit HUC watersheds
An eight-digit code uniquely identifies each of the four levels of classification: Hydrologic Unit Code 01080204:
01-Region
0108- The subregion
010802- The accounting Region
01080204- The cataloging unit

## Slide 8: Hydrologic Unit Codes - ( HUC)
HUC - 2 REGION Major land areas. The lower 48 states have 18 total, 1 additional
each for Alaska, Hawaii, and the Caribbean. ( 21 Total in US) Called 1st Level - or Watershed 1st Level
HUC - 4 SUBREGION Each Region has from 3 to 30 Subregions. The Missouri River
Region has 30 Subregions. The lower 48 states have 204. ( 222 Total in US). Called 2nd Level
HUC - 6 BASIN Accounting Unit. ( 352 Total in US). Called 3Rd Level
HUC - 8 SUBBASIN Cataloging Unit. The smallest is 448 K Acres (700 mi²). Most
are much larger. National HQ compilations have this as the smallest size unit. ( 2,149 Total in US) Called 4th Level
HUC - 10 WATERSHED Typically from 40 to 250 K Acres (62 to 390 mi²) Called 5 th Level or Watershed 5 th Level.
HUC - 12 SUBWATERSHED Typically from 10 to 40 K Acres (15 to 62 mi²) Called 6 th Level or Watershed 6th Level.

## Slide 9: Watershed Hierarchy
8 HUC
4
2
6
NHDPlus
10
12
Available
In Progress
Digit #
Each hydrologic unit is identified by a unique hydrologic unit code (HUC) consisting of two to eight digits based on the four levels of classification in the hydrologic unit system.

## Slide 10: Hydrologic Unit Code Watersheds
~ 2000 HUC 8 for US, about the size of counties

## Slide 11: Watershed Boundary Dataset
National Program by USGS and USDA (NRCS)
Boundaries for 10- and 12- digit watersheds
First cut is by automated delineation from NED
Hand checked and edited
10-digit watersheds

## Slide 12: Watershed Boundary DataSet
http://www.ncgc.nrcs.usda.gov/products/datasets/watershed/

## Slide 13: Watershed Boundary Dataset for Nebraska
2990 HUC12 watersheds of average area 39.3 square miles
HUC12:HUC ~ 40:1 watersheds
Notes: HUCs are important for estimating water supply, water quality, and runoff. They are building blocks of water studies

## Slide 14: WBD for Nebraska
71 HUC-8 watersheds of average area 1654 square miles

## Slide 15: EPA River Reach File 1 (RF1)
EPA uses river reaches to assign water quality information
Hydrologic ordering of reaches so that larger rivers and segment accurately defined along with connectedness and flow direction
In the 1980's, RF1 was used by EPA for performing water quality modeling on whole river basins for all of the hydrologic regions in the United States

## Slide 16
State and Local Data
Decisions
Watershed Management
.
TMDL
.
Source Water Protection
.
Stormwater
Data
Cartographic
Monitoring
Loadings
Models
HSPF - NPSM
QUAL2E
TOXIROUTE
Post-Processors
Tools
Target
Assessment
Data Mining
Reporting
BASINS - Integrating GIS and Water Quality Modeling
Target
Assess
DM
Notes: Basins is a premier water quality model developd by EPA that heavily uses GIS data

## Slide 17
River networks
for 8-digit HUC
watersheds
http://nhd.usgs.gov/

## Slide 19
Lower West Fork, Trinity River Basin
HUC = 12030102

## Slide 20: NHD River Reaches
412 River Reaches
In Upper West Fork of Trinity Basin

## Slide 21: River Reach Codes Used for river address locations
ReachCode =
12030102000151
ReachCode = 12030102000005
HUC#
Segment#
Location 0.392
on Reach
12030102000005

## Slide 22
http://www.horizon-systems.com/nhdplus/

## Slide 23: NHDPlus for a Portion of Oregon
http://www.horizon-systems.com/nhdplus/

## Slide 24: NHDPlus Reach Catchments ~ 3km2
About 1000 reach catchments in each 8-digit HUC
Average reach length = 2km
2.3 million reaches for continental US

## Slide 25: NHDPlus Reach Attributes
Slope
Elevation
Mean annual flow
  Corresponding velocity
Drainage area
% of upstream drainage area in different land uses
Stream order

## Slide 26: National Elevation Dataset
Digital Elevation Model with 1 arc-second (30m) cells
Seamless in 1° blocks for the United States
10 billion data
Derived from USGS 1:24,000 quadrangle sheets
Get the data:
http://ned.usgs.gov/
http://nationalmap.gov/viewer.html

## Slide 27
From http://seamless.usgs.gov

## Slide 28
For LIDAR data: Go to http://lidar.cr.usgs.gov/

## Slide 29: Digital Elevation Model (DEM)
Contours
720
700
680
740
680
700
720
740
720
720

## Slide 30
Digital Elevation Model (DEM)-30 meter

## Slide 31: Austin West 30 Meter DEM

## Slide 32
Elevation (m)
Slope (percent)
Terrain Analysis. DEM derived slope: First derivative of elevation

## Slide 33
32
16
8
64
4
128
1
2
Eight Direction Pour Point Model
Water in a given cell flows one or more of eight adjacent cells in the direction of steepest descent (ArcGIS)
ArcGIS raster operations involved in watershed delineation are derived from the premise that “water flows downhill, in doing so, will follow the steepest descent

## Slide 34: Flow Direction Grid
32
16
8
64
4
128
1
2

## Slide 35: Delineation of Streams and Watersheds on a DEM

## Slide 36
http://srtm.usgs.gov/

## Slide 37: HydroSheds derived from SRTM
http://hydrosheds.cr.usgs.gov/

## Slide 39: GTOPO30 - 1 km Digital Elevation Model of the Earth
http://eros.usgs.gov/#/Find_Data/Products_and_Data_Available/GTOPO30

## Slide 40: Drainage in North America
Hydro1K is
derived from
GTOPO30
using raster
GIS analysis
http://eros.usgs.gov/#/Find_Data/Products_and_Data_Available/gtopo30/hydro

## Slide 41: Soil Data
http://websoilsurvey.nrcs.usda.gov/app/WebSoilSurvey.aspx
http://www.soils.usda.gov/survey/geography/ssurgo/
http://www.soils.usda.gov/survey/geography/statsgo/
Natural Resources Conservation Service (NRCS)
National Cartography and Geospatial Center (NCGC)
State Soil Geographic Database-STASGO
Soil Survey Geographic Database- SURGO

## Slide 42
http://www.soils.usda.gov/survey/geography/statsgo/
1:250,000 Scale Soil Information

## Slide 44
http://www.soils.usda.gov/survey/geography/ssurgo/
1:24,000 scale
soil information
SSURGO:
County Level
Digital Soil Maps

## Slide 45: Ssurgo for Lancaster County, NE
96 soil map units described by 18,565 polygons

## Slide 46: Ssurgo for Travis County
103 soil map units described by 7530 polygons of average area 35.37 ha (87 acres)

## Slide 47
Field capacity (%)
Soil texture

## Slide 48
http://landcover.usgs.gov/

## Slide 49: National Land Cover Dataset
Get the data:
http://www.mrlc.gov/
1992, 2001, and 2006

## Slide 50: http://www.mrlc.gov/finddata.php

## Slide 51: National Land Cover Dataset-NLCD 2006

## Slide 53
http://www.nationalatlas.gov/atlasftp.html

## Slide 54
http://www.ncdc.noaa.gov/oa/ncdc.html

## Slide 55: PRISM Mean Annual Precipitation (Oregon State U.) Historical- Gridded
http://www.wcc.nrcs.usda.gov/climate/prism.html

## Slide 56
http://www.daymet.org/
Historical- Gridded Weather data

## Slide 57: National Water Information System
Web access to USGS water
resources data in real time
http://waterdata.usgs.gov/usa/nwis/

## Slide 58: USGS Water Watch
Web access to USGS water resources data in real time
http://waterdata.usgs.gov/nwis/rt

## Slide 59: USGS National Water Information System.
Real-time and Historic Data
  Streamflow and stage
  Groundwater levels
  Water Quality
  Site information
Tabular or Graphical Format

## Slide 60: NASA Satellite Data
https://lpdaac.usgs.gov/
http://landsatlook.usgs.gov/
http://reverb.echo.nasa.gov

## Slide 61: http://water.weather.gov/ahps/

## Slide 62: http://water.weather.gov/ahps/

## Slide 63
http://www.wcc.nrcs.usda.gov/snotel/

## Slide 64: http://www.cbrfc.noaa.gov

## Slide 65: CBRFC SNOTEL Ensemble
http://www.cbrfc.noaa.gov/station/sweplot/sweplot.cgi?tglu1

## Slide 66: http://www.arcgis.com

## Slide 68: http://gis.utah.gov

## Slide 69: Utah Terrain Basemap
To use as a basemap in ArcGIS see instructions at
http://gis.utah.gov/map-services/new-utah-terrain-base-map-and-cached-tile-service-available

## Slide 70
Utah GIS Portal Download GIS Data
http://gis.utah.gov/download

## Slide 71
http://geology.utah.gov/maps/gis/index.htm

## Slide 72
http://www.wrcc.dri.edu/

## Slide 73
http://dnr.ne.gov/databank/geospatial.html

## Slide 74
http://dnr.ne.gov/databank/spat.html

## Slide 75: “National Map” in Nebraska
http://nmviewogc.cr.usgs.gov/viewer.htm?bbox=-104.5,39.5,-95,43.5

## Slide 76
http://nebraskaview.unl.edu/neview02.php

## Slide 77
http://drought.unl.edu/