## Slide 1: Nitrate analysis in the Seine Basin, France
Arielle Mimouni
GIS in Water Resources
11-21-2013

## Slide 2: Why Nitrate
Nitrogen-containing compounds are an essential source of nutrients and organic matters
Nitrogen forms : NH4-NH3/NO2-NO3
Oxidation of reduced nitrogen consumes O2 and causes eutrophication
NH4+ harmful to fish
NO3 can cause Blue Baby Syndrome

## Slide 3
Total catchment area of the Seine : 75000 km2
Length of the Seine :
776 km from Northeastern France to the English Channel

## Slide 4: The Seine Basin in France
Paris conurbation : 10 million inhabitants – 2.1 million in Paris
Very urban area in Paris, and intensive agricultural area in surroundings of Paris

## Slide 5: Data
Ahmad Tavakoly has generated daily nitrogen leaching in the Seine for 39 years (1971-2010) and 6481 cells covering the river network
Notes: Cell = 1 kmx1km
Map from Ahmad

## Slide 6: Modeling Nitrogen
Eau-Dyssée : calculates hydrological parameters : flow, runoff, water level…
STICS : calculates water, carbon, and nitrogen within the crop-soil system
Results: nitrogen load to river due to runoff and groundwater
Notes: Eau-Dyssée : surface water balance (runoff/soil) / ISO (routes surface runoff water flux + RAPID (flow and volume in each cell)+ QTOZ (water level in each cell)
STICS : impact of climate, soil and crop management on plant and environment

## Slide 7: Coupling Eau-Dyssée and STICS
Slide provided by Ahmad Tavakoly
Notes: Slide from Ahmad

## Slide 8: My contribution to the project
Spatial and Temporal analysis of the nitrogen leaching to the river
Study of the possible impacts of wastewater treatment plants effluents on nitrate load to the river
Notes: Compare point sources and non point sources approach

## Slide 9: Leaching nitrate in 2009 in the Seine River
3000 cells with daily nitrate leaching to represent
January,1st 2009
Notes: 1,095,000 cells

## Slide 10
January,1st 2009
High Nitrate loads to the river correspond to intensive agriculture areas
Low nitrate loads for the urban area of Paris
Red : urban area
Green : forests
Yellow : agricultural area
Spatial analysis

## Slide 11: Temporal analysis
Chart: Evolution of Nitrate Leaching and Runoffs in 2009 for cell 2496
High surface water runoffs correspond to high nitrate loads to the river

## Slide 12: Wastewater Treatment plants in the Seine Basin
2596 wwtp in the Seine Basin

## Slide 13: Wastewater treatment plants in the Seine Basin
Selection of relevant data :
If effluent in river (85% of WWTP in rivers/15% in groundwater)
10% largest emitter of NO3
Within 1 km of a river cell

## Slide 14
In 1999-2007,
4 WWTP to treat wastewater from Paris
-> Today, Paris: Combined sewerage network :160 km of collectors 10 to 100 m underground collectors leading to WWTP
Outside of Paris area : separate networks : only wastewater goes to WWTP
Notes: -> system started in 1884 : household waste water, waste water and runoffs collected in sewerage system

## Slide 15: WWTP and Urbanization
Red : urban and industrial areas
Large treatment of NO3 by WWTP corresponds to urban areas

## Slide 16
High population density corresponds to high loads of NO3 in WWTP

## Slide 17
4 WWTP treat influents from Paris :
Seine Aval (downstream)
Seine Centre
Seine Amont (upstream)
Marne Aval
High population density corresponds to high loads of NO3 in WWTP

## Slide 18: Focus on Seine-Amont
Chart: NO3 load treated by the WWTP Seine Amont
| 1999.0 | 2000.0 | 2001.0 | 2002.0 | 2003.0 | 2004.0 | 2005.0 | 2006.0 | 2007.0
ZNO3 | 11564.5147 | 11214.0547 | 9678.24 | 10152.1174 | 9704.6374 | 10530.2974 | 11832.48 | 16948.1347 | 17097.3
Chart: Volume of wastewater treated by the WWTP Seine Amont
| 1999.0 | 2000.0 | 2001.0 | 2002.0 | 2003.0 | 2004.0 | 2005.0 | 2006.0 | 2007.0
QREJ | 292033.7 | 283183.7 | 244400.5 | 256367.1 | 245067.1 | 265917.1 | 298800.5 | 427983.7 | 431750.5
Chart: Increase in the population around the WWTP Seine Amont
| 2000.0 | 2001.0 | 2002.0 | 2003.0 | 2004.0 | 2005.0 | 2006.0 | 2007.0
Increase in population (%) | -0.030305 | -0.13695 | 0.048963 | -0.044078 | 0.085079 | 0.12366 | 0.43234 | 0.0088013
Increase in population in 2006 > increase in nitrate load to the wwtp

## Slide 19: Conclusions and Future Work
Conclusions:
Non point sources of Nitrate: (important Paris periphery)
Effects of land use on nitrate loads to the river
Effects of precipitations on nitrate loads to the river
Point sources of Nitrate: (important in Paris area)
- Effects of population density on wwtp nitrate load
Next steps :
Quantitatively analyze the impacts of nitrate loads from wwtp in the river
Formulate recommendations if they need to be taken into account in the overall nitrate modeling

## Slide 20
Thank you to Ahmad
Thank you to Carlos and Denny
Questions ?

## Slide 21
Paris sewage system in the 1884 and today – Collectors of 2.5 to 4 m diameter.