## Slide 1: GIS in Water Resources: Lecture 1
In-class and distance learning
Geospatial database of hydrologic features
GIS and HIS
Curved earth and a flat map
Reading Assignment: Introduction to Map Projections http://resources.arcgis.com/en/help/main/10.2/#/What_are_map_projections/003r00000001000000/

## Slide 2: Six Basic Course Elements
Lectures
  Powerpoint slides
  Video streaming
Readings
  Online readings and lecture synopses
Homework
  Computer exercises
  Hand exercises
Term Project
  Oral presentation
  PDF report
Class Interaction
  Email
  Discussion
Examinations
  Midterm, final

## Slide 3: Our Classroom
Dr David Tarboton
Students at Utah State University
Dr David Maidment Students at University of Texas at Austin

## Slide 4
B.E. in Agricultural Engineering (with First Class Honors) from University of Canterbury, Christchurch, New Zealand, 1972
MS, PhD in Civil Engineering from University of Illinois, 1974 and 1976, respectively
1981 – joined University of Texas at Austin as an Assistant Professor, and have been on the faculty ever since. Now Hussein M. Alharthy Centennial Chair in Civil Engineering
Initiated the GIS in Water Resources course in 1991.
Worked with ESRI since 1994 on a GIS Hydro Preconference seminar for the ESRI Users Conference
Leader of the CUAHSI Hydrologic Information System project from 2004-2011
Developing World Water Online with ESRI and Kisters
David R. Maidment

## Slide 5: David Tarboton
B.Sc Eng in Civil Engineering from the University of Natal, Durban, South Africa 1981
M.S. and Sc.D from MIT, Cambridge, Massachusetts, 1987 and 1990 respectively
1990 - Joined Faculty at Utah State University in Civil and Environmental Engineering
1996 - Developed D-Infinity and gradually adapted research terrain analysis codes (Fortran and C) into TauDEM
Participated in GISWR since 1999 (this year is the 14th time)
Research includes snow energy balance, stochastic streamflow and physically based hydrologic modeling
Leader of HydroShare project to extend the capability of CUAHSI HIS to collaborative data sharing, additional data types and models

## Slide 6: University Without Walls
Traditional Classroom
Community
Inside and Outside
The Classroom

## Slide 7: Learning Styles
Instructor-Centered Presentation
Community-Centered Presentation
Student
Instructor
We learn from the instructors and each other

## Slide 8: GIS in Water Resources: Lecture 1
In-class and distance learning
Geospatial database of hydrologic features
GIS and HIS
Curved earth and a flat map

## Slide 9: What is GIS
A geographic information system (GIS) is a system designed to capture, store, manipulate, analyze, manage, and present all types of geographical data. -- Wikipedia
maps
data
tools
computers

## Slide 10: Geography is visualized in maps
www.arcgis.com
map

## Slide 11: Maps are built from data
map
data
Road
Name: E. Dean Keeton St
Type: Div Highway
Speed: 35 mph
Shape: [Geometry]
Building
Name: Ernest Cockrell Jr Hall
Address: 301 E. Dean Keeton St
Shape: [Geometry]
Shape includes the geometry of the feature and where it is located on earth

## Slide 12: Vector data represent discrete features
map
data
polygons
lines
points

## Slide 13: Raster data form a grid of cells or pixels
map
data

## Slide 14: More Raster Examples
map
data
rainfall
elevation
land use

## Slide 15: There are many more data types
map
data
triangulated
irregular network
multipatch
annotation
Martin Luther King Dr W

## Slide 16: Connected Map, Chart and Animation
Tropical Storm Fernand
http://www.msnbc.msn.com/id/26295161/ns/weather/

## Slide 17: Geographic Data Model
Conceptual Model – a set of concepts that describe a subject and allow reasoning about it
Mathematical Model – a conceptual model expressed in symbols and equations
Data Model – a conceptual model expressed in a data structure (e.g. ascii files, Excel tables, …..)
Geographic Data Model – a conceptual model for describing and reasoning about the world expressed in a GIS database

## Slide 18
Data Model based on a collection of data themes

## Slide 19: Spatial Data: Vector format
Point - a pair of x and y coordinates
(x1,y1)
Line - a sequence of points
Polygon - a closed set of lines
Node
vertex
Vector data are defined spatially:
Notes: DRM

## Slide 20: Kissimmee watershed, Florida
Themes

## Slide 21: Attributes of a Selected Feature

## Slide 22: Raster and Vector Data
Point
Line
Polygon
Vector
Raster
Raster data are described by a cell grid, one value per cell
Zone of cells
Notes: DRM

## Slide 23
http://srtm.usgs.gov/srtmimagegallery/index.html
Santa Barbara, California

## Slide 24: The challenge of increasing Digital Elevation Model (DEM) resolution (Dr Tarboton’s research)
1980’s DMA 90 m
102 cells/km2
1990’s USGS DEM 30 m
103 cells/km2
2000’s NED 10-30 m
104 cells/km2
2010’s LIDAR ~1 m
106 cells/km2

## Slide 25: How do we combine these data?
Digital Elevation
Models
Watersheds
Streams
Waterbodies

## Slide 26: An integrated raster-vector database

## Slide 27: Three Views of GIS
Geodatabase view: Structured data sets that represent geographic information in terms of a generic GIS data model.
Geovisualization view: A GIS is a set of intelligent maps and other views that shows features and feature relationships on the earth's surface. "Windows into the database" to support queries, analysis, and editing of the information.
Geoprocessing view: Information transformation tools that derive new geographic data sets from existing data sets.
adapted from www.esri.com

## Slide 28: Programming
Automation of repetitive tasks (workflows)
Implementation of functionality not available (programming new behavior)

## Slide 29: GIS in Water Resources: Lecture 1
In-class and distance learning
Geospatial database of hydrologic features
GIS and HIS
Curved earth and a flat map

## Slide 30: Linking Geographic Information Systems and Water Resources
GIS
Water
Resources

## Slide 31: A Key Challenge
GIS
Water Environment
(Watersheds, streams, gages, sampling points)
How to connect water environment with water observations
Time Series Data
Water Observations
(Flow, water level concentration)

## Slide 32
CUAHSI is a consortium representing 125 US universities
Supported by the National Science Foundation Earth Science Division
Advances hydrologic science in nation’s universities
Includes a Hydrologic Information System project
http://www.cuahsi.org

## Slide 33: How the web works
Catalog (Google)
Web Server
(CNN.com)
Browser
(Firefox)
Access
Catalog harvest
Search
HTML – web language for text and pictures

## Slide 34
Rainfall
Water quantity
Meteorology
Soil water
Groundwater
We Collect Lots of Water Data
Water quality

## Slide 35: The Data have a Common Structure
A point location in space
A series of values in time
Gaging – regular time series
Sampling – irregular time series
Notes: These data are recorded over time to monitor a hydrologic process or property.

## Slide 36: WaterML as a Web Language for Colorado River at Austin
http://waterservices.usgs.gov/nwis/iv?sites=08158000&period=P17D&parameterCd=00060
I accessed this WaterML service from USGS at 4:06PM
and got back these flow data from USGS which are up to 3:30PM
USGS has real-time WaterML services for about 11,000 sites available 24/7/365
http://waterservices.usgs.gov/nwis/iv?sites=08158000&period=P1D&parameterCd=00060

## Slide 37: ArcGIS Online
GIS on the web – online map services
http://www.arcgis.com

## Slide 38: Online Base Maps (20 scales)

## Slide 39: Topographic Base Map in ArcGIS Online
World
United States
Texas
Austin
Home

## Slide 40
Map Service
Data Service
Map and Data Services for USGS Water Observations
http://bit.ly/13KKQyi
ArcGIS Online Map

## Slide 41: ArcGIS Resources
http://resources.arcgis.com/

## Slide 42: Hydro Resource Center
http://resources.arcgis.com/en/communities/hydro/

## Slide 43: World Hydro Overlay Map
World
United States
Texas
My Home
My Stream

## Slide 44: HydroShare is a web based collaborative system to support analysis, modeling and data publication
Observers and instruments
Data
Analysis
Models
Collaboration
Publication, Archival, Curation
Notes: HydroShare will be a collaborative environment for sharing hydrologic data and models aimed at giving hydrologists the technology infrastructure they need to address critical issues related to water quantity, quality, accessibility, and management.
HydroShare will expand the data sharing capability of the CUAHSI Hydrologic Information System by broadening the classes of data accommodated, expanding capability to include the sharing of models and model components, and taking advantage of emerging social media functionality to enhance information about and collaboration around hydrologic data and models.
Functionality will include
A web portal for model and data sharing
Sharing features added to HydroDesktop client software
Access to more types of hydrologic data using standards compliant data formats and interfaces
Enhanced catalog functionality that broadens discovery functionality to different data types and models
New model sharing and discovery functionality
Enhanced easy to use access to high performance computing
Social media and collaboration functionality
Linkages to other data and modeling systems such as USGS and CUAHSI data services, NASA earth exchange and HPC resources e.g. at CSDMS

## Slide 45: GIS in Water Resources: Lecture 1
In-class and distance learning
Geospatial database of hydrologic features
GIS and HIS
Curved earth and a flat map

## Slide 46: Origin of Geographic Coordinates
(0,0)
Equator
Prime Meridian

## Slide 47: Latitude and Longitude
Longitude line (Meridian)
N
S
W
E
Range: 180ºW - 0º - 180ºE
Latitude line (Parallel)
N
S
W
E
Range: 90ºS - 0º - 90ºN
(0ºN, 0ºE)
Equator, Prime Meridian

## Slide 48: Latitude and Longitude in North America
90 W
120 W
60 W
30 N
0 N
60 N
Austin:
Logan:
(30°18' 22" N, 97°45' 3" W)
(41°44' 24" N, 111°50' 9" W)

## Slide 49: Map Projection
Curved Earth
Geographic coordinates: f, l
(Latitude & Longitude)
Flat Map
Cartesian coordinates: x,y
(Easting & Northing)
Notes: DRM

## Slide 50: Earth to Globe to Map
Representative Fraction
Globe distance Earth distance
=
Map Scale:
Map Projection:
Scale Factor
Map distance Globe distance
=
(e.g. 1:24,000)
(e.g. 0.9996)

## Slide 51: Coordinate Systems
(fo,lo)
(xo,yo)
X
Y
Origin
A planar coordinate system is defined by a pair
of orthogonal (x,y) axes drawn through an origin
Geographic Coordinates
Projected Coordinates

## Slide 52: ArcGIS Help for Map Projections
http://resources.arcgis.com/en/help/main/10.2/#/What_are_map_projections/003r00000001000000/

## Slide 53: Summary (1)
GIS in Water Resources is about empowerment through use of information technology – helping you to understand the world around you and to investigate problems of interest to you
This is an “open class” in every sense where we learn from one another as well as from the instructors

## Slide 54: Summary (2)
GIS offers a structured information model for working with geospatial data that describe the “water environment” (watersheds, streams, lakes, land use, ….)
Water resources also needs observations and modeling to describe “the water” (discharge, water quality, water level, precipitation)

## Slide 55: Summary (3)
Geography “brings things together” through georeferencing on the earth’s surface
Understanding geolocation on the earth and working with geospatial coordinate systems is fundamental to this field
GIS has traditionally been used on the desktop but increasingly there is a transition to information sharing on the web