## Slide 1: Extending ArcGIS using programming
David Tarboton
GIS in Water Resources 22 October 2013

## Slide 2: Why Programming
Automation of repetitive tasks (workflows)
Implementation of functionality not available (programming new behavior)

## Slide 3: ArcGIS programming entry points
Model builder
Python scripting environment
ArcObjects library (for system language like C++, .Net)
Open standard data formats that anyone can use in programs (e.g. shapefiles, geoTIFF, netCDF)

## Slide 4: Three Views of GIS
Geodatabase view: Structured data sets that represent geographic information in terms of a generic GIS data model.
Geovisualization view: A GIS is a set of intelligent maps and other views that shows features and feature relationships on the earth's surface. "Windows into the database" to support queries, analysis, and editing of the information.
Geoprocessing view: Information transformation tools that derive new geographic data sets from existing data sets.
adapted from www.esri.com

## Slide 5
http://resources.arcgis.com/en/help/main/10.2/#/What_is_ModelBuilder/002w00000001000000/

## Slide 6: An example – time series interpolation
Soil moisture at 8 sites in field
Hourly for a month
~ 720 time steps
What is the spatial pattern over time
Data from Manal Elarab

## Slide 7: How to use in ArcGIS
Time series in Excel imported to Object class in ArcGIS
Joined to Feature Class (one to many)

## Slide 8: Time enabled layer with 4884 records that can be visualized using time slider

## Slide 9: But what if you want spatial fields
Interpolate using spline or inverse distance weight at each time step
Analyze resulting rasters
30 days – 720 hours ???
A job for programming

## Slide 10: The program workflow
Set up inputs
Get time extents from the time layer
Create a raster catalog (container for raster layers)
For each time step
  Query and create layer with data only for that time step
  Create raster using inverse distance weight
  Add raster to raster catalog
Add date time field and populate with time values

## Slide 11: I used PyScripter (as suggested by an ESRI programmer http://blogs.esri.com/esri/arcgis/2011/06/17/pyscripter-free-python-ide/)
http://code.google.com/p/pyscripter/

## Slide 12: This shows the reading of time parameters and creation of raster catalog

## Slide 13: This shows the iterative part

## Slide 14: The result

## Slide 15: TauDEM
http://hydrology.usu.edu/taudem/
Stream and watershed delineation
Multiple flow direction flow field
Calculation of flow based derivative surfaces
MPI Parallel Implementation for speed up and large problems
Open source platform independent C++ command line executables for each function
Deployed as an ArcGIS Toolbox with python scripts that drive command line executables

## Slide 16: Model Builder Model to Delineate Watershed using TauDEM tools

## Slide 17: Catchments linked to Stream Network

## Slide 18: D-Infinity Contributing Area
Tarboton, D. G., (1997), "A New Method for the Determination of Flow Directions and Contributing Areas in Grid Digital Elevation Models," Water Resources Research, 33(2): 309-319.)
D
D8
Notes: This slide shows how the terrain flow field is represented. Early DEM work used a single flow direction model, D8. In 1997 I published the Dinfinity method that proportions flow from each grid cell among downslope neighbors. This, at the expense of some dispersion, allows a better approximation of flow across surfaces.

## Slide 19: Generalization to Flow Algebra
Pki
Pki
Pki
i
Replace
by general function

## Slide 20
Useful for a tracking contaminant or compound subject to decay or attenuation

## Slide 21: Transport limited accumulation
Supply
Capacity
Transport
Deposition
2
2
)
tan(
b
T
cap
ca
=
å
+
=
}
,
min{
cap
in
out
T
T
S
T
å
-
+
=
out
in
T
T
S
D
Useful for modeling erosion and sediment delivery, the spatial dependence of sediment delivery ratio and contaminant that adheres to sediment
S
Flow Algebra provides a general modeling framework for static flow field based geospatial concepts

## Slide 22: TauDEM Parallel Approach
MPI, distributed memory paradigm
Row oriented slices
Each process includes one buffer row on either side
Each process does not change buffer row

## Slide 23: Parallelization of Flow Algebra
Executed by every process with grid flow field P, grid dependencies D initialized to 0 and an empty queue Q. FindDependencies(P,Q,D) for all i for all k neighbors of i if Pki>0 D(i)=D(i)+1 if D(i)=0 add i to Q next
Executed by every process with D and Q initialized from FindDependencies. FlowAlgebra(P,Q,D,,) while Q isn’t empty get i from Q i = FA(i, Pki, k, k) for each downslope neighbor n of i if Pin>0 D(n)=D(n)-1 if D(n)=0 add n to Q next n end while swap process buffers and repeat
1. Dependency grid
2. Flow algebra function

## Slide 24: Programming
C++ Command Line Executables that use MPI
ArcGIS Python Script Tools
Python validation code to provide file name defaults
Shared as ArcGIS Toolbox

## Slide 25: Q based block of code to evaluate any “flow algebra expression”
while(!que.empty())
{
//Takes next node with no contributing neighbors
temp = que.front(); que.pop();
i = temp.x; j = temp.y;
// FLOW ALGEBRA EXPRESSION EVALUATION
if(flowData->isInPartition(i,j)){
float areares=0.; // initialize the result
for(k=1; k<=8; k++) { // For each neighbor
in = i+d1[k]; jn = j+d2[k]; flowData->getData(in,jn, angle);
p = prop(angle, (k+4)%8);
if(p>0.){
if(areadinf->isNodata(in,jn))con=true;
else{
areares=areares+p*areadinf->getData(in,jn,tempFloat);
}
}
}
}
// Local inputs
areares=areares+dx;
if(con && contcheck==1)
areadinf->setToNodata(i,j);
else
areadinf->setData(i,j,areares);
// END FLOW ALGEBRA EXPRESSION EVALUATION
}
C++

## Slide 26: Maintaining to do Q and partition sharing
while(!finished) { //Loop within partition
while(!que.empty())
{ .... // FLOW ALGEBRA EXPRESSION EVALUATION
}
// Decrement neighbor dependence of downslope cell
flowData->getData(i, j, angle);
for(k=1; k<=8; k++) {
p = prop(angle, k);
if(p>0.0) {
in = i+d1[k]; jn = j+d2[k];
//Decrement the number of contributing neighbors in neighbor
neighbor->addToData(in,jn,(short)-1);
//Check if neighbor needs to be added to que
if(flowData->isInPartition(in,jn) && neighbor->getData(in, jn, tempShort) == 0 ){
temp.x=in; temp.y=jn;
que.push(temp);
}
}
}
}
//Pass information across partitions
areadinf->share();
neighbor->addBorders();
C++

## Slide 27: Python Script to Call Command Line
mpiexec –n 8 pitremove –z Logan.tif –fel Loganfel.tif

## Slide 28: PitRemove
Python

## Slide 29: Validation code to add default file names
Python

## Slide 30: Summary
GIS and Water Resources analysis capabilities are readily extensible with programming
to do something new
to repeat something needed frequently
Model builder provides visual programming and helps learn ArcGIS python commands
Python – cross platform, powerful and easy to use is a good programming language to start with (when your time is valuable)
Compiled language programming for developers (C++) to achieve optimal efficiency (when the computers time is valuable)