## Slide 1: Data Sources for GIS in Water Resources by David R. Maidment, and David G. Tarboton GIS in Water Resources Fall 2015

## Slide 2: Outline
The hierarchical system of watersheds and basins
Where to obtain data and maps
  National/State/Global Data repositories
  Hydrography
  USGS National Water Information System
  Land Cover
  Census
  Elevation
  Soil (Statsgo/Surgo)
  Weather
  Regional data for Texas and Utah

## Slide 3: Open Water Data Initiative (OWDI)
Subcommittee on Spatial Water Data leads this effort
Al Rea (USGS) and Ed Clark (NWS) are co-chairs
This reports to both FGDC and ACWI
Sponsoring a series of “experiments” with water information services
NFIE is one of these experiments
Developing a “Geospatial Hydrologic Framework” for the US
Chair
Anne Castle, Former Asst Secretary for Water and Science, Dept of Interior

## Slide 4: NHDPlus Version 2.1
National Elevation Dataset
National Hydrography Dataset
National Land Cover Dataset
Watershed Boundary Dataset
NHDPlus
Foundation for a Geospatial Hydrologic Framework for the United States
2.7 million reach catchments in US
average area 3 km2
reach length 2 km
Uniquely labelled

## Slide 5
500,000 processors operating in parallel
Stampede
1.2 million gallon cooling tank

## Slide 6: WRF-Hydro Forecasting Model
Runoff
Streamflow
RAPID flow routing (for continental US)
Probabilistic flood forecasts
Weather model and forecasts (HRRR)
Land-Atmosphere Model (NOAH-MP)
Precipitation
Weather
Catchment-level forecasts
Computed for the continental US in 10 minutes at Texas Advanced Computing Center

## Slide 7: Current and NFIE Forecast Systems
130 Catchments and Flowlines
uniquely labelled
Two basins and one forecast point
becomes
Current: 6600 basins and 3600 forecast points
NFIE: 2.7 million stream reaches and catchments
A national flow network
Blanco River at Wimberley
Basin ~ 400 Sq Mile
Reach Catchment ~ 1 Sq Mile

## Slide 8: Linear Referencing on Flowlines
Lat.
Long.
Measure
Bridge and Stream Gage at RR 12 is at Measure 70.246
on Flowline 1630223
Measure is the % distance upstream from most downstream point on line
Using measures, the flow can be estimated at any point along the line

## Slide 9: CUAHSI HydroShare
http://www.hydroshare.org

## Slide 10: NFIE-Geo in Hydroshare

## Slide 11: Watershed Hierarchy
8 HUC
4
2
6
NHDPlus
10
12
Digit #
Each hydrologic unit is identified by a unique hydrologic unit code (HUC) consisting of two to or more digits based on the levels of classification in the hydrologic unit system.
HAW HUC 8 03030002
Little Creek HUC 12 030300020603

## Slide 12: Hydrologic Unit Code Watersheds
~ 2000 HUC 8 for US, about the size of counties

## Slide 13: Watershed Boundary Dataset
National Program by USGS and USDA (NRCS)
Boundaries for 10- and 12- digit watersheds
First cut is by automated delineation from NED
Hand checked and edited
10-digit watersheds
http://nhd.usgs.gov/wbd.html

## Slide 14: The National Map
http://nationalmap.gov/
A central source for US Government data

## Slide 15
River networks
for 8-digit HUC
watersheds
http://nhd.usgs.gov/

## Slide 17
Slope
Elevation
Mean annual flow
  Corresponding velocity
Drainage area
% of upstream drainage area in different land uses
Stream order
http://www.horizon-systems.com/nhdplus/

## Slide 18: River Reach Codes Used for river address locations
ReachCode =
12030102000151
ReachCode = 12030102000005
HUC#
Segment#
Location 0.392
on Reach
12030102000005

## Slide 19: National Elevation Dataset
Digital Elevation Model with 1 arc-second (30m), 1/3 arc-second (10m) and some 1/9 arc second (3m) cells
Distributed as part of the National Map
10 billion data
Derived from USGS 1:24,000 quadrangle sheets and at higher resolution from LIDAR
Get the data:
http://ned.usgs.gov/
http://nationalmap.gov/viewer.html

## Slide 20: National Elevation Dataset Availability
From http://nationalmap.gov/viewer.html

## Slide 21: Digital Elevation Model (DEM)
Contours
720
700
680
740
680
700
720
740
720
720

## Slide 22
Digital Elevation Model (DEM)-30 meter

## Slide 23: Austin West 30 Meter DEM

## Slide 24
32
16
8
64
4
128
1
2
Eight Direction Pour Point Model
Water in a given cell flows one or more of eight adjacent cells in the direction of steepest descent (ArcGIS)
ArcGIS raster operations involved in watershed delineation are derived from the premise that “water flows downhill, in doing so, will follow the steepest descent

## Slide 25: Flow Direction Grid
32
16
8
64
4
128
1
2

## Slide 26: Delineation of Streams and Watersheds on a DEM

## Slide 27
http://srtm.usgs.gov/

## Slide 28: HydroSheds derived from SRTM
http://hydrosheds.cr.usgs.gov/

## Slide 30: GTOPO30 - 1 km Digital Elevation Model of the Earth
https://lta.cr.usgs.gov/GTOPO30

## Slide 31: Drainage in North America
Hydro1K is
derived from
GTOPO30
using raster
GIS analysis
https://lta.cr.usgs.gov/HYDRO1K

## Slide 32: Soil Data
Natural Resources Conservation Service (NRCS)
State Soil Geographic Database-STATSGO
Soil Survey Geographic Database- SSURGO
http://www.nrcs.usda.gov/wps/portal/nrcs/site/soils/home/
http://websoilsurvey.sc.egov.usda.gov/App/WebSoilSurvey.aspx
https://gdg.sc.egov.usda.gov/

## Slide 33
1:250,000 Scale Soil Information
https://gdg.sc.egov.usda.gov/

## Slide 34
1:24,000 scale
soil information
SSURGO:
County Level
Digital Soil Maps
http://websoilsurvey.nrcs.usda.gov/DataAvailability/SoilDataAvailabilityMap.pdf

## Slide 35: Ssurgo for Travis County
103 soil map units described by 7530 polygons of average area 35.37 ha (87 acres)

## Slide 36
http://landcover.usgs.gov/

## Slide 37: National Land Cover Dataset
Get the data:
http://www.mrlc.gov/
1992, 2001, 2006 and 2011

## Slide 39
Hierarchy of Census Geographic Entities
11,000,000
220,000 (avg 600 households/block grp)
74,000
US Population: 316 million US Households: 133 million
http://www.caee.utexas.edu/prof/maidment/giswr2014/Census/AccessingCensusData.pdf
Notes: This diagram depicts the geographic hierarchy, as a series of nesting relationships, based on the legal, administrative, or areal relationships of the entities. For example, a line joining the lower-level entity “place” and the higher-level entity “state” means that a place cannot cross a state boundary.

## Slide 40: American Community Survey
Source of detailed demographic and housing characteristics, including:
  Income
  Language spoken at home
  Educational attainment
  Occupation
  Place of work and journey to work
Data collected annually from approximately 3 million households per year. Approximately 250,000 households per month.
Data collected throughout the year—produces period estimates rather than point estimates.
 | ACS 1-Year Data | ACS 3-Year Data | ACS 5-Year Data
Geographic Areas | 65,000 or more population | 20,000 or more population | All areas, block group or higher

## Slide 41
Census Block 370210020004000
Census Block Group 370210020004
Zip Code 28803
Buncombe County
North Carolina
Scales of
Data Aggregation
A single property – 211 Caribou Rd

## Slide 42: Census Block Groups for the US
State
County
Tract
Block Group
http://www.caee.utexas.edu/prof/maidment/giswr2014/census/census.gdb.zip (308MB)
Definition query to isolate Travis and Williamson Counties

## Slide 43: Census Block Groups in Travis and Williamson Counties
Travis County
Williamson County

## Slide 44: Demographic Analysis
Two Counties
307 Tracts
823 Block Groups
Travis
Williamson

## Slide 45: www.climate.gov

## Slide 46
http://www.ncdc.noaa.gov/oa/ncdc.html

## Slide 47: PRISM Mean Annual Precipitation (Oregon State U.)
http://www.wcc.nrcs.usda.gov/climate/prism.html

## Slide 48: National Water Information System
Web access to USGS water
resources data in real time
http://waterdata.usgs.gov/usa/nwis/

## Slide 49: USGS Water Watch
Web access to USGS water resources data in real time
http://waterdata.usgs.gov/nwis/rt

## Slide 50: USGS National Water Information System.
Real-time and Historic Data
  Streamflow and stage
  Groundwater levels
  Water Quality
  Site information
Tabular or Graphical Format
http://water.usgs.gov

## Slide 51: CUAHSI Water Data Services
http://data.cuahsi.org

## Slide 52: ArcGIS Online: Living Atlas
Land Cover
Soils
Elevation
http://doc.arcgis.com/en/living-atlas/

## Slide 53: ArcGIS Online Services
http://landscape1.arcgis.com/arcgis/services/
http://landscape2.arcgis.com/arcgis/services/
http://landscape3.arcgis.com/arcgis/services/
http://elevation.arcgis.com/arcgis/services
http://hydro.arcgis.com/arcgis/services

## Slide 54: Ready to Use Services in Arc Catalog
You have to sign in to your AGOL account in ArcMap to use these

## Slide 55: Elevation Services
http://elevation.arcgis.com/arcgis/services

## Slide 56: Other Dynamic Map Services

## Slide 57: http://water.weather.gov/ahps/

## Slide 58: http://water.weather.gov/ahps/

## Slide 59: http://enviroatlas.epa.gov/enviroatlas/

## Slide 60: EnviroAtlas
All data is available for download
Some data is available for download as web service

## Slide 61
http://www.wcc.nrcs.usda.gov/snotel/

## Slide 62
SNOTEL System for Measuring Snow and Supporting Spring Runoff and Water Supply Forecasts

## Slide 63: USU Doc Daniels SNOTEL Site

## Slide 64: Measuring Snow Water Equivalent

## Slide 65: http://www.cbrfc.noaa.gov

## Slide 66: CBRFC SNOTEL Ensemble
http://www.cbrfc.noaa.gov/station/sweplot/sweplot.cgi?tglu1

## Slide 67
Texas Natural Resource Information System http://www.tnris.org/

## Slide 68: TWDB http://www.twdb.texas.gov/mapping/gisdata.asp

## Slide 69: http://gis.utah.gov

## Slide 70: Utah Terrain Basemap
To use as a basemap in ArcGIS see instructions at
http://gis.utah.gov/map-services/new-utah-terrain-base-map-and-cached-tile-service-available

## Slide 71
Utah GIS Portal Download GIS Data
http://gis.utah.gov/data/

## Slide 72
http://geology.utah.gov/maps/gis/index.htm

## Slide 73
http://www.wrcc.dri.edu/

## Slide 74: Bear River Watershed
http://www.bearriverinfo.org/

## Slide 75: Great Salt Lake Info System
http://greatsaltlakeinfo.org/

## Slide 76: MODIS on NASA Worldview (Shrinking Great Salt Lake)
https://earthdata.nasa.gov/labs/worldview/?p=geographic&l=MODIS_Aqua_CorrectedReflectance_TrueColor,MODIS_Terra_CorrectedReflectance_TrueColor,Reference_Features,Coastlines&t=2012-05-11&v=-114.20487628044651,40.12581729563662,-110.51347003044651,42.16048526438662
2012-05-11
https://earthdata.nasa.gov/labs/worldview/?p=geographic&l=MODIS_Aqua_CorrectedReflectance_TrueColor,MODIS_Terra_CorrectedReflectance_TrueColor,Reference_Features,Coastlines&t=2015-08-31&v=-114.20487628044651,40.12581729563662,-110.51347003044651,42.16048526438662
2015-08-31

## Slide 77: Smoke from Fires over W US MODIS 2015-08-19
https://earthdata.nasa.gov/labs/worldview/?p=geographic&l=MODIS_Aqua_CorrectedReflectance_TrueColor,MODIS_Terra_CorrectedReflectance_TrueColor,Reference_Features,Coastlines&t=2015-08-19&v=-134.01859698357154,33.61092471751162,-104.48734698357154,49.88826846751162

## Slide 78: Summary
There are a plethora of data sources available
Knowing what is available is important to scope GIS analyses and projects
GIS is about creating knowledge, telling stories, making decisions – all involve integrating information from multiple sources
The way that data is organized can enhance or inhibit the analyses that can be done
Data dissemination is increasingly becoming service based