## Slide 1: General workflow for Hydrologic Terrain Analysis Using Digital Elevation Models
Raw DEM
Pit Removal (Filling)
Flow Field
Channels, Watersheds, Flow Related Terrain Information
Watersheds are the most basic hydrologic landscape elements
Notes: This slide shows the general model for deriving flow field related derivative surfaces from digital elevation data. The input is a raw digital elevation model, generally elevation values on a grid. This is basic information used to derive further hydrology related spatial fields that enrich the information content of this basic data. The first step is to remove sinks, either by filling, or carving. Then a flow field is defined. This enables the calculation of flow related terrain information. My focus has been on flow related information working within this framework. I try to leave other GIS functionality, like radiation exposure, line of sight analyses and visualization to others. I have distributed my software in ways that it easily plugs in to mainstream systems, such as ArcGIS to enhance ease of use.

## Slide 2: Outline
Raster to Vector Connection and relational model of catchments, watersheds and channel networks
Using vector stream information (DEM reconditioning)
Enhanced pit removal
Channelization threshold selection
Hydrologic Terrain Analysis Software

## Slide 3
Watershed Draining to Outlet
Watershed mapped as all grid cells that drain to an outlet
Streams mapped as grid cells with flow accumulation greater than a threshold

## Slide 4: Watershed and Stream Grids
Watershed mapped as all grid cells that drain to an outlet
Streams mapped as grid cells with flow accumulation greater than a threshold

## Slide 5
ArcHydro Page 74
172
201
204
202
206
203
209
Each link has a unique identifying number
Stream Segments

## Slide 6
Vectorized Streams Linked Using Grid Code to Cell Equivalents
Vector
Streams
Grid
Streams
ArcHydro Page 75

## Slide 7
DrainageLines are drawn through the centers of cells on the stream links. DrainagePoints are located at the centers of the outlet cells of the catchments
ArcHydro Page 75

## Slide 8
Catchments, DrainageLines and DrainagePoints of the San Marcos basin
ArcHydro Page 75

## Slide 9
Catchment, Watershed, Subwatershed.
ArcHydro Page 76
Watershed outlet points may lie within the interior of a catchment, e.g. at a USGS stream-gaging site.
Catchments
Subwatersheds
Watershed

## Slide 10: Using Vector Stream Information
+
=
 Take a mapped stream network and a DEM
 Make a grid of the streams
 Raise the off-stream DEM cells by an arbitrary elevation
increment
 Produces "burned in" DEM streams = mapped streams
“Burning In” the Streams

## Slide 11
AGREE Elevation Grid Modification Methodology – DEM Reconditioning

## Slide 12: Carving
Lower elevation of neighbor along a predefined drainage path until the pit drains to the outlet point

## Slide 13: Carving
Pits
Carve outlets
Original DEM
Carved DEM
Notes: Elevations are filled to that of the pools pour point

## Slide 14
Filling
Carving
Minimizing Alterations

## Slide 15: Minimizing DEM Alterations
Optimally adjusted
Pits
Original DEM
Carved
Filled
Notes: Elevations are filled to that of the pools pour point

## Slide 16: Summary of Key Processing Steps
[DEM Reconditioning]
Pit Removal (Fill Sinks)
Flow Direction
Flow Accumulation
Stream Definition
Stream Segmentation
Catchment Grid Delineation
Raster to Vector Conversion (Catchment Polygon, Drainage Line, Catchment Outlet Points)

## Slide 17: How to decide on stream delineation threshold ?
AREA 1
AREA 2
3
12
Why is it important?

## Slide 18: Delineation of Channel Networks and Catchments
500 cell theshold
1000 cell theshold

## Slide 19
Hydrologic processes are different on hillslopes and in channels. It is important to recognize this and account for this in the delineation of streams.
Drainage area can be concentrated or dispersed (specific catchment area) representing concentrated or dispersed flow.

## Slide 20: Examples of differently textured topography
Badlands in Death Valley. from Easterbrook, 1993, p 140.
Coos Bay, Oregon Coast Range.
from W. E. Dietrich

## Slide 21: Gently Sloping Convex Landscape
From W. E. Dietrich

## Slide 22: Topographic Texture and Drainage Density
Same scale, 20 m contour interval
Sunland, CA
Driftwood, PA

## Slide 23
Lets look at some geomorphology.
    Drainage Density
    Horton’s Laws
    Slope – Area scaling
    Stream Drops
“landscape dissection into distinct valleys is limited by a threshold of channelization that sets a finite scale to the landscape.” (Montgomery and Dietrich, 1992, Science, vol. 255 p. 826.)
Suggestion: One contributing area threshold does not fit all watersheds.

## Slide 24: Drainage Density
Dd = L/A
Hillslope length  1/2Dd
L
B
B
Hillslope length = B
A = 2B L
Dd = L/A = 1/2B
 B= 1/2Dd

## Slide 25: Drainage Density for Different Support Area Thresholds
EPA Reach Files
100 grid cell threshold
1000 grid cell threshold

## Slide 26: Drainage Density Versus Contributing Area Threshold

## Slide 27: Hortons Laws: Strahler system for stream ordering
1
1
1
1
1
1
1
1
1
1
1
1
1
1
2
2
2
2
3

## Slide 28: Length Ratio

## Slide 29: Slope Ratio

## Slide 30: Constant Stream Drops Law
Broscoe, A. J., (1959), "Quantitative analysis of longitudinal stream profiles of small watersheds," Office of Naval Research, Project NR 389-042, Technical Report No. 18, Department of Geology, Columbia University, New York.

## Slide 31: Stream Drop Elevation difference between ends of stream
Note that a “Strahler stream” comprises a sequence of links (reaches or segments) of the same order
Nodes
Links
Single Stream

## Slide 32: Suggestion: Map channel networks from the DEM at the finest resolution consistent with observed channel network geomorphology ‘laws’.
Look for statistically significant break in constant stream drop property as stream delineation threshold is reduced
Break in slope versus contributing area relationship
Physical basis in the form instability theory of Smith and Bretherton (1972), see Tarboton et al. 1992

## Slide 33: Statistical Analysis of Stream Drops

## Slide 34: T-Test for Difference in Mean Values
72
130
0
T-test checks whether difference in means is large (> 2)
when compared to the spread of the data around the mean values

## Slide 35: Objectively Selected Support Area Threshold

## Slide 36
200 grid cell constant support area based stream delineation

## Slide 37: Hydrologic Terrain Analysis Software
ArcGIS Online Hydro
ArcGIS Hydrology Tools
ArcHydro
TauDEM
[RiverTools]
[GRASS]

## Slide 38: ArcGIS Online Hydro

## Slide 39: ArcGIS Hydrology Toolset

## Slide 40: ArcHydro
http://resources.arcgis.com/en/communities/hydro/

## Slide 41: TauDEM
Stream and watershed delineation
Multiple flow direction flow field
Calculation of flow based derivative surfaces
MPI Parallel Implementation for speed up and large problems
Open source platform independent C++ command line executables for each function
Deployed as an ArcGIS Toolbox with python scripts that drive command line executables
CSDMS Cluster Implementation
Open Topography implementation
CyberGIS Implementation
http://hydrology.usu.edu/taudem/

## Slide 42: Workflow to automatically generate stream network upstream of outlet

## Slide 43: Catchments linked to Stream Network
The starting point for catchment based distributed hydrologic modeling

## Slide 44: Edge contamination
Edge contamination arises when a contributing area value depends on grid cells outside of the domain. This occurs when drainage is inwards from the boundaries or areas with no data values. The algorithm recognizes this and reports "no data" resulting in streaks of "no data" values extending inwards from boundaries along flow paths that enter the domain at a boundary.

## Slide 45: Representation of Flow Field
D
D8
67
56
52
48
Steepest single direction
Tarboton, D. G., (1997), "A New Method for the Determination of Flow Directions and Contributing Areas in Grid Digital Elevation Models," Water Resources Research, 33(2): 309-319.)
Notes: This slide shows how the terrain flow field is represented. Early DEM work used a single flow direction model, D8. In 1997 I published the Dinfinity method that proportions flow from each grid cell among downslope neighbors. This, at the expense of some dispersion, allows a better approximation of flow across surfaces.

## Slide 46
D8
Contributing Area
D

## Slide 47: Wetness Index
Slope (S)
Specific Catchment Area (a)
Wetness Index ln(a/S)

## Slide 48
Generalized Flow Accumulation
x
w(x)

## Slide 49: Generalization to Flow Algebra
Replace
by general function
Pki
Pki
Pki
i

## Slide 50
Useful for a tracking contaminant or compound subject to decay or attenuation

## Slide 51: Transport limited accumulation
Supply
Capacity
Transport
Deposition
Useful for modeling erosion and sediment delivery, the spatial dependence of sediment delivery ratio and contaminant that adheres to sediment
S
2
2
)
tan(
b
T
cap
ca
=
å
+
=
}
,
min{
cap
in
out
T
T
S
T
å
-
+
=
out
in
T
T
S
D

## Slide 52: The challenge of increasing Digital Elevation Model (DEM) resolution
1980’s DMA 90 m
102 cells/km2
1990’s USGS DEM 30 m
103 cells/km2
2000’s NED 10-30 m
104 cells/km2
2010’s LIDAR ~1 m
106 cells/km2

## Slide 53: TauDEM Parallel Approach
MPI, distributed memory paradigm
Row oriented slices
Each process includes one buffer row on either side
Each process does not change buffer row
Improved runtime efficiency
Capability to run larger problems

## Slide 54: Do you have the access or know how to take advantage of advanced computing capability?
HPC Specialists
Researchers
Experimentalists
Modelers
awk
grep
vi
#PBS -l nodes=4:ppn=8
mpiexec
chmod
#!/bin/bash

## Slide 55: Using TauDEM today requires
Expertise in Hydrologic DEM analysis
The software
  ArcGIS licenses
  The ability to install software
  TauDEM command functions with MPI installation
  Compilation for other platforms
Sufficient Hardware (RAM and Disk)
The data (uncompressed GeoTIFF, projected, consistent grid size and spatial reference)

## Slide 56
Can we deliver GIS functionality in general, and TauDEM specifically, as a service over the web
Data Sources
Functions and Tools
Server
Software as a Service
Users
Based on slide from Norm Jones

## Slide 57: XSEDE Extended Collaboration Support Services (ECSS) improvements
Reconfiguration of multiple file header reads to be broadcast from single node
Reconfiguration of output files to avoid spanning processors
Execution time of the three most costly TauDEM functions on a 36GB DEM dataset.
#cores | Compute | Header Read | Data Read | Data Write
32 | 42.7 / 42.8 | 193.5 / 3.8 | 0.4 / 0.4 | 153.5 / 3.5
64 | 35.3 / 34.8 | 605.5 / 3.9 | 1.5 / 1.1 | 160.2 / 2.3
128 | 33.7 / 33.0 | 615.2 / 2.6 | 0.9 / 1.0 | 173.2 / 2.3
256 | 37.5 / 38.0 | 831.7 / 2.3 | 0.5 / 0.9 | 391.3 / 1.6
I/O Time Comparison (before / after; in seconds) for 2 GB DEM

## Slide 58: www.opentopography.org

## Slide 59: Open Topography Data and Product Selection

## Slide 60: Open Topography Result

## Slide 61: TauDEM Wetness index
Eel River ln(a/S)
a in meters

## Slide 62: Contributing area from D-Infinity
Notes: Note the detail in the representation of flow paths at features such as roads

## Slide 63: CyberGIS TauDEM App http://gateway.cigi.illinois.edu/ (Production) http://sandbox.cigi.illinois.edu/home/ (Experimental)

## Slide 65: Select the products you want
The wizard configures the sequence of functions to run to get the result

## Slide 66: Input parameters are set if needed

## Slide 67: The job progresses through the system
Analysis submitted
Analysis running
Results data created
Results Ready

## Slide 68: Results displayed in browser

## Slide 69: Summary Concepts
The GIS grid based terrain flow data model enables derivation of a wide variety of information useful for the study of hydrologic processes.
Terrain surface derivatives enhanced by use of DInfinity model.
Flow algebra a general “recipe” for terrain flow related modeling.
Edge contamination checking important to ensure that results are not impacted by area outside the domain of the DEM analyzed
Parallelism required to process big terrain data.
Software as a service approach is moving functionality into the cloud