## Slide 1: GISWR 2015 Midterm Review

## Slide 3: Definition of Latitude, f
(1) Take a point S on the surface of the ellipsoid and define there the tangent plane, mn
(2) Define the line pq through S and normal to the
tangent plane
(3) Angle pqr which this line makes with the equatorial
plane is the latitude f, of point S
O
f
S
m
n
q
p
r

## Slide 4: Definition of Longitude, l
0°E, W
90°W
(-90 °)
180°E, W
90°E
(+90 °)
-120°
-30°
-60°
-150°
30°
-60°
120°
150°
l
l = the angle between a cutting plane on the prime meridian
and the cutting plane on the meridian through the point, P
P

## Slide 5: Length on Meridians and Parallels
0 N
30 N
Df
Re
Re
R
R
A
B
C
Dl
(Lat, Long) = (f, l)
Length on a Meridian:
AB = Re Df
(same for all latitudes)
Length on a Parallel:
CD = R Dl = Re Dl Cos f
(varies with latitude)
D

## Slide 6
A map of Texas and a set of map projection parameters for the state are given above.
(a) Please draw and label on the map: the central meridian, the latitude of origin, and the two standard parallels.
(b) Give the numerical values (in degrees and minutes) for (ϕ0, λ0):
(c) Give the numerical values for (X0, Y0):
(d) What earth datum is used?
(e) What spheroid is used?
(f) What map projection is used?
(g) What are the distance units in the coordinate system?

## Slide 7: Utah State Plane System (North)
Std Parallel 2
Std Parallel 1
Latitude of Origin
Central Meridian
Origin

## Slide 9: Subwatershed Precipitation by Thiessen Polygons
Thiessen Polygons
Intersect with Subwatersheds
Evaluate A*P Product
Summarize by subwatershed

## Slide 10: Runoff Coefficients
Interpolated precip for each subwatershed
Convert to volume, P
Sum over upstream subwatersheds in Excel
Runoff volume, Q
Ratio of Q/P
Watershed | HydroID's
Plum Ck at Lockhart, TX | 330
Blanco Rv nr Kyle, TX | 331, 332
San Marcos Rv at Luling, TX | 331,332,333,336

## Slide 12: Pit Filling
Pits
Pour Points
Original DEM
Pits Filled
Grid cells or zones completely surrounded by higher terrain
The lowest grid cell adjacent to a pit
Notes: Elevations are filled to that of the pools pour point

## Slide 13
80
74
63
69
67
56
60
52
48
80
74
63
69
67
56
60
52
48
30
Slope:
Hydrologic Slope
- Direction of Steepest Descent
30

## Slide 15
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
10
1
0
14
4
1
19
1
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
10
1
0
1
4
14
19
1
Flow Accumulation Grid.
Area draining in to a grid cell
ArcHydro Page 72

## Slide 16
Watershed Draining to Outlet
Watershed mapped as all grid cells that drain to an outlet
Streams mapped as grid cells with flow accumulation greater than a threshold

## Slide 18: Zonal Average of Raster over Subwatershed
Join

## Slide 19: 2013 Midterm Questions

## Slide 20: Curved Earth Distance (from A to B)
Shortest distance is along a “Great Circle”
A “Great Circle” is the intersection of a sphere with a plane going through its center.
1. Spherical coordinates converted to Cartesian coordinates.
2. Vector dot product used to calculate angle  from latitude and longitude
3. Great circle distance is R, where R=6378.137 km2
X
Z
Y
•

A
B
Ref: Meyer, T.H. (2010), Introduction to Geometrical and Physical Geodesy, ESRI Press, Redlands, p. 108

## Slide 23: NHDPlus Version 2.1
National Elevation Dataset
National Hydrography Dataset
National Land Cover Dataset
Watershed Boundary Dataset
NHDPlus
Foundation for a Geospatial Hydrologic Framework for the United States
2.7 million reach catchments in US
average area 3 km2
reach length 2 km
Uniquely labelled

## Slide 26
Note that behind “networks” in ArcGIS there is a data model that enables the network functionality that you used.
We did not cover that this year as it is hidden from a user so you would not get this question. However you should know how networks work and what they can be used for.

## Slide 27: Geographic Data Model
“All geographic information systems are built using formal models that describe how things are located in space. A formal model is an abstract and well-defined system of concepts. A geographic data model defines the vocabulary for describing and reasoning about the things that are located on the earth. Geographic data models serve as the foundation on which all geographic information systems are built.”
Scott Morehouse, Preface to “Modeling our World”, First Edition. He is the chief software engineer at ESRI
Or, more simply: the way that data is organized can enhance or inhibit the analysis that can be done

## Slide 28: The connectivity in the network data model enables analyses such as tracing for selection of the upstream network and watershed

## Slide 29: Subnetwork analysis enabled by attributes joined with a network

## Slide 30: 2012 Midterm Questions

## Slide 33
g
d
a
h
e
b
i
f
c
Similarly
Slope magnitude =
ArcGIS “Slope” tool
a
b
c
d
e
f
g
h
i
x
y
x
y

## Slide 34: ArcGIS Aspect – the steepest downslope direction
Use atan2 to resolve ambiguity in atan direction

## Slide 35
Example
30
80
74
63
69
67
56
60
52
48
a
b
c
d
e
f
g
h
i
145.2o

## Slide 36
80
74
63
69
67
56
60
52
48
80
74
63
69
67
56
60
52
48
30
Slope:
Hydrologic Slope (Flow Direction Tool)
- Direction of Steepest Descent
30