## Slide 1: Current and NFIE Forecast Systems
130 Catchments and Flowlines
uniquely labelled
Two basins and one forecast point
becomes
Current: 6600 basins and 3600 forecast points
NFIE: 2.7 million stream reaches and catchments
A national flow network
Blanco River at Wimberley
Basin ~ 400 Sq Mile
Reach Catchment ~ 1 Sq Mile

## Slide 2: Real-Time Flood Inundation Mapping (NWS/AHPS)
http://water.weather.gov/ahps2/inundation/inundation_google.php?gage=atit2

## Slide 3: Flood Extent Map for each 1 ft of geodetic elevation

## Slide 4: Reach Hydraulic Parameters
Comid | H | A | R | P | T | V | Ab | As
5781175 | 3 |  |  |  |  |  |  | 
5781175 | 4 |  |  |  |  |  |  | 
Wetted Bed Area
L
As
Ab
V
T
P
A
h
Surface Area
Volume
Depth
T
P
Cross Section Area
Wetted Perimeter
Top Width
R
Hydraulic Radius

## Slide 5: Real-Time Water Surface Elevation: Two Methods
Each reach has a center point and a flow forecast
(1) Establish a rating curve at center point and use this to convert flow, Q, to water depth, h, and water surface elevation
(2) Use the SPRNT model to compute both flow and depth
Forecast, Q
h
Q
h
Depth
Rating Curve

## Slide 6: Elevation-Indexed Flood Response Mapping
Coastal
Mapping
Riverine
Mapping
Treat these
in a common way
Elevation-indexed flood
inundation mapping
Flood water surface elevation
modeling and forecasting
Take blue line network, raise it and
flood it out, continue for increments
of elevation
Inundation map library for each NHDPlus Reach
for coastal and riverine reaches

## Slide 7: Combining NHD and NED to Define River Channel Geometry and Flood Extent

## Slide 8: Web based collaboration environment
Being developed by partnership between USU, RENCI, BYU, UNC, UVA, CUAHSI, Tufts, Texas, Purdue, Caktus
OCI-1148453
OCI-1148090
2012-2017

## Slide 9: At its heart, HydroShare is a system for sharing Resources and Collaborating
Files and sets of files structured to represent a hydrologic process, model, or element in the hydrologic environment
Standard data models enhance interoperability and support functionality “hydro value added”
Tools that act on resources to visualize, modify and create new resources
  Encode standard/best practices
Access control and sharing model

## Slide 10: Types of data to support as resources
Resource Types
Generic 
Geographic Raster 
Time Series 
Multidimensional Space Time dataset 
Model program 
Model instance 
Referenced Time Series (CUAHSI HIS web service link)
Application
Geographic Feature set
River Geometry
Sample based observations (ODM2 and CZO)
Model component
Composite resources
x
y
t

## Slide 11: NFIE-GEO
A map resource on ArcGIS.com
URL: http://arcg.is/1JW0DBm
Each polygon links to a resource in HydroShare

## Slide 12: NFIE-GEO Region
A ~130 MB Geodatabase file as a generic resource in HydroShare
5 Feature Classes
Usability limited to users with ArcGIS.
Need to have this become geographic feature resource in HydroShare in open format.
What hydro value added functionality is needed?
  Visualization
  Subsetting
  Web feature services
  Discovery

## Slide 13: River Hydraulic Properties
Comid | H | A | R | P | T | V | Ab | As
5781175 | 3 |  |  |  |  |  |  | 
5781175 | 4 |  |  |  |  |  |  | 
Wetted Bed Area
L
As
Ab
V
T
P
A
T
P
Cross Section Area
Wetted Perimeter
Top Width
h
Surface Area
Volume
Depth
A table with reach hydraulic parameters as an addition to a geographic feature resource
This may be derived from LIDAR using an automated tool or HEC RAS cross sections
R
Hydraulic Radius

## Slide 14
Representing River Geometry in HydroShare
Hydraulic Calculations
LiDAR
Cross Sections
Cross Sections Attached to River Network

## Slide 15: DEM Based Flood Plain Mapping
Each reach has a water depth hw from SPRNT
Each reach has an ID
Each grid cell has the ID of the reach it connects to and the height above the stream hs
Flood extent is “rapidly” mapped as
  If(hw(id) > hs(id))
    Inundation depth = hw(id) - hs(id)
  Else
    Inundation depth = 0

## Slide 16: Example
Reach and Watershed id
Height above nearest stream raster hs
hw(1) = 1.5
hw(2) = 2.5
hw(3) = 3.5
Notes: Elevations are filled to that of the pools pour point

## Slide 18: Drop to Stream from TauDEM for Onion Creek

## Slide 19: Inundation for DTS < 4m

## Slide 20: Drop to stream and inundation (DTS < 2 m)

## Slide 21: Notes
Based on 1/3 arc sec National Elevation Dataset (pit filled)
Drop to stream used Dinfinity average (could modify to shortest distance)
Thresholding based on catchment not (yet) implemented