## Slide 1: Flooding in the Amite River Basin (August 12- August 22, 2016)
trey Stewart – The University of Texas – 14Sep16
Raedle, Joe. Signs in Flood. [Photograph]. Retrieved from http://wgno.com/2016/08/17/206724/
Clause, Scott. Flooding in Youngsvile. [Photograph]. Retrieved from http://gridironnow.com/baton-rouge-flooding-louisiana-floods

## Slide 2: Research Goal
To report on the August 2016 flooding in Louisiana by looking at the following data:
  Precipitation (NWS and USGS)
  River Stage (USGS)
  Elevation (USGS)
  High Water Marks (USGS)

## Slide 3: Flood Details
Historic amount of precipitation in south Louisiana
    Over 2 feet in some locations
    Most occurred within 2-day period (August 12-13)
    1000 year event
Stage records recorded in 8 Louisiana rivers
    One Amite river gauge beat record by 6 feet!
13 Deaths reported

## Slide 4: Watershed Location
Amite Watershed Flowlines
Nations Online Project. Map of Louisiana. [Photograph]. Retrieved from http://www.nationsonline.org/oneworld/map/USA/louisiana_map.htm

## Slide 5: Watershed Location
Amite River
Amite River
Comite River
East Baton Rouge
Amite Watershed Flowlines
Nations Online Project. Map of Louisiana. [Photograph]. Retrieved from http://www.nationsonline.org/oneworld/map/USA/louisiana_map.htm

## Slide 6: South Louisiana is Flat!
Amite River
Amite River
Comite River
East Baton Rouge
Amite Watershed Flowlines
Nations Online Project. Map of Louisiana. [Photograph]. Retrieved from http://www.nationsonline.org/oneworld/map/USA/louisiana_map.htm

## Slide 7: Precipitation Mapping
Louisiana precipitation according to NWS August 9-August 16
Amite Watershed precipitation 8/12-8/13 (in inches) generated using Empirical Bayesian Kriging Method with precipitation station data

## Slide 8: Precipitation Mapping
Louisiana precipitation according to NWS August 9-August 16
Amite Watershed precipitation 8/12-8/13 (in inches) generated using Empirical Bayesian Kriging Method with precipitation station data
My Hometown

## Slide 9: Quantifying Precipitation
South Louisiana:
  7.1 trillion gallons of water
  3x more than Hurricane Katrina
Amite River Basin:
  Average of 14 inches of precipitation
  0.5 trillion gallons of water
Thiessen polygons for precipitation stations

## Slide 10: Contour Affects Flooding Behavior
Flooding downstream lagged precipitation
Amite Watershed Contour Plot – Lines indicate 10 m height difference
Baton Rouge
Date | River Stage (feet)
8/11/2016 | 16.85P
8/12/2016 | 28.54P
8/13/2016 | 42.36P
8/14/2016 | 45.60P
8/15/2016 | 42.27P
8/16/2016 | 36.77P
8/17/2016 | 30.18P
8/18/2016 | 26.69P
8/19/2016 | 24.33P
8/20/2016 | 20.47P
8/21/2016 | 18.30P
8/22/2016 | 17.24P
Main Rainfall Occurred
Amite and Comite Junction
Amite and Comite Junction

## Slide 11: Contour Affects Flooding Behavior
Backwater flooding occurred south of Baton Rouge
Amite Watershed Contour Plot – Lines indicate 10 m height difference
Baton Rouge
Date | River Stage (feet)
8/11/2016 | 16.85P
8/12/2016 | 28.54P
8/13/2016 | 42.36P
8/14/2016 | 45.60P
8/15/2016 | 42.27P
8/16/2016 | 36.77P
8/17/2016 | 30.18P
8/18/2016 | 26.69P
8/19/2016 | 24.33P
8/20/2016 | 20.47P
8/21/2016 | 18.30P
8/22/2016 | 17.24P
Main Rainfall Occurred
Date | River Stage (feet)
8/11/2016 | 1.11
8/12/2016 | 3.15
8/13/2016 | 7.82
8/14/2016 | 14.46
8/15/2016 | 16.56
8/16/2016 | 15.55
8/17/2016 | 13.42
8/18/2016 | 11.00
8/19/2016 | 8.69
8/20/2016 | 6.97
8/21/2016 | 5.69
8/22/2016 | 4.60
Tributary Stage
Amite and Comite Junction
Tributary
Amite and Comite Junction

## Slide 12: High Water Mark Locations
High water marks indicate locations with >5 feet of flooding
Notice lots of flooding where Comite and Amite Rivers join
Amite Watershed High Water Marks and Flowlines
Amite River
Amite River
Comite River

## Slide 13: High Water Mark Locations
At least 110,000 homes damaged across South Louisiana
Much flooding occurred outside FEMA’s “high-risk” zone
  Most homes are not covered by flood insurance
Amite Watershed High Water Marks and Land Cover

## Slide 14: High Water Mark Locations
Flooding on I-10 and I-12 made them unusable from August 12th-16th
I-10 West of Baton Rouge remained closed until August 18th
Interstate Flooding
Baton Rouge
I-12
I-10

## Slide 15: Final Thoughts and Next Steps
Conclusions:
  Historic rainfall event requiring many days for water to drain
  Damaged homes and loss of life
  Buy flood insurance!
Next Steps
  Map HAND for watershed to compare modeled flood inundation depth with HWM data
  Determine total precipitation volume upstream from Comite and Amite River junction
  Look at Amite River slope and the velocity of the stage peak

## Slide 16: Acknowledgements
University of Texas
  Dr. David Maidment
  Paul Ruess
Louisiana State University
  Dr. Clint Wilson

## Slide 17: Questions?
References:
Ball, J. (2016, September 23). Louisiana Flood of 2016 made worse by growth-focused policies. Retrieved from NOLA.com: http://www.nola.com/news/baton-rouge/index.ssf/2016/09/louisiana_flood_of_2016_develo.html
Barney, A. (2016, August 24). Review of Historic Flooding in Louisiana. Retrieved from WeatherWorks: http://www.weatherworksinc.com/Louisiana-Floods-2016-Historic
Moscona, M. (2016, August 16). Historic flooding has brought Baton Rouge to its knees . Retrieved from gridironnow.com: http://gridironnow.com/baton-rouge-flooding-louisiana-floods
Samenow, J. (2016, August 19). No-name storm dumped three times as much rain in Louisiana as Hurricane Katrina. Retrieved from The Washington Post: https://www.washingtonpost.com/news/capital-weather-gang/wp/2016/08/19/no-name-storm-dumped-three-times-as-much-rain-in-louisiana-as-hurricane-katrina/
Unknown. (2016, August 22). Death toll rises to 13 in historic flood. Retrieved from wwltv.com: http://www.wwltv.com/news/death-toll-rises-to-13-in-historic-flood/298408105
Unknown. (2016, August 17). Historic flood death toll climbs to 12 after body found in Livingston Parish. Retrieved from wgno.com: http://wgno.com/2016/08/17/206724/
Unknown. (2016, August 14). Louisiana Flooding: 4 Dead, 20,000 Rescued, 10,000 in Shelters, Drivers Still Stranded on Interstate. Retrieved from Weather.com: https://weather.com/news/weather/news/gulf-coast-flooding-latest-news-rescues-motorists-interstate
Wells, C. K. (2016, August 18). I-10 reopens in Lafayette after historic flooding. Retrieved from Nola.com: http://www.nola.com/traffic/index.ssf/2016/08/i10_reopens_lafayette_flooding.html
Wells, C. K. (2016, August 16). Louisiana flooding: Interstate 12 reopens, parts of I-10 still closed. Retrieved from Nola.com: http://www.nola.com/traffic/index.ssf/2016/08/i12_open_i10_closed_flood.html