## Slide 1: Height above Nearest Drainage (HAND) Flood Inundation mapping
David Tarboton
Utah State University
dtarb@usu.edu
Acknowledgements: David Maidment, Nazmus Sazib, Xing Zheng, Yan Liu, Shaowen Wang, Ahmet Yildirim

## Slide 2: Flood Inundation Mapping
3
2
1
1. Forecast discharge with National Water Model
2. Convert discharge to depth using rating curve
3. Convert depth to inundation using HAND
Slide from David Maidment

## Slide 3: Flooding occurs when Water Depth is greater than Height Above Nearest Drainage (HAND)
Height Above
Nearest Drainage
(HAND)
Address Point
Flood Depth
Normal Depth
Stream Bed
May be used to determine flood risk
Slide from David Maidment

## Slide 4: Objective
The National Water Model produces flows at reach scale
Need a way to obtain reach level hydraulic properties for inputs to these models
Need a way to map from reach scale stage to flood inundation depth
Exploit high resolution topography and 1:1 relationship between stream reaches (NHD) and their catchments

## Slide 5: Mapping Flood Inundation with Height above the nearest drainage (HAND)
Each stream reach has a water depth hw (from a hydraulic model)
Each stream reach has an ID
Each grid cell has the ID of the reach it connects to and the height above the nearest stream hs
Evaluate inundation using hw-hs
    If(hw(id) > hs(id))
      Inundation depth = hw(id) - hs(id)
    Else
      Inundation depth = 0
This is approximate because it neglects many details of the river hydraulics and flow over flood plains. But more detailed approaches often demand hard to obtain and uncertain inputs so this may be a helpful approach to get screening level and real time flood maps

## Slide 6: How to calculate the height above the nearest drainage?
TauDEM (http://hydrology.usu.edu/taudem)
Tesfa, T. K., D. G. Tarboton, D. W. Watson, K. A. T. Schreuders, M. E. Baker and R. M. Wallace, (2011), "Extraction of hydrological proximity measures from DEMs using parallel processing," Environmental Modelling & Software, 26(12): 1696-1709, http://dx.doi.org/10.1016/j.envsoft.2011.07.018.
Nobre, A. D., L. A. Cuartas, M. Hodnett, C. D. Rennó, G. Rodrigues, A. Silveira, M. Waterloo and S. Saleska, (2011), "Height Above the Nearest Drainage – a hydrologically relevant new terrain model," Journal of Hydrology, 404(1–2): 13-29, http://dx.doi.org/10.1016/j.jhydrol.2011.03.051.
Nobre, A. D., L. A. Cuartas, M. R. Momo, D. L. Severo, A. Pinheiro and C. A. Nobre, (2015), "HAND contour: a new proxy predictor of inundation extent," Hydrological Processes, http://dx.doi.org/10.1002/hyp.10581.

## Slide 7: TauDEM Dinfinity Representation of Flow Field
D8
D
Tarboton, D. G., (1997), "A New Method for the Determination of Flow Directions and Contributing Areas in Grid Digital Elevation Models," Water Resources Research, 33(2): 309-319.)
http://hydrology.usu.edu/taudem

## Slide 8: HAND evaluated using TauDEM Dinfinity Vertical Distance Down function
D
Tesfa, T. K., D. G. Tarboton, D. W. Watson, K. A. T. Schreuders, M. E. Baker and R. M. Wallace, (2011), "Extraction of hydrological proximity measures from DEMs using parallel processing," Environmental Modelling & Software, 26(12): 1696-1709, http://dx.doi.org/10.1016/j.envsoft.2011.07.018.
hs
hr
Ridge
pr
ps
ss
sr
hs
hr
vr
vs
Stream
pr
ps
ss
sr
Point of interest
TauDEM Distance Down and Distance Up
Vertical distance to stream evaluated as weighted average over multiple flow paths. This results in a “smooth” height above nearest stream layer

## Slide 9: HAND Algorithm
0
0
0
0
0
0
0
Set h=0 along streams (target input set)
Mark remaining grid cells as “ready” if all down results are available and “not ready” if down results not yet computed
For a “ready” cell find its flow direction and elevation differences to down cells
Calculate h using weighted average
= 0.99
==0.92
==1.13
0.99

## Slide 10: HAND Algorithm Continued
0
0
0
0
0
0
0
Evaluate up cells when they become “ready”
= 4.88
==2.1
==2.74
0.99
0.95
2.64
1.88
4.88

## Slide 11: Result
435.56
436.01
436.44
0
0
0
0.99
0.92
2.64
1.88
Elevation z (m)
HAND h (m)
436.47
437.49
439.20
437.15
438.65
436.48
438.13
440.22
0.71
2.20
3.31
4.68

## Slide 12: TauDEM model for vertical drop to stream (aka HAND)
Could use D8 instead of Dinfinity
Could use Euclidean distances
Premised on good elevation model and consistent stream raster
Can be applied separately by catchment
  parallelism
  Incremental refinement of DEM
i
Pik
Pik

## Slide 13: HAND from TauDEM for Onion Creek near Austin Texas
1/3 arc second NED DEM

## Slide 14: Mapping Flood Extent and Depth by Reach in each Catchment based on depth in each stream
Flowlines
Catchments
Height above stream (relative elevation of land surface cell above cell in stream to which it flows)
Inundation map
Reach Scale Flood Depth
Comid | Depth (ft)
5781365 | 8
5781381 | 9
5781405 | 10
5781401 | 15
5781399 | 14
5781383 | 12
5781933 | 11

## Slide 15
Reach and Watershed id
Height above nearest drainage raster hHAND
hw(1) = 3.5
hw(2) = 2.5
hw(3) = 1.5
Mapping from height above nearest drainage to flood extent
      depth = hw(id) - hs(id)
      = 1.5-1 = 0.5
Notes: Elevations are filled to that of the pools pour point

## Slide 16: From NHD-HAND to Inundation
3 | 2 | 3 | 6 | 7 | 13 | 15
6 | 0 | 0 | 0 | 3 | 11 | 17
14 | 7 | 1 | 0 | 4 | 9 | 16
19 | 13 | 4 | 2 | 0 | 4 | 4
17 | 15 | 13 | 4 | 1 | 0 | 0
16 | 16 | 15 | 12 | 7 | 5 | 3
18 | 17 | 19 | 17 | 17 | 11 | 7
Inundation Extent
hHAND<=Hstage
Water Depth Raster
2 | 3 | 2 |  |  |  | 
 | 5 | 5 | 5 |  |  | 
 |  | 4 | 5 | 1 |  | 
 |  | 1 | 3 | 5 | 1 | 1
 |  |  | 1 | 4 | 5 | 5
 |  |  |  |  | 0 | 2
ywater=Hstage-hHAND
Slide from David Maidment

## Slide 17: Reach based height above nearest stream flood map example
hw=8 ft
hw=9 ft
hw=11 ft
hw=12 ft
hw=14 ft
hw=10 ft
hw=15 ft

## Slide 18: Reach Scale River Hydraulic Properties
Comid | H | A | R | P | T | V | Ab | As
5781175 | 3 |  |  |  |  |  |  | 
5781175 | 4 |  |  |  |  |  |  | 
Wetted Bed Area
L
As
Ab
V
T
P
A
T
P
Cross Section Area
Wetted Perimeter
Top Width
h
Surface Area
Volume
Depth
A table with reach hydraulic parameters as keyed to hydrography
Derived from DEM, LIDAR or HEC RAS cross sections
R
Hydraulic Radius
Slide from David Maidment

## Slide 19: Terrain based derivation of “reach scale” hydraulic properties
For each Catchment
For each height h
Identify cells where hs < h
Bed Area
Surface area
Single Cell Plan Area =dx * dy
Volume =
T
P
A
Cross Section Area
P
Wetted Perimeter
T
Top Width
Wetted Bed Area
L
As
Ab
V
Surface Area
Volume
R
Hydraulic Radius
Approximates each cell as sloping plane
Based on slide from David Maidment

## Slide 20: Reach Hydraulic Properties Example
1 m inundation
3 m inundation
Height (m) | As (m2) | Vol (m3) | Ab | L (m) | A=V/L (m2) | P=Ab/L (m) | T=As/L (m) | R=A/P (m)
1 | 129878 | 79466 | 129948 | 2975 | 26.7 | 43.7 | 43.7 | 0.612
3 | 319877 | 530378 | 320414 | 2975 | 178.3 | 107.7 | 107.5 | 1.655

## Slide 21: Terrain Approximated Reach Average Hydraulic Properties
Need for input to reach scale hydraulic model
Hydraulic Radius
Wetted Perimeter
Cross-sectional Area
Top Width

## Slide 22: Reach Catchment 5781289
Eanes Creek, Rollingwood, Texas
Drainage area = 3.13 mi2
Reach Length = 4.3 miles
Slide from David Maidment

## Slide 23: Discharge Computation
Hydraulic Radius, R
n = 0.035 Manning roughness of channel
So = 0.0163 Bed slope
Cross section Area, A
Flood Depth, h (ft)
Flood Discharge, Q (cfs)
Slide from David Maidment

## Slide 24: Rating Curve for Eanes Creek
Chart: Rating Curve for Eanes Creek, ComID = 5781289
| 0 | 607.56406134719509 | 2490.8796015163871 | 5785.1592347077531 | 10565.65567829302 | 16808.943658196447 | 24277.138771673799
Stage Height, h (ft) | 0 | 2.0669 | 3.937 | 5.807 | 7.6443 | 9.4159 | 10.9907
Forecast Discharge, Q, from National Water Model
Flood Depth, y (ft)
Slide from David Maidment

## Slide 25: Decompose computation by catchments or River Corridor
Parallel computation
High resolution in some areas
Incremental improvement

## Slide 26: DEM Flowlines challenged by road barriers
Need for hydrography conditioned DEM

## Slide 27: Obstacle Removal using NHD HR
48 | 48 | 49 | 48 | 47
48 | 46 | 50 | 46 | 45
47 | 45 | 51 | 43 | 39
44 | 40 | 51 | 47 | 47
41 | 45 | 52 | 48 | 48
48 | 48 | 49 | 48 | 47
48 | 46 | 50 | 46 | 45
47 | 45 | 51 | 43 | 39
44 | 40 | 51 | 47 | 47
41 | 45 | 52 | 48 | 48
48 | 48 | 49 | 48 | 47
48 | 46 | 50 | 46 | 45
47 | 45 | 40 | 40 | 39
44 | 40 | 51 | 47 | 47
41 | 45 | 52 | 48 | 48
Obstacles, like this railroad that are present in DEM are removed tracing down NHD HR streams ensuring that elevation never increases along a stream.

## Slide 28: Effect of obstacle removal
Before
After
HAND inundation based on raw 10 m NED DEM
Hand inundation for 10 m NED DEM with obstacles removed using NHD HR

## Slide 29: Complete HAND Workflow
USGS 3DEP 10m DEM
NHD HR Flowline
1:24000
NHDPlus Flowline
1:100000
Obstacle Removal
D∞ Flow Direction
D8 Flow Direction
D8 Flow Accumulation
Pit Removal
Stream Definition by Threshold
D∞ Distance Down
(Vertical Average)
Channel Head Extraction
Rasterization
Channel Head Weight Grid
Stream Raster
D∞ Flow Direction
Raster
HAND Raster
Catchment Features
Flood Inundation Mapping

## Slide 30: Continental-Scale HAND layer evaluated on ROGER supercomputer at NCSA
Catchments and Flowlines
Digital Elevation Model
Height Above Nearest
Drainage (HAND) (relative elevation of land
surface cell above cell in
stream to which it flows)
Slide from David Maidment

## Slide 31: Conclusions
The height above nearest stream approach suggested as way to rapidly approximate real time flood inundation
Includes an approach to approximate reach scale hydraulic properties
DEM topography should represent river bed elevations to maximal extent possible
Research ways to align and reconcile elevation and hydrography (present obstacle removal approach not ideal)
Investigate incorporating high resolution (e.g. LIDAR) data in areas where accuracy is critical