## Slide 1: Arc Hydro Groundwater Data Model
GIS in Water Resources - Fall 2017
Thanks to Dr Tim Whiteaker for help with the slides
Dr Tim Whiteaker

## Slide 2: What To Look For in this Presentation
Ideas on how we think about groundwater features in a GIS context
What kinds of geologic features does the model cover? What does it not cover?
How are relationships used to tie pieces of the data model together

## Slide 3: Resources
Groundwater Tools and Data Model aquaveo.com/archydro-groundwater
Tutorials aquaveo.com/ahgw-learning
Contact for tool support support@aquaveo.com
Hydro Resource Center resources.arcgis.com/en/communities/hydro

## Slide 4: A data model helps you design your database
Photo:PhoTones Works #6940 by Takuma Kimura.
Shared under CC BY-SA 2.0. https://creativecommons.org/licenses/by-sa/2.0/legalcode
My_Database
|
Waterbody
- Name
- AreaSqKm
TimeSeries
Water Level
Time
Notes: What is this kind of thing (e.g., polygon feature class)? What does it know (attributes)? Who does it know (relationships)?

## Slide 5: Why Use a Data Model
Concepts
Sharing
Tools

## Slide 6: Arc Hydro: GIS for Water Resources
A data model for water resources
A toolset for implementation
A framework for linking hydrologic simulation models
Focus on surface water
Free
(2002)
Notes: Industrial partners: ESRI, Danish Hydraulic Institute, Camp,Dresser and McKee, Dodson and Associates
Government partners:
Federal: EPA, USGS, Corps of Engineers (Hydrologic Engineering Center)
State: Texas Natural Resource Conservation Commission, Texas Water Development Board
Local: Lower Colorado River Authority, City of Austin, Dept of Watershed Protection
Academic Partners: University of Texas, Brigham Young University, Utah State University

## Slide 7: Arc Hydro Describes Surface Water
Time Series
Hydrography
Network
Channel
Drainage
Features

## Slide 8: A key concept from Arc Hydro is HydroID
Lake
Name = Lake Henry
HydroID = 1001
DamID = 5700
Like Social Security Number for features
Unique in a geodatabase
Used in relationships
Dam
Name = Henry Dam
HydroID = 5700
Feature Class
Attribute 1
Attribute 2
…
Legend

## Slide 9: Arc Hydro Groundwater: GIS For Hydrogeology
Builds on Arc Hydro
Includes data model and tools
Expands Arc Hydro temporal components
Some tools free, some not
(2011)

## Slide 10: Arc Hydro Groundwater Data Model
http://www.archydrogw.com/File:Archydrogw_overview.JPG

## Slide 11: Arc Hydro Groundwater Data Model
Framework
Temporal
Simulation
Boreholes
Hydrostratigraphy
Cross Sections
Geology

## Slide 12: Arc Hydro Framework
Extensible representation of surface water and groundwater
http://www.archydrogw.com/File:Archydrogw_framework.JPG

## Slide 13: Surface Water Features
WaterLine, WaterBody represent hydrography
Watershed represents drainage areas

## Slide 14: WaterPoint
Structures, dams, springs, diversions, etc.

## Slide 15: MonitoringPoint
Locations where water is measured

## Slide 16: Aquifer
Polygon features of aquifer boundaries
http://www.twdb.texas.gov/groundwater/aquifer/major.asp

## Slide 17: Well
Location where the subsurface has been drilled
Attributes describe depth, use, etc.
Notes: Photos: unknown

## Slide 18: Aquifers are related to Wells
An aquifer can be related to one or more wells (1:M)
*
HydroID
HydroCode
Name
HGUID
FType
Aquifer
HydroID
HydroCode
LandElev
WellDepth
AquiferID
AqCode
HGUID
FType
Well
1

## Slide 19: Aquifer and well

## Slide 20: Time Series Variables
VariableDefinition table is a catalog of time varying parameters (e.g., streamflow, water levels, concentrations)
Each variable is indexed with a HydroID

## Slide 21: TimeSeries table
Each measurement is indexed by space, time, and type
Space = FeatureID
Time = TsTime
Type = VarID
VarID
VariableDefinition
Information about
variables

## Slide 22: Time Series Views
We can slice the data cube to get specific views of the data
(FeatureID = 2791)
Where?
2791
TsTime
FeatureID
VarID
(VarID = 6875)
What?
FeatureID
VarID
TsTime
6875
(FeatureID = 2791 VarID = 6875)
Where and What?
2791
FeatureID
VarID
TsTime
6875

## Slide 23: Time Series Views
Well HydroID = 2791
Create a plot of time series related to a feature
Get all the data of VarID 6875 measured at Feature 2791

## Slide 24: Time Series Views
A type-time view: Get water levels (VarID=6875) for 1/1999
Water level in the Edwards Aquifer in 1/1999
Set of layers for different times creates an animation
1/1991
FeatureID
VarID
6875
TsTime

## Slide 25: Wells and TimeSeries
Wells are related with time series (e.g., water levels, water quality)
San Marcos springs
Springs
Sink Creek
San Marcos
Monitoring Well
(
295443097554201
)
TimeSeries
FeatureID
Well
HydroID

## Slide 26: MonitoringPoints and Time Series
Streamflow,
Precipitation,
Etc.

## Slide 27
Streamflow Gage at Comal Springs
Well in the Edwards Aquifer
The common framework supports analysis of surface water and groundwater data together

## Slide 28: Surface water - groundwater linkage
Relationships between surface water and aquifer enable analysis based on spatial and hydrologic relationships
Streams over the outcrop = recharge features

## Slide 29: Arc Hydro Framework - Review
Note the relationships (the lines connecting the boxes)
http://www.archydrogw.com/File:Archydrogw_framework.JPG

## Slide 30: Arc Hydro Groundwater Data Model
Framework
Temporal
Simulation
Boreholes
Hydrostratigraphy
Cross Sections
Geology
Framework
Geology

## Slide 31: Geologic maps
Are closely tied to geology
Vary in scale (continental, regional, local)
Geology
Aquifers
maps from http://nationalatlas.gov

## Slide 32: Arc Hydro Geology Component
Map modified from: Geologic map of the Edwards Aquifer recharge zone, south-central Texas. U.S. Geological Survey SIM 2873
GeologyPoint: e.g., springs, caves, sinks, observation points
GeologyLine: e.g., faults, contacts
GeologyArea: e.g., outcrops
A simple data model to support
geologic maps
GeologyPoint
GeologyLine
GeologyArea
GeologyLine
HydroID
HydroCode
GeoAbbrev
Description
HGUID
HGUCode
FType
GeologyArea
HydroID
HydroCode
GeoAbbrev
Description
HGUID
HGUCode
FType
GeologyPoint
HydroID
HydroCode
GeoAbbrev
Description
HGUID
HGUCode
FType

## Slide 33: Arc Hydro Groundwater Data Model
Framework
Temporal
Simulation
Boreholes
Hydrostratigraphy
Cross Sections
Geology
Geology
Boreholes

## Slide 34: Borehole data
Vertical data (screens, stratigraphy) referenced along the well
From depth (top), To depth (bottom), and Description
well

## Slide 35: Arc Hydro Borehole Component
Stores borehole data and represents data in 3D
http://www.archydrogw.com/File:Archydrogw_wellsandboreholes.JPG

## Slide 36: BoreholeLog table
Stores 3D borehole data related with well features
Each row represents a point/interval along a borehole
Data are related to Wells using the WellID attribute
3D geometry is defined by the TopElev and BottomElev attributes

## Slide 37: BorePoints and BoreLines
3D features representing data in the BoreholeLog table
BorePoint is a 3D point feature class for representing point locations along a borehole (e.g., geologic contacts, samples)
BoreLine is a 3D line feature class for representing intervals along a borehole

## Slide 38: Arc Hydro Groundwater Data Model
Framework
Temporal
Simulation
Boreholes
Hydrostratigraphy
Cross Sections
Geology
Boreholes
Hydrostratigraphy

## Slide 39: Hydrogeologic units
“Hydrogeologic unit is any soil or rock unit or zone which by virtue of its hydraulic properties has a distinct influence on the storage or movement of ground water” (USGS glossary of hydrologic terms)
Hydrogeology can be derived by classifying stratigraphic units
Georgetown Fm. (GTOWN)
Cyclic + Marine member (CYMRN)
Upper confining unit
Leached + collapsed member (LCCLP)
Regional dense member (RGDNS)
Grainstone member (GRNSTN)
Kirschberg evaporite member (KSCH)
Dolomitic member (DOLO)
Upper Glen Rose (UGLRS)
Stratigraphic units
Hydrogeologic units
Pearson Fm.
Basal Nodular member (BSNOD)
Kainer Fm.
Georgetown Fm.
Edwards Aquifer

## Slide 40: Arc Hydro Hydrostratigraphy
http://www.archydrogw.com/File:Archydrogw_hydrostratigraphy.JPG
Hydrogeologic units in 2D and 3D

## Slide 41: Hydrogeologic unit table
Provides a conceptual description of hydrogeologic units
Units are indexed with an HGUID
Units can be grouped into an aquifer via AquiferID

## Slide 42: Hydrogeologic unit table
Hydrogeologic units are described with different spatial instances (outcrops, borehole intervals, surfaces, cross sections, and volumes)
HGUID is the key attribute
HGUID
HGUID
Conceptual description
Spatial description
GeoArea
Polygon
feature class
HydrogeologicUnit
Table
SectionLine
PointZ
feature class
GeoRasters
Raster dataset
GeoSection
Multipatch
feature class
GeoVolume
Multipatch
feature class
1
*

## Slide 43: GeoArea (vs GeologyArea)
GeoArea feature representing the Kainer hydrogeologic unit
GeologyArea features represent data from geologic maps
GeologyArea
2D polygons defining boundaries of hydrogeologic units
GeoArea (conceptual/interpolated boundary) ≠ GeologyArea (mapped outcrop)
Data points representing top elevations of the Kainer formation

## Slide 44: 3D Representation of Cross Sections
SectionLine defines the location of the 2D cross section
GeoSection represent 3D sections as 3D features
SectionID of a GeoSection feature relates back to the section line
A
A’
B
B’

## Slide 45: GeoSections

## Slide 46: GeoRasters
Raster catalog for storing and indexing raster datasets
Can store top and bottom of formations
Each raster is related with a HGU in the hydrogeologic unit table
Georgetown
Glen Rose
Kainer
Person

## Slide 47: GeoRasters
GeoRasters also store hydraulic properties such as transmissivity, conductivity, and specific yield
K (feet/day)
Raster of hydraulic conductivity in the Edwards Aquifer

## Slide 48: GeoVolume
Features representing 3D volume objects
Geometry is multipatch

## Slide 49: Arc Hydro Groundwater Data Model
Framework
Temporal
Simulation
Boreholes
Hydrostratigraphy
Cross Sections
Geology
Hydrostratigraphy
Cross Sections

## Slide 50: Cross sections
…And interpret the rest
We can sample the subsurface…
A
A’
A
A’
Wells
Section A-A’
Cross sections help us understand local geology
Map
Notes: Cross sections help us visualize / conceptualize / understand the 3D structure of the subsurface.
We can sample strata at wells/boreholes drilled into the subsurface.
We then interpolate between the known points to create a continuous model of subsurface strata.

## Slide 51: Cross section coordinates
Cross sections use a (Distance, Elevation) coordinate system
And includes vertical exaggeration…
Each system is unique to the cross section…
x
y
S
Z
S
Notes: Cross sections have a unique coordinate system.
Data are transformed from X, Y, and Z coordinates to S and Z.
S = length along the section line
Z = vertical elevation – many times exaggerated for better visualization.
Data from nearby wells are projected to the closest point on the cross section.
Subsurface Analyst includes special tools to do these transformations.

## Slide 52: GIS datasets
Spatial and attribute relationships tie features together …
Borehole log
Section lines
Wells
Raster surfaces
…Creating the connectivity we need to construct meaningful cross sections
We’d like to create cross sections from GIS datasets
Geologic features
Notes: We use different GIS datasets:
  Wells with related borehole logs
  Geologic features – outcrops from geologic maps, faults
  Surfaces - DEMs, rasters representing water levels, tops of units, etc.
  Section lines
The different datasets need to be managed in a meaningful fashion.
Relationships between feature classes, manage multiple cross sections in a single geodatabase.

## Slide 53: XS2D Component
http://www.archydrogw.com/File:Archydrogw_XS2D.JPG

## Slide 54: 2D Cross Section Editing
Outcrop
Salt water interface
Borehole data
Panel
Panel divider
Edit cross sections in ArcMap

## Slide 55: Transform to 3D GeoSection

## Slide 56: Arc Hydro Groundwater Data Model
Framework
Temporal
Simulation
Boreholes
Hydrostratigraphy
Cross Sections
Geology
Cross Sections
Temporal

## Slide 57: Temporal Component
http://www.archydrogw.com/File:Archydrogw_XS2D.JPG

## Slide 58: Types of time varying datasets

## Slide 59: Multi-variable time series (attribute series)
Variables (VarKey)
Multiple variables recorded simultaneously at the same location
Example – water quality parameters
Indexed by location (FeatureID) and time (TsTime)
Relationship to the VariableDefinition table is through the VarKey

## Slide 60: Raster Series
January 1991
January 1992
January 1993
Raster datasets indexed by time
Each raster represents a continuous surface describing a variable for a given time

## Slide 61: Feature Series
A collection of features indexed by time
Example - particle tracks
Features are indexed by VarID, TsTime, and GroupID
Each group of features creates a track over time

## Slide 62: Time Series Catalogs
Like a library’s card catalog, but for time series
Series Catalog
  For a single variable at a single feature
  E.g., a summary of all water level measurements for a well
Dataset Catalog
  For an entire temporal dataset
  E.g., a summary of raster series representing water level across the entire aquifer
Both catalogs include start time, end time, and count

## Slide 63: Series Catalog Example
TimeSeries
SeriesCatalog
water depth in a well

## Slide 64: Arc Hydro Groundwater Data Model
Framework
Temporal
Simulation
Boreholes
Hydrostratigraphy
Cross Sections
Geology
Temporal
Simulation

## Slide 65: Representing simulation models
Georeference model inputs and outputs (in space and time)
Focus on MODFLOW, block centered finite difference grid (nodes are in the center of the cells)
Represent 2D and 3D models
Block-centered finite difference grid

## Slide 66: Simulation Component
http://www.archydrogw.com/File:Simulation_Features.png

## Slide 67: Boundary
Polygon feature class for representing the extent and orientation of a simulation model

## Slide 68: Cell2D and Node
Cell2D: polygon feature class that represents cells or elements associated with a two-dimensional simulation model or a single layer of a three-dimensional model
Node: point feature class used in combination with Cell2D to represent the model’s mesh/grid.
Finite element mesh
Mesh centered finite difference grid
Cell centered finite difference grid

## Slide 69: Cell2D and Node for Mapping

## Slide 70: Node3D and Cell3D
Node3D - a Z enabled point feature class
Cell3D - Multipatch feature class
Represent three-dimensional cells and Nodes
Used mostly for visualization of 3D models

## Slide 71: Arc Hydro Groundwater Data Model
Framework
Temporal
Boreholes
Hydrostratigraphy
Cross Sections
Geology
Simulation
Simulation

## Slide 72: Groundwater Tools for GIS

## Slide 73: Built-in Tools
Time-enabled Layers
Groundwater and Hydrology Toolsets

## Slide 74: Arc Hydro Groundwater Tools
Groundwater Analyst
MODFLOW Analyst
Subsurface Analyst
  3D Features
  2D Cross Sections

## Slide 75: Groundwater Analyst
Import and Manage Well Data
Point and Click Graphing Tool
Compute Time Series Statistics

## Slide 76: MODFLOW Analyst
Import and Export MODFLOW models
Run MODFLOW from ArcGIS

## Slide 77: Subsurface Analyst
3D Features
Create 2D Cross Sections

## Slide 78: Subsurface Analyst – 3D
Create
GeoSections
Create GeoVolumes
Create and Edit Borehole Data

## Slide 79: Arc Hydro Groundwater Summary Concepts
Arc Hydro helps us represent surface and groundwater systems in GIS
The groundwater data model includes aquifers, wells, hydrogeologic features, time series, and simulation model features
Relationships connect features with geologic data, aquifers, and time series