## Slide 1: Using Digital Elevation Model Derived Height Above the Nearest Drainage for flood inundation mapping and determining river hydraulic geometry in ungauged basins
David Tarboton1, Xing Zheng2, David Maidment2, Yan Liu3
1. Utah State University, dtarb@usu.edu
2. University of Texas at Austin, 3. University of Illinois
http://hydrology.usu.edu/dtarb

## Slide 2: Flood Inundation Mapping
3
2
1
1. Forecast discharge with National Water Model
2. Convert discharge to depth using rating curve
3. Convert depth to inundation using HAND
Slide from David Maidment

## Slide 3: Real-Time Flood Inundation Mapping Onion Creek at Highway 183
http://water.weather.gov/ahps2/inundation/inundation_google.php?gage=atit2
Slide from David Maidment

## Slide 4: Flooding occurs when Water Depth is greater than Height Above Nearest Drainage (HAND)
Height Above
Nearest Drainage
(HAND)
Address Point
Flood Depth
Normal Depth
Stream Bed
May be used to determine flood risk
Slide from David Maidment

## Slide 5: Background
Rodda, H. J. E., (2005), "The Development and Application of a Flood Risk Model for the Czech Republic," Natural Hazards, 36(1): 207-220, http://dx.doi.org/10.1007/s11069-004-4549-4.
Rennó, C. D., A. D. Nobre, L. A. Cuartas, J. V. Soares, M. G. Hodnett, J. Tomasella and M. J. Waterloo, (2008), "HAND, a new terrain descriptor using SRTM-DEM: Mapping terra-firme rainforest environments in Amazonia," Remote Sensing of Environment, 112(9): 3469-3481, http://doi.org/10.1016/j.rse.2008.03.018.
Nobre, A. D., L. A. Cuartas, M. Hodnett, C. D. Rennó, G. Rodrigues, A. Silveira, M. Waterloo and S. Saleska, (2011), "Height Above the Nearest Drainage – a hydrologically relevant new terrain model," Journal of Hydrology, 404(1–2): 13-29, http://dx.doi.org/10.1016/j.jhydrol.2011.03.051.
Tesfa, T. K., D. G. Tarboton, D. W. Watson, K. A. T. Schreuders, M. E. Baker and R. M. Wallace, (2011), "Extraction of hydrological proximity measures from DEMs using parallel processing," Environmental Modelling & Software, 26(12): 1696-1709, http://dx.doi.org/10.1016/j.envsoft.2011.07.018.
Nobre, A. D., L. A. Cuartas, M. R. Momo, D. L. Severo, A. Pinheiro and C. A. Nobre, (2016), "HAND contour: a new proxy predictor of inundation extent," Hydrological Processes, 30(2): 320-333, http://dx.doi.org/10.1002/hyp.10581.

## Slide 6: Readings on our approach
Zheng, X., D. G. Tarboton, D. R. Maidment, Y. Y. Liu and P. Passalacqua, (2017), "River channel geometry and rating curve estimation using height above the nearest drainage,". [http://hydrology.usu.edu/dtarb/Zheng_JAWRA_Oct2017_AuthorSubmitted.pdf ]
Liu, Y. Y., D. R. Maidment, D. G. Tarboton, X. Zheng and S. Wang, (2017), "A cybergis integration and computation framework for high-resolution continental-scale flood inundation mapping," Submitted to Journal of the American Water Resources Association. [http://hydrology.usu.edu/dtarb/Liu_JAWRA_2017_AuthorSubmitted.pdf]

## Slide 7: Traditional Floodplain mapping has used cross sections
Scaling this approach is intractable
NHDPlus MR: 5.2 million kilometers rivers and streams
Cross-Sections for Alabama Rivers compiled in NFIE-I
Slide from David Maidment

## Slide 8: Objective
The National Water Model produces flows at reach scale
Need a way to obtain reach level hydraulic properties for inputs to these models
Need a way to map from reach scale stage to flood inundation depth
Exploit high resolution topography and 1:1 relationship between stream reaches (NHD) and their catchments

## Slide 9: Mapping Flood Inundation with Height above the Nearest Drainage (HAND)
Each stream reach has a water depth hw (from a hydraulic model)
Each stream reach has an ID
Each grid cell has the ID of the reach it connects to and the height above the nearest stream hs
Evaluate inundation using hw-hs
    If(hw(id) > hs(id))
      Inundation depth = hw(id) - hs(id)
    Else
      Inundation depth = 0
This is approximate because it neglects many details of the river hydraulics and flow over flood plains. But more detailed approaches often demand hard to obtain and uncertain inputs so this may be a helpful approach to get screening level and real time flood maps
Premised on good elevation model and consistent stream raster

## Slide 10
Mapping from height above nearest drainage to flood extent
Reach and Watershed id
Height above nearest drainage raster hHAND
hw(1) = 3.5
hw(2) = 2.5
hw(3) = 1.5
Notes: Elevations are filled to that of the pools pour point

## Slide 11: Implementation based on NHDPlus catchments and reaches
Flowlines
Catchments
Height above stream (relative elevation of land surface cell above cell in stream to which it flows)
Inundation map
Reach Scale Flood Depth
Comid | Depth (ft)
5781365 | 8
5781381 | 9
5781405 | 10
5781401 | 15
5781399 | 14
5781383 | 12
5781933 | 11

## Slide 12: Reach based height above nearest stream flood map example
hw=8 ft
hw=9 ft
hw=11 ft
hw=12 ft
hw=14 ft
hw=10 ft
hw=15 ft

## Slide 13
D
D8
67
56
52
48
Steepest single direction
Tarboton, D. G., (1997), "A New Method for the Determination of Flow Directions and Contributing Areas in Grid Digital Elevation Models," Water Resources Research, 33(2): 309-319.
Calculation of HAND from a Digital Elevation Model (DEM)
D8
D
Notes: This slide shows how the terrain flow field is represented. Early DEM work used a single flow direction model, D8. In 1997 I published the Dinfinity method that proportions flow from each grid cell among downslope neighbors. This, at the expense of some dispersion, allows a better approximation of flow across surfaces.

## Slide 14: HAND evaluated using TauDEM Dinfinity Vertical Distance Down function
D
Tesfa, T. K., D. G. Tarboton, D. W. Watson, K. A. T. Schreuders, M. E. Baker and R. M. Wallace, (2011), "Extraction of hydrological proximity measures from DEMs using parallel processing," Environmental Modelling & Software, 26(12): 1696-1709, http://dx.doi.org/10.1016/j.envsoft.2011.07.018.
hs
hr
Ridge
pr
ps
ss
sr
hs
hr
vr
vs
Stream
pr
ps
ss
sr
Point of interest
TauDEM Distance Down and Distance Up
Vertical distance to stream evaluated as weighted average over multiple flow paths. This results in a “smooth” height above nearest drainage layer

## Slide 15: TauDEM model for vertical drop to stream (aka HAND)
i
Pik
Pik

## Slide 16: HAND Algorithm
0
0
0
0
0
0
0
Set h=0 along streams (target input set)
Mark remaining grid cells as “ready” if all down results are available and “not ready” if down results not yet computed
For a “ready” cell find its flow direction and elevation differences to down cells
Calculate h using weighted average
= 0.99
==0.92
==1.13
0.99

## Slide 17: HAND Algorithm Continued
0
0
0
0
0
0
0
Evaluate up cells when they become “ready”
= 4.88
==2.1
==2.74
0.99
0.95
2.64
1.88
4.88

## Slide 18: Result
Elevation z (m)
HAND h (m)
435.56
436.01
436.44
0
0
0
0.99
0.92
2.64
1.88
436.47
437.49
439.20
437.15
438.65
436.48
438.13
440.22
0.71
2.20
3.31
4.68

## Slide 19: HAND from TauDEM for Onion Creek near Austin Texas
1/3 arc second NED DEM

## Slide 20: Evaluating River Hydraulic Properties
Comid | H | A | R | P | T | V | Ab | As
5781175 | 3 |  |  |  |  |  |  | 
5781175 | 4 |  |  |  |  |  |  | 
Wetted Bed Area
L
As
Ab
V
T
P
A
T
P
Cross Section Area
Wetted Perimeter
Top Width
h
Surface Area
Volume
Depth
R
Hydraulic Radius
A table with reach hydraulic parameters keyed to hydrography

## Slide 21: Terrain based derivation of “reach scale” hydraulic properties
For each Catchment
For each height h
Identify cells where hs < h
Bed Area
Surface area
Single Cell Plan Area =dx * dy
Volume =
T
P
A
Cross Section Area
P
Wetted Perimeter
T
Top Width
Wetted Bed Area
L
As
Ab
V
Surface Area
Volume
R
Hydraulic Radius
Approximates each cell as sloping plane
Based on slide from David Maidment

## Slide 22: Reach Hydraulic Properties Example
1 m inundation
3 m inundation
Height (m) | As (m2) | Vol (m3) | Ab | L (m) | A=V/L (m2) | P=Ab/L (m) | T=As/L (m) | R=A/P (m)
1 | 129878 | 79466 | 129948 | 2975 | 26.7 | 43.7 | 43.7 | 0.612
3 | 319877 | 530378 | 320414 | 2975 | 178.3 | 107.7 | 107.5 | 1.655

## Slide 23: Terrain Approximated Reach Average Hydraulic Properties
Used for input to reach scale hydraulic model
Hydraulic Radius
Wetted Perimeter
Cross-sectional Area
Top Width

## Slide 24: Example - Reach Catchment 5781289
Eanes Creek, Rollingwood, Texas
Drainage area = 3.13 mi2
Reach Length = 4.3 miles
Slide from David Maidment

## Slide 25: Discharge Computation
Hydraulic Radius, R
n = 0.035 Manning roughness of channel
So = 0.0163 Bed slope
Cross section Area, A
Flood Depth, h (ft)
Flood Discharge, Q (cfs)
Slide from David Maidment

## Slide 26: Rating Curve for Eanes Creek
Chart: Rating Curve for Eanes Creek, ComID = 5781289
| 0 | 607.56406134719509 | 2490.8796015163871 | 5785.1592347077531 | 10565.65567829302 | 16808.943658196447 | 24277.138771673799
Stage Height, h (ft) | 0 | 2.0669 | 3.937 | 5.807 | 7.6443 | 9.4159 | 10.9907
Forecast Discharge, Q, from National Water Model
Flood Depth, y (ft)
Slide from David Maidment

## Slide 27: Decompose computation by catchments or River Corridor
Parallel computation
High resolution in some areas
Incremental refinement of DEM
Incremental improvement

## Slide 28: Obstacle Removal or “etching” using Vector Stream Information
48 | 48 | 49 | 48 | 47
48 | 46 | 50 | 46 | 45
47 | 45 | 51 | 43 | 39
44 | 40 | 51 | 47 | 47
41 | 45 | 52 | 48 | 48
48 | 48 | 49 | 48 | 47
48 | 46 | 50 | 46 | 45
47 | 45 | 51 | 43 | 39
44 | 40 | 51 | 47 | 47
41 | 45 | 52 | 48 | 48
48 | 48 | 49 | 48 | 47
48 | 46 | 50 | 46 | 45
47 | 45 | 40 | 40 | 39
44 | 40 | 51 | 47 | 47
41 | 45 | 52 | 48 | 48
Digital Elevation Model Conditioning
Obstacles, like this railroad that are present in DEM are removed tracing down NHD HR streams ensuring that elevation never increases along a stream.

## Slide 29: Obstacle Removal “Etch in” Workflow
Rasterize NHDPlus HR flowline;
Lower the elevation of stream cells on DEM by 100m;
Remove pits on the burned DEM;
Derive D8 flow direction on the pit-removed DEM;
Keep D8 flow direction on stream cells only;
Call TauDEM:flowdircond to burn the original DEM
  Identify ‘top cells’ which are on NHDPlus HR streams, have D8 direction, and are not downstream cells. Put them in a queue;
  For each cell in the queue:
    If the elevation is higher than its neighbors, level the elevation with neighbors;
    If above step makes any of the neighboring cell a non-downstream cell, add the neighboring cell to the queue. This step propagates the burn-in until the upstream connects to the downstream.

## Slide 30: Effect of obstacle removal
Before
After
HAND inundation based on raw 10 m NED DEM
Hand inundation for 10 m NED DEM with obstacles removed using NHD HR

## Slide 31: Adjustments at railroad crossing
Original DEM – Flow Direction Conditioned DEM

## Slide 32: Deriving Terrain Aligned Flow Network
Grids from the NHD Plus channel head cell to the outlet cell are defined as Stream Cells
Channel Head
NHD Plus Flowline
NHD Plus channel head and flowline
DEM derived stream
NHD HR Stream
D8 Flow direction from each grid cell set in the steepest downslope direction to one of eight adjacent neighbors
Routing across flats away from high terrain and towards low terrain (Garbrecht and Martz, 1997)
67
56
52
48

## Slide 33: DEM derived stream network is consistent with the DEM but at the scale (drainage density) of NHD Plus.

## Slide 34: Height Above Nearest Drainage (HAND) evaluated from 1/3 arc sec NED DEM relative to stream raster derived from NHDPlus medium resolution stream network source grid cells. 2 m contour interval.

## Slide 35: Complete HAND Workflow
USGS 3DEP 10m DEM
NHD HR Flowline
1:24000
NHDPlus Flowline
1:100000
Obstacle Removal
D∞ Flow Direction
D8 Flow Direction
D8 Flow Accumulation
Pit Removal
Stream Definition by Threshold
D∞ Distance Down
(Vertical Average)
Channel Head Extraction
Rasterization
Channel Head Weight Grid
Stream Raster
D∞ Flow Direction
Raster
HAND Raster
Catchment Features
Flood Inundation Mapping

## Slide 36: Continental-Scale HAND layer evaluated on ROGER supercomputer at NCSA
Catchments and Flowlines
Digital Elevation Model
Height Above Nearest
Drainage (HAND) (relative elevation of land
surface cell above cell in
stream to which it flows)
Slide from David Maidment

## Slide 37: Automated workflow prototyped for Texas Flood Response System by David Maidment and Colleagues
Summary of Impacts for Disaster Districts
Inundation mapping and local impact assessment
National Water Model discharge forecasts
Conversion of discharge to depth using rating curves
ESRI

## Slide 38: Conclusions
The height above nearest stream approach suggested as way to rapidly approximate real time flood inundation
Includes an approach to approximate reach scale hydraulic properties
DEM topography should represent river bed elevations to maximal extent possible
DEM conditioning used to align and reconcile elevation and hydrography (obstacle removal approach)
Can exploit high resolution (e.g. LIDAR) data in areas where accuracy is critical

## Slide 39
Acknowledgements
Multiple grants from US National Science Foundation and USGS
Papers
Liu, Y. Y., D. R. Maidment, D. G. Tarboton, X. Zheng and S. Wang, (2017), "A cybergis integration and computation framework for high-resolution continental-scale flood inundation mapping," Submitted to Journal of the American Water Resources Association.
Zheng, X., D. G. Tarboton, D. R. Maidment, Y. Y. Liu and P. Passalacqua, (2017), "River channel geometry and rating curve estimation using height above the nearest drainage," Submitted to Journal of the American Water Resources Association

## Slide 40: Are there any questions?
HAND 10m for CONUS