## Slide 1
Carolyn Cooper
Flooding Surrounding the Addicks Reservoir during Hurricane Harvey
November 2018

## Slide 2: History of Addicks Reservoir
1929
1935
1948
Flood causes $2.5M in damage
Addicks Reservoir Construction Complete
Flood causes $1.4M in damage
Port of Houston crippled for months
7 people killed
1937
Harris County Flood Control District Founded
Addicks Reservoir
Barker Reservoir

## Slide 3: Upstream Flooding in the Addicks Watershed
Substantial changes in land usage in Addicks Watershed
Reservoir pools flooded for first time during Hurricane Harvey
1992 Land Cover
2011 Land Cover
Notes: https://www.npr.org/2017/11/09/563016223/exploring-why-hurricane-harvey-caused-houstons-worst-fooding

## Slide 4: Digital Elevation Model Evaluation
10 M DEM from USGS National Elevation Dataset
Generated Elevation-Area Capacity Curve using Model Builder with the Surface Volume Tool
  DEM is fairly accurate
  Filled DEM is not representative

## Slide 5: Height Above Nearest Drainage Calculation
HAND calculated to reservoir outlet
  Approximates full reservoir
Address points exist within the area where HAND is zero

## Slide 6: Inundation Comparison
 | Reservoir Height, ft above NAVD88 | Homes Flooded
Max during Harvey | 109.1 | 3,750
1% Error | 110.2 | 5,999
2% Error | 111.3 | 7,840
HCFD | - | 6,010
Differences between DEM and reservoir may contribute to error

## Slide 7: Downstream Flooding
Corps began controlled releases during Hurricane Harvey on August 29th
  4,000 CFS – 8,000 CFS from both reservoirs
Notes: https://www.lincolninst.edu/publications/articles/houston-surveys-post-harvey-policy-landscape
https://www.hcfcd.org/hurricane-harvey/flooding-impacts-in-connection-with-the-reservoirs/

## Slide 8: Height Above Nearest Drainage and Rating Curve
Generated HAND for Buffalo Bayou
Developed rating curves for delineated catchments

## Slide 9: Inundation Comparison
 | Homes Flooded
Current Estimate | 3,146
City of Houston | 4,000
HCFD | 17,090
Discrepancies due to difference in extent of Buffalo Bayou
Still working to improve estimate

## Slide 10: Conclusions
HAND provided relatively accurate estimates
  Still refining downstream inundation estimate
Understanding flooding around Houston’s reservoirs is crucial to improving flooding infrastructure
Notes: https://spacecityweather.com/addicks-barker-reservoirs-emptied/