## Slide 1: Data Sources for GIS in Water Resources by David R. Maidment, and David G. Tarboton GIS in Water Resources Fall 2018

## Slide 2: Outline
The hierarchical system of watersheds and basins
Where to obtain data and maps
  National/State/Global Data repositories
  Hydrography
  USGS National Water Information System
  Land Cover
  Census
  Elevation
  Soil (Statsgo/Surgo)
  Weather
  Regional data for Texas and Utah

## Slide 3: The National Map
http://nationalmap.gov/
A central source for US Government data

## Slide 4
https://nhd.usgs.gov/wbd.html

## Slide 5: Watershed Boundary Dataset
National Program by USGS and USDA (NRCS)
Boundaries for 10- and 12- digit watersheds
First cut is by automated delineation from NED
Hand checked and edited
10-digit watersheds
http://nhd.usgs.gov/wbd.html

## Slide 6: Watershed Hierarchy
8 HUC
4
2
6
NHDPlus
10
12
Digit #
Each hydrologic unit is identified by a unique hydrologic unit code (HUC) consisting of two to or more digits based on the levels of classification in the hydrologic unit system.
HAW HUC 8 03030002
Little Creek HUC 12 030300020603

## Slide 7: National Hydrography Dataset
https://nhd.usgs.gov/

## Slide 8
River networks
for 8-digit HUC
watersheds
http://nhd.usgs.gov/

## Slide 10: River Reach Codes Used for river address locations
ReachCode =
12030102000151
ReachCode = 12030102000005
HUC#
Segment#
Location 0.392
on Reach
12030102000005

## Slide 11: National Elevation Dataset
https://nationalmap.gov/elevation.html

## Slide 12: National Elevation Dataset
Digital Elevation Model with 1 arc-second (30m), 1/3 arc-second (10m) and some 1/9 arc second (3m) cells
Distributed as part of the National Map
10 billion data
Derived from USGS 1:24,000 quadrangle sheets and at higher resolution from LIDAR

## Slide 13: National Elevation Dataset Availability
https://viewer.nationalmap.gov/basic/

## Slide 14
Slope
Elevation
Mean annual flow
  Corresponding velocity
Drainage area
% of upstream drainage area in different land uses
Stream order
http://www.horizon-systems.com/nhdplus/

## Slide 15: NHDPlus Version 2.1
National Elevation Dataset
National Hydrography Dataset
National Land Cover Dataset
Watershed Boundary Dataset
NHDPlus
Foundation for a Geospatial Hydrologic Framework for the United States
2.7 million reach catchments in US
average area 3 km2
reach length 2 km
Uniquely labelled
http://www.arcgis.com/home/item.html?id=5600cf6b463043ec97b764fb258997be#!

## Slide 16: NHDPlus Data Download
http://www.horizon-systems.com/nhdplus/NHDPlusV2_data.php

## Slide 17: Digital Elevation Model (DEM)
Contours
720
700
680
740
680
700
720
740
720
720

## Slide 18
Digital Elevation Model (DEM)-30 meter

## Slide 19: Austin West 30 Meter DEM

## Slide 20
32
16
8
64
4
128
1
2
Eight Direction Pour Point Model
Water in a given cell flows to one of eight adjacent cells in the direction of steepest descent
ArcGIS raster operations involved in watershed delineation are derived from the premise that “water flows downhill, in doing so, will follow the steepest descent

## Slide 21: Flow Direction Grid
32
16
8
64
4
128
1
2

## Slide 22: Delineation of Streams and Watersheds on a DEM

## Slide 23
https://lta.cr.usgs.gov/SRTM

## Slide 24: SRTM Topographic Data (all 30m data now public for world)
http://www2.jpl.nasa.gov/srtm/

## Slide 25: HydroSheds derived from SRTM
http://hydrosheds.cr.usgs.gov/

## Slide 27: GTOPO30 - 1 km Digital Elevation Model of the Earth
https://lta.cr.usgs.gov/GTOPO30

## Slide 28: Drainage in North America
Hydro1K is
derived from
GTOPO30
using raster
GIS analysis
https://lta.cr.usgs.gov/HYDRO1K

## Slide 29: Soil Data
Natural Resources Conservation Service (NRCS)
State Soil Geographic Database-STATSGO
Soil Survey Geographic Database- SSURGO
http://www.nrcs.usda.gov/wps/portal/nrcs/site/soils/home/
http://websoilsurvey.sc.egov.usda.gov/App/WebSoilSurvey.aspx
https://gdg.sc.egov.usda.gov/

## Slide 30
1:250,000 Scale Soil Information
https://gdg.sc.egov.usda.gov/

## Slide 31
1:24,000 scale
soil information
SSURGO:
County Level
Digital Soil Maps
http://websoilsurvey.nrcs.usda.gov/DataAvailability/SoilDataAvailabilityMap.pdf

## Slide 32: Ssurgo for Travis County
103 soil map units described by 7530 polygons of average area 35.37 ha (87 acres)

## Slide 33: POLARIS: A 30-meter probabilistic soil series map of the contiguous United States
Chaney, N. W., E. F. Wood, A. B. McBratney, J. W. Hempel, T. W. Nauman, C. W. Brungard and N. P. Odgers, (2016), "POLARIS: A 30-meter probabilistic soil series map of the contiguous United States," Geoderma, 274: 54-67, http://www.sciencedirect.com/science/article/pii/S0016706116301434.
http://stream.princeton.edu/POLARIS/

## Slide 34
http://landcover.usgs.gov/

## Slide 35: National Land Cover Data
http://www.mrlc.gov/

## Slide 37
Hierarchy of Census Geographic Entities
11,000,000
220,000 (avg 600 households/block grp)
74,000
US Population: 316 million US Households: 133 million
http://www.caee.utexas.edu/prof/maidment/giswr2014/Census/AccessingCensusData.pdf
Notes: This diagram depicts the geographic hierarchy, as a series of nesting relationships, based on the legal, administrative, or areal relationships of the entities. For example, a line joining the lower-level entity “place” and the higher-level entity “state” means that a place cannot cross a state boundary.

## Slide 38: American Community Survey
Source of detailed demographic and housing characteristics, including:
  Income
  Language spoken at home
  Educational attainment
  Occupation
  Place of work and journey to work
Data collected annually from approximately 3 million households per year. Approximately 250,000 households per month.
Data collected throughout the year—produces period estimates rather than point estimates.
 | ACS 1-Year Data | ACS 3-Year Data | ACS 5-Year Data
Geographic Areas | 65,000 or more population | 20,000 or more population | All areas, block group or higher

## Slide 39
Census Block 370210020004000
Census Block Group 370210020004
Zip Code 28803
Buncombe County
North Carolina
Scales of
Data Aggregation
A single property – 211 Caribou Rd

## Slide 40: Census Block Groups for the US
State
County
Tract
Block Group
http://www.caee.utexas.edu/prof/maidment/giswr2014/census/census.gdb.zip (308MB)
Definition query to isolate Travis and Williamson Counties

## Slide 41: Census Block Groups in Travis and Williamson Counties
Travis County
Williamson County

## Slide 42: Demographic Analysis
Two Counties
307 Tracts
823 Block Groups
Travis
Williamson

## Slide 43
https://www.ncei.noaa.gov/

## Slide 44: www.climate.gov

## Slide 45: PRISM Mean Annual Precipitation (Oregon State U.)
http://prism.oregonstate.edu/

## Slide 46: National Water Information System
Web access to USGS water
resources data in real time
http://waterdata.usgs.gov/usa/nwis/

## Slide 47: USGS Water Watch
Web access to USGS water resources data in real time
http://waterdata.usgs.gov/nwis/rt

## Slide 48: USGS National Water Information System.
Real-time and Historic Data
  Streamflow and stage
  Groundwater levels
  Water Quality
  Site information
Tabular or Graphical Format
http://water.usgs.gov

## Slide 49: ArcGIS Online: Living Atlas
http://doc.arcgis.com/en/living-atlas/

## Slide 50: Ready to Use Services in ArcGIS Pro e.g Watershed Delineation

## Slide 51: Hurricane Florence Forecast as of 11AM Weds 12 Sept 2018
Source: National Hurricane Center
https://www.nhc.noaa.gov/

## Slide 52: National Water Model Forecasts for Carolina Coast
http://water.noaa.gov/map

## Slide 53: River Discharge Forecast from Florence
Sat
Sun
Mon
Fri
River Discharge
(cubic feet per second)
160,000 cfs
on Sunday evening
Thu
Wed
Forecast as of Weds Sept 12 at 8 AM

## Slide 54: http://water.weather.gov/ahps/

## Slide 55: http://water.weather.gov/ahps/

## Slide 56: CUAHSI HydroClient http://data.cuahsi.org Query for Streamflow Data in the Houston Area during Hurricane Harvey – 39 time series identified

## Slide 57: Time Series Data Downloaded to Excel

## Slide 58: http://enviroatlas.epa.gov/enviroatlas/

## Slide 59
Texas Natural Resource Information System http://www.tnris.org/

## Slide 60: TWDB http://www.twdb.texas.gov/mapping/gisdata.asp

## Slide 61
Preserving A Flood of Data:
Hurricane Harvey 2017 Data Archive
Presentation to the 2018 Hurricane Harvey Research Symposium, Port Aransas
Acknowledgments for Harvey data: David R. Maidment, Harry R. Evans, Michael Ouimet
For Data Archive: Dave Tarboton, Jerad Bales, Martin Seul, Tony Castronova, Ray Idaszak
University of Texas at Austin, Texas DPS Division of Emergency Management, City of Austin,
National Weather Service, Univ of Illinois Urbana-Champaign, Utah State Univ, CUAHSI, RENCI*, Esri, Kisters,
Interagency Flood Risk Management Group, Harris County Flood Control District, Dept of Homeland Security,
Commission for State Emergency Communications, Texas 911 Alliance, Emergency GIS Response Team,
Texas GIS 911 User Group. *RENCI is an Institute at the University of North Carolina at Chapel Hill
Dr. David Arctur
Center for Water and the Environment
University of Texas at Austin
NSF RAPID
Award 1761673
Notes: This is the story about a project that’s been my main focus since 2 yr before Hurricane Harvey: to help develop a flood response system for Texas. Our team, under the scientific leadership of Dr. David Maidment, started in earnest on this project in the spring of 2015, after severe flash floods in central Texas. Because of our work on that project, our team was in a position to help with the flood mapping during Hurricane Harvey, 2 years later. Harry Evans is former chief of staff for the Austin Fire Dept, and served as our liaison to the Public Safety community. Mike Ouimet is Manager of Critical Information Systems with the Texas Division of Emergency Management, and sponsored our work during the 2 years before Harvey.

## Slide 62: Hurricane Harvey Story Map
http://arcg.is/001jje

## Slide 63: CUAHSI Project: Hurricanes 2017 Data Archive
https://www.cuahsi.org/projects/hurricanes-2017-data-archive
Notes: Here’s the landing page at cuahsi.org for the three data archives, with links highlighted for the Harvey archive.

## Slide 64
https://www.hydroshare.org/resource/2836494ee75e43a9bfb647b37260e461/
Notes: Scrolling down on the HydroShare resource page, we can see the area of coverage represented by data in this collection, and the collection contents. There are enough different types of data in this overall collection that we have multiple levels of hierarchy, eg, root collection > flood data collections > types of flood data. We’ll see some of these later on.

## Slide 65: River Forecast Centers
https://www.cbrfc.noaa.gov

## Slide 66: Logan River
1460 cfs 6/5/17

## Slide 67
http://www.wcc.nrcs.usda.gov/snotel/

## Slide 68
SNOTEL System for Measuring Snow and Supporting Spring Runoff and Water Supply Forecasts

## Slide 69: USU Doc Daniels SNOTEL Site

## Slide 70: Measuring Snow Water Equivalent

## Slide 71: http://www.cbrfc.noaa.gov

## Slide 72: CBRFC SNOTEL Ensemble
http://www.cbrfc.noaa.gov/station/sweplot/sweplot.cgi?tglu1

## Slide 73: NASA Airborne Snow Observatory
https://nsidc.org/data/aso

## Slide 74: SNODAS gridded mapping of snow across US
https://www.nohrsc.noaa.gov/archived_data/

## Slide 75: http://gis.utah.gov

## Slide 76
Utah GIS Portal Download GIS Data
http://gis.utah.gov/data/

## Slide 77
http://geology.utah.gov/maps/gis/index.htm

## Slide 78
http://www.wrcc.dri.edu/

## Slide 79: Bear River Watershed
http://www.bearriverinfo.org/

## Slide 80: MODIS on NASA Worldview (Shrinking Great Salt Lake)
https://worldview.earthdata.nasa.gov/?p=geographic&l=MODIS_Aqua_CorrectedReflectance_TrueColor,MODIS_Terra_CorrectedReflectance_TrueColor,Reference_Features,Coastlines&t=2012-05-11&v=-114.20487628044651,40.12581729563662,-110.51347003044651,42.16048526438662
2012-05-11
https://worldview.earthdata.nasa.gov/?p=geographic&l=MODIS_Aqua_CorrectedReflectance_TrueColor,MODIS_Terra_CorrectedReflectance_TrueColor,Reference_Features,Coastlines&t=2017-08-27&z=3&v=-114.20487628044651,40.12581729563662,-110.51347003044651,42.16048526438662
2017-08-27

## Slide 81: Smoke from Fires over W US MODIS 2018-08-04
https://worldview.earthdata.nasa.gov/?p=geographic&l=MODIS_Aqua_CorrectedReflectance_TrueColor,MODIS_Terra_CorrectedReflectance_TrueColor,Reference_Features,Coastlines&t=2018-08-04-T00%3A00%3A00Z&z=3&v=-133.43412432732154,32.05965518626162,-103.90287432732154,48.91707706126162

## Slide 82: Summary
There are a plethora of data sources available
Knowing what is available is important to scope GIS analyses and projects
GIS is about creating knowledge, telling stories, making decisions – all involve integrating information from multiple sources
The way that data is organized can enhance or inhibit the analyses that can be done
Data dissemination is increasingly becoming service based