## Slide 1: Extended Hydrologic Terrain Analysis
Establishing the terrain flow analysis framework
Hydrologic Terrain Analysis Software
Channelization threshold?
Geomorphology
Dinfinity
Generalized flow accumulation
Height above the nearest drainage (HAND)

## Slide 2: Terrain Flow Analysis Framework
Conditioned DEM (Fill)
Flow Direction
Flow Accumulation
Stream Definition
Stream Links
Catchments

## Slide 3: A Hydrologically Conditioned Digital Elevation Model (DEM) is one where there is a non increasing flow path from each grid cell to the outlet or edge of the domain

## Slide 4: Conditioning the DEM - Pit Filling
Original DEM
Pits Filled
Pits
Grid cells or zones completely surrounded by higher terrain
Increase elevation until the pit drains to a neighbor and ultimately out of the domain

## Slide 5: Using Vector Stream Information
+
=
 Take a mapped stream network and a DEM
 Make a grid of the streams
 Raise the off-stream DEM cells by an arbitrary elevation
increment
 Produces "burned in" DEM streams = mapped streams
“Burning In” the Streams

## Slide 6
AGREE Elevation Grid Modification Methodology – DEM Reconditioning

## Slide 7: AGREE Implemented using Raster Calculator
“dem" - 10 * “streamraster" - 0.02 * (500 - "distance") * ("distance" < 500)
Subtract 10 at all stream grid cells
Subtract an amount that tapers from 0.02*500=10 when distance is 0, to 0 when distance is 500 from stream
Only do taper when distance is less than 500, otherwise this is 0 and nothing is subtracted
500
500
10
10
Convert stream vector to raster
Distance
Raster Calculation

## Slide 8: Profiles (using 3D Analyst)
Original DEM
Conditioned DEM
Difference

## Slide 9: Conditioning the DEM - Carving
Lower elevation of neighbor along a predefined drainage path until the pit drains to the outlet point

## Slide 10: Carving
Pits
Carve outlets
Original DEM
Carved DEM
Notes: Elevations are filled to that of the pools pour point

## Slide 11
Filling
Carving
Minimizing Alterations

## Slide 12: Minimizing DEM Alterations
Optimally adjusted
Pits
Original DEM
Carved
Filled
Notes: Elevations are filled to that of the pools pour point

## Slide 13: Key Watershed Delineation Processing Steps
[DEM Reconditioning]
Pit Removal (Fill Sinks)
Flow Direction
Flow Accumulation
Stream Definition
Stream Segmentation
Catchment Grid Delineation
Raster to Vector Conversion (Catchment Polygon, Drainage Line, Catchment Outlet Points)

## Slide 14: Fill and Flow Direction
32
16
8
64
4
128
1
2
1
2

## Slide 15: Flow Accumulation
3

## Slide 16: Stream definition by theshold
5000
500
4

## Slide 17: Stream Segmentation
5

## Slide 18: Catchment Delineation
6

## Slide 19: Conversion to Vector
7
8

## Slide 20: Hydrologic Terrain Analysis Software
ArcGIS Portal ready to use tools
ArcGIS Hydrology Tools
ArcHydro
TauDEM
[RiverTools]
[GRASS]

## Slide 21: ArcGIS Pro Ready to Use Tools

## Slide 22: ArcGIS Hydrology Toolset

## Slide 23: ArcHydro
http://resources.arcgis.com/en/communities/hydro/

## Slide 24: TauDEM
Stream and watershed delineation
Multiple flow direction flow field
Calculation of flow based derivative surfaces
MPI Parallel Implementation for speed up and large problems
Open source platform independent C++ command line executables for each function
Deployed as an ArcGIS Toolbox with python scripts that drive command line executables
CSDMS Cluster Implementation
Open Topography implementation
CyberGIS Implementation
http://hydrology.usu.edu/taudem/

## Slide 25: Workflow to automatically generate stream network upstream of outlet

## Slide 26: Catchments linked to Stream Network
The starting point for catchment based distributed hydrologic modeling

## Slide 27: Edge contamination
Edge contamination arises when a contributing area value depends on grid cells outside of the domain. This occurs when drainage is inwards from the boundaries or areas with no data values. The algorithm recognizes this and reports "no data" resulting in streaks of "no data" values extending inwards from boundaries along flow paths that enter the domain at a boundary.

## Slide 28: How to decide on stream delineation threshold ?
AREA 1
AREA 2
3
12
Why is it important?

## Slide 29: Delineation of Channel Networks and Catchments
500 cell theshold
1000 cell theshold

## Slide 30
Hydrologic processes are different on hillslopes and in channels. It is important to recognize this and account for this in the delineation of streams.
Drainage area can be concentrated or dispersed (specific catchment area) representing concentrated or dispersed flow.

## Slide 31: Examples of differently textured topography
Badlands in Death Valley. from Easterbrook, 1993, p 140.
Coos Bay, Oregon Coast Range.
from W. E. Dietrich

## Slide 32: Gently Sloping Convex Landscape
From W. E. Dietrich

## Slide 33: Topographic Texture and Drainage Density
Same scale, 20 m contour interval
Sunland, CA
Driftwood, PA

## Slide 34
Lets look at some geomorphology.
    Drainage Density
    Horton’s Laws
    Slope – Area scaling
    Stream Drops
“landscape dissection into distinct valleys is limited by a threshold of channelization that sets a finite scale to the landscape.” (Montgomery and Dietrich, 1992, Science, vol. 255 p. 826.)
Suggestion: One contributing area threshold does not fit all watersheds.

## Slide 35: Drainage Density
Dd = L/A
Hillslope length  1/(2Dd)
L
B
B
Hillslope length = B
A = 2B L
Dd = L/A = 1/(2B)
 B= 1/(2Dd)

## Slide 36: Drainage Density for Different Support Area Thresholds
EPA Reach Files
100 grid cell threshold
1000 grid cell threshold

## Slide 37: Drainage Density Versus Contributing Area Threshold

## Slide 38: Hortons Laws: Strahler system for stream ordering
1
1
1
1
1
1
1
1
1
1
1
1
1
1
2
2
2
2
3

## Slide 39: Constant Stream Drops Law
Broscoe, A. J., (1959), "Quantitative analysis of longitudinal stream profiles of small watersheds," Office of Naval Research, Project NR 389-042, Technical Report No. 18, Department of Geology, Columbia University, New York.

## Slide 40: Stream Drop Elevation difference between ends of stream
Note that a “Strahler stream” comprises a sequence of links (reaches or segments) of the same order
Nodes
Links
Single Stream

## Slide 41: Suggestion: Map channel networks from the DEM at the finest resolution consistent with observed channel network geomorphology ‘laws’.
Look for statistically significant break in constant stream drop property as stream delineation threshold is reduced
Break in slope versus contributing area relationship
Physical basis in the form instability theory of Smith and Bretherton (1972), see Tarboton et al. 1992

## Slide 42: Statistical Analysis of Stream Drops

## Slide 43: T-Test for Difference in Mean Values
72
130
0
T-test checks whether difference in means is large (> 2)
when compared to the spread of the data around the mean values

## Slide 44: Objectively Selected Support Area Threshold

## Slide 45
100 grid cell constant support area threshold stream delineation

## Slide 46
200 grid cell constant support area based stream delineation

## Slide 47: Local Curvature Computation (Peuker and Douglas, 1975, Comput. Graphics Image Proc. 4:375)
43
41
48
47
48
47
54
51
54
51
56
58

## Slide 48: Contributing area of upwards curved grid cells only

## Slide 49: Upward Curved Contributing Area Threshold

## Slide 50
Curvature based stream delineation

## Slide 51: Dinfinity Representation of Flow Field
D8
D
Tarboton, D. G., (1997), "A New Method for the Determination of Flow Directions and Contributing Areas in Grid Digital Elevation Models," Water Resources Research, 33(2): 309-319.)
http://hydrology.usu.edu/taudem

## Slide 52
D8
Contributing Area
D

## Slide 53: Contributing area from D-Infinity
Notes: Note the detail in the representation of flow paths at features such as roads

## Slide 54: Contributing area from D-Infinity
Notes: Note the detail in the representation of flow paths at features such as roads

## Slide 55
Generalized Flow Accumulation
x
w(x)

## Slide 56: Generalization to Flow Algebra
Tarboton, D. G. and M. E. Baker, (2008), "Towards an Algebra for Terrain-Based Flow Analysis," in Representing, Modeling and Visualizing the Natural Environment: Innovations in GIS 12, Edited by N. J. Mount, G. L. Harvey, P. Aplin and G. Priestnall, CRC Press, Florida, p.496, http://dx.doi.org/10.1201/9781420055504.ch12.
i = F(i, Pki, k, k)
Replace
by general function
Pki
Pki
Pki
i
Output Result,
Quantity being calculated
Input Results from upslope
Flow direction proportions
Other inputs at cell and upslope

## Slide 57: General Pseudocode Upstream Flow Algebra Evaluation
Pki
Global P, ,  FlowAlgebra(i) for all k neighbors of i if Pki>0 FlowAlgebra(k) next k i = FA(i, Pki, k, k) return

## Slide 58: Example: Retention limited runoff generation with run-on
Global P, (r,c), q FlowAlgebra(i) for all k neighbors of i if Pki>0 FlowAlgebra(k) next k return
r
c
qi
qk

## Slide 59: General Pseudocode Downstream Flow Algebra Evaluation
Pki
Global P, ,  FlowAlgebra(i) for all k neighbors of i if Pik>0 FlowAlgebra(k) next k i = FA(i, Pik, k, k) return

## Slide 60
Dependence function of grid cells y
0
1
0
0
1
0
0
0.6
0
0.3
0.3
0
0.6
0
0
Grid cells y
Useful for example to track where a contaminant may come from

## Slide 61: General Proximity Functions as weighted distance to a target set along Dinfinity Flow Directions
Tesfa, T. K., D. G. Tarboton, D. W. Watson, K. A. T. Schreuders, M. E. Baker and R. M. Wallace, (2011), "Extraction of hydrological proximity measures from DEMs using parallel processing," Environmental Modelling & Software, 26(12): 1696-1709, http://dx.doi.org/10.1016/j.envsoft.2011.07.018.
D
hs
hr
Ridge
pr
ps
ss
sr
hs
hr
vr
vs
Stream
pr
ps
ss
sr
Point of interest

## Slide 62: Height above Nearest Drainage (HAND) evaluated using TauDEM Dinfinity Vertical Distance Down function
D
Tesfa, T. K., D. G. Tarboton, D. W. Watson, K. A. T. Schreuders, M. E. Baker and R. M. Wallace, (2011), "Extraction of hydrological proximity measures from DEMs using parallel processing," Environmental Modelling & Software, 26(12): 1696-1709, http://dx.doi.org/10.1016/j.envsoft.2011.07.018.
hs
hr
Ridge
pr
ps
ss
sr
hs
hr
vr
vs
Stream
pr
ps
ss
sr
Point of interest
TauDEM Vertical Distance Down a special case of a general hydrological proximity measure
Vertical distance to stream evaluated as weighted average over multiple flow paths. This results in a “smooth” height above nearest drainage layer
D

## Slide 63
Flooding occurs when water depth is greater than Height Above Nearest Drainage (HAND)
hs
hr
Ridge
pr
ps
ss
sr
hs
hr
vr
vs
Stream
pr
ps
ss
sr
Point of interest
Height Above
Nearest Drainage
(HAND)
Flood Depth
Normal Depth
Height Above the Nearest Drainage. The distance to streams (nearest drainage) calculated vertically along TauDEM Dinfinity flow directions
Serves to support flood inundation mapping where the data to support hydraulic calculations is limited
Enables evaluation of reach level hydraulic properties
Can take advantage of high resolution DEM data (but is only as good as the given DEM data)
Has been evaluated across continental US using 10 m resolution DEM and NHDPlus streams for use in US National Water Model flood inundation mapping

## Slide 64: HAND from TauDEM for Onion Creek near Austin Texas
1/3 arc second NED DEM

## Slide 65: Mapping Flood Inundation with Height above the Nearest Drainage (HAND)
Each stream reach has a water depth hw (from a hydraulic model)
Each stream reach has an ID
Each grid cell has the ID of the reach it connects to and the height above the nearest drainage hd
Evaluate inundation using hw-hd
    If(hw(id) > hd(id))
      Inundation depth = hw(id) - hd(id)
    Else
      Inundation depth = 0
This is approximate because it neglects many details of the river hydraulics and flow over flood plains. But more detailed approaches often demand hard to obtain and uncertain inputs so this may be a helpful approach to get screening level and real time flood maps
Premised on good elevation model and consistent stream raster

## Slide 66: Flood Inundation Mapping – HAND Method
Comid | Depth (ft)
5781365 | 8
5781381 | 9
5781405 | 10
5781401 | 15
5781399 | 14
5781383 | 12
5781933 | 11
Catchments and Flowlines
Digital Elevation Model
Height Above Nearest Drainage (relative elevation of land surface cell above cell in stream to which it flows)
Inundation map (Height above
drainage < water depth)
Reach Scale Flood Depth

## Slide 67: Summary Concepts
The GIS grid based terrain flow data model enables derivation of a wide variety of information useful for the study of hydrologic processes.
Knowledge from geomorphology enables objective selection of channel network delineation threshold
Terrain surface derivatives enhanced by use of DInfinity model.
Flow algebra a general “recipe” for terrain flow related modeling.
Programming supports automation of repetitive tasks and implementation of functionality not available