## Slide 1: Data Sources for GIS in Water Resources by David R. Maidment, and David G. Tarboton GIS in Water Resources Fall 2018

## Slide 2: Hurricane Story Map
http://bit.ly/2018HurricanePhotos

## Slide 3: Length on Meridians and Parallels
0 N
30 N
Df
Re
Re
R
R
A
B
C
Dl
(Lat, Long) = (f, l)
Length on a Meridian:
AB = Re Df
(same for all latitudes)
Length on a Parallel:
CD = R Dl = Re Dl Cos f
(varies with latitude)
D

## Slide 4
Example: What is the length of a 1º increment along
on a meridian and on a parallel at 30N, 90W?
Radius of the earth = 6370 km.
Solution:
A 1º angle has first to be converted to radians
p radians = 180 º, so 1º = p/180 = 3.1416/180 = 0.0175 radians
For the meridian, DL = Re Df = 6370 * 0.0175 = 111 km
For the parallel, DL = Re Dl Cos f
= 6370 * 0.0175 * Cos 30
= 96.5 km
Parallels converge as poles are approached

## Slide 5: Curved Earth Distance (from A to B)
Shortest distance is along a “Great Circle”
A “Great Circle” is the intersection of a sphere with a plane going through its center.
1. Spherical coordinates converted to Cartesian coordinates.
2. Vector dot product used to calculate angle  from latitude and longitude
3. Great circle distance is R, where R=6378.137 km2
X
Z
Y
•

A
B
Ref: Meyer, T.H. (2010), Introduction to Geometrical and Physical Geodesy, ESRI Press, Redlands, p. 108

## Slide 6
https://nhd.usgs.gov/wbd.html

## Slide 7: Watershed Hierarchy
8 HUC
4
2
6
NHDPlus
10
12
Digit #
Each hydrologic unit is identified by a unique hydrologic unit code (HUC) consisting of two to or more digits based on the levels of classification in the hydrologic unit system.
HAW HUC 8 03030002
Little Creek HUC 12 030300020603

## Slide 8
River networks
for 8-digit HUC
watersheds
http://nhd.usgs.gov/

## Slide 9
Slope
Elevation
Mean annual flow
  Corresponding velocity
Drainage area
% of upstream drainage area in different land uses
Stream order
http://www.horizon-systems.com/nhdplus/

## Slide 10: NHDPlus Version 2.1
National Elevation Dataset
National Hydrography Dataset
National Land Cover Dataset
Watershed Boundary Dataset
NHDPlus
Foundation for a Geospatial Hydrologic Framework for the United States
2.7 million reach catchments in US
average area 3 km2
reach length 2 km
Uniquely labelled
http://www.arcgis.com/home/item.html?id=5600cf6b463043ec97b764fb258997be#!

## Slide 11: National Land Cover Data
http://www.mrlc.gov/