## Slide 1: National Flood Interoperability Experiment (NFIE)
Prepared by David R. Maidment Center for Research in Water Resources University of Texas at Austin
Presented at the Engineering Research and Development Center, US Army Corps of Engineers,
Vicksburg, MS
20 March 2015

## Slide 2: The Opportunity…
New National Water Center established on the Tuscaloosa campus of University of Alabama by the National Weather Service and federal agency partners
Has a mission to assess hydrology in a new way at the continental scale for the United States

## Slide 3
Roadmap Document
(February 2009)
3
Aligns multiple agencies with complimentary water-related missions to:
Integrate services and service delivery
Improve river and flood forecasts
Provide new summit-to-sea water resources analyses and forecasts
Enable more effective use of resources
http://www.nohrsc.noaa.gov/~cline/IWRSS/IWRSS_ROADMAP_v1.0.pdf
Integrated Water Resources Science and Services (IWRSS)
Purpose, Scope, Vision and Goals
Cross-Cutting Themes
National and Regional
Operations and Business Concepts
Slide: Ed Clark, NWS

## Slide 4: NWS River Forecast Centers
Perform precipitation, runoff and river flow simulation and forecasting for five days ahead, updated daily, more frequently during floods

## Slide 5: Nationally Synthesize Operations of Regional River Forecast Centers

## Slide 6
National Water Data Infrastructure
Temporal information
Geospatial information

## Slide 7
Inaugural Meeting – May, 2014

## Slide 8: Transformative Research (NSF)
Transformative research involves ideas, discoveries, or tools that radically change our understanding of an important existing scientific or engineering concept or educational practice or leads to the creation of a new paradigm or field of science, engineering, or education. Such research challenges current understanding or provides pathways to new frontiers.
http://www.nsf.gov/about/transformative_research/definition.jsp
How to move from evolutionary change
to transformative change?

## Slide 9: Partnership with the academic community …
National Weather Service has joined with CUAHSI to conduct a one-year National Flood Interoperability Experiment (NFIE)
Includes a Summer Institute for students and faculty at the National Water Center, June 1 to July 17, 2015

## Slide 10: NFIE Summer Institute
Runs from June 1 to July 17
  Kickoff Event, week of June 1
  Capstone conference July 15-17
48 graduate students and post-docs from 15 Universities: Alabama, Texas (Arlington, Austin), Utah State, SUNY Syracuse, BYU, Colorado (Boulder), Illinois (Urbana-Champaign), Purdue, Oklahoma, Iowa, Michigan State, Arizona, Alaska (Fairbanks), Tufts

## Slide 11: Goal of the Experiment …
Close the gap between National Flood Forecasting and Local Emergency Response
Demonstrate forecasting of flood impacts at “stream and street level”
National
Local
Weather and Hydrology
National Weather Service and federal agencies
National Water Center
River Flooding and Emergency Response
Local, State and Regional Agencies
Citizens

## Slide 12: Technical Readiness Levels
The NFIE is a research effort
It will not create an operational system
It will not produce public forecast information
NFIE
http://en.wikipedia.org/wiki/Technology_readiness_level

## Slide 13: NFIE Conceptual Framework…
NFIE-Services: Web services for flood information
NFIE-Geo: National geospatial framework for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Wide area planning for flood emergency response

## Slide 14: NFIE Continental scale…
NFIE-Services: Web services for flood information
NFIE-Geo: National geospatial framework for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Wide area planning for flood emergency response

## Slide 15: NHDPlus Version 2
National Elevation Dataset
National Hydrography Dataset
National Land Cover Dataset
Watershed Boundary Dataset
NHDPlus
Geospatial foundation for a national water data infrastructure
2.67 million reach catchments in US
average area 3 km2
reach length 2 km

## Slide 16: Open Water Data Initiative
Subcommittee on Spatial Water Data leads this effort
Al Rea (USGS) and Ed Clark (NWS) are co-chairs
This reports to both FGDC and ACWI
Sponsoring a series of “experiments” with water information services
NFIE is one of these experiments
Chair
Anne Castle, Former Asst Secretary for Water and Science, Dept of Interior

## Slide 17: NFIE-Geo for National Flood Interoperability Experiment
Enhanced geospatial database for a national water data infrastructure
NWS Basins and
Forecast Points
USGS Water Watch
Points
National Flood
Hazard Layer
NHDPlus
Feature classes:
Subwatershed (HUC12) Catchment
Flowline
Waterbody Dam
NFIE-Geo
9 feature classes
5 from NHDPlus
4 from IWRSS

## Slide 18: NFIE-Geo in HydroShare
https://www.arcgis.com/home/webmap/viewer.html?webmap=2c30160429984a59873f26b9d118dbfe
David Tarboton, Utah State Univ
and Ray Idaszak, RENCI

## Slide 19: Mobile-Alabama River System
Mobile Bay
Black Warrior River
TombigbeeRiver
Alabama River
Mobile River
Coosa River
Cahaba River

## Slide 20: Tuscaloosa County
Black Warrior River

## Slide 21: NFIE-Geo for a county….
http://www.caee.utexas.edu/prof/maidment/CE397Flood/Assignment2/NFIEGeo.pdf
County subset of national geospatial data layers

## Slide 22: NFIE-Geo around University of Alabama Campus
Black Warrior River

## Slide 23: Catchment 18228725

## Slide 24: Geo to Hydro…
High spatial resolution hydrologic modeling at continental scale
Built upon NFIE-Geo: A national geospatial framework for hydrology
  Continental landscape divided into 2.67 million local catchments, each containing a single stream reach
  Stream reaches connect to form a national stream network
2.67 million catchments
Average area 3 km2
Average reach length 2 km

## Slide 25: Flood risk zones…
Each catchment has a flood hazard zone defined from FEMA flood data
Probabilistic forecast from NFIE-Hydro defines flood risk
Color the zones according to risk

## Slide 26: NFIE-Hydro Forecasting Model…
Runoff
Streamflow
RAPID flow routing (for continental US)
Probabilistic flood forecasts
Weather model and forecasts (HRRR)
Land-Atmosphere Model (WRF-Hydro)
Precipitation
Weather
Catchment-level forecasts

## Slide 27: Soil Moisture Percentile Map
http://statsnldas.azurewebsites.net/
Current value expressed as a percentile based on historical data [1979 to present] on this calendar day at this spatial point
Compare present soil moisture with past conditions

## Slide 28: NFIE-Hydro Workflow
Implemented in Microsoft Azure

## Slide 29: Tethys Application ….
http://demo.tethys.ci-water.org/
Brigham Young University
Catchment
18228725

## Slide 30: NFIE Regional and Local scale…
NFIE-Services: Web services for flood information
NFIE-Geo: National geospatial framework for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Wide area planning for flood emergency response

## Slide 31: NFIE-River…
NFIE-River: Dynamic flood modeling, forecasting and inundation mapping in space and time
Requires LIDAR terrain data so can only be done for particular regions
Iowa Flood Information System

## Slide 32: CrossSections on Lower Mississippi River
173 cross-sections over 543 km, or 3.1 km between cross-sections, on average
41,479 cross-section points (x,y,z) of bed elevation, or 240 points per cross-section, on average

## Slide 33: NFIE-Hydro and NFIE-River
Junction
XSIntersect
Tributary inflow
Catchment inflow

## Slide 34: Cross-sections from HEC-RAS models
Travis County
Hayes County
Onion Creek watershed
We need a national repository -- use HydroShare
Map: Xing Zheng
Data Source: City of Austin

## Slide 35
North Carolina Floodplain Mapping Program HEC- RAS Models
  5 Recurrence Intervals: 10, 25, 50, 100, 500
  300,000 cross-sections
  Each cross-section has a rating curve
Slide: Ken Ashe, NCFMP

## Slide 36: Return Period – Discharge – Stage Height – Water Surface Elevation

## Slide 37: Real-Time Flood Inundation Mapping (USGS/NWS)
http://water.weather.gov/ahps2/inundation/inundation_google.php?gage=atit2

## Slide 38: NFIE-River Advances …
River Cross-Sections and Ratings Template
Hydraulic modeling on large rivers
  Mississippi
  Tar Basin (NC)
  Mobile-Alabama
  Iowa ….
River-Coast interaction
SPRNT Modeling for St Venant Equations
(like electricity flow in computer chips)

## Slide 39: Hurricane Ivan, September 2004
The most expensive disaster in the history of Alabama

## Slide 40: Hurricane Ivan as a case study
http://en.wikipedia.org/wiki/Hurricane_Ivan#Alabama

## Slide 41
NWS River Forecast Centers
No River Forecast
Notes: THERE’S A MAJOR GEOGRAPHIC GAP – WE DON’T FORECAST ALONG THE COAST

## Slide 43: Severe Flooding in Mobile during Ivan
Black Warrior River
Case study for river-coastal interaction

## Slide 44: Corps of Engineers Modeling, Mapping and Consequences program
Source: R. Simrall, USACE

## Slide 45
NFIE-Response…

## Slide 46: Flood Emergency Response…
NFIE-Response: Work with the first response community to define flood strategy and tactics
https://www.youtube.com/watch?v=ympaR6YUxiA&feature=youtube

## Slide 47
Actual Rainfall Totals
Onion Creek watershed

## Slide 49
Incident Command Locations
11:30PM, Oct 30
4.25AM, Oct 31
5.50AM, Oct 31
6.00AM, Oct 31

## Slide 51: Address Points -- used for directing emergency response vehicles
All legal residences have an address point
Established when the lot is legally platted and registered with the county

## Slide 52: Address Points and the Flood Hazard Zone
495,000 Address points in the two counties
How many points are in the flood hazard zone?
Where are the high flood risk areas in these counties?
Travis County
Williamson County
Austin, Texas

## Slide 53: Address Points and the Floodplain

## Slide 54: Intersection of Streams and Roads
Both datasets at 24K resolution
5517 intersection points in Travis and Williamson Counties
Data: Xing Zheng

## Slide 55: Tuscaloosa as a case study for local flood emergency response
Start with NFIE-Geo for Tuscaloosa County
Wide Area Flood Planning
Interact with local emergency response community
Real-time flood mapping and response

## Slide 56: Transformative for the nation…
Forecasts produced by
  Current system – 3600 locations
  NFIE system – 2.67 million locations
New Information to help emergency managers save lives and keep people safe
700 times more
Current
Proposed

## Slide 57: Flood Emergency Response…
NFIE-Response: Work with the first response community to define flood strategy and tactics
https://www.youtube.com/watch?v=ympaR6YUxiA&feature=youtube