## Slide 1
David R. Maidment
Center for Research in Water Resources
University of Texas at Austin
Water Summer, Open Geospatial Consortium Technical Committee Meeting
Boulder, CO| 3 June 2015
Acknowledgements: David Arctur, Ed Clark, Fernando Salas, Marcelo Somos Valenzuela,
Andy Ernest, Sagy Cohen, Sarah Praskievicz, David Gochis, Kristin Tolle, Cedric David
National Flood Interoperability Experiment

## Slide 2: National Flood Interoperability Experiment
The Bad News ….
The Good News ….
Where do we go from here?

## Slide 3: National Flood Interoperability Experiment
The Bad News ….
The Good News ….
Where do we go from here?

## Slide 4: Flood Disaster in Texas
Enough rain to cover entire state in 8” of water
70 Texas counties declared flood disaster areas by the state
23 flood deaths, other people are still missing
Swift water rescue

## Slide 5
Storm Rainfall during last week ….
Sunday, Midnight
Monday, 6AM
Monday, noon
Monday, 6PM
Monday,Midnight
Tuesday 6 AM
Tuesday, noon
Tuesday, 6 PM
Tuesday, Midnight
Wednesday, 6 AM
Wednesday, noon
Wednesday, 6 PM
Wednesday, Midnight
Thursday, 6 AM
Thursday, noon
Thursday, 6 PM
Thursday, Midnight
Friday, 6 AM
Friday, noon
Friday, 6 PM
Friday, midnight
http://gis.ncdc.noaa.gov/map/viewer/#app=cdo&cfg=radar&theme=radar&display=nexrad
Saturday, 6 AM
Saturday, noon
Saturday, 6 PM
Saturday, Midnight
Sunday, 6 AM
Sunday, noon
Sunday, 6 PM
Sunday, Midnight
Monday, 6 AM
Where are the corresponding flood maps on the ground?

## Slide 6: Drought to Deluge!
Reservoir storage doubled in last 10 days
Lake Travis near Austin, Texas, has been in drought for the last four years
How can this happen?

## Slide 10: Incident Command Locations
11:30PM, Oct 30
4.25AM, Oct 31
5.50AM, Oct 31
6.00AM, Oct 31

## Slide 11: National Flood Interoperability Experiment
The Bad News ….
The Good News ….
Where do we go from here?

## Slide 12
Transforming the
National Weather Service’s Water Services
Edward Clark
National Weather Service, NOAA
Notes: OUTLINE:
NEW MISSION FOCUS
TECHNICAL APPROACH
SCALE IMPLICATIONS
NATIONAL WATER CENTER (Organization, Functions, Staffing, Initial Activities, Design Tour)
SUMMARY

## Slide 13: National Academy of Sciences Report Weather Services for the Nation: Second to None
Three inter-related issues:
  inadequate state of NWS hydrologic science
  inefficient function and structure of the NWS’s hydrologic forecasting operations, and
  lack of expertise, skills and training needed to support a modern hydrologic program
Recommendations:
  Improve pathways to accelerate research to operations
  Improve RFC operational workflow to reflect state of the art science
  Implement consistent framework to assess hydrologic prediction skill
  National Water Center test-bed for hydrologic prediction
  Enhance core competencies of hydrologic workforce
Assessment of the NWS Hydrology Program
Notes: NAS IS TELLING US WE NEED TO CHANGE

## Slide 14: NWS River Forecast Centers (RFCs)
  Prepare river and flood forecasts using models based on average basin characteristics
  Provide forecast guidance to Weather Forecast Offices (WFOs)
  Issue daily stage and streamflow forecasts, rainfall and drought data and information, and flash flood guidance
  Work with water managers and other Federal Agencies
14
Notes: RFC Summary

## Slide 15
NWS River Forecast Centers
No River Forecast
Notes: THERE’S A MAJOR GEOGRAPHIC GAP – WE DON’T FORECAST ALONG THE COAST

## Slide 16
NWS River Forecast Centers
Seattle
San
Francisco
Los Angeles
Houston
New Orleans
Jacksonville
Savannah
Charleston
Washington
Baltimore
New York
City
Boston
12 Coastal Cities: 20 Million People
Notes:   >50% of U.S. population live within 50 miles of the coast
  60% of GDP generated in coastal counties
  Aging infrastructure, expensive to upgrade/replace
  Rise in LOSSES of at least $1B insured damages per event
  Runoff from land-falling rain often a major contribution to coastal inundation

## Slide 17
FY15 Centralized Water Forecasting
Centralized Data Archive – all RFC data
Modeling Evaluation Service
  RFC and NWC modeling and forecasts
Modeling Testbed – new NWC capabilities
Centralized Water Forecasting Demonstration
National Water Center
Notes: TRANSITION INTO METHODS
FY15 PROJECT HAS FOUR CORE COMPONENTS
RFC archive
Model evaluation service
Modeling testbed
Centralized modeling demonstration

## Slide 18: Stakeholder Priorities
Flooding
Water Quality
Water Availability
Drought
Climate Change
Need integrated understanding of near- and long-term outlook and risks
Actionable Water Intelligence
Notes: The message was loud and clear:
  While flooding remains a high priority, most stakeholders are concerned about the full gamut of water
  They need more, and better integrated water prediction information
  They need actionable WATER INTELLIGENCE
<< CLICK ONCE TO REVEAL LIST >>

## Slide 19: WATER PREDICTION (NHD Plus) + GeoINTELLIGENCE
“Street Level” Water Prediction and
Impact-Based Decision Support

## Slide 20: Hydrography, AHPS Forecast Points

## Slide 21: Hydrography, AHPS Forecast Points
1000 km
ABRFC
MBRFC
LMRFC
NCRFC
OHRFC

## Slide 22: NATIONAL INFRASTRUCTURE Hospitals, EMS & Fire Stations Full Resolution National Hydrography Dataset NHD+
AHPS Forecast Point
James River at Galena, MO
150 km
Springfield, MO

## Slide 23: NATIONAL INFRASTRUCTURE Hospitals, EMS & Fire Stations
18 km
Ward Branch
Workman Branch

## Slide 24: NATIONAL INFRASTRUCTURE Emergency Services
HOSPITALS
PHARMACIES
EMS STATIONS
FIRE STATIONS

## Slide 25: NATIONAL INFRASTRUCTURE Electric Power Grid

## Slide 26: NWS Water Prediction
TOMORROW
Approximately 6000 forecast locations at points
Driven by large catchment “lumped” modeling
Requires:
  Precipitation and Air Temperature (averaged over watershed)
  Reservoir Information
  River Network Topology
  Hydraulic modeling for large channels
  Stream Gage Data
  General Impacts near Gages
  Local servers and storage
TODAY
Approximately 2,700,000 forecast stream reaches
Driven by high/hyper resolution Earth System modeling
Requires:
  Full high-resolution meteorological suite
  Reservoir Information
  Stream Network Topology
  Hydraulic modeling for small channels
  High Resolution Terrain Data
  Land Cover Change Data
  Stream Gage Data (enhanced)
  Reach-based Inundation Mapping and Impacts
  Centralized high-performance computing
Notes: Comparison of today and tomorrow – orders of magnitude more ‘complex’ prediction paradigm – mainly in data density

## Slide 27
Transforming the
National Weather Service’s Water Services
Edward Clark
National Weather Service, NOAA
End of Slides by Edward Clark
Notes: OUTLINE:
NEW MISSION FOCUS
TECHNICAL APPROACH
SCALE IMPLICATIONS
NATIONAL WATER CENTER (Organization, Functions, Staffing, Initial Activities, Design Tour)
SUMMARY

## Slide 28: President’s Climate Data Initiative
John Podesta, Counsellor to the President, White House, March 19, 2014
https://www.youtube.com/watch?v=pfe5oRdsCp0&feature=youtu.be&t=7s

## Slide 29: Open Water Data Initiative
Subcommittee on Spatial Water Data leads this effort
This reports to both FGDC and ACWI
Sponsoring a series of “experiments” with water information services
National Flood Interoperability Experiment
Chair
Anne Castle, Former Asst Secretary for Water and Science, Dept of Interior

## Slide 30: Water Observation – In Situ
Water Quantity
Rainfall
Soil Water
Water Quality
Meteorology
Groundwater
Time series data at point locations

## Slide 31
www.cuahsi.org
Consortium of Universities for the Advancement of Hydrologic Science, Inc.
CUAHSI
A consortium representing 125 US universities
Dr. Richard Hooper, President and CEO
Building an academic prototype system
Supported by the National Science Foundation Earth Science Division
Advances hydrologic science in nation’s universities
Includes a Hydrologic Information System project
Invented WaterML language for water resources time series

## Slide 32: WaterML Web Services – CUAHSI, USGS, OGC, WMO …..
Water time series data on the internet
24/7/365 service
For daily and real-time data
. . . Operational water web services system for the United States
http://waterservices.usgs.gov/nwis/iv/?format=waterml,2.0&sites=08158000&period=P1D&parameterCd=00060

## Slide 33: Web Pages and Web Services
Web pages deliver text and images
http://water.usgs.gov
Web services deliver data encoded in XML
http://waterservices.usgs.gov/

## Slide 34: NWISWeb and NWIS Water Services
Water Service Requests
Web Page Requests
Requests per month

## Slide 35: WaterML – an international standard for time series
2005
2007
2009
2011
2015
November 2009
CUAHSI Hydrologic Information System project
starts working on WaterML
Technical Meetings Each 3 Months Four Interoperability Experiments
(Surface water, groundwater, forecasting)
Annual week-long workshops
Involvement by many countries
Acknowledgements: OGC, WMO, GRDC, CUAHSI, BoM/CSIRO, USGS, GSC, Kisters, …….
2013
TimeSeriesML being
processed for adoption
by OGC and WMO for all
forms of time series
USGS adopts
WaterML
Adopted and endorsed by
Executive Office of the President
Notes: (1) A four-year international effort has been undertaken to reconcile WaterML with international standards;
(2) This effort was initiated with the establishment of an Hydrology Domain Working Group by the Open Geospatial Consortium in September 2008;
(3) An OGC representative attended the WMO Congress of the Commission for Hydrology in 2008
(4) A formal agreement between Secretary General of WMO and President of OGC in 2009 to jointly develop standards for hydrology, climatology, oceanography and climatology;
(5) The joint OGC/WMO Hydrology Domain Working Group was supported by a large work effort, annual week-long workshops, four interoperability experiments for surface and groundwater data exchange, and participation by many countries;
(6) In June 2012, the OGC voted to adopt the revised version, WaterML2 as an international standard for exchange of water resources time series (the first such public standard that has existed);
(7) This Congress to the WMO Commission for Hydrology to whom I am speaking is considering WaterML2 for adoption as an official standard by WMO

## Slide 36: National Flood Interoperability Experiment
The Bad News ….
The Good News ….
Where do we go from here?

## Slide 37
Inaugural Meeting – May, 2014

## Slide 38: Transformative Research (NSF)
Transformative research involves ideas, discoveries, or tools that radically change our understanding of an important existing scientific or engineering concept or educational practice or leads to the creation of a new paradigm or field of science, engineering, or education. Such research challenges current understanding or provides pathways to new frontiers.
http://www.nsf.gov/about/transformative_research/definition.jsp
How to move from evolutionary change
to transformative change?

## Slide 39: Partnership with the academic community (Interagency Agreement between NSF and NOAA)
National Weather Service has joined with CUAHSI to conduct a one-year National Flood Interoperability Experiment (NFIE)
Includes a Summer Institute for students and faculty at the National Water Center, June 1 to July 17, 2015

## Slide 40: NFIE Summer Institute
Runs from June 1 to July 17
  Kickoff Event, week of June 1
  Capstone conference July 15-17
46 graduate students and post-docs from 19 Universities: Alabama, Texas (Arlington, Austin), Utah State, SUNY Syracuse, BYU, Colorado (Boulder), Illinois (Urbana-Champaign), Purdue, Oklahoma, Iowa, Michigan State, Arizona, Alaska (Fairbanks), Tufts, Sweden, China, Korea, Netherlands

## Slide 41: Goal of the Experiment …
Close the gap between National Flood Forecasting and Local Emergency Response
Demonstrate forecasting of flood impacts at “stream and street level”
National
Local
Weather and Hydrology
National Weather Service and federal agencies
National Water Center
River Flooding and Emergency Response
Local, State and Regional Agencies
Citizens

## Slide 42: Technical Readiness Levels
The NFIE is a research effort
It will not create an operational system
It will not produce public forecast information
NFIE
http://en.wikipedia.org/wiki/Technology_readiness_level

## Slide 43: NFIE Conceptual Framework…
NFIE-Services: Web services for flood information
NFIE-Geo: National geospatial framework for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Wide area planning for flood emergency response

## Slide 44: NFIE Continental scale…
NFIE-Services: Web services for flood information
NFIE-Geo: National geospatial framework for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Wide area planning for flood emergency response

## Slide 45: NHDPlus Version 2
National Elevation Dataset
National Hydrography Dataset
National Land Cover Dataset
Watershed Boundary Dataset
NHDPlus
Geospatial foundation for a national water data infrastructure
2.67 million reach catchments in US
average area 3 km2
reach length 2 km

## Slide 46: NFIE-Geo for National Flood Interoperability Experiment
Enhanced geospatial database for a national water data infrastructure
NWS Basins and
Forecast Points
USGS Water Watch
Points
National Flood
Hazard Layer
NHDPlus
Feature classes:
Subwatershed (HUC12) Catchment
Flowline
Waterbody Streamgage
NFIE-Geo
9 feature classes
5 from NHDPlus
4 from IWRSS

## Slide 47: NFIE-Geo in HydroShare
https://www.arcgis.com/home/webmap/viewer.html?webmap=2c30160429984a59873f26b9d118dbfe
David Tarboton, Utah State Univ
and Ray Idaszak, RENCI

## Slide 48: NFIE-Geo for Mobile-Alabama River System
Mobile Bay
Black Warrior River
TombigbeeRiver
Alabama River
Mobile River
Coosa River
Cahaba River

## Slide 49: Tuscaloosa County
Black Warrior River

## Slide 50: NFIE-Geo for a county….
http://www.caee.utexas.edu/prof/maidment/CE397Flood/Assignment2/NFIEGeo.pdf
County subset of national geospatial data layers

## Slide 51: NFIE-Geo around University of Alabama Campus
Black Warrior River

## Slide 52: Catchment 18228725

## Slide 53: Geo to Hydro…
High spatial resolution hydrologic modeling at continental scale
Built upon NFIE-Geo: A national geospatial framework for hydrology
  Continental landscape divided into 2.67 million local catchments, each containing a single stream reach
  Stream reaches connect to form a national stream network
2.67 million catchments
Average area 3 km2
Average reach length 2 km

## Slide 54: NFIE-Hydro Forecasting Model
Runoff
Streamflow
RAPID flow routing (for continental US)
Probabilistic flood forecasts
Weather model and forecasts (HRRR)
Land-Atmosphere Model (NOAH-MP)
Precipitation
Weather
Catchment-level forecasts
Computed for the continental US in 10 minutes at Texas Advanced Computing Center

## Slide 55: Flood risk zones…
Each catchment has a flood hazard zone defined from FEMA flood data
Probabilistic forecast from NFIE-Hydro defines flood risk
Color the zones according to risk

## Slide 56: Tethys Application …. ECMWF-RAPID
http://demo.tethys.ci-water.org/apps/erfp-tool/
Brigham Young University
Catchment
18228725

## Slide 57: NFIE-Hydro Workflow
Implemented in Microsoft Azure

## Slide 58: Soil Moisture Percentile Map
http://statsnldas.azurewebsites.net/
Current value expressed as a percentile based on historical data [1979 to present] on this calendar day at this spatial point
Compare present soil moisture with past conditions
Slide: Gonzalo Espinoza

## Slide 59: NFIE Regional and Local scale…
NFIE-Services: Web services for flood information
NFIE-Geo: National geospatial framework for hydrology
NFIE-Hydro: National high spatial resolution hydrologic forecasting
NFIE-River: River channel information and real-time flood inundation mapping
NFIE-Response: Wide area planning for flood emergency response

## Slide 60: NFIE-River…
NFIE-River: Dynamic flood modeling, forecasting and inundation mapping in space and time
Requires LIDAR terrain data so can only be done for particular regions
Iowa Flood Information System

## Slide 61: Case Study: North Carolina Cross Section Dataset 17637 Cross Sections
Slide: Xing Zheng

## Slide 62: Return Period – Discharge – Stage Height – Water Surface Elevation

## Slide 63: Real-Time Flood Inundation Mapping (USGS/NWS)
http://water.weather.gov/ahps2/inundation/inundation_google.php?gage=atit2

## Slide 64: NWS River Forecast Centers
No River Forecast
Notes: THERE’S A MAJOR GEOGRAPHIC GAP – WE DON’T FORECAST ALONG THE COAST

## Slide 66: Hurricane Ivan, September 2004
The most expensive disaster in the history of Alabama

## Slide 67: Hurricane Ivan as a case study
http://en.wikipedia.org/wiki/Hurricane_Ivan#Alabama

## Slide 68: Severe Flooding in Mobile during Ivan
Black Warrior River
Case study for river-coastal interaction

## Slide 69: NFIE-Response

## Slide 70: Address Points -- used for directing emergency response vehicles
All legal residences have an address point
Established when the lot is legally platted and registered with the county

## Slide 71: Address Points and the Flood Hazard Zone
495,000 Address points in the two counties
How many points are in the flood hazard zone?
Where are the high flood risk areas in these counties?
Travis County
Williamson County
Austin, Texas

## Slide 72: Address Points and the Floodplain

## Slide 73: Transformative for the nation
Forecasts produced by
  Current system – 3600 locations
  NFIE system – 2.67 million locations
New Information to help emergency managers save lives and keep people safe
700 times more
Current
Proposed in NFIE

## Slide 74: Connecting with Local Decision Makers
Work with the first response community to define flood strategy and tactics
https://www.youtube.com/watch?v=ympaR6YUxiA&feature=youtube