## Slide 1: Wide Area Flood Plan
By David R. Maidment Center for Research in Water Resources University of Texas at Austin
Presented to the Texas Flash Flood Coalition University of Texas 12 November 2014
This presentation has been edited from the form in which it was originally given

## Slide 2: Wide Area Flood Plan
A Wide Area Flood Plan enhances flood emergency response for communities
Linked to new flood forecast procedures being developed at the National Water Center in the National Flood Interoperability Experiment
Develop this plan for Travis and Williamson Counties in one year
Engage the Texas Flash Flood Coalition to guide the development of the effort
Have quarterly meetings of the TFFC to review progress and provide feedback
Use the discussion at this meeting to set the direction and identify leadership from the community

## Slide 3: Why – People
On average, more people die annually from flooding than from any other form of natural disaster
Spatial Distribution of Flood Fatalities 2007-2013 (source: NWS StormDat)
Low water crossing
84

## Slide 4
Located on Tuscaloosa Campus of University of Alabama
Operated by National Weather Service to support IWRSS partners (NWS, USGS, Corps of Engineers, FEMA)

## Slide 5
Inaugural Meeting – May, 2014

## Slide 6: NWS River Forecast Centers
Perform precipitation, runoff and river flow simulation and forecasting for five days ahead, updated daily, more frequently during floods

## Slide 7: Nationally Synthesize Operations of Regional River Forecast Centers

## Slide 8
Open Water Data Infrastructure
Temporal information
Geospatial information

## Slide 9: Goals National Flood Interoperability Experiment
Close the gap between national flood forecasting and local emergency response
  Impact at the street level
Create real-time flood information services
  Shared among organizations, geographies, people
Engage academic community through the National Water Center
  Innovation for transformative change

## Slide 10: Linkages among federal agencies for flood response
Atmosphere
Stream
Street
Data

## Slide 11: President’s Climate Data Initiative
John Podesta, Counsellor to the President, White House, March 19, 2014
https://www.youtube.com/watch?v=pfe5oRdsCp0&feature=youtu.be&t=7s

## Slide 12: Goals of Climate Data Initiative
Prepare for climate change
Make government data accessible
Engage private sector
  ESRI, Microsoft, Google, Intel ….
Engage communities
  Chesapeake, New Orleans, World Bank, …
Why not a Water Data Initiative?

## Slide 13: Open Water Data Initiative
Subcommittee on Spatial Water Data will lead this effort
This reports to both FGDC and ACWI
Chair
Anne Castle, Asst Secretary for Water and Science, Dept of Interior

## Slide 14: Open Water Data Initiative
Open Water Web (applications)
Water
Pollution
Ecological
Integrity
Drought
Flood
National Water
Data Infrastructure
Concept: Nate Booth, USGS

## Slide 15: National Water Data Infrastructure (NWDI)
A thematically organized set of water information data layers
Authoritative for the nation
Assembled from best available sources
Made freely available through water information services.

## Slide 16: Hydrologic Measurement
Water Quantity
Rainfall
Soil Water
Water Quality
Meteorology
Groundwater
Time series data at point locations

## Slide 17
www.cuahsi.org
Consortium of Universities for the Advancement of Hydrologic Science, Inc.
CUAHSI
A consortium representing 125 US universities
Dr. Richard Hooper, President and CEO
Designed the WaterML language
Supported by the National Science Foundation Earth Science Division
Advances hydrologic science in nation’s universities
Includes a Hydrologic Information System project

## Slide 18: WaterML Web Services – CUAHSI, USGS, OGC, WMO …..
Water time series data on the internet
24/7/365 service
For daily and real-time data
. . . Operational water web services system for the United States
http://waterservices.usgs.gov/nwis/iv/?format=waterml,2.0&sites=08158000&period=P1D&parameterCd=00060

## Slide 19: Water Data Distribution by US Geological Survey
Web page requests (millions/month)
Web service requests (millions/month)

## Slide 20: Goals National Flood Interoperability Experiment
Close the gap between national flood forecasting and local emergency response
  Impact at the street level
Create real-time flood information services
  Shared among organizations, geographies, people
Engage academic community through the National Water Center
  Innovation for transformative change

## Slide 21: NHDPlus Geospatial base for National Water Data Infrastructure
National Elevation Dataset
National Hydrography Dataset
National Land Cover Dataset
Watershed Boundary Dataset
NHDPlus
3 million catchments average area 3 km2,
reach length 2 km
(built 2004-2014)

## Slide 22: Spatial Coverage of NFIE-Hydro Built on top of the NHDPlus
2.67 million catchments, average area 3 km2, average length 2 km

## Slide 23: Modelling the terrestrial water cycle
Atmosphere
Observation datasets and numerical weather models
Precipitation, temperature, solar radiation etc.
Land Surface
Remote sensing and land surface models
Evaporation, soil moisture, surface runoff etc.
Rivers
Lidar, surveys and river routing models
Streamflow, water level, fish etc.

## Slide 24: Why – Technology
Build a national high spatial resolution, near real-time river and stream model
Like this but for whole continental US
Build on NHDPlus
(from EPA and USGS)
using RAPID river model
Link to current
NWS River Forecasts
Use Weather Research and Forecasting Hydro model (WRF-Hydro)
(from NCAR)
Source: http://rapid-hub.org/
River flow in the Mississippi River Basin

## Slide 25
RAPID River Routing Model
River Application for Parallel ComputatIon of Discharge
Sprism = KQ
Swedge = KX (I – Q)
Muskingum
Method
Flow
Legend
Dam
Junction
Catchment
Computational Unit for Rivers
Forcing: Runoff and reservoir releases

## Slide 26: NWS Forecast Services
Web services provide data in csv, ascii, WaterML etc.
KEMT2
JOCT2
http://wwokiweb01.cloudapp.net:8080/KiWIS/KiWIS?datasource=0&service=kisters&type=queryServices&request=getTimeseriesValues&format=ascii&ts_id=62806042&period=p5d&metadata=true&md_returnfields=station_no,ts_id
Surface runoff in
mm per unit area

## Slide 27: Dynamic Downscaling of NWS Forecasts NWS Forecast Basin to NHDPlus Catchment
NWS River Forecast Centers
Forecast Subbasins for
West Gulf River Forecast Center
NWS Forecast
Subbasin ATIT2
NHDPlus
Catchments
Azure
Wiski

## Slide 28: NWS West Gulf Region
COMID
5557990
COMID
5586778
Web services provide data in csv, ascii, WaterML etc.
http://wwokiweb01.cloudapp.net:8080/KiWIS/KiWIS?datasource=0&service=kisters&type=queryServices&request=getTimeseriesValues&format=ascii&ts_id=58261042&period=p10d&metadata=true&md_returnfields=station_no,ts_id
Streamflow in cfs

## Slide 29: West Gulf River Flow Animation World Wide Telescope

## Slide 30
Flood Water Elevation
Time
Ensemble Flood
Forecasting

## Slide 31: Percentile Maps of Soil Moisture
http://texassoilmoisture.azurewebsites.net/

## Slide 32: HUC-10 Watersheds and Rivers in Travis and Williamson Counties
San Gabriel River
Brushy Creek
Colorado River
Onion Creek
Barton Creek
Pedernales River

## Slide 33: City Jurisdiction
Austin

## Slide 34: 100-year floodplain for Travis and Williamson Counties
13% ( > 1/8) of the land is in the 100-year floodplain

## Slide 35: HUC-10 Watersheds for City of Austin-Colorado River
19 Watersheds: Prioritize and Rank in Order of Importance

## Slide 36: HUC-12 Subwatersheds in City of Austin-Colorado River HUC-10
Use these Units for Wide Area Flood Planning

## Slide 37: Eanes Creek Model
Upstream
Downstream
Slide:
Tomas Rodriguez
City of Austin

## Slide 38
CAD Report Rcvd 02:11
75 m2 Model Resolution
Slide:
Tomas Rodriguez
City of Austin
Eanes Creek Model

## Slide 39: NHDPlus Catchments in Lake Austin-Town Lake HUC12 Subwatershed
Flood forecasting operates at this level. Each catchment has one stream reach.
A flow forecast is made for that stream reach

## Slide 40: Eanes Creek – Flood Response Mapping and Planning
Catchment 5781289

## Slide 41: Eanes Creek Floodplain
Identify buildings at flood risk

## Slide 42: Eanes Creek Transportation
Bee Cave Rd (FM 2244)
Identify streets with flood risk

## Slide 43: Eanes Creek Jurisdiction
West Lake Hills
Rollingwood
Austin
Austin

## Slide 44: Cells of US National Grid
5596 cells
Each 1km x 1km

## Slide 45: US National Grid Cells in Eanes Creek

## Slide 46: NHDPlus Catchments in Travis and Williamson Counties
1020 Catchments and Stream Reaches
Dry Creek

## Slide 47: How to connect gridded input runoff data (WRFHydro) to NHDplus network
209

## Slide 48: Upper Brushy Creek Water Control & Improvement District
Ruth Haberman, General Manager, UBCWCID

## Slide 49: JURISDICTIONAL BOUNDARIES

## Slide 50
DRAINAGE AREAS

## Slide 51: Upper Brushy Flood Geodatabase

## Slide 52: Upper Brushy Flood Geodatabase
Subwatersheds

## Slide 53: Upper Brushy Flood Geodatabase
Floodplain

## Slide 54: Upper Brushy Flood Geodatabase
FlowLines

## Slide 55: Upper Brushy Flood Geodatabase
Catchments

## Slide 56: Upper Brushy Flood Geodatabase
Each Catchment has one FlowLine
This identifier, 5671589,
is unique for the whole United States
There are 2.6 million of these catchments
3.62 km
6.23 km2

## Slide 57: Upper Brushy Flood Geodatabase
US National Grid

## Slide 58: Upper Brushy Flood Geodatabase
Transportation

## Slide 59: Upper Brushy Flood Geodatabase
Address Points

## Slide 60: Upper Brushy Flood Geodatabase
A National Grid Cell

## Slide 61: National Grid Cells and Catchments
Cells are 1x1 km, hence smaller than catchments.
Clip floodplain so that there is a piece in each cell

## Slide 62: 4km mesh for WRF-Hydro
USGS Water Resource Region 12
Austin watershed region

## Slide 63: Case Study
RAPID Model is built for all the NHDPlus reaches in Travis and Williamson County. The simulation results are published on the Internet using web service
Travis
Williamson
http://wwokiweb01.cloudapp.net:8080/KiWIS/KiWIS?service=kisters&type=queryServices&request=getTimeseriesList&datasource=0&format=ascii&&timeseriesgroup_id=146856&returnfields=station_name,parametertype_name,coverage&dateformat=yyyy-MM-dd%20HH:mm:ss

## Slide 64: HEC Software
Data Collection
Database
Modeling
Information dissemination
Data
Visualization
RAS
(Hydraulics)
FIA
(Damages)
ResSim
(Storage)
HMS
(Hydrology)
Modeling

## Slide 65: Current Progress
Workflow for connecting the NFIE with HEC-RAS model in Upper Brushy Creek
NWS Forecasts Data
RAPID Model
Flow data for
every NHD reach
at a 3-hour interval
Web Service
HEC DSS File
HEC-RAS
Flood Inundation Map
Flood Velocity Map
Rating Curve
…

## Slide 66: Unsteady Simulation in HEC-RAS
North Fork of Brushy Creek Tributary1
Geometry Data
Flow Data

## Slide 67: Unsteady Simulation Results using HEC-RAS

## Slide 68: Wide Area Flood Plan
A Wide Area Flood Plan enhances flood emergency response for communities
Linked to new flood forecast procedures being developed at the National Water Center in the National Flood Interoperability Experiment
Develop this plan for Travis and Williamson Counties in one year
Engage the Texas Flash Flood Coalition to guide the development of the effort
Have quarterly meetings of the TFFC to review progress and provide feedback
Use the discussion at this meeting to set the direction and identify leadership from the community