## Slide 1: Delivering on National Water Information Needs
David R. Maidment
Director, Center for Research in Water Resources
University of Texas at Austin
WIRADA Science Symposium
Melbourne, Australia
4 August 2011

## Slide 2: In Memory of Ian Moore, 1951-1993
A pioneer of digital characterization of the landscape for hydrology
Worked at Australian National University and the University of Minnesota
He would have been so happy with WIRADA!
Welcome to Aussie Hydro

## Slide 3: Questions
What is the most exciting trend or opportunity?
How does WIRADA research measure up?
What research or technological breakthrough is required to secure our intended outcomes?
From Greg Ayers: “In looking forward to the remaining two years of the alliance agreement, ….. examine the remaining research challenges and ….. inject fresh ideas and shape research directions”

## Slide 4: The Premise of WIRADA
CSIRO
Bureau of Meteorology
Sound water management is based on sound science and data
Implementation
Requirements
Research and Development
What science foundations are needed to make this structure strong?
Maidment’s First Law of Information System Development:
Anybody can be complicated.
It takes real insight to be simple.

## Slide 5: Our Journey Begins….. Melbourne Cup Day, November 2006
I was in Canberra doing a seminar jointly with Rob Vertessy about geospatial data for water
The Prime Minister met on this day in Canberra with the Premiers of all the States to confront the drought
The country was in crisis
The drought was already severe and its ultimate magnitude and duration were unknown
Action was needed!!!

## Slide 6: What was the state of water knowledge in Australia at that time?
Science – Rich – a real legacy of historical investment in CSIRO, ANU and elsewhere
Modeling – Rich – CRC’s for Catchment Hydrology and eWater, and elsewhere
Information – Limited
  250m DEM
  No consistent digital blue line stream hydrography (ouch!!)
  37 separate stream gaging networks
AWRIS and WIRADA were prompted by these and other deficiencies in information

## Slide 7: River Gage Networks
9079 gages in 37 networks
Average = 245 gages/network

## Slide 8: Some months pass…. then comes (Jan 2007)
http://www.nalwt.gov.au/files/national_plan_for_water_security.pdf
An announcement by the Prime Minister of Australia

## Slide 9
Slide: Rob Vertessy
Australian Water Resources Information System (AWRIS)

## Slide 10
Slide: Rob Vertessy, BoM
Components of AWRIS
Notes: 10
10
AWRIS on a page.

## Slide 11: WIRADA (2008-2013) Water Information Research and Development Alliance
Slide: Rob Vertessy, BoM
CSIRO research program to support the AWRIS development being done by the Bureau of Meteorology

## Slide 12: Three years in ….. What is the state of Water Information now?
Progress has been made in each of these four components
They are very different to one another
The challenge now is how to link them

## Slide 13: Australian National Climate Database
This is a core competency of the BoM
Augment with evaporation derived from remote sensing
Std Dev of 8 methods of estimating evaporation
Image: Albert van Dijk, CSIRO

## Slide 14: Lake Argyll – Remote Sensing as Time Series!
Lake timeseries plus statistics and curve-fiting analysis.
Slide: Philippa Berry, DeMontfort University

## Slide 15: Australian Hydrological Geospatial Fabric
Four key constructs
  Cell to cell water movement on DEMs
  Line to Line water movement on networks
  Area flows to line (connect land and water systems – Reach Catchments)
  Area flows to point on line (Contracted Nodes and Catchments)

## Slide 17: United States Experience with DEM Improvement
Error in delineated watershed area
5%
0.5%
3 arcsec: 90 m
1 arcsec: 30 m
DEM Cell Size
1990’s
2000’s

## Slide 18: National Elevation Dataset for Australia
9 Arc Second – 250 m
1 Arc Second – 30 m
1 cell
81 cells
Existing
New
Two orders of magnitude improvement! Wow!
Images: John Gallant, CSIRO

## Slide 19: National River Network for Australia
Line flows to Line
Geometric Network
Geometry model: Where am I? (x,y coordinates)
Logical model: Who am I connected to? (topology)
Addressing model: Where are things on me? (linear referencing)
Image: Elizabeth McDonald, BoM

## Slide 20: A challenge: those messy Aussie rivers have lots of loops and branches
Image: Michael Hutchinson, ANU

## Slide 21: A fundamental innovation: Connecting the Cell to Cell and Line to Line Models
Flow divergences have multiple flow directions on a single DEM cell
Image and Research: Janet Stein, ANU
Cell flows to Cell

## Slide 22: Reach Catchments Every stream reach has a local drainage area
Area flows to Line
Fundamental connection between the water and land systems
Image: Elizabeth McDonald, BoM

## Slide 23: Contracted Nodes and Catchments
Contracted Nodes
Contracted Catchments
Contracted nodes persist through successive versions of the geofabric
Area flows to a point on a line
A standardized tessellation of the landscape – one chosen among the infinite number of tessellations possible
Images: Elizabeth McDonald, BoM

## Slide 24: AWRA River Reporting Regions
Aggregate contracted catchments to form reporting regions
Images: Elizabeth McDonald, BoM

## Slide 25: Geofabric Summary
I’ve used test versions of these data – they work!
This enables water management to be built on a digital landscape rather than paper maps
Huge implications for all forms of water management in Australia
Large institutional and cultural change required to fully achieve benefits

## Slide 26: Geofabric Recommendation
The Geofabric team has Version 1 out, and Version 2 is due out in a few months
You’ve largely solved the special problems that pertain to Australian conditions
I suggest taking the foot off the gas pedal and stepping back a bit for a “mid-course review”
Ask experienced developers and users of comparable geofabrics from the US, UK, New Zealand …. for their review and input (and vacuum up their free tools!)
The question is not now how best to produce the geofabric, it is how best to use it.

## Slide 27: Hydrologic Models
Long historical experience with catchment hydrology modeling in Australia (CRC for Catchment Hydrology)
AWRIS requires a transition to landscape hydrology modeling
  AWRA-L; AWRA-R, AWRA-G
“I’m in hydrology heaven ……”

## Slide 28
Slide: Neil Viney, CSIRO

## Slide 29: What I was thinking about on the plane
I was asked to address “Delivering on National Water Information Needs”
In hydrology, we’ve always thought of national information as being built up from state and local information
Question: to what degree is national hydrologic modeling informed by global information?
Answer: Yes, for climate drivers

## Slide 30
http://gewex-srb.larc.nasa.gov/
W/m2

## Slide 31
IBM is collaborating with UT….
…. to help build a Smarter Planet

## Slide 32
Solve 100 million equations simultaneously!

## Slide 33
VLSI simulation models for electric circuit design…..
….. model right on top of the river geofabric
3500 reaches

## Slide 34: Assembly of lots and lots of time series from more than 200 organizations
Rain gages
River gages
Evaporation gages
Reservoir levels
Groundwater levels
Water Pumpage
Diversions
A network of networks

## Slide 35
Slide: Brett Anderson, BoM

## Slide 36
Slide: Brett Anderson, BoM

## Slide 37
Slide: Brett Anderson, BoM

## Slide 38
CUAHSI is a consortium representing 125 US universities
Supported by the National Science Foundation Earth Science Division
Advances hydrologic science in nation’s universities
Includes a Hydrologic Information System project
http://www.cuahsi.org

## Slide 39
Rainfall
Water quantity
Meteorology
Soil water
Groundwater
We Collect Lots of Water Data
Water quality

## Slide 40: The Data have a Common Structure
A point location in space
A series of values in time
Gaging – regular time series
Sampling – irregular time series
Notes: These data are recorded over time to monitor a hydrologic process or property.

## Slide 41
The Data are Collected by Many Organizations
…. and the data are continuously accumulating
Federal Agencies
State Agencies
Cities
River Authorities
Water Districts
Universities

## Slide 42: How the web works
Catalog (Google)
Web Server
(CNN.com)
Browser
(Firefox)
Access
Catalog harvest
Search
HTML – web language for text and pictures

## Slide 43: Services-Oriented Architecture for Water Data
Catalog
Server
User
Data access
Service registration
Search
Catalog harvest
WaterML – web language for water data

## Slide 44: Some terms and definitions
Web Service: A web service allows for information to be exchanged computer-to-computer over the internet
Portal: A one-stop shop that pulls together information from various sources and provides it to the user in a seamless fashion using a web site
Catalog: Like a library card-catalog, these provide summary level information on what data are available at the various sources
Exchange Schema: An agreed-upon data sharing format via which data owners publish data (e.g. WaterML)
Source: Dwane Young, Western States Water Council
Notes: In order to understand what I’d talk about, these are some basic terms that need to be defined. The key term that needs to be understood is the idea of a web service. The best way to describe a web service is to relate it to something that they may already be familiar with. The best example I’ve been able to come up with is describing the ‘Weather Bug’ web service. A lot of people have interacted with this type of service. They have a little application that’s running on their computer that required a ‘Input parameter’, in this case a zip code. The application uses that to query another computer out on the internet. That computer returns to your computer a file that has all the information about the weather for your zip code. The application reads that file and turns it into a nice little icon that says that it’s raining and 42 degrees. The user never needs to know that this application is going out there and doing this, and doesn’t need to re-enter their information or interact with a web site or anything. It all happens in the back-ground as computer-to-computer communication.

## Slide 45: What is a “services-oriented architecture”? Networks of computers connected through the web …….
Everything is a service
  Data, models, visualization, ……
A service receives requests and provides responses using web standards (WSDL)
It uses customized web languages
  HTML (HyperText Markup Language) for text and pictures
  WaterML for water time series (CUAHSI/OGC)
  GML for geospatial coverages (OGC)
….. supporting a wide range of users

## Slide 46: WaterML as a Web Language
Discharge of the San Marcos River at Luling, TX June 28 - July 18, 2002
USGS Streamflow data in WaterML language
The USGS now publishes its time series data as WaterML web services

## Slide 47: Colorado River at Austin
http://waterservices.usgs.gov/nwis/iv?sites=08158000&period=P7D&parameterCd=00060
I accessed this WaterML service from USGS at 3:10AM this morning
And got back these flow data from USGS which are up to 1:45AM Melbourne time (UTC +10:00)
USGS has real-time WaterML services for about 22,000 sites available 24/7/365

## Slide 48: CUAHSI Water Data Services Catalog
69 public services
18,000 variables
1.9 million sites
23 million series
5.1 billion data values
And growing
The largest water data catalog in the world
maintained at the San Diego Supercomputer Center
All the data comes out in WaterML

## Slide 49: Point Observations Information Model
Data Source
Network
Sites
Variables
Values
{Value, Time, Metadata}
Niagara Peninsula Conservation Authority
Water Quality
BA001
Total Phosphorus
0.89 mg/L, 20 April 2009
A data source operates an observation network
A network is a set of observation sites
A site is a point location where one or more variables are measured
A variable is a property describing the flow or quality of water
A value is an observation of a variable at a particular time
A metadata quantity provides additional information about the value
GetSites
GetSiteInfo
GetVariableInfo
GetValues
Information is transmitted through the internet in WaterML as web services

## Slide 50: BoM Rain Gage Network
24,343 rain gages
An observation network
= one web service

## Slide 51: River Gage Networks
9079 gages in 37 networks
Average = 245 gages/network
A network of observation networks
= a collection of web services

## Slide 52: Multisensor Precipitation Estimate (MPE) West Gulf River Forecast Center
Exported by NWS to CUAHSI Observations Data Model and WaterML web services at University of Texas at Arlington
Capital Area Council of Governments (CAPCOG)

## Slide 53: Rainfall in Cypress Creek Watershed Drainage area – 38 Sq. Mi.
“Virtual Rain Gages”— Nexrad Radar Rainfall points
Time Series of Rainfall
Data obtained via WaterML web service from NWS and UT Arlington
A Virtual Observation Network and web services

## Slide 54: HydroDesktop – Desktop HIS
Metadata
Data
Catalog

## Slide 55: Semantic Integration using an Ontology of Concepts
Hydrosphere
Chemical
Physical
Biological
Ontology of Concepts
Nutrients in Florida
EPA SRS
http://his.cuahsi.org/ontologyfiles.html

## Slide 56: Organize Water Data Into “Themes”
Integrating Water Data Services From Multiple Sources
. . . Across Groups of Organizations
WaterML
WaterML
WaterML
WaterML
WaterML

## Slide 57
Streamflow Data Services
2 services
7 variables
4,363 sites
11,484 series
9,493,968 records
Notes: Here’s an example showing where streamflow is measured in Texas from two different services (i.e., data providers).

## Slide 58
Water
Temperature Data Services
6 services
11 variables
11,158 sites
22,953 series
1,546,841 records

## Slide 59
Bacteria Data Services
1 service
21 variables
4,801 sites
15,483 series
297,849 records

## Slide 60: WOFpy
Water One Flow web services in Python
Easy, low cost way to create water web services
Delivers both WaterML1 and WaterML2
https://github.com/swtools/WOFpy

## Slide 61: Open Geospatial Consortium Web Service Standards
Map Services
Web Map Service (WMS)
Web Feature Service (WFS)
Web Coverage Service (WCS)
Catalog Services for the Web (CS/W)
Observation Services
Observations and Measurements Model
Sensor Web Enablement (SWE)
Sensor Observation Service (SOS)

## Slide 62
Meets every 3 months
Teleconferences most weeks
WaterML Version 2 standard proposed
Vote for adoption later this year or early next year
Jointly with World Meteorological Organization
Evolving WaterML into an International Standard
November 2009
Hydrology, Meteorology, Climatology, and Oceanography

## Slide 63: Catalog Services for the Web (CS/W)
An OGC standard for cataloging web services
  Provides a single URL reference point for all services from an organization https://hydroportal.crwr.utexas.edu/geoportal/csw/......
  Enables searching of underlying Web Feature Services using the “who, what, when, where” approach
Select Region (where)
Start
End
Select Time Period
(when)
Select Service(s)
(who)
Filter Results
Save Theme
Select Keyword(s)
(what)

## Slide 64: Web Services Stack for Time Series
Time
Series
Services
OGC Catalog Service for the Web with standard metadata: ISO, Dublin Core, ..
OGC Web Feature Service
Catalog
Metadata
Data
WaterML or OGC WaterML2
Who, What?
Where, When?
Get the data

## Slide 65: Water Agency Service Stacks Each agency maintains its own data and metadata
NWIS
Storet
NCDC
TWDB
State
MetaCatalog is a listing of the URL addresses of all the agency catalogs
All linked via a Metacatalog
Notes: The Federal Government already supports Catalog Services for the Web through Geodata.gov and is moving to Data.Gov and a new initiative called the Geoplatform (requested by OMB in 2011). Cataloging water observations data under this system is a straightforward extension of what is already being done to federate the federal government’s geospatial data layers. State water observations data systems like that coming from the Texas Water Development Board can be federated and searched along with the federal water observations data services

## Slide 66: Searching Federal and State Data
USGS Daily Values
Texas TWDB
Texas Agencies
(Federal)
(State)
A single search accesses federal water data from a catalog at HIS Central ….
…. and state water data from a catalog in Austin, Texas

## Slide 67
Searching Search Federal, State and Local Data

## Slide 68
Slide: Brett Anderson, BoM
Build this on top of a Services-Oriented Architecture

## Slide 69: Bringing it all Together: the Services “Hub”
Progress has been made in each of these four components
They are very different to one another
The challenge now is how to link them

## Slide 70
Slide: Rob Vertessy

## Slide 71: Tropical Storm Hermine, Sept 7-8, 2010

## Slide 72: Local Information during Tropical Storm Hermine (7-8 Sept 2010)
http://hydromet.lcra.org
http://coagis1.ci.austin.tx.us/website/COAViewer_fews/viewer.htm
http://ubcwcid.org/Overview/Overview.aspx?id=1
LCRA
City of Austin
Upper Brushy Creek (Round Rock)
TV
Bring data together into one system

## Slide 73: Situational Awareness for Flash Flooding in the CAPCOG region
Combines federal, river authority, city and water district data ….
…. to support real-time flood emergency response
National Weather Service,
USGS, Corps of Engineers

## Slide 74: Web Services HUB
USGS
LCRA
NWS
COA
AHPS
Web Services HUB
Inputs
Observation
Data
Services
(WaterML)
Channel
Data
Services
(WFS)
Models
Modeling
Services
Data
Services
(WFS)
Mapping
Services
(WFS)
Maps
Outputs
Observation
Data
Services
(WaterML)
Mapping
Services
(WFS)

## Slide 75
Slide: Brett Anderson, BoM
Build this on top of a Services-Oriented Architecture

## Slide 76
Build this on top of a Services-Oriented Architecture
Slide: Rob Vertessy, BoM

## Slide 77
Build this on top of a Services-Oriented Architecture
Slide: Rob Vertessy, BoM

## Slide 78
Slide: Rob Vertessy, BoM
And then you get real-time situational awareness

## Slide 79: Questions and Answers
What is the most exciting trend or opportunity?
  WIRADA has a global impact
How does WIRADA research measure up?
  Excellently – Geofabric, Water Web Services
What research or technological breakthrough is required to secure our intended outcomes?
  A web services hub
From Greg Ayers: “In looking forward to the remaining two years of the alliance agreement, ….. examine the remaining research challenges and ….. inject fresh ideas and shape research directions”