## Slide 1
paola passalacqua
Associate Professor, Department of Civil, Architectural and Environmental Engineering, The University of Texas at Austin
Maidment Symposium
12 May 2022
TOPOGRAPHY, GEOMORPHOLOGY, AND FLOOD MODELING
…with a couple of additional stories

## Slide 2: How it all started…

## Slide 3
Channel initiation
Identification of accurate centerline
Presence of roads and bridges
Artificial drainage ditches
Small signal to noise ratio
Identification of channel banks

## Slide 4: GeoNet: channel extraction from lidar STEP 1: Nonlinear filtering
github.com/passaH2O/GeoNet
Passalacqua et al., JGR-ES, 2010; Perona & Malik, 1990

## Slide 5: GeoNet: channel extraction from lidar STEP 2: Statistical analysis of curvature
github.com/passaH2O/GeoNet
Channel
Road
Ditch
Laplacian
Geometric
Passalacqua et al., WRR, 2012

## Slide 6: We extract all pixels above a curvature threshold to identify the likely channelized pixels
github.com/passaH2O/GeoNet
The point at which the curvature deviates from a Normal distribution in the positive tail is interpreted as the transition from hillslope to valley.

## Slide 7: GeoNet: channel extraction from lidar STEP 3: Channel network extraction
github.com/passaH2O/GeoNet
Passalacqua et al., JGR-ES, 2010
The cost function ψ represents the cost of traveling between point a and point b in terms of, e.g., surface curvature and flow accumulation:
The curve with minimum cost is the geodesic curve:
A
B
Channel head
Basin outlet
Geodesic curve
Channel

## Slide 8
David’s enthusiasm for learning new things
…as the first time we met during my interview

## Slide 9: HAND requires information on channel centerlines
Zheng et al., 2018; Zheng et al., 2022
Normal
Depth
Flood
Depth
HAND
DATUM

## Slide 11: GeoNet could resolve the issues with accuracy of the NHD lines
Zheng et al., 2018; Zheng et al., 2022
NHDPlus
GeoNet centerline

## Slide 12: GeoNet combined with HAND became GeoFlood
Zheng et al., 2018; Zheng et al., 2022
GeoFlood
NHDPlus HR

## Slide 13
David’s view of any challenge as an opportunity
…as that time he walked into my office while I was preparing for my lecture

## Slide 14: Developing and integrating methods for coastal and pluvial flooding in GeoFlood
Wang et al, in preparation
Preisser et al., under review

## Slide 15: Pin2Flood: providing emergency responders with real time inundation mapping
By standing at the edge of the flood water and clicking their position (pin drop) on a web map. The flood maps are looked up from the library. Results include estimated damage impacts using GIS.
Project funded by Texas Division of Emergency Management for:
Mobile application development
Testing
Implementation
Security/maintenance

## Slide 16
Investigation of river hydraulics and improvement of the NWM
Datasphere
Radar sensor data provides information on river hydraulics -> hysteresis
Integrated into NOAA’s National Water Model via Data Assimilation to improve flood forecasting

## Slide 17
David’s ability to have a vision and enable its transformation into operational tools