## Slide 1: CE 394K.2 Precipitation
Precipitation mechanisms
Rainall maps
Rainfall hyetographs
Nexrad measurement of rainfall
Reading: Applied Hydrology Sections 3.5 to 3.6 on Evaporation for Thursday

## Slide 2: Precipitation
Precipitation: water falling from the atmosphere to the earth.
  Rainfall
  Snowfall
  Hail, sleet
Requires lifting of air mass so that it cools and condenses.

## Slide 3: Mechanisms for air lifting
Frontal lifting
Orographic lifting
Convective lifting

## Slide 4: Frontal Lifting
Boundary between air masses with different properties is called a front
Cold front occurs when cold air advances towards warm air
Warm front occurs when warm air overrides cold air
Cold front (produces cumulus cloud)
Cold front (produces stratus cloud)

## Slide 5: Orographic lifting
Orographic uplift occurs when air is forced to rise because of the physical presence of elevated land.

## Slide 6: Convective lifting
Hot earth surface
Convective precipitation occurs when the air near the ground is heated by the earth’s warm surface. This warm air rises, cools and creates precipitation.

## Slide 7: Condensation
Condensation is the change of water vapor into a liquid. For condensation to occur, the air must be at or near saturation in the presence of condensation nuclei.
Condensation nuclei are small particles or aerosol upon which water vapor attaches to initiate condensation. Dust particulates, sea salt, sulfur and nitrogen oxide aerosols serve as common condensation nuclei.
Size of aerosols range from 10-3 to 10 mm.

## Slide 8: Precipitation formation
Lifting cools air masses so moisture condenses
Condensation nuclei
  Aerosols
  water molecules attach
Rising & growing
  0.5 cm/s sufficient to carry 10 mm droplet
  Critical size (~0.1 mm)
  Gravity overcomes and drop falls

## Slide 9: Forces acting on rain drop
Fd
Fd
Fb
Fg
D
Three forces acting on rain drop
  Gravity force due to weight
  Buoyancy force due to displacement of air
  Drag force due to friction with surrounding air

## Slide 10: Terminal Velocity
Terminal velocity: velocity at which the forces acting on the raindrop are in equilibrium.
If released from rest, the raindrop will accelerate until it reaches its terminal velocity
Raindrops are spherical up to a diameter of 1 mm
For tiny drops up to 0.1 mm diameter, the drag force is specified by Stokes law
Fd
Fd
Fb
Fg
D
V
At standard atmospheric pressure (101.3 kpa) and temperature (20oC), rw = 998 kg/m3 and ra = 1.20 kg/m3

## Slide 11: Rainfall patterns in the US

## Slide 12: Global precipitation pattern

## Slide 13: Spatial Representation
Isohyet – contour of constant rainfall
Isohyetal maps are prepared by interpolating rainfall data at gaged points.
Austin, May 1981
Wellsboro, PA 1889

## Slide 14: Texas Rainfall Maps

## Slide 15: Temporal Representation
Rainfall hyetograph – plot of rainfall depth or intensity as a function of time
Cumulative rainfall hyetograph or rainfall mass curve – plot of summation of rainfall increments as a function of time
Rainfall intensity – depth of rainfall per unit time

## Slide 16: Rainfall Depth and Intensity

## Slide 17: Incremental Rainfall
Rainfall Hyetograph

## Slide 18: Cumulative Rainfall
Rainfall Mass Curve

## Slide 19: Arithmetic Mean Method
Simplest method for determining areal average
P1
P2
P3
P1 = 10 mm
P2 = 20 mm
P3 = 30 mm
Gages must be uniformly distributed
Gage measurements should not vary greatly about the mean

## Slide 20: Thiessen polygon method
P1
P2
P3
A1
A2
A3
Any point in the watershed receives the same amount of rainfall as that at the nearest gage
Rainfall recorded at a gage can be applied to any point at a distance halfway to the next station in any direction
Steps in Thiessen polygon method
  Draw lines joining adjacent gages
  Draw perpendicular bisectors to the lines created in step 1
  Extend the lines created in step 2 in both directions to form representative areas for gages
  Compute representative area for each gage
  Compute the areal average using the following formula
P1 = 10 mm, A1 = 12 Km2
P2 = 20 mm, A2 = 15 Km2
P3 = 30 mm, A3 = 20 km2

## Slide 21: Isohyetal method
P1
P2
P3
10
20
30
Steps
  Construct isohyets (rainfall contours)
  Compute area between each pair of adjacent isohyets (Ai)
  Compute average precipitation for each pair of adjacent isohyets (pi)
  Compute areal average using the following formula
A1=5 , p1 = 5
A2=18 , p2 = 15
A3=12 , p3 = 25
A4=12 , p3 = 35

## Slide 22: Inverse distance weighting
P1=10
P2= 20
P3=30
Prediction at a point is more influenced by nearby measurements than that by distant measurements
The prediction at an ungaged point is inversely proportional to the distance to the measurement points
Steps
  Compute distance (di) from ungaged point to all measurement points.
  Compute the precipitation at the ungaged point using the following formula
d1=25
d2=15
d3=10
p

## Slide 23: Rainfall interpolation in GIS
Data are generally available as points with precipitation stored in attribute table.

## Slide 24: Rainfall maps in GIS
Nearest Neighbor “Thiessen” Polygon Interpolation
Spline Interpolation

## Slide 25: NEXRAD
NEXRAD Tower
NEXt generation RADar: is a doppler radar used for obtaining weather information
A signal is emitted from the radar which returns after striking a rainfall drop
Returned signals from the radar are analyzed to compute the rainfall intensity and integrated over time to get the precipitation
Working of NEXRAD

## Slide 26: NEXRAD WSR-88D Radars in Central Texas (Weather Surveillance Radar-1988 Doppler) scanning range = 230 km
Stage I: Just Radar
Stage II: gages, satellite, and surface temperature
Stage III: Continuous mosaic from radar overlaps
NEXRAD Products:
Source: PBS&J, 2003
EWX – NEXRAD Radar in New Braunfels
Notes: One of the strong motivation points for integration is the availability of
good quality precipitation estimates at higher temporal and spatial resolutions to feed engineering models!!
In particular the NEXRAD products of the NWS that now provide “true spatial realizations of rainfall fields”
With historical and real time sources

## Slide 27: NEXRAD data
NOAA’s Weather and Climate Toolkit (JAVA viewer)
  http://www.ncdc.noaa.gov/oa/wct/
West Gulf River Forecast Center
  http://www.srh.noaa.gov/wgrfc/
National Weather Service Precipitation Analysis
  http://www.srh.noaa.gov/rfcshare/precip_analysis_new.php