## Slide 1: CE 374K Hydrology, Lecture 4 Atmosphere and Atmospheric water
Energy balance of the earth
Drought in Texas
Atmospheric circulation
Atmospheric water
Reading for next Tuesday – Applied Hydrology, Sections 3.4 to 3.4 Precipitation

## Slide 2: Energy Balance of Earth
http://www.uwsp.edu/geo/faculty/ritter/geog101/textbook/energy/radiation_balance.html
6
4
100
70
51
21
26
38
6
20
15
Sensible heat flux 7
Latent heat flux 23
19

## Slide 3: Net Radiation
Mean annual net radiation over the earth and over the year is 105 W/m2
http://geography.uoregon.edu/envchange/clim_animations/flash/netrad.html

## Slide 4: Energy Balance in the San Marcos Basin from the NARR (July 2003)
Average fluxes over the day
310
72
415
495
3
61
112
Net Shortwave = 310 – 72 = 238; Net Longwave = 415 – 495 = - 80
Note the very large amount of longwave radiation exchanged between land and atmosphere

## Slide 5
Increasing carbon dioxide in the atmosphere (from about 300 ppm in preindustrial times)
We are burning fossil carbon (oil, coal) at 100,000 times the rate it
was laid down in geologic time

## Slide 6: Absorption of energy by CO2

## Slide 7: Drought Monitor for Texas
http://droughtmonitor.unl.edu/archive.html

## Slide 8: Trends in Drought in Texas
Currently, 91% of Texas is in some form of drought

## Slide 9
In the summer of 2011, Texas and Oklahoma experienced the hottest summer ever recorded in the history of the United States
Source: John Nielson-Gammon

## Slide 10
Sources: Danny Reible, John Nielson-Gammon
What does the future hold?
Temperature is expected to rise…
whether due to natural variations or anthropogenic causes
As temperatures rise, rain decreases….

## Slide 11: Heating of earth surface
Heating of earth surface is uneven
  Solar radiation strikes perpendicularly near the equator (270 W/m2)
  Solar radiation strikes at an oblique angle near the poles (90 W/m2)
Emitted radiation is more uniform than incoming radiation
Amount of energy transferred from equator to the poles is approximately 4 x 109 MW

## Slide 12: Hadley circulation
Warm air rises, cool air descends creating two huge convective cells.
Atmosphere (and oceans) serve to transmit heat energy from the equator to the poles

## Slide 13: Atmospheric circulation
Tropical Easterlies/Trades
Westerlies
Polar easterlies
Intertropical convergence zone (ITCZ)/Doldrums
Horse latitudes
Subpolar low
Polar high
Ferrel Cell
Polar Cell
Hadley cell
Ferrel Cell
Polar cell
Latitudes
Winds
Circulation cells

## Slide 14: Shifting in Intertropical Convergence Zone (ITCZ)
Owing to the tilt of the Earth's axis in orbit, the ITCZ shifts north and south.
Southward shift in January
Northward shift in July
Creates wet Summers (Monsoons) and dry winters, especially in India and SE Asia

## Slide 15: Structure of atmosphere

## Slide 16: Atmospheric water
Atmospheric water exists
  Mostly as gas or water vapor
  Liquid in rainfall and water droplets in clouds
  Solid in snowfall and in hail storms
Accounts for less than 1/100,000 part of total water, but plays a major role in the hydrologic cycle

## Slide 17: Water vapor
Suppose we have an elementary volume of atmosphere dV and
we want quantify how much water vapor it contains
Atmospheric gases:
Nitrogen – 78.1%
Oxygen – 20.9%
Other gases ~ 1%
http://www.bambooweb.com/articles/e/a/Earth's_atmosphere.html
dV
ma = mass of moist air
mv = mass of water vapor
Water vapor density
Air density

## Slide 18: Specific Humidity, qv
Specific humidity measures the mass of water vapor per unit mass of moist air
It is dimensionless

## Slide 19: Vapor pressure, e
Vapor pressure, e, is the pressure that water vapor exerts on a surface
Air pressure, p, is the total pressure that air makes on a surface
Ideal gas law relates pressure to absolute temperature T, Rv is the gas constant for water vapor
0.622 is ratio of mol. wt. of water vapor to avg mol. wt. of dry air (=18/28.9)

## Slide 20: Saturation vapor pressure, es
Saturation vapor pressure occurs when air is holding all the water vapor
that it can at a given air temperature
Vapor pressure is measured in Pascals (Pa), where 1 Pa = 1 N/m2
1 kPa = 1000 Pa

## Slide 21: Relative humidity, Rh
es
e
Relative humidity measures the percent
of the saturation water content of the air
that it currently holds (0 – 100%)

## Slide 22: Dewpoint Temperature, Td
e
Dewpoint temperature is the air temperature
at which the air would be saturated with its current
vapor content
T
Td

## Slide 23: Water vapor in an air column
We have three equations describing column:
  Hydrostatic air pressure, dp/dz = -rag
  Lapse rate of temperature, dT/dz = - a
  Ideal gas law, p = raRaT
Combine them and integrate over column to get pressure variation elevation
Column
Element, dz
1
2

## Slide 24: Precipitable Water
In an element dz, the mass of water vapor is dmp
Integrate over the whole atmospheric column to get precipitable water,mp
mp/A gives precipitable water per unit area in kg/m2
Column
Element, dz
1
2
Area = A

## Slide 25: Precipitable Water
http://geography.uoregon.edu/envchange/clim_animations/flash/pwat.html
25 mm precipitable water divides frontal from thunderstorm rainfall
Frontal rainfall in the winter
Thunderstorm rainfall in the summer