## Slide 1: Geographic Information Systems in Hydrology
Presented by Dr. Tim Whiteaker
The University of Texas at Austin
3 May, 2011

## Slide 2: Outline
What is GIS
Data Types
Data Models
Data Sources
Software

## Slide 3: Geographic Information Systems (GIS)
A GIS consists of software, data, and services for visualizing and analyzing spatially referenced information.
Notes: Google Maps is an example of a GIS. The map gives you a pretty picture, but the features in the map are smart. The roads know how long it takes to travel along them and which other roads they are connected to, allowing the software to compute directions and travel times. The map consists of different layers, and I can swap out the background map for satellite imagery while still keeping the roads and street names visible.

## Slide 4: StreamStats http://water.usgs.gov/osw/streamstats
Notes: StreamStats is a GIS application for hydrology

## Slide 5
GIS uses an information model based on inventory of data layers

## Slide 6: Spatial Data: Vector format
Point - a pair of x and y coordinates
(x1,y1)
Line - a sequence of points
Polygon - a closed set of lines
Node
vertex
Notes: DRM

## Slide 7: Some Vector Hydrology Layers
Vector data: point, line or polygon features

## Slide 8: Austin’s Flood Early Warning System (FEWS)
FEWS Gage measuring water level and rainfall at a low water crossing
Image: Susan Janek, City of Austin

## Slide 9: Attributes of a Selected Feature

## Slide 10: A raster is a matrix of identically-sized square cells. Each cell holds a numeric value that measures an attribute (like elevation) for that unit of space.
Spatial Data: Raster format

## Slide 11: Raster Properties
Number
of
rows
Number of Columns
(X,Y)
Cell size
NODATA cell

## Slide 12: Some Raster Layers
Santa Barbara, California

## Slide 13: Raster Calculator
Precipitation
-
Losses (Evaporation, Infiltration)
=
Runoff
5
2
2
3
2
4
3
3
7
6
5
6
-
=
Cell by cell evaluation of mathematical functions
Example

## Slide 14: 3D Data Types
Triangulated Irregular Network (TIN)
Multipatch

## Slide 15: Linking Geographic Information Systems and Water Resources
GIS
Water
Resources

## Slide 16: Terrain Processing: Computing Watersheds from Elevation Data
Raw DEM
Pit Removal (Filling)
Flow Field
Channels, Watersheds, Flow Related Terrain Information
Notes: This slide shows the general model for deriving flow field related derivative surfaces from digital elevation data. The input is a raw digital elevation model, generally elevation values on a grid. This is basic information used to derive further hydrology related spatial fields that enrich the information content of this basic data. The first step is to remove sinks, either by filling, or carving. Then a flow field is defined. This enables the calculation of flow related terrain information. My focus has been on flow related information working within this framework. I try to leave other GIS functionality, like radiation exposure, line of sight analyses and visualization to others. I have distributed my software in ways that it easily plugs in to mainstream systems, such as ArcGIS to enhance ease of use.

## Slide 17
3-D detail of the Tongue river at the WY/Mont border from LIDAR.
Roberto Gutierrez
University of Texas at Austin

## Slide 18
80
74
63
69
67
56
60
52
48
80
74
63
69
67
56
60
52
48
30
Slope:
Hydrologic Slope
- Direction of Steepest Descent
30
(67-48)/(30*(2^0.5)) = 0.45
(67-52)/30 = 0.50

## Slide 19
32
16
8
64
4
128
1
2
Eight Direction Pour Point Model
Value indicates direction of flow

## Slide 20
2
2
4
4
8
1
4
16
1
2
4
8
4
4
1
2
4
8
2
4
4
4
4
2
1
Flow Direction Grid
32
16
8
64
4
128
1
2

## Slide 21
Grid Network

## Slide 22
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
10
1
0
14
4
1
19
1
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
10
1
0
1
4
14
19
1
Flow Accumulation Grid.
Area draining in to a grid cell

## Slide 23
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
10
1
0
1
4
14
19
1
Flow Accumulation >= 10 Cell Threshold
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
1
0
4
1
1
10
14
19
Stream Network for 10 cell Threshold Drainage Area

## Slide 24
Watershed Draining to Outlet

## Slide 25: The Pit Removal Problem
DEM creation results in artificial pits in the landscape
A pit is a set of one or more cells which has no downstream cells around it
Unless these pits are removed they become sinks and isolate portions of the watershed
Pit removal is first thing done with a DEM

## Slide 26: Pit Filling
Increase elevation until the pit drains to a neighbor

## Slide 27
+
=
 Take a mapped stream network and a DEM
 Make a grid of the streams
 Raise the off-stream DEM cells by an arbitrary elevation
increment
 Produces "burned in" DEM streams = mapped streams
“Burning In” the Streams

## Slide 28
172
201
204
202
206
203
209
Each link has a unique identifying number
Stream Segments

## Slide 29
Vectorized Streams Linked Using Grid Code to Cell Equivalents
Vector
Streams
Grid
Streams

## Slide 30
DrainageLines are drawn through the centers of cells on the stream links. DrainagePoints are located at the centers of the outlet cells of the catchments

## Slide 31: Catchments
For every stream segment, there is a corresponding catchment
Catchments are a tessellation of the landscape through a set of physical rules

## Slide 32: Raster Zones and Vector Polygons
Catchment GridID
Vector Polygons
DEM GridCode
Raster Zones
3
4
5
One to one connection

## Slide 33
Catchments, DrainageLines and DrainagePoints of the San Marcos basin

## Slide 34: Summary of Key Processing Steps
[DEM Reconditioning]
Pit Removal (Fill Sinks)
Flow Direction
Flow Accumulation
Stream Definition
Stream Segmentation
Catchment Grid Delineation
Raster to Vector Conversion (Catchment Polygon, Drainage Line, Catchment Outlet Points)

## Slide 35: Arc Hydro: GIS for Water Resources
Arc Hydro
  An ArcGIS data model for water resources
  Arc Hydro toolset for implementation
  Framework for linking hydrologic simulation models
The Arc Hydro data model and
application tools are in the public
Domain.
Published in 2002, now in revision for Arc Hydro II

## Slide 36: Arc Hydro — Hydrography
The blue lines on maps

## Slide 37: Arc Hydro — Hydrology
The movement of water through the hydrologic system

## Slide 38: Tracing Path of Water Movement
Relationships between
features linked by HydroID

## Slide 39
Flow
Time
Time Series
Hydrography
Hydro Network
Channel System
Drainage System
Arc Hydro Components

## Slide 40
Streams
Watersheds
Waterbody
Hydro Points
Arc Hydro Framework
Notes: The Arc Hydro Framework is a simplified version of the full Arc Hydro data model designed for an entry level user who just wants to put together a basic data set for streams, watersheds, waterbodies and hydro points like stream gages and water quality monitoring points

## Slide 41: Network Definition
A network is a set of edges and junctions that are topologically connected to each other.

## Slide 42: Hydrologic Networks
Hydrologic data includes:
  Single-line streams
  Double-line streams
  Braided streams
  Manmade channel systems
  Waterbodies

## Slide 43: Network Flow Direction
Enable flow in flow-paths
Disable flow in shorelines
Sink
Flow direction is known

## Slide 44: Network Tracing
Trace Upstream
Trace Downstream

## Slide 45
Hydro Network Junctions

## Slide 46
Connecting Drainage Areas
using Relationships

## Slide 47: Space-time datasets

## Slide 48: Variable Definition table
Catalog of time varying parameters (e.g. streamflow, water levels, concentrations, etc.)
Each variable is indexed with a HydroID

## Slide 49: TimeSeries table
Each measurement is indexed by space, time, and type
Space = FeatureID
Time = TsTime
Type = VarID
VarID provides information on the variable

## Slide 50: Time series views
We can “slice” through the data cube to get specific views of the data
Query by location
(FeatureID = 2791)
Where?
2791
TsTime
FeatureID
VarID
Query by type
(VarID = 6875)
What?
FeatureID
VarID
TsTime
6875
Query by location and type
(FeatureID = 2791 VarID = 6875)
Where and What?
2791
FeatureID
VarID
TsTime
6875

## Slide 51: Time series views
Well HydroID = 2791
Create a plot of time series related to a feature
Get all the data of VarID 6875 measured at Feature 2791

## Slide 52: Time series views
Water level in the Edwards Aquifer in 1/1999
1/1991
FeatureID
VarID
6875
TsTime
FeatureID
VarID
TsTime

## Slide 53: Multi-variable time series
Variables (VarKey)
Multiple variables recorded simultaneously at the same location
Example – water quality parameters
Indexed by location (FeatureID), and time (TsTime)
Relationship to the VariableDefinition table is through the VarKey

## Slide 54: Raster Series
January 1991
January 1992
January 1993
Raster datasets indexed by time
Each raster represents a continuous surface describing a variable for a given time

## Slide 55: Feature Series
A collection of features indexed by time
Example of particle tracks
Features are indexed by VarID, TsTime, and GroupID
Each group of features creates a track over time

## Slide 56: Arc Hydro Groundwater Book 2011

## Slide 57: Arc Hydro Data Model
Arc Hydro
Framework
Surface water
Network
Groundwater
Boreholes
Drainage
Hydrography
Channel
Hydrostratigraphy
Geology
Simulation
Temporal
  General model for representing water resources, including surface water components and groundwater components centered on a common framework
Notes: When we released the first draft of AHGW for review, we got back comments that asked for tighter integration of the surface water data model and the groundwater data model.
We redesigned both data models to be structured around an Arc Hydro Framework (in green in the center).
Then the data models were broken into components that represent a specific aspect or type of datasets.
The temporal component deals with managing temporal data, and is shared by both data models. E.g., you can store surface water and groundwater time series in the same tables, and apply the same tools to map data.
You don’t have to implement all components, if you are dealing only with simulation model you just implement the simulation component.

## Slide 58: Components
Framework – Surface water features, wells, and aquifers
Temporal – Representation of time series data
Geology – Representation of data from geologic maps
Boreholes – Borehole log table and 3D description of borehole lines and contact points
Hydrostratigraphy – 2D and 3D description of hydrogeologic units
Simulation – Representation of groundwater simulation models

## Slide 59: Framework
Notes: On the left feature classes from the surface water data model – hydrography (points, lines, polygons) – the “Blue Lines” on maps.
Aquifer and Well features
Time Series – tabular structure for managing time series related with spatial features.
Time series are related to monitoring points and to wells.
The graph shows the change in water levels and streamflow.

## Slide 60: Components
Framework – Surface water features, wells, and aquifers
Temporal – Representation of time series data
Geology – Representation of data from geologic maps
Boreholes – Borehole log table and 3D description of borehole lines and contact points
Hydrostratigraphy – 2D and 3D description of hydrogeologic units
Simulation – Representation of groundwater simulation models

## Slide 61: Components
Framework – Surface water features, wells, and aquifers
Temporal – Representation of time series data
Geology – Representation of data from geologic maps
Boreholes – Borehole log table and 3D description of borehole lines and contact points
Hydrostratigraphy – 2D and 3D description of hydrogeologic units
Simulation – Representation of groundwater simulation models

## Slide 62: Geology
Representation of data from geologic maps
Simplified data model – not comprehensive geologic map design

## Slide 63: Components
Framework – Surface water features, wells, and aquifers
Temporal – Representation of time series data
Geology – Representation of data from geologic maps
Boreholes – Borehole log table and 3D description of borehole lines and contact points
Hydrostratigraphy – 2D and 3D description of hydrogeologic units
Simulation – Representation of groundwater simulation models

## Slide 64: BoreholeLog table
Combining the well geometry (x, y) and the vertical data stored in the BoreholeLog table we can describe a set of 3D geometries (x, y, z)
Notes: The Well feature gives the 2D location (X, Y coordinates).
Vertical borehole data are related to the well via the HydroID – WellID relationship.
The example shows data stored in the BoreholeLog table representing hydrostratigraphy.
You can see that a set of hydrogeologic picks (elevation is given by TopElev) have the same WellID – pointing to well 3266.
The top left figure shows the stratigraphy in a conceptual diagram.

## Slide 65: 3D features (BorePoints and BoreLines)
From the tabular data we create 3D features that can be viewed in ArcScene.
Notes: From the tabular data we can create 3D features that can be visualized in ArcScene.
On the left – BorePoints (3D points) representing hydrogeologic picks (top of a formation)
On the right – BoreLine features representing hydrostratigraphy as 3D intervals (3D line features).

## Slide 66: Components
Framework – Surface water features, wells, and aquifers
Temporal – Representation of time series data
Geology – Representation of data from geologic maps
Boreholes – Borehole log table and 3D description of borehole lines and contact points
Hydrostratigraphy – 2D and 3D description of hydrogeologic units
Simulation – Representation of groundwater simulation models

## Slide 67: GeoSections
Notes: GeoSections represent 3D panels (“slices”) of the subsurface.
GeoSections are represented as multipatch features (3D features) that can be rendered in ArcScene.
The GeoSection features shown here are from a subsurface model near Roseville California.
The sections were created by “slicing” a set of “stacked” rasters. Each raster represents the top of a hydrogeologic unit.

## Slide 68: 2D Cross Sections
Notes: The XS2D component is used to create 2D cross sections in ArcMap.
The cross sections are displayed in “special” data frames.
To create a 2D cross section in ArcMap – we transform the Y coordinate to a Z coordinate.
Also, in many cases we apply an exaggeration factor to better visualize the data.

## Slide 69: GeoRasters
Notes: GeoRasters – store rasters in a raster catalog
Rasters can be indexed with a HGUID ( hydrogeologic unit identifier).
We also index with a HorizonID – gives the sequence of deposition from bottom to top.
Cataloging the rasters enables us to use tools to create 3D features - cross sections, volumes.

## Slide 70: GeoVolumes
Notes: GeoVolume - represents hydrogeologic units as 3D elements.
GeoVolumes are 3D multipatches.
Can be built with SA tools by filling between rasters in a GeoRaster catalog.

## Slide 71: Components
Framework – Surface water features, wells, and aquifers
Temporal – Representation of time series data
Geology – Representation of data from geologic maps
Boreholes – Borehole log table and 3D description of borehole lines and contact points
Hydrostratigraphy – 2D and 3D description of hydrogeologic units
Simulation – Representation of groundwater simulation models

## Slide 72: Simulation Feature Data Set
Notes: On top of the simulation component a custom data model for representing MODFLOW models have been developed.
We call this the MODFLOW Data Model – will expand at the later parts of the course.
The simulation component includes 5 feature classes:
  Boundary for giving the spatial location and orientation of the model
  Cell2D and Node2D represent a 2D model mesh/grid, or one layer in a 3D model.
  Cell3D and Node3D represent 3D models meshes/grids.
The CellIndex table is used to associate cells and nodes of the model based on the I, J, and K indices. It is part of the MODFLOW Data Model.

## Slide 73: GIS Data Sources

## Slide 74: Useful Links
TNRIS - http://www.tnris.state.tx.us/
USGS - http://water.usgs.gov/maps.html
ArcGIS.com - http://www.arcgis.com/
Geodata.gov - http://www.geodata.gov/
Dr. Maidment’s links (from his home page)
  http://www.caee.utexas.edu/prof/maidment/gishydro/docs/websites/othr_web.htm

## Slide 75: Watersheds of the US
2-digit water resource regions
8-digit HUC watersheds

## Slide 76: Watershed Hierarchy
8 HUC
4
2
6
NHDPlus
10
12
Digit #

## Slide 77
River networks shown
for 8-digit HUC watersheds
http://nhd.usgs.gov/

## Slide 78: NHDPlus Reach Catchments ~ 3km2
About 1000 reach catchments in each 8-digit HUC
Average reach length = 2km
2.3 million reaches for continental US

## Slide 79: NHDPlus Reach Attributes
Slope
Elevation
Mean annual flow
  Corresponding velocity
Drainage area
% of upstream drainage area in different land uses
Stream order

## Slide 80: HydroSheds derived from SRTM
http://hydrosheds.cr.usgs.gov/

## Slide 82
http://www.ncgc.nrcs.usda.gov/products/datasets/statsgo/
1:250,000 Scale Soil Information
Notes: State Soil Geographic

## Slide 83
http://www.ncgc.nrcs.usda.gov/products/datasets/ssurgo/
1:24,000 scale
soil information
SSURGO:
County Level
Digital Soil Maps
Notes: Survey Soil Geographic

## Slide 84: SSURGO for Travis County
103 soil map units described by 7530 polygons of average area 35.37 ha (87 acres)

## Slide 85: National Land Cover Dataset
http://seamless.usgs.gov/
Get the data:

## Slide 86: PRISM Mean Annual Precipitation
http://www.wcc.nrcs.usda.gov/climate/prism.html
Notes: Parameter-elevation Regressions on Independent Slopes Model. Monthly, too.

## Slide 87
http://www.daymet.org/
Notes: daily surfaces of temperature, precipitation, humidity, and radiation

## Slide 88: CUAHSI-HIS
http://his.cuahsi.org
56 public services
18,000+ variables
1.88+ million sites
23.3 million series
Referencing 5.1 billion data values

## Slide 89: GIS Software

## Slide 91: ArcMap
Create
maps
View and
edit data
Analyze data
(Geoprocessing)

## Slide 92: ArcCatalog
View data
(like Windows Explorer)
Graphical
previews
Metadata
Tables

## Slide 93: ArcToolbox
Map Projections
Tools for commonly used tasks

## Slide 94: Geoprocessing
Toolbox tools linked together using the model builder to automate data processing

## Slide 95: Desktop, Server, Web
Desktop GIS

## Slide 96: World Topographic Base Map
With content added by the City of Austin
Cartographic map built from GIS data

## Slide 97: ArcGIS.com

## Slide 98: Google Earth 3D With Terrain

## Slide 99: HydroDesktop (DotSpatial)
http://hydrodesktop.codeplex.com/

## Slide 100: Where Is GIS Going?
Cloud
  Basemaps
  Online operational layers
  Processing services (watershed delineation)
Mobile
Volunteered geographic information
Sharing
Mashups

## Slide 101: Web Services HUB
USGS
LCRA
NWS
COA
NDFD
Web Services HUB
Inputs
Data
Services
(WaterML)
Mapping
Services
Models
Flood Mapping
Services
Maps
Outputs
Modeling
Services
Data and Mapping
Services
Data
Services
(WaterML)
Mapping
Services

## Slide 102: ArcGIS Resource Centers http://resources.arcgis.com
Desktop
Help

## Slide 103: Hydro Resource Center
http://resources.arcgis.com/content/hydro/

## Slide 104: Data.CRWR Blog
http://data.crwr.utexas.edu/blog/