## Slide 1: A Statistical Analysis and Geospatial Distribution of Soil Moisture in Texas
Flood Forecasting
February 11th, 2015
Gonzalo E. Espinoza
Center for Research in Water Resources

## Slide 2: Outline
Land Assimilation System (LDAS)
  NLDAS NOAH and soil moisture
Statistical Analysis
  Cumulative Distribution Functions (CFDs)
  Applications
    Texas Drought 2011
    “Halloween Flood”. Onion Creek, 2013
Web Application Architecture
  Client
  Server
  Cloud
Work in progress

## Slide 3: Land Assimilation System (LDAS)
Land-surface hydrologic model
Global (GLDAS ) National (NLDAS)
NOAH NLDAS-2
  Variables ~ 52
  Hourly and Monthly data
  1/8° cellsize ~14km
  Data since 1979
http://ldas.gsfc.nasa.gov/nldas/NLDASgoals.php

## Slide 4: NLDAS NOAH & Soil moisture
Soil Moisture in the top meter
Top meter (4 layers)
  0-10cm
  10-40cm
  40-60cm
  60cm-100
Kg of water/m^2
Equivalent depth of water (mm)
http://ldas.gsfc.nasa.gov/nldas/NLDAS2model.php

## Slide 5: Statistical Analysis
Soil Moisture
-Variable
-Time
-Space
Time Series
Quad: 30097-C6
Date: 12/04/2014
NLDAS Data
CDF modelling
Empirical CFD calculation
CDFs construction
-Time step (day)
-Cell size (1/8°)
-Soil Moisture
-Evapotranspiration
-Precipitation
-Runoff
-Temperature
Cell
Day
Soil Moisture
Variables
Quad: 30097-C6
Date: June, 15th
Cloud Storage
Validation
Implementation
  Python/R
  HPC
Results
  Cloud
  Web app
http://texassoilmoisture.azurewebsites.net

## Slide 6: Cumulative Distribution Functions (CFDs)
Daily values for each cell
  4,136 cells
  1979 – 2013
Cumulative Distribution Functions (CDFs)
  For each cell and each day
  Statistical parameters (min, max, mean, standard deviation, etc.)
Comparing the latest soil moisture value
    Cell
    Day of the year
West: El Paso
Central: North of Austin
Coast: South of Houston
Examples:

## Slide 7: Cumulative Distribution Functions (CFDs)
West: El Paso
Central: North of Austin
Coast: South of Houston

## Slide 8: Cumulative Distribution Functions (CFDs)
West
Central
Coast

## Slide 9: Applications: Texas Drought 2011
September 2011
5% percentile
Anomaly -55mm

## Slide 10: Applications: Onion Creek, 10/31/2013
Drainage Area: 730km2
Pre-storm soil moisture 87% percentile

## Slide 11: Web Application Architecture
Azure cloud
  Storage
  Django
ArcGIS
  Mapping
  Javascript
NASA
  Data rods
Microsoft Azure
Storage Account
Django (python)
ArcGIS server
ArcGIS API for JavaScript
Client-Side
Cloud deployment
Server-Side
User
Web App
Hydrologic Data
NLDAS web services
Geographic data
Latest Values
Site & Date
stats
Web Deployment
Web app framework
Stats
http://texassoilmoisture.azurewebsites.net

## Slide 12: Work in progress
Process more variables
  Precipitation
  Runoff
  Evapotranspiration
  Temperature
Update the website design
  Layout
  Latest values
  Data storage communication
Improve the performance of the cloud storage
Risk scenarios
  Relationship between variables