## Slide 1: Flood flow prediction in a river system using artificial neural network: Case study Guadalupe Basin
Ahmad Tavakoly
April 2010

## Slide 2
Importance of Flow Forecast
Optimize the Water Resources System
Warning system for approaching flood
Regulating reservoir outputs

## Slide 3: Why ANNs?
Limit inputs vs. a large number of inputs for distributed models
Computationally fast and reliable
Not expensive
ANN solution is obtained through an optimization process...

## Slide 4: How do ANNs work?
Random mapping between an input and an output.
The input layer neurons Transmit the values to the next layer
A typical ANN consists three layers namely, input, hidden, and output

## Slide 5: How do ANNs work?
data passing through one neuron to another are multiplied by the weights
Weights control the strength of the passing signal
Optimized weight has a minimum MSE of the difference between results and observed data
Sum of the product transferred by a special functions

## Slide 6: Transfer functions
wji= weight of the connection joining the jth node in a layer with the ith node in the previous layer; and xi= value of the ith node in the previous layer

## Slide 7: A typical feed-forward ANN
Input
Output
Hidden Layer
Input
Input
Input

## Slide 8: Qnet

## Slide 9: Case Study

## Slide 10: Precipitation Gages

## Slide 11: Data: Flow Rate and Precipitation
http://www1.ncdc.noaa.gov/pub/orders/CDO2735594221956.html
http://waterdata.usgs.gov/nwis/nwisman/?site_no=08175800
Daily Data: Time Period
01/01/2008-04/15/2010

## Slide 12: Input Patter: Gonzales Station
pattern | Input data
1 | QKyle (t-2), Qsattler (t-2), Qluing (t-2)
2 | QKyle (t-1), Qsattle(t-1), Qluing(t-1)
3 | QKyle (t-2), Qsattler (t-2), Qluing (t-2) , QKyle (t-1), Qsattle(t-1), Qluing(t-1)
4 | QKyle (t-2), Qsattler (t-2), Qluing (t-2) , QKyle (t-1), Qsattle(t-1), Qluing(t-1), Qgonzales (t-1)
5 | QKyle (t-2), Qsattler (t-2), Qluing (t-2), PSeguin1 (t-1), Pkingsbury (t-1), Pluling (t-1),PLuling12 (t-1)
6 | QKyle (t-2), Qsattler (t-2), Qluing (t-2), PSeguin1 (t-2), Pkingsbury (t-2), Pluling (t-2),PLuling12 (t-2)

## Slide 13: Flow prediction: Gonzales Station, Training
pattern | R2 | RMS Error | Transfer Function
1 | 0.8 | 0.051 | Sigmoid
1 | 0.8 | 0.048 | Hyperbolic Tangent
2 | 0.91 | 0.027 | Sigmoid
2 | 0.92 | 0.022 | Hyperbolic Tangent
3 | 0.93 | 0.015 | Sigmoid
3 | 0.945 | 0.0135 | Hyperbolic Tangent
4 | 0.95 | 0.014 | Sigmoid
4 | 0.96 | 0.013 | Hyperbolic Tangent
5 | 0.93 | 0.018 | Sigmoid
5 | 0.93 | 0.013 | Hyperbolic Tangent
6 | 0.845 | 0.044 | Sigmoid
6 | 0.862 | 0.042 | Hyperbolic Tangent

## Slide 14: Flow prediction: Gonzales Station, Verifying
pattern | R2 | RMS Error | Transfer Function
1 | 0.81 | 0.063 | Sigmoid
1 | 0.84 | 0.055 | Hyperbolic Tangent
2 | 0.84 | 0.070 | Sigmoid
2 | 0.85 | 0.075 | Hyperbolic Tangent
3 | 0.83 | 0.052 | Sigmoid
3 | 0.85 | 0.053 | Hyperbolic Tangent
4 | 0.89 | 0.03 | Sigmoid
4 | 0.91 | .028 | Hyperbolic Tangent
5 | 0.83 | 0.06 | Sigmoid
5 | 0.83 | 0.06 | Hyperbolic Tangent
6 | 0.85 | .053 | Sigmoid
6 | 0.86 | .053 | Hyperbolic Tangent

## Slide 15: Calibration: Gonzales
Chart: Time(day)

## Slide 16: Gonzales: Comparison of predicted and measured data

## Slide 17: Sensitivity Analysis
Input Node |  | Percent Contribution
1 | Sattler(t-1) | 2.06
2 | Sattler(t-2) | 3.62
3 | Kyle(t-1) | 10.66
4 | Kyle(t-2) | 6.59
5 | Luling(t-1) | 31.52
6 | Luling(t-2) | 21.72
7 | Gonzales(t-1) | 23.83

## Slide 18: Input Pattern: Cuero Station
pattern | Input data
1 | Qgonzales (t-2), Qdilworth (t-2), Qwesthoff (t-2)
2 | Qgonzales (t-1), Qdilworth (t-1), Qwesthoff (t-1)
3 | Qgonzales (t-2), Qdilworth (t-2), Qwesthoff (t-2), Qgonzales (t-1), Qdilworth (t-1), Qwesthoff (t-1)
4 | Qgonzales (t-2), Qdilworth (t-2), Qwesthoff (t-2), Qgonzales (t-1), Qdilworth (t-1), Qwesthoff (t-1) QCuero (t-1)
5 | Qgonzales (t-2), Qdilworth (t-2), Qwesthoff (t-2), Pcheapside (t-1), Pgonzales (t-1), Pnixon (t-1),
6 | Qgonzales (t-2), Qdilworth (t-2), Qwesthoff (t-2), Pcheapside (t-2), Pgonzales (t-2), Pnixon (t-2),

## Slide 19: Flow prediction: Cuero Station, Training
pattern | R2 | RMS Error | Transfer Function
1 | 0.87 | 0.06 | Sigmoid
1 | 0.87 | 0.06 | Hyperbolic Tangent
2 | 0.90 | .037 | Sigmoid
2 | 0.90 | .035 | Hyperbolic Tangent
3 | 0.96 | 0.033 | Sigmoid
3 | 0.96 | 0.036 | Hyperbolic Tangent
4 | 0.98 | 0.03 | Sigmoid
4 | 0.98 | 0.025 | Hyperbolic Tangent
5 | 0.96 | 0.05 | Sigmoid
5 | 0.96 | 0.04 | Hyperbolic Tangent
6 | 0.90 | 0.05 | Sigmoid
6 | 0.90 | 0.048 | Hyperbolic Tangent

## Slide 20: Flow prediction: Cuero Station, Verifying
pattern | R2 | RMS Error | Transfer Function
1 | 0.81 | 0.07 | Sigmoid
1 | 0.81 | 0.07 | Hyperbolic Tangent
2 | 0.93 | 0.017 | Sigmoid
2 | 0.93 | 0.016 | Hyperbolic Tangent
3 | 0.93 | 0.016 | Sigmoid
3 | 0.93 | 0.016 | Hyperbolic Tangent
4 | 0.93 | 0.014 | Sigmoid
4 | 0.93 | 0.013 | Hyperbolic Tangent
5 | 0.91 | 0.031 | Sigmoid
5 | 0.91 | 0.033 | Hyperbolic Tangent
6 | 0.84 | 0.06 | Sigmoid
6 | 0.84 | 0.06 | Hyperbolic Tangent

## Slide 21: Calibration: Cuero
Chart: Time(day)

## Slide 22: Cuero: Comparison of predicted and measured data

## Slide 23: Sensitivity Analysis
Input Node |  | Percent Contribution
1 | Gonzales(t-1) | 16.17
2 | Gonzales(t-2) | 0.52
3 | Dilworth(t-1) | 28.93
4 | Dilworth(t-2) | 2.81
5 | Westhoff(t-1) | 39.74
6 | Westhoff(t-2) | 2.73
7 | Cuero(t-1) | 9.1

## Slide 24: Results
The ANN model was able to predict flow accurately.
Only flow rate can be define as input variables.
The model for Gonzales gage shows the highest Sensitivity to Qluing(t-1) and Qgonzales (t-1).
Qdilworth (t-1), Qwesthoff (t-1) have the begest effects on Flow rate at Cuero gage.

## Slide 25: Future Work
Work with more data (bigger time period)
Test the model
Write repot

## Slide 26: Thank you Question?
Manipulation Art: Zebrafrog by Jerico Santander